## Slide 1
R.A. Forrest
Nuclear Data Section
Department of Nuclear Sciences and Applications
Status of FENDL-3
and the future

## Slide 2: Contents
History of CRP
Status of FENDL-3
  n-,p-,d-induced GP
  Shadow library
  n-,p-,d-induced activation
  Processed files
Decisions
Testing
CRP Final report
Future work

## Slide 3: History
FENDL-2.1 dates from 2004
A Technical Meeting aiming at identifying possible detailed objectives for a CRP was held at October/November 2007
  1st RCM held December 2008
  2nd RCM held March 2010
  Web site http: //www-nds.iaea.org/fendl3

## Slide 4: Objectives
Update the FENDL-2.1 library with presently available evaluations
Extend the neutron induced library to energies up to 150 MeV
Include p- and d-induced general purpose and activation libraries for incident energies up to 150 MeV
Creation of a library based on model calculations which contains covariances files

## Slide 5: n-induced GP
180 materials
List available on FENDL-3 web site
Upper energy limit typically 150, 200 MeV but all files have upper limit ≥ 60 MeV
Covariance data still limited
  Complete - 11
  TENDL - 23
  Partial - 11
  None - 135
Some remaining problems

## Slide 6: p-induced GP
Same 180 materials as for n-induced
Based on TENDL-2011
Some replacements by better files from JENDL-HE and LA-150
Processing will be done during next 3 months

## Slide 7: d-induced GP
Same 180 materials as for n-induced
Based completely on TENDL-2011
Will use processed files produced by NRG

## Slide 8: Shadow library
Same 180 materials as for n-induced
Based completely on TENDL-2011
Contains complete covariances
Purpose:
  Calculation needs complete covariances
  Calculate with FENDL-3 (R1  DR1)
  Calculate with Shadow library (R2  DR2)
  Answer = R1  DR2 (check that R2 ≈ R1)

## Slide 9: n-induced Activation
  Identical to EAF-2010, but the EAF format file has been converted to ENDF format, including the uncertainty information
  A GND (xml) version is also available
  Can use the validation work that has already been done for EAF-2010

## Slide 10: p-induced Activation
  Based on EAF-2007
  Contains data for 67,925 reactions
  No uncertainty data
  Available in EAF format

## Slide 11: d-induced Activation
  Based on EAF-2007, but includes improved data for some channels
  Contains data for 66,864 reactions
  No uncertainty data
  Available in EAF format

## Slide 12: Processing (GP)
n-induced (Done)
  PEND files
  ACE files
  MG (211 groups, VITAMIN+) - upper limit is 55 MeV
p-induced (Soon)
  PEND files
  ACE files
d-induced (Done)
  PEND files
  ACE files

## Slide 13: Decisions
Missing reactions
Choice of data for low mass targets
Covariance data in n-induced GP not consistent, options to make file ‘clean’:
  Remove all covariance data
  Formally extend by raising upper limit
  Use TENDL data
211-group covariance library useful?
How to include ‘last minute’ improvements

## Slide 14: Testing and validation
Because of delays no testing has been done
CRP formally extended (but no extra money!) so that testing can be done over next 6 months
For GP files corrections will be made for a small number of materials
Files finalised 30 June 2012

## Slide 15: Final report
Discuss at this meeting
Include work of CRP participants
FENDL-3 library description
Validation results
Parts can be produced now, aim for completed version 30 Sept 2012

## Slide 16: The Future
Recognise that while FENDL-3 is a major step forward it is not as good as we can make it
Suggest that work continues as DDP during 2013 to respond to new data and feedback to replace data for materials
Aim for FENDL-3.1 (containing same set of materials and same energy range) at start of 2014
What else?

## Slide 17
Thank you all for your contributions!