Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo 4C-3/396

Date:		30 April 2014

To:		Distribution

From:		V. Semkova, N. Otsuka

Subject:		Dictionary 236 (Quantities) – NUM,PN; UNW,PN; ,PN

If the (- decay energy (Q() is larger than the two or more neutron separation energy (S2n, 3n…) of the product of the decay a process of multiple neutron emission may take place. The following quantities are defined for the cases when Q Sxn >0 (x=1,2,...):

- Pxn (x=1,2,3): probability to emit x β-delayed neutrons per decay

- Pn:	probability to emit at least one β-delayed neutron per decay (Pn= P1n+P2n+P3n+…)

- P’n:	multiplicity of β-delayed neutrons per decay (P′n=P1n+2P2n+3P3n+…)

The current description LEXFOR “Delayed Fission Neutrons” does not distinguish the multiplicity from probability. In the relation with the IAEA CRP on “Development of reference database for beta-delayed neutron emission”, we foresee compilation of above three quantities. We propose to keep the current quantity code ,PN for the multiplicity P’n, and also to add new quantity codes for Pxn and Pn.

Dictionary 236 (Quantities)

NUM,PN: 	probability for emission of N beta-delayed neutrons

UNW,PN:	probability for emission of at least one beta-delayed neutrons

,PN:		multiplicity of beta-delayed neutrons (P′n=P1n+2P2n+…)

| Quantity | Reaction Type | Dimension |
| --- | --- | --- |
| NUM,PN | PN | NO |
| UNW,PN | PN | NO |
| ,PN | PN | PN |

There is no consistent nomenclature established in the literature and Pn value is referred in some articles to the β-delayed neutron emission probability and in other articles to the multiplicity. However, the compilers should verify the meaning of the determined quantity. Free text explanation could be useful for users as well. For cases when only 1 beta-delayed neutron emission is feasible P′n≡ Pn. For consistency of the compilation in such cases UNW,PN coding is proposed.

In order to make each data set searchable not only by the precursor nuclide but also by the decay product, we would like to forbid use of the variable nuclide formalism ELEM/MASS in REACTION SF1 and to code the decay product always in REACTION SF4.

Revision to the LEXFOR entry is proposed at the end of this memo.

Example

Table 1 of T.Björnstad et al., Delayed neutron emission probabilities of 11Li, Nucl. Phys. A359 (1981) 1

| Quantity | Probability (%) |
| --- | --- |
| P1n | 85±1 |
| P2n | 4.1±0.4 |
| P3n | 1.9±0.2 |
| Pn | 91±1 |
| P′n | 98±1 |

(Pn value is not given in this article, but calculated for explanation of the coding rule.)

SUBENT        01230002   20140417

BIB

REACTION   (3-LI-11(0,B-),NUM,PN)

STATUS     (TABLE) Text (p6) of Nucl.Phys.A359(1981)1

ENDBIB

NOCOMMON

DATA

PART-OUT   DATA       DATA-ERR

NO-DIM     NO-DIM     NO-DIM

1.         0.85       0.01

2.         0.041      0.004

3.         0.019      0.002

ENDDATA

ENDSUBENT

SUBENT        01230003   20140417

BIB

REACTION   (3-LI-11(0,B-),UNW,PN)

STATUS     (TABLE) Private communication

ENDBIB

NOCOMMON

DATA

DATA       DATA-ERR

NO-DIM     NO-DIM

0.91       0.01

ENDDATA

ENDSUBENT

SUBENT        01230004   20140417

BIB

REACTION   (3-LI-11(0,B-),,PN)

COMMENT    Average multiplicity of beta-delayed neutron

STATUS     (TABLE) Text (p6) of Nucl.Phys.A359(1981)1

ENDBIB

NOCOMMON

DATA

DATA       DATA-ERR

PC/DECAY  PC/DECAY

98.         1.

ENDDATA

ENDSUBENT

## LEXFOR Entry (Addition and deletion to “Delayed fission neutrons”)

## Delayed-Neutron Emission Multiplicity (<n>)

Definition:  Multiplicity of (-delayed neutron per decay

REACTION Coding: (Z-S-A(0,B-)Z’-S’-A’,,PN)

where	Z-S-A is the precursor nucleus (i.e., before β-decay)

Z’-S’-A’ is the decay product nucleus (i.e., after β-decay)

Units: a code from Dictionary 25 with dimension PN (e.g., PC/DECAY)

## Delayed-Neutron Emission Probability (Pn value)

Definition:  Neutron yield per ( decay for a given nucleus.  This is a decay quantity of the fission product nucleus and is independent of the fissioning target nucleus.  It is related to the fission yield by

Pn = absolute delayed neutron yield / cumulative fission yield

REACTION Coding:

- ((Z-S-A(0,B-)Z’-S’-A’,,PN)  for a single fragment

where: 	Z-S-A is the fission product nucleus (precursor nucleus before ( decay);

Z'-S’-A’ is the delayed-neutron emitting fission fragment.

- (ELEM/MASS(0,B-),,PN)  for a series of fragments

The fission product nucleus is entered as a variable in the data table (see EXFOR Chapter 6: Variable Nucleus).

Units:  a code from Dictionary 25 with dimension PN (e.g., PC/DECAY)

Definition:  Probability for emission of at least one (-delayed neutron

REACTION Coding: (Z-S-A(0,B-)Z’-S’-A’,UNW,PN)

Units: a code from Dictionary 25 with dimension NO (e.g., NO-DIM)

## Delayed-Neutron Emission Probability (PNn value)

Definition:  Probability to emit N (-delayed neutrons (P1n, P2n,…)

REACTION Coding: (Z-S-A(0,B-)Z’-S’-A’,NUM,PN)

Units: a code from Dictionary 25 with dimension NO (e.g., NO-DIM)

The number of emitted neutrons is give under the data heading PART-OUT with units of NO-DIM.

From these definitions Pn=P1n+P2n+… and <n>=P1n+2P2n+… Especially Pn=<n> only one neutron emission is energetically possible, and ,PN must be always used. Note that some authors use the symbol “Pn” not for the probability but for the multiplicity.

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru, cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

iwamoto.osamu@jaea.go.jp

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kamskaya@expd.vniief.ru

kato@nucl.sci.hokudai.ac.jp

kiyoshi.matsumoto@oecd.org

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

sbabykina@yandex.ru

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn

cc:

p.dimitriou@iaea.org