RUSSIA NUCLEAR DATA CENTER - RNDC

Alias: CENTR JADERNYKH DANNYKH - CJD

Institute of Physics and Power Engineering - IPPE

Bondarenko Sq., 1,Obninsk 249033

Kaluga Region, RUSSIA

Telephone:	+7 (48439)98986 (A.Blokhin)

+7 (48439)98779 (M.Mikhaylyukova)

Fax:			+7 (48439)68225

Internet: 	www.ippe.ru/podr/cjd

MEMO CP-4/181

| DATE: | 9 March 2010 |
| --- | --- |
| TO: | Distribution |
| From: | M.Mikhaylyukova, A.Blokhin, V.Pronyaev |
| Subject: | Fission yields, for discussion at NRDC2010 Agenda 9.8 |

In EXFOR - reaction is defined as (SF1-SF4+ branch in SF5).

For fission yields:

SF1(*,F)SF4,SF5,FY,

*=0 – spontaneous fission,

*=N – neutron fission;

SF5 branch	= empty– all fission events considered,

= BIN – only binary fission events considered,

= TER – only ternary fission events considered,

= QTR – only quaternary fission events considered.

For fission yields - SF4 is used for ELEM/MASS or to define the element, for which the yield is given in DATA block.

Yields are given usually in units like PRT/FIS .

It means that yields are given per one fission reaction.

And for FY - reaction is defined really in SF1-SF3 +branch in SF5.

Examples:

A.

J,PR/C,7,373,1973

– an example of comparison of BIN and LRA TER fission yields.

For BIN – yield for one binary reaction,

For TER –yield for one ternary reaction accompanied by LRA.

CF-252(0,F)ELEM/MASS,,TER,FY,FF

FF are defined in DATA block as ELEM1, MASS1,

Alpha is defined in COMMON as ELEM2, MASS2.

– Yields of FF per one ternary spontaneous fission accompanied by alpha (only accompanied by alpha events of spontaneous ternary fission are considered).

CF-252(0,F)ELEM/MASS,BIN,FY,FF

FF defined as ELEM and MASS in DATA block.

– Yields of FF per one binary spontaneous fission (only binary fission events are considered)

CF-252(0,F)ELEM/MASS,,FY,FF

FF defined as ELEM and MASS in DATA block.

– Yields of FF  per one spontaneous fission (all fission events are considered)

B.

CF-252(0,F)2-HE-4,,FY,LCP

– Yield of alpha per one fission reaction (value about 1.E-3)

CF-252(0,F)2-HE-4,TER,FY,LCP

– Yield of alpha per one ternary fission reaction (value about 0.98).

PROPOSAL:

Add in LEXFOR Manual, Chapter Fission Yields:

Fission yields are given for one fission reaction defined in

SF1+SF2+SF3+(branch in SF5 if needed) as:

- for all fission events – SF1(SF2,F)*,,FY,#

- for binary fission events - SF1(SF2,F)*,BIN,FY,#

- for ternary fission events - SF1(SF2,F)*,,TER,FY,#

- for quaternary fission events - SF1(SF2,F)*,QTR,FY,# ,

where 	* =ELEM(and/or)MASS (preferable) or concrete isotope,

# = FF, LF, HF or LCP.

If in SF4 the concrete isotope is given, then SF7 could be avoided.

Detailed explanation in free text (especially of normalization) is recommended.

For ternary and quaternary fission – ELEM2/MASS2, ELEM3/MASS3 have to be used in COMMON to define particle in coincidence, if such events are considered, ELEM1/MASS1 have to be used in DATA block.

Distribution list:

blokhin@ippe.ru,

chiba@earth.sgu.ac.jp,

claes.nordborg@oecd.org,

emmeric.dupont@oecd.org,

exfor@nea.fr,

ganesan@barc.gov.in,

gezg@ciae.ac.cn,

hans.henriksson@foi.se,

hongwei@ciae.ac.cn,

jhchang@kaeri.re.kr,

j.roberts@iaea.org,

kaltchenko@kinr.kiev.ua,

katakura.junichi@jaea.go.jp,

kato@nucl.sci.hokudai.ac.jp,

kiralyb@atomki.hu,

l.vrapcenjak@iaea.org,

manuel.bossant@oecd.org,

manokhin@ippe.ru,

mmarina@ippe.ru,

mwherman@bnl.gov,

nklimova@kinr.kiev.ua,

nicolas.soppera@oecd.org,

n.otsuka@iaea.org,

ogritzay@kinr.kiev.ua,

otto.schwerer@aon.at,

oblozinsky@bnl.gov,

pronyaev@ippe.ru,

r.forrest@iaea.org,

samaev@obninsk.ru,

sbabykina@yandex.ru,

scyang@kaeri.re.kr,

stakacs@atomki.hu,

stanislav.hlavac@savba.sk,

s.dunaeva@iaea.org,

taova@expd.vniief.ru,

tarkanyi@atomki.hu,

varlamov@depni.sinp.msu.ru,

vlasov@kinr.kiev.ua,

vmclane@optonline.net,

v.zerkin@iaea.org,

yolee@kaeri.re.kr