Memo issued on behalf of

National Nuclear Data Center

Brookhaven National Laboratory

USA

Memo CP-C/399

Date:		1 November 2011

To:		Distribution

From:		O. Schwerer and N. Otsuka

Subject:		Coding of energy spectrum and yield of prompt fission gammas:

Addition of PR,FY/DE and PR/PAR,FY to dictionary 236

Reference:	Memo CP-D/542 (item 1 to be withdrawn)

Memo CP-D/599

In the article by R.W.Peelle et al., PR/C,3,373,1971 (being compiled in entry 14201 to be submitted on Prelim 1376), two quantities for prompt fission gammas are measured:

- Energy spectrum of prompt fission gammas in units photons/fission/MeV

- Partial yields of prompt fission gammas in units photons/fission.

(Partial due to gamma energy range)

Proposed coding:

1) ….(N,F)0-G-0,PR,FY/DE  with units PT/FIS/MEV

2) ….(N,F)0-G-0,PR/PAR,FY with units PRD/FIS

Note that for reaction 2) another code (PR/PAR,MLT,G) was used in one entry (14195) according to our earlier memo CP-D/542.

However, in an effort to streamline the coding of fission quantities, it was decided later in memo CP-D/599, to code all yields of fission particles with SF6 = FY.

To harmonise the coding of gamma yields with this concept, we therefore withdraw item 1 of memo CP-D/542 and propose the following dictionary additions:

Additions to dictionary 236 (Quantities)

PR,FY/DE  	FYE FYDE	 Energy spectrum of prompt fission particles

PR/PAR,FY		FY  FY	 Partial yield of prompt fission particles

Make obsolete:

PR/PAR,MLT,G

Distribution:

blokhin@ippe.ru

cgc@ciae.ac.cn

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

fukahori.tokio@jaea.go.jp

ganesan@barc.gov.in

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

j.roberts@iaea.org

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re

zhuangyx@ciae.ac.cn