Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/542

Date:		15 January 2009

To:		Distribution

From:		O. Schwerer, N. Otsuka,

Subject:	Intensity of prompt and delayed fission gammas

- Prompt fission gamma spectra integrated over a partial energy range

New entry 14195 (V. V. Verbinski et al., Phys. Rev. C 7 (1973) 1173) compiles multiplicity of prompt fission gammas obtained by continuous spectra of prompt fission gammas integrated over a partial range of gamma energy. Because existing quantity code PR,SPC is for prompt discrete gamma lines, we need a new quantity code for 14195.

The data are given in the article in units photons/fission (in the table annotation misspelled as “protons per fission”). These units correspond to EXFOR units PRT/FIS which has in our dictionary the dimension code FY

# Dictionary 236 (Quantities)

PR/PAR,MLT,G Partial multiplicity of prompt gamma

(Use PR,SPC for prompt discrete gamma)

| Quantity | Reaction Type | Dimension | Subentry |
| --- | --- | --- | --- |
| PR/PAR,MLT,G | PZ | FY | 14195.002-004 |

- Intensity of prompt and delayed fission gammas – unit dimension

Dictionary 236, the quantity PR,SPC and DL,SPC have still an old dimension code SPC which is no longer used in the quantity dictionary 25. Therefore, whatever units are used with quantity PR,SPC or DL,SPC, they will generate an error message.

It is not surprising that these inconsistencies were not yet found, because in the master file there is not a single EXFOR entry of PR,SPC or DL,SPC using “real” units. These are all the occurrences:

PR,SPC	 20956		NODATA

20957		Relative data with ARB-UNITS

20958		Relative data with ARB-UNITS

DL,SPC	 20956		NODATA

21592		Relative data with ARB-UNITS

PR/TER,SPC	 30760		NODATA

Note that other quantities with SF6=SPC have dimension YLD, which includes following units:

PC/INC, PC/REAC, PRD/INC, PRD/REAC, PRT/INC, PRT/REAC

On the other hand, dimension FY corresponds to these units:

PC/FIS, PRD/FIS, PRT/FIS.

So FY units are very similar to YLD units except that REAC is replaced by FIS. It is a special case for fission, to be similar to units traditionally used in the literature. Since both quantities, PR,SPC and DL,SPC, are restricted to fission reactions, it is logical to use units of dimension FY.

# Dictionary 236 (Quantities)

PR,SPC		Change unit family code from SPC to FY

DL,SPC		Change unit family code from SPC to FY

PR/TER,SPC	Change unit family code from YLD to FY

Distribution:

a.mengoni@iaea.org

a.nichols@iaea.org

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

exfor@nea.fr

ganesan@barc.gov.in

gezg@ciae.ac.cn

hasegawa@nea.fr

henriksson@near.fr

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kirarlyb@atomki.hu

l.vrapcenjak@iaea.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

samaev@obninsk.ru

s.babykina@polyn.kiae.su

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@exped.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.kr