Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/563

Date:		18 May 2009

To:		Distribution

From:		N. Otsuka, O. Schwerer

Subject:		Angular distribution of fission fragment gamma

A new quantity code is proposed for partial angular distribution of fission gamma with respect to the relative angle between the outgoing fission fragment and gamma momenta (gammas / sr / fission) presented in two articles [1, 2].

# Dictionary 236 (Quantities)

PAR,FY/DA,G/G+FF     Differential partial fission fragment gamma yield with respect to relative angle between gamma and fission fragment

Unit code PRT/FIS/SR is now defined with dimension 1/A in dictionary 26. But it would be more logical to link this unit code with a new dimension code FYDA as we have two dimension codes, FY and YLD, for integrated fission yield and other integrated yield (or multiplicity), respectively. The following update is therefore also proposed:

# Dictionary 25 (Data units)

PRT/FIS/SR           (change of dimension from 1/A to FYDA)

# Dictionary 26 (Dimensions)

FYDA                 per-cent per fission per solid angle

| Quantity code | Reaction Type | Dimension |
| --- | --- | --- |
| 236 | 213 | 26 |
| PAR,FY/DA,G/G+FF | FYA | FYDA (new) |

There are four quantity codes which are relevant to fission and their dimension codes are 1/A:

| Quantity code | Subentries | Unit code |
| --- | --- | --- |
| MLT/DA,G/FF | C1460.002-004 | PRT/FIS/SR |
| PR,DA,N | (always coded with REL in SF8) | (ARB-UNIT) |
| PR/TER,DA,N | (always coded with REL in SF8) | (ARB-UNIT) |
| PR,DA,N+LF | 41516.002 (new code to be added) | PRT/FIS/SR |

For consistency, the following change and addition is also proposed:

# Dictionary 236 (Quantities)

FY/DA,G/FF      Differential fission fragment gamma yield with respect to angle of fission fragment (replaces MLT/DA,G/FF)

MLT/DA,G/FF     (Made obsolete, use FY/DA,G/FF)

PR,DA,N         (Change of dimension from 1/A to FYDA)

PR/TER,DA,N     (Change of dimension from 1/A to FYDA)

Consequently, the quantity code should be changed from MLT/DA,G/FF to FY/DA,G/FF when subentries C1460.002-004 are updated. All other subentries are not affected by this proposal.

References

[1] A. T. Kandil et al., Nucl. Phys. A224(1974)468 (EXFOR 30411)

[2] L.S.El-Mekkawi, Indian J. Pure Appl. Phys. 9(1971)470 (EXFOR 30442)

Distribution:

a.mengoni@iaea.org

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hasegawa@nea.fr

henriksson@near.fr

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kirarlyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

samaev@obninsk.ru

s.babykina@polyn.kiae.su

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@exped.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.kr