Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/564

Date:		20 May 2009

To:		Distribution

From:		N. Otsuka

Subject:		Compilation of covariance matrix given in the AGS format

Compilation of experimental covariance matrix for transmission and reaction yield will be proposed in the NRDC 2009 meeting by Drs. Stefan Kopecky and Peter Schillebeeckx (EC-JRC-IRMM, Geel). By using their expression of covariance matrix - AGS (Analysis of Geel Spectra) - total size covariance matrix is reduced from n2 to n(k+1), where n is the total number of TOF (time of flight) channel (~104). A note for this formalism in Appendix 3 might be helpful for discussion.

They propose compilation of matrices D and S defined in Eqs.10 and 11 in the note as a function of TOF. I prepared a coding sample (Appendix 2) according to their template for EXFOR compilation (Appendix 1). Some possible technical questions are summarized below:

- Can we add TOF (in second) as an independent variable instead of incident energy?

- Can we allow negative values under ERR-n? Sensitivity coefficient in Eq. 12 (∂σi / ∂xl) can be negative.

- We do not need new headings for uncertainties in the coding sample because the size of covariance matrices of systematic effect sources (defined in matrices W in Eq. 7) is 1 x 1 for all 4 sources, and the matrix S then gives usual partial uncertainty (See Eq.12). Can we still regard the matrix S as partial uncertainty (ERR-n) if W is larger than 2 x 2 ?

Appendix 1: EXFOR template from Geel

1. Experiment description

| Main Reference |  | 1 |
| --- | --- | --- |
| Facility | GELINA | 2,3 |
| Neutron production |  | 4 |
| Primary neutron production target | Uranium |  |
| Time resolution primary beam (ns) | 1 ns |  |
| Moderator material | H2O |  |
| Surface Dimensions (mm x mm or diameter in mm) | 2 containers 100 x 100 mm |  |
| Thickness (mm) | 40 mm |  |
| Experimental details |  |  |
| Measurement type | Transmission |  |
| Flight path length (m) (moderator – target (detector): face to face distance) | 26.444 +/- 0.006 m |  |
| Angle (with respect to cp beam) | 99 deg |  |
| Beam dimensions (mm x mm or diameter in mm) | Diameter 40 mm |  |
| Detector |  |  |
| Type | Scintillator |  |
| Material | Li-glass (NE 905) |  |
| Surface Dimensions (mm x mm or diameter in mm) | 120 mm diameter |  |
| Thickness (mm) | 12.7 mm |  |
| Sample |  |  |
| Type (metal, powder) | Metal |  |
| Chemical composition | Cd |  |
| Atomic abundance of main element Weight | 100 % 2.0993 +/- 0.0001 g |  |
| Weight per unit area (g/cm2) | 0.04172 g/cm2 |  |
| Geometry |  |  |
| Surface dimensions (mm x mm or diameter in mm) | Diameter 80.04 +/- 0.03 mm |  |
| Thickness (mm) | 0.050 mm (nominal) |  |
| Thickness of main element (at/b) | 2.2352 10-4 at/b |  |
| Containment description | No container |  |
| Uncertainties (at 1 sigma level) |  |  |
| Normalization (relative ) |  |  |
| Other sources creating correlated uncertainty components (see data format) | Dead Time correction sample in [1] Background correction sample in parameter one [2] Dead Time correction sample out [3] Background correction sample out parameter one [4] |  |

References

[1] S. Kopecky et al., submitted to NIMB

[2] J.M. Salome and R. Cools, Nucl. Instrum. Methods Phys. Res. A 179 (1981), 13

[3] D. Tronc, J.M. Salome, K.H. Böckhoff, Nucl. Instrum. Methods Phys. Res. A 228 (1985), 217

[4] M. Flaska et al. Nucl. Instrum. Methods Phys. Res. A 531 (2004), 392

2. Data format

According to AGS format

| Time-of-Flight [ns] | Observable | Uncertainty |
| --- | --- | --- |
| Low | High | Transmission | Total | Uncorrelated | Correlated Components |
|  |  |  |  | 2 | [1] | [2] | [3] | [4] |
| 3.1188E+06 | 3.1444E+06 | 9.1309E-01 | 5.2664E-03 | 2.7570E-05 | 6.5601E-06 | -1.0072E-04 | -7.4295E-06 | 9.3673E-05 |
| 3.1444E+06 | 3.1700E+06 | 9.0347E-01 | 5.2812E-03 | 2.7719E-05 | 6.3922E-06 | -1.0226E-04 | -7.2767E-06 | 9.4143E-05 |
| 3.1700E+06 | 3.1956E+06 | 9.0134E-01 | 5.2989E-03 | 2.7902E-05 | 6.3386E-06 | -1.0281E-04 | -7.2228E-06 | 9.4387E-05 |
| 3.1956E+06 | 3.2212E+06 | 8.8804E-01 | 5.2316E-03 | 2.7195E-05 | 6.2074E-06 | -1.0196E-04 | -7.1256E-06 | 9.2229E-05 |
| 3.2212E+06 | 3.2468E+06 | 8.8347E-01 | 5.2576E-03 | 2.7461E-05 | 6.1074E-06 | -1.0321E-04 | -7.0280E-06 | 9.2872E-05 |
| … | … | … | … | … | … | … | … | … |
| 6.5116E+06 | 6.6140E+06 | 5.1049E-01 | 1.7897E-03 | 3.0786E-06 | 2.7113E-06 | -5.1153E-05 | -4.0677E-06 | 2.6553E-05 |
| 6.6140E+06 | 6.7164E+06 | 5.1780E-01 | 1.8092E-03 | 3.1479E-06 | 2.7654E-06 | -5.0203E-05 | -4.1206E-06 | 2.6437E-05 |
| 6.7164E+06 | 6.8188E+06 | 5.2519E-01 | 1.8266E-03 | 3.2107E-06 | 2.8231E-06 | -4.9156E-05 | -4.1785E-06 | 2.6257E-05 |
| 6.8188E+06 | 6.9212E+06 | 5.3394E-01 | 1.8541E-03 | 3.3090E-06 | 2.8821E-06 | -4.8495E-05 | -4.2320E-06 | 2.6329E-05 |
| 6.9212E+06 | 7.0236E+06 | 5.4117E-01 | 1.8762E-03 | 3.3897E-06 | 2.9320E-06 | -4.7730E-05 | -4.2778E-06 | 2.6267E-05 |
| 7.0236E+06 | 7.0246E+06 | 5.6613E-01 | 1.9202E-02 | 3.6855E-04 | 3.0999E-06 | -4.8282E-05 | -4.4270E-06 | 2.7783E-05 |

Appendix 2: Coding sample

ENTRY            00001   20090507                                 0000100000001

SUBENT        00001001   20090507                                 0000100100001

BIB                 14         66                                 0000100100002

TITLE      The total cross section and resonance parameters for   0000100100003

the 0.178 eV resonance of 113Cd                        0000100100004

AUTHOR     (S.Kopecky, I.Ivanov, M.Moxon, P.Schillebeeckx,        0000100100005

P.Siegler, I.Sirakov)                                  0000100100006

INSTITUTE  (2ZZZGEL)                                              0000100100007

REFERENCE  (J,NIM/B,,,2009) Submitted to NIM/B                    0000100100008

#doi: 10.1016/j.nimb.2009.04.010                       0000100100009

REL-REF    (N,,J,NIM/A,179,13,1981)                               0000100100010

J.M.Salome+, Details of GELINA facility               0000100100011

(N,,J,NIM/A,228,217,1985)                              0000100100012

D.Tronc+, Details of GELINA facility                  0000100100013

(N,,J,NIM/A,531,392,2004)                              0000100100014

M.Flaska+, Details of neutron production              0000100100015

FACILITY   (LINAC,2ZZZGEL) GELINA                                 0000100100016

INC-SOURCE Diameter of neutron beam = 40 mm                       0000100100017

(PHOTO) (g,n) on uranium target                        0000100100018

(2 containers, 100 x 100 mm, 40 mm thick)      0000100100019

(THCOL) Water moderator                                0000100100020

METHOD     (TRN,TOF) Flight path (moderator - target (detector)   0000100100021

face to face distance) = 26.444 +/- 0.006 m  0000100100022

DETECTOR   (SCIN,GLASD) Li-glass scintillator (NE 905)            0000100100023

120 mm diameter, 12.7 mm thick            0000100100024

SAMPLE     Physical type:             Metal                       0000100100025

Chemical composition:      Element (Cd)                0000100100026

Purity of main element:    100%                        0000100100027

Weight per area:           0.04172 g/cm2               0000100100028

Diameter:                  80.04 +/- 0.03 mm           0000100100029

Thickness:                 0.050 mm (nominal)          0000100100030

Thickness of main element: 2.2352E-04 atom/b           0000100100031

CORRECTION Data are corrected for                                 0000100100032

- dead time at sample-in detector   (din);          0000100100033

- background at sample-in detecto   (Bin);          0000100100034

- dead time at sample-out detector  (dout);         0000100100035

- background at sample-out detector (Bout),         0000100100036

as follows:                                            0000100100037

T=(din*Cin-Bin)/(dout*Cout-Bout)                     0000100100038

, where                                                0000100100039

T:    Transmission;                                 0000100100040

Cin:  Count at sample-in detector;                  0000100100041

Cout: Count at sample-out detector.                 0000100100042

ERR-ANALYS (ERR-T) Total uncertainty                              0000100100043

(ERR-S) Sum of uncorrelated uncertainties              0000100100044

due to counting statistics                     0000100100045

(sample-in and sample-out)                     0000100100046

(ERR-1) Uncertainty due to dead-time correction        0000100100047

(sample-in)                                    0000100100048

(ERR-2) Uncertainty due to background correction       0000100100049

(sample-in)                                    0000100100050

(ERR-3) Uncertainty due to dead-time correction        0000100100051

(sample-out)                                   0000100100052

(ERR-4) Uncertainty due to background correction       0000100100053

(sample-out)                              0000100100054

COVARIANCE If i=j,                                                0000100100055

cov(T_i,T_j) = (ERR-S)i**2 +(ERR-1)i**2+(ERR-2)i**2   0000100100056

+(ERR-3)i**2+(ERR-4)i**2   0000100100057

,else                                                  0000100100058

cov(T_i,T_j) = (ERR-1)i*(ERR-1)j                      0000100100059

+ (ERR-2)i*(ERR-2)j                      0000100100060

+ (ERR-3)i*(ERR-3)j                      0000100100061

+ (ERR-4)i*(ERR-4)j                      0000100100062

.                                                      0000100100063

HISTORY    (20090403R) On. Received by e-mail from S.Kopecky      0000100100064

(20090423C) On.                                        0000100100065

(20090507A) On. ERR-ANALYSIS updated,                  0000100100066

CORRECTION and COVARIANCE added.       0000100100067

(20090520A) On. TITLE added, AUTHOR corrected          0000100100068

ENDBIB              66          0                                 0000100100069

NOCOMMON             0          0                                 0000100100070

ENDSUBENT           69          0                                 0000100199999

SUBENT        00001002   20090507                                 0000100200001

BIB                  3          3                                 0000100200002

REACTION   (48-CD-0(N,TOT),TRN)                                   0000100200003

STATUS     (TABLE) Data on MS word file                           0000100200004

ENDBIB               3          0                                 0000100200006

COMMON               2          3                                 0000100200007

TOF-L       TOF-L-ERR                                             0000100200008

M           M                                                     0000100200009

26.444      0.006                                                 0000100200010

ENDCOMMON            3          0                                 0000100200011

DATA                 9        101                                 0000100200012

TOF-MIN    TOF-MAX    DATA       ERR-T      ERR-S      ERR-1      0000100200013

ERR-2      ERR-3      ERR-4                                       0000100200014

NS         NS         NO-DIM     NO-DIM     NO-DIM     NO-DIM     0000100200015

NO-DIM     NO-DIM     NO-DIM                                      0000100200016

3.1188E+06 3.1444E+06 9.1309E-01 5.2664E-03 5.2507E-03 6.5601E-060000100200017

-1.0072E-04-7.4295E-06 9.3673E-05                                 0000100200018

3.1444E+06 3.1700E+06 9.0347E-01 5.2812E-03 5.2649E-03 6.3922E-060000100200019

-1.0226E-04-7.2767E-06 9.4143E-05                                 0000100200020

3.1700E+06 3.1956E+06 9.0134E-01 5.2989E-03 5.2822E-03 6.3386E-060000100200021

-1.0281E-04-7.2228E-06 9.4387E-05                                 0000100200022

3.1956E+06 3.2212E+06 8.8804E-01 5.2316E-03 5.2149E-03 6.2074E-060000100200023

-1.0196E-04-7.1256E-06 9.2229E-05                                 0000100200024

…

6.7164E+06 6.8188E+06 5.2519E-01 1.8266E-03 1.7918E-03 2.8231E-060000100200211

-4.9156E-05-4.1785E-06 2.6257E-05                                 0000100200212

6.8188E+06 6.9212E+06 5.3394E-01 1.8541E-03 1.8191E-03 2.8821E-060000100200213

-4.8495E-05-4.2320E-06 2.6329E-05                                 0000100200214

6.9212E+06 7.0236E+06 5.4117E-01 1.8762E-03 1.8411E-03 2.9320E-060000100200215

-4.7730E-05-4.2778E-06 2.6267E-05                                 0000100200216

7.0236E+06 7.0246E+06 5.6613E-01 1.9202E-02 1.9198E-02 3.0999E-060000100200217

-4.8282E-05-4.4270E-06 2.7783E-05                                 0000100200218

ENDDATA            206          0                                 0000100200219

ENDSUBENT          218          0                                 0000100299999

ENDENTRY             2          0                                 0000199999999

ENDTRANS             1          0                                 Z999999999999

Distribution:

a.mengoni@iaea.org

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hasegawa@nea.fr

henriksson@near.fr

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kirarlyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

samaev@obninsk.ru

s.babykina@polyn.kiae.su

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@exped.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.kr

cc:

stefan.kopecky@ec.europa.eu

peter.schillebeeckx@ec.europa.eu