Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/569

Date:		2 July 2009

To:		Distribution

From:		N. Otsuka

Subject:		Dictionaries 31 and 236- provisional fragment mass (PRV)

In prelim 2211 (and also in prelim.2191 and 2207), several entries give fission data for “provisional mass” of fission fragment. This should be distinguished from pre-neutron emission fission fragment mass (primary fission fragment mass PRE) and post-neutron emission fission fragment mass (secondary fission fragment mass SEC).

In general, there are momentum and mass conservations for fission:

m1*E1*=m2*E2*   (momentum conservation in center-of-mass system)

m1*+m2*=mf       (mass conservation)

, where mi (i=1, 2) and mf denote the mass of fission fragment and compound nucleus, respectively. Asterisk means the quantity before neutron emission. If we assume the velocity of fission fragment is unchanged by prompt neutron emission (vi = vi*), we can derive the pre-neutron emission fission fragment mass from above equations:

m1*= mf  v2/(v1+v2),

m2*= mf  v1/(v1+v2)

E*tot = (1/2) mf  v1 v2

m1= 2E1/v12,

m2= 2E2/v22

Therefore we can obtain pre-neutron emission fission fragment masses mi*, pre-neutron emission total kinetic energy E*tot and post-neutron emission fission fragment masses mi* if we can measure velocities (vi) and kinetic energies (Ei) of two post-neutron emission fragments (2v2E method) [1].

Authors of old articles sometimes introduced the provisional fission fragment mass μi which satisfies the following relation:

μ1E1=μ2E2

μ1+μ2=mf

, and obtained μi from measurement of the kinetic energies of post-neutron emission fission fragments Ei [2]. I would propose to the following new branch code and quantity codes for provisional fission fragment mass.

# Dictionary 31 (Branch codes)

PRV            Provisional (For use in fission)

# Dictionary 236 (Quantities)

PRV,AP,HF      Most probable provisional mass for heavy fragment

PRV,AP,LF      Most probable provisional mass for light fragment

Sum rule: If sum of two fragment masses is equal to compound mass, they are pre-neutron emission fragment masses PRE or provisional fragment masses PRV.

Checking of the following entries is necessary:

PRELIM.2191: 21752,

PRELIM.2207: 21313, 21543, 21544, 21545, 21771

.

References

[1] For example, I. Nishinaka et al., Phys.Rev.C70(2004)014609

[2] H. W. Schmitt et al., Phys. Rev. 141 (1966) 1146

Distribution:

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hasegawa@nea.fr

henriksson@near.fr

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kirarlyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.kr