Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/590

Date:		13 October 2009

To:		Distribution

From:		N. Otsuka

Subject:		Self-indication and raw data

Reference:	WP1999-7, CP-D/584

There are 6 entries (40876, 40884, 41151, 41290, 41394, 41426) compiled with SIF in SF6. All were measured by Yu. V. Grigor’ev et al. at Dubna and Obninsk reactors.

Because the definition of the self-indication is not very clear from the entry (which was proposed in WP1999-7) and it is closely related to transmission and reaction yield, I would propose to collect explanation of these quantities into a new LEXFOR entry “Transmission and Reaction Yield”.

Distribution:

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hasegawa@nea.fr

henriksson@near.fr

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kirarlyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.pronyaev@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

cc :

griguv@ippe.ru

oigawa.hiroyuki@jaea.go.jp

Draft of new LEXFOR entry “Transmission and Reaction Yield”)

Transmission and Reaction Yield

Definition: Transmission T(E) and reaction yield Yx(E) are defined by

(x = capture, fission etc.)

# , where, nT is the sample thickness in nuclei/barn, σT (E) and σx (E) are the Doppler-broadened total cross section and cross section for the channel x.

REACTION coding:

(…(N,TOT)),,TRN)            Transmission

(…(N,G)…),,TRN,,RYL)  Capture yield

Independent variables:

Incident energy (EN etc.)

Sample thickness (THICKNESS)

Sample temperature (TEMP)

Units:  NO-DIM

Usually these data are reduced from raw data as follows:

, where in, out, r and φ stand for sample-in, sample-out, reaction channel and beam flux measurement, NT and Nx are normalization factors, and C’ and B’ denote count and background count corrected for dead time, respectively. In addition, reaction yield from incident particles scattered before inducing the reaction of type x should be subtracted from Yx. Corrections applied to compiled data should be described under keyword CORRECTION. If appropriate corrections are not applied to data received by compilers, it should be indicated by RAW in SF8. (See Raw Data.).

# In neutron time-of-flight measurements, the observed value broadened by resolution function is defined by

, where T is the channel number (e.g. time-of-flight channel) and R (T,E) is the resolution function (probability to find outgoing particle having E in T).

Transmission ratio and self-indication ratio

Transmission (ratio) Tg and self-indication (ratio) Rgx are defined as

Rgx=

, where εT(E) and εx(E) give efficiencies detectors for transmission and reaction yield measurements, nx gives the sample thickness of the thin reaction target, φ(E) gives spectrum of incoming particles. Integration is performed over a given energy range of the energy group g. The approximation ~ is applied when the efficiencies are regarded as constants and the spectrum is proportional to 1/E. These ratios can be used to derive self-shielding factors in reactor physics [1,2].

REACTION coding:

(…(N,TOT)),,TRN,,SPA)            Transmission (ratio)

(…(N,G)…),,SIF,,SPA)              Self-indication (ratio) for capture

Independent variables:

Upper and lower boundary of incident energy (EN-MIN, EN-MAX)

Sample thickness (THICKNESS)

Sample temperature (TEMP)

Units:  NO-DIM

Spectrum should be explained under INC-SPECT.

(a) Transmission measurement for 238U

(b) Self-indication measurement for 238U

References

[1] H. Oigawa et al., J. Nucl. Sci. Technol. 28 (1991) 879

[2] T. Bakalov et al., Proc. of Int. Conf. on Nuclear Cross Sections for Technology, Knoxville, Tennessee, 22 - 26 Oct 1979, p692.

# Text boxes

nT (atom/b)

Detector

γ

γ

10B

exp [-nTσT (E)]φ(E)

φ(E)

238U

238U

nx (atom/b)

nT (atom/b)

Detector

γ

γ

exp [-nTσT (E)]φ(E)

φ(E)

238U