Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/614

Date:		18 Februrary 2010

To:		Distribution

From:		N. Otsuka, S. Dunaeva

Subject:		Use of REACTION combination

Below are examples of quantities which can be codedwithout reaction combination under certain conditions (e.g. incident energy):

a) Data for natural target = Sum data for all contributing target nuclide

(46-PD-0(P,X)45-RH-105-G,CUM,SIG)or

(46-PD-106(P,2P)45-RH-105-G,CUM,SIG,,A)+

(46-PD-108(P,X)45-RH-105-G,CUM,SIG,,A)+

(46-PD-110(P,X)45-RH-105-G,CUM,SIG,,A)

b) Inclusive cross section = Sum of exclusive cross section

(40-ZR-91(P,X)0-NN-1,,SIG) or

(40-ZR-91(P,N)41-NB-91,,SIG)+

(40-ZR-91(P,N+P)40-ZR-90,,SIG)+

(40-ZR-91(P,N+A)39-Y-87,,SIG)

c) Production = Sum of processes

(46-PD-102(P,X)46-PD-101,CUM,SIG) or

(46-PD-102(P,D)46-PD-101,CUM,SIG)+

(46-PD-102(P,N+P)46-PD-101,CUM,SIG)

d) Scattering = Elastic scattering + inelastic scattering

(3-LI-7(N,SCT)3-LI-7,PAR,SIG) or

(3-LI-7(N,EL)3-LI-7,,SIG)+(3-LI-7(N,INL)3-LI-7,PAR,SIG)

e) Alpha value = Capture cross section / fission cross section

(92-U-235(N,ABS),,ALF) or

(92-U-235(N,G)92-U-236,,SIG)/(92-U-235(N,F),,SIG)

f) Resonance strength (Capture kernel)

(82-PB-208(N,G)82-PB-209,,WID/STR) or

((82-PB-208(N,EL),,WID,,G)*(82-PB-208(N,G),,WID))/

(82-PB-208(N,TOT),,WID))

The EXFOR Formats Manual “Reaction Combinations” mentions that

“Note that the reaction combination formalism is not used for certain frequently occurring sums, ratios, and products for which specific quantity codes have been introduced”

We propose to add above cases as examples of “frequently occurring sums, ratios, and products” into the Formats Manual to help users who want to find a given reaction/quantity easier.

Distribution:

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

henriksson@near.fr

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

j.roberts@iaea.org

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.pronyaev@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.k