Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/635

Date:		14 April, 2010

To:		Distribution

From:		N. Otsuka, V. Pronyaev, R Capote Noy

Subject:		Prompt fission neutron spectra

Fission neutron spectrum is an important quantity in reactor applications. It was reported in the IAEA Consultant Meeting (November 2008) that the uncertainty in prompt fission neutron spectrum (PFNS) results in about 0.3% to 0.4% of the uncertainty in keff value in a sensitivity analysis of the JEZEBEL experiment. Importance of PFNS was also stressed in WPEC Subgroup 26.

However the current translator from EXFOR to C4 does not support fission neutron spectrum compiled in EXFOR; it is pointed out by several WPEC SG30 members that PFNS should be in the C4 library. In order to realize the translation for PFNS, however, we need clean up of the PFNS entries in EXFOR because the EXFOR quantity PR,DE,N is coded with various unit codes (B/MEV, 1/MEV etc.).

Type of measurement and normalization (useful for EXFOR compilation)

1. Detection type (TOF, proton recoil detector, fission detector)

2. Various normalizations

- Relative (shape) spectrum

- Absolute spectrum (neutrons/fiss/MeV) – neutron detection by 6Li(n,t) or 235U(n,f)

- Absolute ratio of two spectra, e.g. 252Cf(sf) PFNS / 235U(n,f) PFNS

- Shape of ratio of two spectra

- Spectrum relative to Maxwellian spectrum with fixed kT

Most inconvenient is when authors used 252Cf(sf) PFNS for determination of the efficiency detector, but not giving which standard was used foe 252Cf(sf).

Note that coding of total kinetic energy and prompt neutron fission number as a function of fragment mass (K. Nishio et al.) should be also clarified in future.

Summary of prompt fission neutron quantities for EXFOR

(for discussion in the 2010 NRDC meeting, April 20-23, Sapporo)

NT1:	New modifier for “normalized to 1” (Do you have a better one?)

PR:	Branch code when prompt neutron is exclusively measured (time of flight measurement where fission event is used as the start signal)

(0) 98-CF-252(0,F),NU

Prompt fission neutron multiplicity ν-bar (Unit: 1/FIS)

(1) 98-CF-252(0,F),,NU/DE

PFNS χ(E), where.  (Unit: PT/MEV/FIS)

Absolute multiplicity used for normalization should be coded under MONIT.

(2) (92-U-235(N,F),,NU/DE)/(98-CF-252(0,F),,NU/DE)

PFNS relative to the 252Cf spontaneous PFNS

χ(E) / χ252(E), where  and  (Unit: NO-DIM)

(3) 98-CF-252(0,F),,NU/DE,,MXD

PFNS relative to Maxwell distribution  (Unit: NO-DIM)

. Temperature should be coded under KT-NRM (or introduce a new quantity code?)

(4) 98-CF-252(0,F),,NU/DE,,NT1

Normalized PFNS X(E), where  (Unit: 1/MEV/FIS)

(5) (92-U-235(N,F),,NU/DE,,NT1)/(98-CF-252(0,F),,NU/DE,,NT1)

Normalized PFNS relative to the normalized 252Cf spontaneous PFNS

X(E) / X252(E), where  and  (Unit: NO-DIM)

(6) 98-CF-252(0,F),,NU/DE,,RTE

(Unit: NO-DIM, but always given in arbitrary unit)

Distribution:

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

j.roberts@iaea.org

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.

cc:

r.capotenoy@iaea.org

Prompt fission neutron spectrum (SF3=F, SF6=DE, SF7=N) in EXFOR (Preliminary result by Naohiko Otsuka)

(Type: Type of quantity, R: data in arbitrary unit)

| Subentry | pt | Institute | Year | Emin | Emax | REACTION (current coding) | Unit (current | Type | Unit (new) | Remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10612.002 |  | 1USAANL | 1967 | Spon |  | (98-CF-252(0,F),,DE,N,FCT) | 1/MEV | 6R? |  | N(E)/sqrt(E) compiled, N(E) is normalized to 1 |
| 10612.003 |  | 1USAANL | 1967 | Spon |  | (98-CF-252(0,F),,DE,N,FCT) | 1/MEV | 6R? |  | N(E)/sqrt(E) compiled, N(E) is normalized to 1 |
| 10612.004 |  | 1USAANL | 1967 | Spon |  | (98-CF-252(0,F),,DE,N,FCT) | 1/MEV | 6R? |  | N(E)/sqrt(E) compiled, N(E) is normalized to 1 |
| 10612.005 |  | 1USAANL | 1967 | Spon |  | (98-CF-252(0,F),,DE,N,FCT) | 1/MEV | 6R? |  | N(E)/sqrt(E) compiled, N(E) is normalized to 1 |
| 10612.006 |  | 1USAANL | 1967 | Spon |  | (98-CF-252(0,F),,DE,N,FCT) | 1/MEV | 6R? |  | N(E)/sqrt(E) compiled, N(E) is normalized to 1 |
| 10612.007 |  | 1USAANL | 1967 | Spon |  | (98-CF-252(0,F),,DE,N,FCT) | 1/MEV | 6R? |  | N(E)/sqrt(E) compiled, N(E) is normalized to 1 |
| 10614.002 |  | 1USABET | 1973 | Spon |  | (98-CF-252(0,F),PR,DE,N,FCT) | NO-DIM |  |  | log[N(E)/sqrt(E)] compiled, N(E)/Nmax(E) also in figure |
| 10614.003 |  | 1USABET | 1973 | Spon |  | (98-CF-252(0,F),PR,DE,N,FCT) | NO-DIM |  |  | log[N(E)/sqrt(E)] compiled, N(E)/Nmax(E) also in figure |
| 10614.004 |  | 1USABET | 1973 | Spon |  | (98-CF-252(0,F),PR,DE,N,FCT) | NO-DIM |  |  | log[N(E)/sqrt(E)] compiled, N(E)/Nmax(E) also in figure |
| 10614.005 |  | 1USABET | 1973 | Spon |  | (98-CF-252(0,F),PR,DE,N,FCT) | NO-DIM |  |  | log[N(E)/sqrt(E)] compiled, N(E)/Nmax(E) also in figure |
| 10614.006 |  | 1USABET | 1973 | Spon |  | (98-CF-252(0,F),PR,DE,N,FCT) | NO-DIM |  |  | log[N(E)/sqrt(E)] compiled, N(E)/Nmax(E) also in figure |
| 10614.007 |  | 1USABET | 1973 | Spon |  | (98-CF-252(0,F),PR,DE,N,FCT) | NO-DIM |  |  | log[N(E)/sqrt(E)] compiled, N(E)/Nmax(E) also in figure |
| 10911.002 |  | 1USAANL | 1980 | 5.5e5 |  | ((92-U-233(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | (No data) | 2R | ARB-UNITS | Digitize? |
| 10911.003 |  | 1USAANL | 1980 | 5.5e5 |  | ((92-U-235(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | (No data) | 2R | ARB-UNITS | Digitize? |
| 10911.004 |  | 1USAANL | 1980 | 5.5e5 |  | ((94-PU-239(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | (No data) | 2R | ARB-UNITS | Digitize? |
| 10911.005 |  | 1USAANL | 1980 | 8.3e5 |  | ((94-PU-240(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | (No data) | 2R | ARB-UNITS | Digitize? |
| 12727.002 |  | 1USAUI | 1977 | Spon |  | (98-CF-252(0,F),,DE,,REL) | ARB-UNITS | 6R? | ARB-UNITS | Neutron flux /sqrt(E) (neutrons/cm2/sec/MeV**1.5) |
| 12727.003 |  | 1USAUI | 1977 | Spon |  | (98-CF-252(0,F),,DE,,REL) | ARB-UNITS | 6R? | ARB-UNITS | Neutron flux /sqrt(E) (neutrons/cm2/sec/MeV**1.5) |
| 12727.004 |  | 1USAUI | 1977 | Spon |  | (98-CF-252(0,F),,DE,,REL) | ARB-UNITS | 6R? | ARB-UNITS | Neutron flux /sqrt(E) (neutrons/cm2/sec/MeV**1.5) |
| 13810.002 |  | 1USAANL | 1952 | Maxw |  | (92-U-235(N,F),,DE,N,MXW/REL) | 1/MEV | 1R | ARB-UNITS |  |
| 13824.002 |  | 1USALAS | 1956 | Maxw |  | (92-U-235(N,F),,DE,N,MXW/REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/sqrt(E) also in article in table |
| 13824.003 |  | 1USALAS | 1956 | 5.0e3 | 8.0e4 | (92-U-235(N,F),,DE,N,AV/REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/sqrt(E) also in article in table |
| 20175.003 |  | 2SWDAE | 1977 | 5.3e5 |  | (92-U-235(N,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E)/Nmax(E), N(E)/Nwat(E) also in figure |
| 20385.003 |  | 2ZZZGEL | 1973 | 4.0e5 |  | (92-U-235(N,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/sqrt(E) also in figure |
| 20394.008 |  | 2ZZZGEL | 1972 | 1.5e6 |  | (92-U-235(N,F),PR,DE,N) | B/MEV | 6R | ARB-UNITS | N(E)/sqrt(E) compiled |
| 20401.003 |  | 2ZZZGEL | 1973 | Spon |  | (98-CF-252(0,F),PR,DE,N) | 1/MEV | 1R | ARB-UNITS | N(E) compiled |
| 20401.004 |  | 2ZZZGEL | 1973 | Spon |  | (98-CF-252(0,F),PR,DE,N) | 1/MEV | 1R | ARB-UNITS | N(E) compiled |
| 20575.003 |  | 2SWDFOA | 1965 | 4.0e4 |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS | 1R? | ARB-UNITS | N(E) compiled? |
| 20575.004 |  | 2SWDFOA | 1965 | 1.5e6 |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS | 1R? | ARB-UNITS | N(E) compiled? |
| 20575.006 |  | 2SWDFOA | 1965 | 4.0e4 |  | (94-PU-239(N,F),,DE,N,REL) | ARB-UNITS | 1R? | ARB-UNITS | N(E) compiled? |
| 20575.008 |  | 2SWDFOA | 1965 | Spon |  | (98-CF-252(0,F),,DE,N,REL) | ARB-UNITS | 1R? | ARB-UNITS | N(E) compield? |
| 20576.003 |  | 2ZZZGEL | 1975 | 2.2e5 |  | (94-PU-239(N,F),PR,DE,N) | 1/MEV | 1R | ARB-UNITS | N(E) compiled |
| 20616.003 |  | 2GERKFK | 1971 | Maxw |  | (92-U-235(N,F),,DE,N) | 1/MEV | 1R | ARB-UNITS | N(E) per lethargy converted to N(E) per MeV by compiler |
| 20616.005 |  | 2GERKFK | 1971 | Maxw |  | (94-PU-239(N,F),,DE,N) | 1/MEV | 1R | ARB-UNITS | N(E) per lethargy converted to N(E) per MeV by compiler |
| 20616.007 |  | 2GERKFK | 1971 | Spon |  | (98-CF-252(0,F),,DE,N) | 1/MEV | 1R | ARB-UNITS | N(E) per lethargy converted to N(E) per MeV by compiler |
| 20996.003 |  | 2UK HAR | 1975 | 5.2e5 |  | (92-U-235(N,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/Nwat(E) also in table |
| 20997.003 |  | 2FR CAD | 1977 | 1.0e4 | 5.8e4 | (92-U-235(N,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/Nwat(E) also in table |
| 20997.004 |  | 2FR CAD | 1977 | 1.0e4 | 5.8e4 | (94-PU-239(N,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/Nwat(E) also in table |
| 21465.002 |  | 2AUSATI | 1979 | Spon |  | (98-CF-252(0,F),PR,DE,N) | (No data) | 1R, 3 |  | N(E) and N(E)/Nmax(E) in figure |
| 22112.002 |  | 2JPNTOH | 1989 | 2.0e6 |  | (92-U-238(N,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/Nmax(E), N(E)/Nwat(E) also in figure |
| 22112.003 |  | 2JPNTOH | 1989 | 2.0e6 |  | (92-U-238(N,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/Nmax(E), N(E)/Nwat(E) also in figure |
| 22112.004 |  | 2JPNTOH | 1989 | 2.0e6 |  | (90-TH-232(N,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/Nmax(E), NJ(E)/Nwat(E) also in figure |
| 22202.003 | 1 | 2AUSIRK | 1990 | Spon |  | ((98-CF-252(0,F),PR,DE,N,,EXP)/ (98-CF-252(0,F),PR,DE,N,,CALC)) | NO-DIM | 3 | NO-DIM |  |
| 22202.003 | 2 | 2AUSIRK | 1990 | Spon |  | ((98-CF-252(0,F),PR,DE,N,,EXP)/ (98-CF-252(0,F),PR,DE,N,,CALC)) | NO-DIM | 3 | NO-DIM |  |
| 22202.004 | 1 | 2AUSIRK | 1990 | Spon |  | ((98-CF-252(0,F),PR,DE,N,,EXP)/ (98-CF-252(0,F),PR,DE,N,,CALC)) | NO-DIM | 3 | NO-DIM |  |
| 22202.004 | 2 | 2AUSIRK | 1990 | Spon |  | ((98-CF-252(0,F),PR,DE,N,,EXP)/ (98-CF-252(0,F),PR,DE,N,,CALC)) | NO-DIM | 3 | NO-DIM |  |
| 22219.002 |  | 2GERDRE | 1990 | Spon |  | ((98-CF-252(0,F),PR,DE,N,,EXP)/ (98-CF-252(0,F),PR,DE,N,,CALC)) | NO-DIM | 3 | NO-DIM | =30969.004 |
| 22219.003 |  | 2GERDRE | 1990 | Spon |  | (98-CF-252(0,F),PR,DE,N) | 1/MEV | 4 | 1/FIS/MEV | =30969.002 N(E):Emission probability |
| 22219.004 |  | 2GERDRE | 1990 | Spon |  | ((98-CF-252(0,F),PR,DE,N,,EXP)/ (98-CF-252(0,F),PR,DE,N,,CALC)) | NO-DIM | 3 | NO-DIM | =30969.005 |
| 22219.005 |  | 2GERDRE | 1990 | Spon |  | (98-CF-252(0,F),PR,DE,N) | 1/MEV | 4 | 1/FIS/MEV | =30969.003 N(E):Emission probability |
| 22464.002 |  | 2JPNKTO | 1998 | Maxw |  | (92-U-235(N,F)MASS,PR,DE,N,FCT/MXW) | ARB-UNITS |  | ARB-UNITS | N(E,Af)/sqrt(E) in fragment c.m.s. compiled |
| 22650.007 | 1 | 2JPNKTO | 2000 | Maxw |  | (94-PU-239(N,F)MASS,PR,DE,N,REL/MXW) | ARB-UNITS |  | ARB-UNITS | N(E,Af)sqrt(E) in fragment c.m.s compiled |
| 22650.007 | 2 | 2JPNKTO | 2000 | Maxw |  | (94-PU-239(N,F)MASS,PR,DE,N,FCT/MXW) | ARB-UNITS |  | ARB-UNITS | N(E,Af)/sqrt(E) in fragment c.m.s. compiled |
| 22660.002 |  | 2JPNKTO | 1998 | Maxw |  | (92-U-233(N,F)MASS,PR,DE,N,FCT/MXW) | ARB-UNITS |  | ARB-UNITS | N(E,Af)/sqrt(E) in fragment c.m.s. compiled |
| 22688.002 |  | 2JPNTOH | 2002 | 5.5e5 |  | (92-U-233(N,F),PR,DE,N,FCT) | MB/MEV | 1R | ARB-UNITS |  |
| 23056.009 |  | 2ZZZGEL | 2007 | 5.2e5 |  | (92-U-235(N,F),PR,DE,N,MXD) | (No data) | 3 | NO-DIM | Preliminary data |
| 23056.010 |  | 2ZZZGEL | 2007 | 5.2e5 |  | (92-U-235(N,F),PR,DE,N) | (No data) | 3 | NO-DIM | Preliminary data |
| 30099.002 |  | 3HUNKFI | 1971 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled |
| 30099.003 |  | 3HUNKFI | 1971 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, derived from 30099.002? |
| 30426.002 |  | 3HUNKFI | 1977 | Maxw |  | (92-U-235(N,F),PR,DE,N,MXW/FCT) | PT/RCT/MEV |  | P/FS/MEVSR | N(E) in neutrons/MeV/sr, Detector angle not given |
| 30704.002 |  | 3HUNKFI | 1985 | Maxw |  | (92-U-233(N,F),PR,DE,N,MXW/REL) | ARB-UNITS | 1R? | ARB-UNITS? | N(E)/Nmax(E) also in figure |
| 30704.003 |  | 3HUNKFI | 1985 | Maxw |  | (92-U-235(N,F),PR,DE,N,MXW/REL) | ARB-UNITS | 1R? | ARB-UNITS? | N(E)/Nmax(E) also in figure |
| 30704.004 |  | 3HUNKFI | 1985 | Maxw |  | (94-PU-239(N,F),PR,DE,N,REL,MXW) | ARB-UNITS | 1R? | ARB-UNITS? | N(E)/Nmax(E) also in figure |
| 30775.002 |  | 3AULAUA | 1986 | Spon |  | (98-CF-252(0,F),PR,DE,N,MXD) | NO-DIM | 3 | NO-DIM |  |
| 30775.003 |  | 3AULAUA | 1986 | Spon |  | (98-CF-252(0,F),PR,DE,N,MXD) | NO-DIM | 3 | NO-DIM |  |
| 30969.002 |  | 3DDRTUD | 1990 | Spon |  | (98-CF-252(0,F),PR,DE,N) | 1/MEV | 4 | 1/FIS/MEV | =22219.003 N(E):Emission probability |
| 30969.003 |  | 3DDRTUD | 1990 | Spon |  | (98-CF-252(0,F),PR,DE,N) | 1/MEV | 4 | 1/FIS/MEV | =22219.005 N(E): Emission probability |
| 30969.004 |  | 3DDRTUD | 1990 | Spon |  | (98-CF-252(0,F),PR,DE,N,MXD) | NO-DIM | 3 | NO-DIM | =22219.002 |
| 30969.005 |  | 3DDRTUD | 1990 | Spon |  | (98-CF-252(0,F),PR,DE,N,MXD) | NO-DIM | 3 | NO-DIM | =22219.004 |
| 31405.003 |  | 3CPRBJG | 1989 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | ARB-UNITS | 3 | NO-DIM |  |
| 31440.003 |  | 3BZLIPE | 1989 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled |
| 32211.002 |  | 4UKRIJD | 2004 | Maxw |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS |  |  | Reactor neutron spectra. Delete. |
| 32211.003 |  | 4UKRIJD | 2004 | Maxw |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS |  |  | Reactor neutron spectra. Delete. |
| 32211.004 |  | 4UKRIJD | 2004 | Maxw |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS |  |  | Reactor neutron spectra. Delete. |
| 32211.005 |  | 4UKRIJD | 2004 | Maxw |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS |  |  | Reactor neutron spectra. Delete. |
| 32211.006 |  | 4UKRIJD | 2004 | Maxw |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS |  |  | Reactor neutron spectra. Delete. |
| 32587.002 |  | 3CPRAEP | 1989 | Maxw |  | (92-U-235(N,F),PR,DE,N,MXW/REL) | 1/MEV | 1R | ARB-UNITS | N(E) compiled?, N(E)/Nmax(E) also in figure |
| 40137.002 |  | 4RUSRI | 1968 | Spon |  | (96-CM-244(0,F),,DE,N,REL) | ARB-UNITS | 1R? | ARB-UNITS? |  |
| 40137.003 |  | 4RUSRI | 1968 | Spon |  | (94-PU-242(0,F),,DE,N,REL) | ARB-UNITS | 1R? | ARB-UNITS? |  |
| 40137.004 |  | 4RUSRI | 1968 | Maxw |  | (94-PU-239(N,F),,DE,N,REL) | ARB-UNITS | 1R? | ARB-UNITS? |  |
| 40250.002 |  | 4RUSFEI | 1974 | Spon |  | (98-CF-252(0,F),PR,DE,N,RTE/REL) | ARB-UNITS | 6R | ARB-UNITS | N(E)/sqrt(E) PR,DE,N,RTE is used in this subentry only |
| 40358.002 |  | 4RUSFEI | 1975 | 1.0e5 |  | (94-PU-239(N,F),,DE,N,REL) | ARB-UNITS | 6R | ARB-UNITS | N(E)/sqrt(E) |
| 40358.003 |  | 4RUSFEI | 1975 | 1.0e5 |  | (94-PU-239(N,F),,DE,N,REL) | ARB-UNITS | 6R | ARB-UNITS | N(E)/sqrt(E) |
| 40358.004 |  | 4RUSFEI | 1975 | 1.0e5 |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS | 6R | ARB-UNITS | N(E)/sqrt(E) |
| 40358.005 |  | 4RUSFEI | 1975 | 1.0e5 |  | (92-U-235(N,F),,DE,N,REL) | ARB-UNITS | 6R | ARB-UNITS | N(E)/sqrt(E) |
| 40418.002 |  | 4RUSRI | 1977 | Spon |  | (98-CF-252(0,F),,DE,N,REL) | ARB-UNITS | 1R? | ARB-UNITS? |  |
| 40472.003 |  | 4RUSFEI | 1975 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled |
| 40535.002 |  | 4RUSRI | 1980 | Spon |  | (98-CF-252(0,F),PR,DE,N,MXD) | NO-DIM | 3 | NO-DIM |  |
| 40631.002 |  | 4RUSFEI | 1980 | 6.0e6 |  | (92-U-238(N,F),PR,DE,N) | 1/MEV | 1? | PT/FIS/MEV? | “Absolute measurement” |
| 40631.003 |  | 4RUSFEI | 1980 | 7.0e6 |  | (92-U-238(N,F),PR,DE,N) | 1/MEV | 1? | PT/FIS/MEV? | “Absolute measurement” |
| 40631.004 |  | 4RUSFEI | 1980 | 8.0e6 |  | (92-U-238(N,F),PR,DE,N) | 1/MEV | 1? | PT/FIS/MEV? | “Absolute measurement” |
| 40631.005 |  | 4RUSFEI | 1980 | 8.9e6 |  | (92-U-238(N,F),PR,DE,N) | 1/MEV | 1? | PT/FIS/MEV? | “Absolute measurement” |
| 40644.002 |  | 4RUSNIR | 1979 | Spon |  | (98-CF-252(0,F),,DE,,REL) | NO-DIM | 4 | NO-DIM | “Relative to the total number” |
| 40740.002 |  | 4RUSFEI | 1979 | 1.4e7 |  | (92-U-238(N,F),PR,DE,N) | 1/MEV | 1? | PT/FIS/MEV? | “Absolute measurement” |
| 40871.005 |  | 4RUSNIR | 1983 | Spon |  | (98-CF-252(0,F),PR,DE,N) | PT/FIS/MEV | 1 | PT/FIS/MEV | See Pronyaev memo |
| 40871.006 |  | 4RUSNIR | 1983 | Maxw |  | (94-PU-239(N,F),PR,DE,N,MXW) | PT/FIS/MEV | 1 | PT/FIS/MEV |  |
| 40871.007 |  | 4RUSNIR | 1983 | Maxw |  | (92-U-235(N,F),PR,DE,N,MXW) | PT/FIS/MEV | 1 | PT/FIS/MEV | See Pronyaev memo |
| 40871.008 |  | 4RUSNIR | 1983 | Maxw |  | (92-U-235(N,F),PR,DE,N,MXW) | PT/FIS/MEV | 1 | PT/FIS/MEV | See Pronyaev memo |
| 40871.009 |  | 4RUSNIR | 1983 | Maxw |  | ((98-CF-252(0,F),PR,DE,N)// (94-PU-239(N,F),PR,DE,N,MXW)) | NO-DIM | 2 | NO-DIM |  |
| 40871.010 |  | 4RUSNIR | 1983 | Maxw |  | ((98-CF-252(0,F),PR,DE,N)// (94-PU-239(N,F),PR,DE,N,MXW)) | NO-DIM | 2 | NO-DIM |  |
| 40871.011 |  | 4RUSNIR | 1983 | Maxw |  | ((98-CF-252(0,F),PR,DE,N)// (92-U-235(N,F),PR,DE,N,MXW)) | NO-DIM | 2 | NO-DIM | See Pronyaev memo |
| 40871.012 |  | 4RUSNIR | 1983 | Maxw |  | ((98-CF-252(0,F),PR,DE,N)// (92-U-235(N,F),PR,DE,N,MXW)) | NO-DIM | 2 | NO-DIM | See Pronyaev memo |
| 40871.013 |  | 4RUSNIR | 1983 | Maxw |  | ((98-CF-252(0,F),PR,DE,N)// (92-U-233(N,F),PR,DE,N,MXW)) | NO-DIM | 2 | NO-DIM |  |
| 40872.002 |  | 4RUSNIR | 1983 | Spon |  | (98-CF-252(0,F),PR,DE,N) | PT/FIS/MEV | 1 | PT/FIS/MEV | See Pronyaev memo |
| 40872.003 |  | 4RUSNIR | 1983 | Maxw |  | (94-PU-239(N,F),PR,DE,N,MXW) | PT/FIS/MEV | 1 | PT/FIS/MEV | See Pronyaev memo |
| 40872.004 |  | 4RUSNIR | 1983 | Maxw |  | (92-U-235(N,F),PR,DE,N,MXW) | PT/FIS/MEV | 1 | PT/FIS/MEV | See Pronyaev memo |
| 40872.005 |  | 4RUSNIR | 1983 | Maxw |  | (92-U-233(N,F),PR,DE,N) | PT/FIS/MEV | 1 | PT/FIS/MEV |  |
| 40872.006 |  | 4RUSNIR | 1983 | Maxw |  | ((98-CF-252(0,F),PR,DE,N)// (94-PU-239(N,F),PR,DE,N,MXW)) | NO-DIM | 2 | NO-DIM |  |
| 40872.007 |  | 4RUSNIR | 1983 | Maxw |  | ((98-CF-252(0,F),PR,DE,N)// (92-U-235(N,F),PR,DE,N,MXW)) | NO-DIM | 2 | NO-DIM | See Pronyaev memo |
| 40872.008 |  | 4RUSNIR | 1983 | Maxw |  | ((98-CF-252(0,F),PR,DE,N)// (92-U-233(N,F),PR,DE,N,MXW)) | NO-DIM | 2 | NO-DIM |  |
| 40873.002 |  | 4RUSNIR | 1983 | Maxw |  | (92-U-233(N,F),PR,DE,N,REL) | NO-DIM | 3 | NO-DIM |  |
| 40873.004 |  | 4RUSNIR | 1983 | Maxw |  | (92-U-235(N,F),PR,DE,N,REL) | NO-DIM | 3 | NO-DIM | See Pronyaev memo |
| 40873.006 |  | 4RUSNIR | 1983 | Maxw |  | (94-PU-239(N,F),PR,DE,N,REL) | NO-DIM | 3 | NO-DIM | See Pronyaev memo |
| 40874.002 |  | 4RUSNIR | 1983 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | ARB-UNITS | 1 | PT/FIS/MEV | See Pronyaev memo |
| 40874.003 |  | 4RUSNIR | 1983 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | NO-DIM | 3 | NO-DIM | See Pronyaev memo |
| 40874.004 |  | 4RUSNIR | 1983 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | NO-DIM | 3 | NO-DIM | See Pronyaev memo |
| 40875.002 |  | 4RUSFEI | 1983 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | ARB-UNITS |  | P/FS/MEVSR |  |
| 40875.003 |  | 4RUSFEI | 1983 | Spon |  | ((98-CF-252(0,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | NO-DIM | 3 | NO-DIM |  |
| 40916.002 |  | 4RUSFEI | 1986 | 1.5e6 |  | (90-TH-232(N,F),PR,DE,N) | 1/MEV |  | B/MEV | DDX(90deg)*4pi |
| 40930.002 |  | 4RUSNIR | 1985 | Spon |  | ((98-CF-252(0,F),PR,DE,N,,EXP)// (98-CF-252(0,F),PR,DE,N,,CALC)) | NO-DIM | 3 | NO-DIM | See Pronyaev memo |
| 40930.004 |  | 4RUSNIR | 1985 | Maxw |  | ((92-U-233(N,F),PR,DE,N,MXW,EXP)// (92-U-233(N,F),PR,DE,N,MXW,CALC)) | (No data) | 3 | NO-DIM | Digitize? |
| 40930.006 |  | 4RUSNIR | 1985 | Maxw |  | ((92-U-235(N,F),PR,DE,N,MXW,EXP)// (92-U-235(N,F),PR,DE,N,MXW,CALC)) | (No data) | 3 | NO-DIM | Digitize? |
| 40930.008 |  | 4RUSNIR | 1985 | Maxw |  | ((94-PU-239(N,F),PR,DE,N,MXW,EXP)/ (94-PU-239(N,F),PR,DE,N,MXW,CALC)) | (No data) | 3 | NO-DIM | Digitize? |
| 41110.008 | 1 | 4RUSFEI | 1991 | 2.9e6 | 1.5e7 | ((90-TH-232(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | NO-DIM | 5 | NO-DIM |  |
| 41110.008 | 2 | 4RUSFEI | 1991 | 2.9e6 | 1.5e7 | (90-TH-232(N,F),PR,DE,N,REL) | ARB-UNITS | 4 | 1/FIS/MEV |  |
| 41110.009 | 1 | 4RUSFEI | 1991 | 2.9e6 | 1.5e7 | ((92-U-235(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | NO-DIM | 5 | NO-DIM |  |
| 41110.009 | 2 | 4RUSFEI | 1991 | 2.9e6 | 1.5e7 | (92-U-235(N,F),PR,DE,N,REL) | ARB-UNITS | 4 | 1/FIS/MEV |  |
| 41110.010 | 1 | 4RUSFEI | 1991 | 2.9e6 | 1.5e7 | ((92-U-238(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | NO-DIM | 5 | NO-DIM |  |
| 41110.010 | 2 | 4RUSFEI | 1991 | 2.9e6 | 1.5e7 | (92-U-238(N,F),PR,DE,N,REL) | ARB-UNITS | 4 | 1/FIS/MEV |  |
| 41113.003 |  | 4RUSRI | 1991 | Spon |  | (96-CM-248(0,F),PR,DE,N,REL) | NO-DIM | 3 | NO-DIM |  |
| 41132.003 |  | 4RUSLIN | 1981 | 1.4e7 |  | (93-NP-237(N,F),PR,DE,N) | 1/MEV | 1R? | ARB-UNITS? | N(E) compiled |
| 41132.004 |  | 4RUSLIN | 1981 | 1.4e7 |  | (93-NP-237(N,F),PR,DE,N) | 1/MEV | 1R? | ARB-UNITS? | N(E) compiled |
| 41158.002 |  | 4RUSFEI | 1990 | Spon |  | (98-CF-252(0,F),PR,DE,N,REL) | ARB-UNITS | 1R | ARB-UNITS | N(E) compiled, N(E)/Nmax(E) also in Table |
| 41332.002 |  | 4RUSFEI | 1997 | 5.2e5 |  | (93-NP-237(N,F),PR,DE,N) | PT/FIS/MEV | 1 | PT/FIS/MEV |  |
| 41421.002 |  | 4RUSRI | 2002 | Spon |  | ((94-PU-240(0,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | (No data) | 2 | NO-DIM | ISTC #183B-96; Digitize? |
| 41421.003 |  | 4RUSRI | 2002 | Spon |  | ((94-PU-242(0,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | (No data) | 2 | NO-DIM | ISTC #183B-96; Digitize? |
| 41446.004 |  | 4RUSFEI | 2004 | 1.5e7 | 1.8e7 | ((90-TH-232(N,F),PR,DE,N)/ (98-CF-252(0,F),,DE,N)) | NO-DIM | 5 | NO-DIM |  |
| 41447.003 |  | 4RUSFEI | 2004 | 6.0e6 | 7.0e6 | ((92-U-238(N,F),PR,DE,N)/ (98-CF-252(0,F),,DE,N)) | NO-DIM | 5 | NO-DIM |  |
| 41450.003 |  | 4RUSFEI | 2001 | 5.0e6 | 1.3e7 | ((92-U-238(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | NO-DIM | 5 | NO-DIM |  |
| 41461.004 |  | 4RUSFEI | 1996 | 1.6e7 | 1.8e7 | ((92-U-238(N,F),PR,DE,N)/ (98-CF-252(0,F),PR,DE,N)) | NO-DIM | 5 | NO-DIM |  |
| 41502.002 |  | 4RUSLIN | 2004 | Maxw |  | ((92-U-235(N,F),PR,DE,N)/ (98-CF-252(N,F),PR,DE,N)) | NO-DIM | 2 | NO-DIM |  |
| 41502.003 |  | 4RUSLIN | 2004 | Maxw |  | ((94-PU-239(N,F),PR,DE,N)/ (98-CF-252(N,F),PR,DE,N)) | NO-DIM | 2 | NO-DIM |  |
| 41502.004 |  | 4RUSLIN | 2004 | 3.0e-1 |  | ((94-PU-239(N,F),PR,DE,N)/ (98-CF-252(N,F),PR,DE,N)) | NO-DIM | 2 | NO-DIM |  |
| 41516.007 |  | 4RUSLIN | 2009 | Maxw |  | (92-U-235(N,F),PR,DE,N,MXD/MSC) | NO-DIM |  | NO-DIM | N(E,LF)/Nmax |
| 41516.008 |  | 4RUSLIN | 2009 | Maxw |  | (92-U-235(N,F),PR,DE,N,MXD/MSC) | NO-DIM |  | NO-DIM | N(E,HF)/Nmax |