Nuclear DATA Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/639

Date:		10 May 2010

To:		Distribution

From:		N. Otsuka, S. Dunaeva

Subject:		Remarks on MONITOR coding

Monitor information helps users who want to renormalize EXFOR data with the latest monitor values, therefore coded information for monitor should be more complete and accurate, and compiler should pay more attention to it, especially inspecting old entries.

Below are two examples of problems pointed out by V. Zerkin (developing EXFOR correction system, see WP2010-19). Proposed corrections are indicated by bold fonts.

11675.026

Corrections are necessary for

- Correction of monitor reaction (capture to fission);

- Addition of cross reference (headings);

- Addition of uncertainty in monitor value for 197Au(n,γ)198Au;

etc.

30449.001

Correction is needed for incident energy for normalization under en-nrm.

A correction factor 114.03/115.4 = 0.988 was obtained by K. Zolotarev (CJD) on the basis of the current EXFOR 30449.001 (115.4 mb @ 14.6 MeV) and his evaluation [1] (114.03 mb @14.6 MeV). However this should be 115.48/115.4 = 1.001, because 115.4 mb is the data at 14.5 MeV where his evaluation gives 115.48 mb

The neutron energy for monitor (14.5 MeV) is within resolution (0.3 MeV) of incident neutron energy (14.6 MeV). However the above example asks us to give the incident energy for monitor cross section separately under en-nrm if it is different from en.

Heading Field of MONITOR, MONIT-REF, DECAY-MON

EXFOR Formats Manual explains coding rule of heading field under keywords monitor and monit-ref as follows:

MONITOR

Heading Field. Contains the data heading of the field in which the monitor value is given. The heading may be omitted, in which case its parenthesis is omitted.

MONIT-REF

Heading Field: Data heading of the field in which the standard value is given. The

heading may be omitted, in which case, its parentheses is also omitted.

DECAY-MON

Heading field. Contains the data heading of the field in which the monitor value is given. The heading may be omitted, in which case its parenthesis is omitted.

But the heading field must be present when data headings MONIT1, MONIT2 etc. are used. Therefore the following change in the rule for monitor, monit-ref and decay-mon.

Heading Field: Contains the data heading of the field in which the monitor value is given. Must be present when the data headings MONIT1, MONIT2, etc., are used in the data set. Otherwise its presence is optional.

Reference

[1] K. I. Zolotarev, INDC(NDS)-0546, 2009.

Distribution:

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

j.roberts@iaea.org

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.

cc:

zki@ippe.ru

# Text boxes

SUBENT        11675001   20091005

...

DETECTOR   (NAICR) NaI crystal

(FISCH) For thermal and fast neutrons

MONITOR    ((MONIT1)92-U-235(N,F)92-U-236,,SIG)

MONIT-REF  ((MONIT1),W.D.ALLEN+,B,PR.NUC.EN.,2,1,1958)

...

EN-NRM     MONIT1

EV         B

0.0253     584.

…

SUBENT        11675026   20091005

…

REACTION   (79-AU-197(N,G)79-AU-198,,SIG)

DECAY-DATA (79-AU-198,2.70D)

MONITOR    ((MONIT2)79-AU-197(N,G)79-AU-198,,SIG)

MONIT-REF  ((MONIT2),F.T.Gould+,J,PR,100,1248,1955)

ERR-ANALYS (ERR-1) Uncertainty in measured thermal cross section

...

MONIT2     MONIT2-ERR ERR-1

B          B          PER-CENT

99.        2.0        7.

ENDCOMMON            3

DATA                 2         21

EN         DATA

MEV        B

1.45   -01 3.20   -01

SUBENT        30449001   20090311

...

MONITOR    ((MONIT1)13-AL-27(N,P)12-MG-27,,SIG)

75 +- 8 mb at 14.5MeV.

((MONIT2)13-AL-27(N,A)11-NA-24,,SIG)

115.4+-1.4 mb at 14.5MeV

MONIT-REF  ((MONIT1),M.Bormann+,R,IAEA-156,87,1974)

((MONIT2)20111003,H.Vonach+,J,ZP,237,155,1970)

…

EN         EN-RSL     MONIT1     MONIT1-ERR MONIT2     MONIT2-ERR

EN-NRM

MEV        MEV        MB         MB         MB         MB

MEV

1.4600E+01 3.0000E-01 7.5000E+01 8.0000E+00 1.1540E+02 1.4000E+00

14.5