Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/649

Date:		11 June 2010

To:		Distribution

From:		N. Otsuka

Subject:		Fission fragments measured in coincidence

Reference:	Memo 4C-4/181

Coding of fission fragments measured in coincidence is discussed in Memo 4C-4/181. Indication of all measured fragments (incl. light charged particles) under (ELEM1,MASS1), (ELEM2,MASS2) etc. would be a solution.

Here I would like to discuss how we can differentiate such quantities in REACTION code by using three subentries (13698.002, 23012.006-007). I cannot find the best solution without further analysis for each case.

1. Fission yield for triple coincidence (13698.002 in PRELIM.1364)

Alpha ternary secondary neutron-less (νp = 0) independent fission yield is given for 252Cf spontaneous fission. Both heavy and light fragments were identified by de-excitation γ coincidence measurement.

(1) If we follow the coding sample shown in LEXFOR “Fission Yields”(without particle considered in SF7), one will obtain the following coding:

(2) If we adopt the proposal in Memo 4C-4/181, one can code this quantity as follows:

(3) Let us denote this quantity as FYI(ZL,AL,ZH,AH,ZLC,ALC), where (ZLC,ALC)=(2,4) for alpha ternary fission. Because,

(1)

we can regard FYI(ZL,AL,ZH,AH,ZLC,ALC) as a partial yield of FYI(Z,A). Therefore we may introduce a new branch code (say COI), which will be used when two or more (Z,A) are given under (ELEM1,MASS1), (ELEM2,MASS2) to explain fission yield data sets. Below is a coding sample of the same data table with this branch code.

Note that COI is not used if only (ELEM,MASS) is used in data tables.

(4) Use of SF7 for indication of all fragments under (ELEM1,MASS1), (ELEM2,MASS2) , (ELEM3,MASS3) etc. would be also possible. Below are three possibilities with SF7:

or

or

(4) The same quantity is coded in 13698.002 and 007 in PRELIM.1364 as follows (IND must be added in SF5 in final transmission):

We can see the same data line is coded twice in 002 and 007 for 102Zr+146Ba+α ternary fission with different REACTION code. This situation shows difficulty of keeping consistency in fission fragment yield compilation.

2. TKE and νp as functions of fission fragment masses (23012.006-007)

Below are coding samples of two quantities which importance was recently stressed in the 1st RCM of the IAEA CRP for prompt fission neutron spectra (and also mentioned in CP-D/635). Because the sum rule shown in Eq.(1) is not valid for total kinetic energy prompt fission neutron number, parameter code CRL would be better than branch code COI.

23012.006

Total kinetic energy (KE,LF+HF) as a function of fragment (FF) mass

23012.007

Prompt fission neutron number (PR,NU) as a function of fragment (FF) mass

Distribution:

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

j.roberts@iaea.org

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.kr

# Text boxes

SAMPLE

SUBENT        23012007   20071203                                 23012007    1

BIB                  3          4                                 23012007    2

...

REACTION   (94-PU-239(N,F)MASS,PR,NU/CRL,FF,MXW)                  23012007    4

...

ENDBIB               4                                            23012007    7

NOCOMMON             0          0                                 23012007    8

DATA                 2         29                                 23012007    9

MASS       DATA                                                   23012007   10

NO-DIM     PRT/FIS                                                23012007   11

126.       3.454                                                 23012007   12

...

SAMPLE

SUBENT        23012006   20071203                                 23012006    1

BIB                  4          5                                 23012006    2

…

REACTION   (94-PU-239(N,F)MASS,PRE,KE/CRL,LF+HF/FF,MXW)           23012006    5

MISC-COL   (MISC) FWHM of kinetic energy distribution             23012006    6

...

ENDBIB               5                                            23012006    8

NOCOMMON             0          0                                 23012006    9

DATA                 3         79                                 23012006   10

MASS       DATA       MISC                                        23012006   11

NO-DIM     MEV        MEV                                         23012006   12

81.        104.26                                                23012006   13

...

SAMPLE 1

SUBENT        13698002   20100608                                 13698  2    1

BIB                  3          3                                 13698  2    2

REACTION   (98-CF-252(0,F)ELEM/MASS,TER,FY/CRL)                   13698  2    3

...

ENDBIB               3          0                                 13698  2    6

NOCOMMON             0          0                                 13698  2    7

DATA                 6         16                                 13698  2   11

ELEM1      MASS1      ELEM2      MASS2      DATA       DATA-ERR   13698  2   12

NO-DIM     NO-DIM     NO-DIM     NO-DIM     PC/FIS     PC/FIS     13698  2   13

36.        92.        60.       156.        0.002      0.001     13698  2   14

38.        96.        58.       152.        0.008      0.003     13698  2   15

38.        98.        58.       150.        0.014      0.006     13698  2   16

...

40.        102.       56.       146.        0.009      0.004     13698  2

...

SAMPLE 4

SUBENT        13698002   20100608                                 13698  2    1

BIB                  3          3                                 13698  2    2

REACTION   (98-CF-252(0,F)ELEM/MASS,IND/TER/COI,FY,LCP+LF+HF)     13698  2    3

...

ENDBIB               3          0                                 13698  2    6

COMMON               2          3                                 13698  2    7

ELEM1      MASS1                                                  13698  2    8

NO-DIM     NO-DIM                                                 13698  2    9

2.         4.                                                    13698  2   10

ENDCOMMON            2          0                                 13698  2   11

DATA                 6         16                                 13698  2   12

ELEM2      MASS2      ELEM3      MASS3      DATA       DATA-ERR   13698  2   13

NO-DIM     NO-DIM     NO-DIM     NO-DIM     PC/FIS     PC/FIS     13698  2   14

36.        92.        60.       156.        0.002      0.001     13698  2   15

38.        96.        58.       152.        0.008      0.003     13698  2   16

38.        98.        58.       150.        0.014      0.006     13698  2   17

...

40.        102.       56.       146.        0.009      0.004     13698  2

...

SAMPLE 5

SUBENT        13698002   20100608                                 13698  2    1

BIB                  3          3                                 13698  2    2

REACTION   (98-CF-252(0,F)ELEM/MASS,IND/TER/COI,FY,A/LF/HF)       13698  2    3

...

ENDBIB               3          0                                 13698  2    6

NOCOMMON             0          0                                 13698  2    7

DATA                 6         16                                 13698  2   12

ELEM1      MASS1      ELEM2      MASS2      DATA       DATA-ERR   13698  2   13

NO-DIM     NO-DIM     NO-DIM     NO-DIM     PC/FIS     PC/FIS     13698  2   14

36.        92.        60.       156.        0.002      0.001     13698  2   15

38.        96.        58.       152.        0.008      0.003     13698  2   16

38.        98.        58.       150.        0.014      0.006     13698  2   17

...

40.        102.       56.       146.        0.009      0.004     13698  2

...

SAMPLE 4

SUBENT        13698002   20100608                                 13698  2    1

BIB                  3          3                                 13698  2    2

REACTION   (98-CF-252(0,F)ELEM/MASS,IND/TER/COI,FY,LCP/LF/HF)     13698  2    3

...

ENDBIB               3          0                                 13698  2    6

COMMON               2          3                                 13698  2    7

ELEM1      MASS1                                                  13698  2    8

NO-DIM     NO-DIM                                                 13698  2    9

2.         4.                                                    13698  2   10

ENDCOMMON            2          0                                 13698  2   11

DATA                 6         16                                 13698  2   12

ELEM2      MASS2      ELEM3      MASS3      DATA       DATA-ERR   13698  2   13

NO-DIM     NO-DIM     NO-DIM     NO-DIM     PC/FIS     PC/FIS     13698  2   14

36.        92.        60.       156.        0.002      0.001     13698  2   15

38.        96.        58.       152.        0.008      0.003     13698  2   16

38.        98.        58.       150.        0.014      0.006     13698  2   17

...

40.        102.       56.       146.        0.009      0.004     13698  2

...

SAMPLE 6

SUBENT        13698002   20100608                                 13698  2    1

BIB                  3          3                                 13698  2    2

REACTION   (98-CF-252(0,F)ELEM/MASS,TER,FY/CRL,LF+HF)             13698  2    3

...

ENDBIB               3          0                                 13698  2    6

NOCOMMON             0          0                                 13698  2    7

DATA                 6         16                                 13698  2   11

ELEM1      MASS1      ELEM2      MASS2      DATA       DATA-ERR   13698  2   12

NO-DIM     NO-DIM     NO-DIM     NO-DIM     PC/FIS     PC/FIS     13698  2   13

36.        92.        60.       156.        0.002      0.001     13698  2   14

38.        96.        58.       152.        0.008      0.003     13698  2   15

38.        98.        58.       150.        0.014      0.006     13698  2   16

...

40.        102.       56.       146.        0.009      0.004     13698  2

...

SUBENT        13698007   20100608                                 13698  7    1

BIB                  3          3                                 13698  7    2

REACTION   (98-CF-252(0,F)ELEM/MASS,TER,FY/CRL,A+LF)              13698  7    3

...

ENDBIB               3          0                                 13698  7    6

NOCOMMON             0          0                                 13698  7    7

DATA                 6         16                                 13698  7   12

ELEM1      MASS1      ELEM2      MASS2      DATA       DATA-ERR   13698  7   13

NO-DIM     NO-DIM     NO-DIM     NO-DIM     PC/FIS     PC/FIS     13698  7   14

40.        102.       56.       146.        0.009      0.004     13698  7   15

...

SAMPLE 3

SUBENT        13698002   20100608                                 13698  2    1

BIB                  3          3                                 13698  2    2

REACTION   (98-CF-252(0,F)ELEM/MASS,IND/TER/COI,FY)               13698  2    3

...

ENDBIB               3          0                                 13698  2    6

COMMON               2          3                                 13698  2    7

ELEM1      MASS1                                                  13698  2    8

NO-DIM     NO-DIM                                                 13698  2    9

2.         4.                                                    13698  2   10

ENDCOMMON            2          0                                 13698  2   11

DATA                 6         16                                 13698  2   12

ELEM2      MASS2      ELEM3      MASS3      DATA       DATA-ERR   13698  2   13

NO-DIM     NO-DIM     NO-DIM     NO-DIM     PC/FIS     PC/FIS     13698  2   14

36.        92.        60.       156.        0.002      0.001     13698  2   15

38.        96.        58.       152.        0.008      0.003     13698  2   16

38.        98.        58.       150.        0.014      0.006     13698  2   17

...

40.        102.       56.       146.        0.009      0.004     13698  2

...

SAMPLE 2

SUBENT        13698002   20100608                                 13698  2    1

BIB                  3          3                                 13698  2    2

REACTION   (98-CF-252(0,F)ELEM/MASS,IND/TER,FY)                   13698  2    3

...

ENDBIB               3          0                                 13698  2    6

COMMON               2          3                                 13698  2    7

ELEM1      MASS1                                                  13698  2    8

NO-DIM     NO-DIM                                                 13698  2    9

2.         4.                                                    13698  2   10

ENDCOMMON            2          0                                 13698  2   11

DATA                 6         16                                 13698  2   12

ELEM2      MASS2      ELEM3      MASS3      DATA       DATA-ERR   13698  2   13

NO-DIM     NO-DIM     NO-DIM     NO-DIM     PC/FIS     PC/FIS     13698  2   14

36.        92.        60.       156.        0.002      0.001     13698  2   15

38.        96.        58.       152.        0.008      0.003     13698  2   16

38.        98.        58.       150.        0.014      0.006     13698  2   17

...

40.        102.       56.       146.        0.009      0.004     13698  2

...