Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/680

Date:		28 January 2011

To:		Distribution

From:		N.Otsuka, S. Kopecky, P Schillebeeckx

Subject:		LEXFOR entry for covariances in the AGS format

Reference:	Memo CP-D/564(Rev.)

IRMM and NDS have recently completed the compilation of neutron transmission data together with and the covariance information. The data resulted from measurements at the GELINA facility (EXFOR 23077) [1]. Two new headings are proposed

# Dictionary 24 (Data Headings)

TOF-MIN     Lower boundary of time-of-flight

TOF-MAX     Upper boundary of time-of-flight.

In order to fulfill the action A51 of the 2010 NRDC meeting, addition to the LEXFOR “Covariance” is proposed below. Headings ERR-1, ERR-2 etc. will be interpreted as “AGS vector” when CHLSK (Cholesky) is coded under the keyword COVARIANCE.

Covariance

Definition

For a measured quantity at two points σi and σj (e.g., cross section at two incident energies; i,j=1,2,…,m), covariance between them are defined as

(1)

If the cross section depends on p parameters (source of uncertainties) {xk} (k=0,1,2,…,p),

(2)

Eq.(1) can be rewritten as

(3)

where k,l = 0 gives the uncorrelated uncertainty Δ0σi=(∂σi/∂x0)Δxi0.and δij is the Kronecker’s delta.

…

Cholesky Decomposition of Covariance Matrix

Eq.(3) is expressed as

(4)

(V=cov(σi, σj), M={Δ0σi}, Sα={∂σi/∂xik}, Vα=cov(xik, xjl))

The p×p matrix Vα=cov(xik, xjl) is positive definite and symmetric, and therefore there is a matrix L which satisfies Vα=LLt (Cholesky decomposition):

,                                                                  (5)

where Dα=SαL is a m×p matrix. The ij-th component of the Eq.(5) is

.                                                   (6)

(Dα={Δkσi}, k=0, 1,2,…,p and i=1,2,…,m). Therefore the m×m covariance matrix V can be expressed by p sets of the m-dimension vectors {Δkσi}. This vector (AGS vector [2,3]) gives a compact expression of the covariance matrix when m is very huge (e.g., high resolution time-of-flight spectra).

If the covariance matrix cov(xik, xjl) is simplified to ΔxikΔxjl δkl (e.g. cor(xik, xjl)=δkl for any i and j), the summation of the last term of Eq.(3) is simplified to the summation of (∂σi/∂xik)Δxik (∂σj/∂xjl) Δxjlδkl, and Δkσi in Eq.(6) becomes the k-th partial uncertainty of the quantity σi by comparing Eq.(3) and Eq.(6).

Though AGS vector {Δkσi} cannot be interpreted as the partial uncertainty of the quantity σi due to the parameter xk in general, the vectors are coded in the same way, and given under headings ERR-1, ERR-2,.... with the code CHLSK under the keyword COVARIANCE.

Example:

REACTION   (48-CD-0(N,TOT),,TRN)

MISC-COL   (MISC1) Width of time-of-flight bin

(MISC2) Uncorrelated uncertainty squared

CORRECTION  Data are corrected for

- dead time at sample-in detector   (din);

- background at sample-in detector  (Bin);

- dead time at sample-out detector  (dout);

- background at sample-out detector (Bout),

as follows:

T=N(din*Cin-Bin)/(dout*Cout-Bout)

, where

N: Normalization factor (N=1 +/- 0.5%)

T:    Transmission;

Cin:  Count at sample-in detector;

Cout: Count at sample-out detector.

Backgrounds were expressed by constant plus sum of

two exponential: a0+a1*exp(-b1*tof)+a2*exp(-b2*tof)

ERR-ANALYS  ERR-1 to ERR-4 gives "correlation vectors" in the

AGS format.

(ERR-T)  Total uncertainty (sigma)

(ERR-S)  Uncorrelated uncertainty (sigma)

(ERR-1)  Correlation dead time correction  (sample)

(ERR-2)  Correlation background correction (sample)

(ERR-3)  Correlation dead time correction  (open beam)

(ERR-4)  Correlation background correction (open beam)

COVARIANCE (CHLSK)  Compiled in ERR-1 to ERR-4 in the AGS format

ENDBIB

NOCOMMON

DATA

EN         TOF-MIN    TOF-MAX    MISC1      DATA       ERR-T

ERR-S      MISC2      ERR-1      ERR-2      ERR-3      ERR-4

EV         NSEC       NSEC       NSEC       NO-DIM     NO-DIM

NO-DIM     NO-DIM     NO-DIM     NO-DIM     NO-DIM     NO-DIM

4.79930E+0   873301.2   873429.2      128.0 1.14780E+0 6.65562E-2

6.65376E-2 4.42725E-3 1.33447E-5-9.12646E-4-1.37145E-5 1.28552E-3

4.79790E+0   873429.2   873557.2      128.0 9.70250E-1 5.63176E-2

5.63021E-2 3.16993E-3 1.09942E-5-8.47529E-4-1.16680E-5 1.00913E-3

…

In this example, ERR-S gives Δ0σi and ERR-1 to ERR-4 give Δkσi  (k=1,2,3,4, i=1,2,…,m) in Eq.(6).

References

[1]	S. Kopecky, I. Ivanov, M. Moxon, P. Schillebeeckx, P. Siegler, I. Sirakov, “The total cross section and resonance parameters for the 0.178 eV resonance of 113Cd”, Nuclear Instruments and Methods B 267 (2009) 2345 - 2350

[2]	C. Bastian, “General procedures and computational methods for generating covariance matrices”, Proc. Int. Symposium on Nuclear Data Evaluation Methodology, Brookhaven National Laboratory, USA, October 12-16, 1992, p642.

[3]	N. Otuka, A. Borella, S. Kopecky, C. Lampoudis, P. Schillebeeckx, “Database for time-of-flight spectra including covarainces”, Proc. Int. Conf. on Nucl. Data for Sci .and Technol., Jeju island, Korea, April 26-30, 2010.

Distribution:

blokhin@ippe.ru

cgc@ciae.ac.cn

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

fukahori.tokio@jaea.go.jp

ganesan@barc.gov.in

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

j.roberts@iaea.org

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re

zhuangyx@ciae.ac.cn

cc:

peter.schillebeeckx@ec.europa.eu

stefan.kopecky@ec.europa.eu