Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/680 (Rev.2)

Date:		7 April 2014

To:		Distribution

From:		N.Otsuka, S. Kopecky, P Schillebeeckx

Subject:		LEXFOR entry for covariances in the AGS format

Reference:	Memo CP-D/564(Rev.)

IRMM and NDS have recently completed the compilation of neutron transmission data together with and the covariance information. The data resulted from measurements at the GELINA facility (EXFOR 23077) [1]. Two new headings are proposed

# Dictionary 24 (Data Headings)

TOF-MIN     Lower boundary of time-of-flight

TOF-MAX     Upper boundary of time-of-flight.

In order to fulfill the action A51 of the 2010 NRDC meeting, addition to the LEXFOR “Covariance” is proposed below. Headings ERR-1, ERR-2 etc. will be interpreted as “AGS vector” when CHLSK (Cholesky) is coded under the keyword COVARIANCE.

In the example adopted in the LEXFOR input, the uncertainty in normalization factor (0.5%) is not treated as coded information under the MONIT-ERR, because the coded total uncertainty (ERR-T) does not include this component. If one receives the total uncertainty including the normalization uncertainty, the normalization uncertainty must be coded information under the heading MONIT-ERR.

Covariance

Definition

For a measured quantity at two points σi and σj (e.g., cross section at two incident energies; i,j=1,2,…,m), covariance between them are defined as

(1)

If the cross section depends on p parameters (source of uncertainties) {xk} (k=0,1,2,…,p),

(2)

Eq.(1) can be rewritten as

(3)

where k,l = 0 gives the uncorrelated uncertainty Δ0σi=(∂σi/∂x0)Δxi0.and δij is the Kronecker’s delta.

Δσij=cov(σi,σj) (i=1,…n) forms the following covariance matrix.

…

Cholesky Decomposition of Covariance Matrix

Eq.(3) is expressed as

(4)

(V=cov(σi, σj), M={Δ0σi}, Sα={∂σi/∂xik}, Vα=cov(xik, xjl))

The p×p matrix Vα=cov(xik, xjl) is positive definite and symmetric, and therefore there is a matrix L which satisfies Vα=LLt (Cholesky decomposition):

,                                                                  (5)

where Dα=SαL is a m×p matrix. The ij-th component of the Eq.(5) is

.                                                   (6)

(Dα={Δkσi}, k=0, 1,2,…,p and i=1,2,…,m). Therefore the m×m covariance matrix V can be expressed by p sets of the m-dimension vectors {Δkσi}. This vector (AGS vector [2,3]) gives a compact expression of the covariance matrix when m is very huge (e.g., high resolution time-of-flight spectra).  One may treat the vectors {Δ0σi} and {Δkσi} (AGS vector [1,2]) as if they are uncorrelated and fully correlated partial uncertainty from the view of the full covariance matrix construction, and they may be coded under ERR-1 etc. with the correlation property flag U or F. See Ref.[3] for a coding sample.

If the covariance matrix cov(xik, xjl) is simplified to ΔxikΔxjl δkl (e.g. cor(xik, xjl)=δkl for any i and j), the summation of the last term of Eq.(3) is simplified to the summation of (∂σi/∂xik)Δxik (∂σj/∂xjl) Δxjlδkl, and Δkσi in Eq.(6) becomes the k-th partial uncertainty of the quantity σi by comparing Eq.(3) and Eq.(6).

Though AGS vector {Δkσi} cannot be interpreted as the partial uncertainty of the quantity σi due to the parameter xk in general, the vectors are coded in the same way, and given under headings ERR-1, ERR-2,.... with the code CHLSK under the keyword COVARIANCE.

Example:

REACTION   (48-CD-0(N,TOT),,TRN)

MISC-COL   (MISC1) Width of time-of-flight bin

(MISC2) Uncorrelated uncertainty squared

CORRECTION  Data are corrected for

- dead time at sample-in detector   (din);

- background at sample-in detector  (Bin);

- dead time at sample-out detector  (dout);

- background at sample-out detector (Bout),

as follows:

T=N(din*Cin-Bin)/(dout*Cout-Bout)

, where

N: Normalization factor (N=1 +/- 0.5%)

T:    Transmission;

Cin:  Count at sample-in detector;

Cout: Count at sample-out detector.

Backgrounds were expressed by constant plus sum of

two exponential: a0+a1*exp(-b1*tof)+a2*exp(-b2*tof)

ERR-ANALYS  ERR-1 to ERR-4 gives "correlation vectors" in the

AGS format.

(ERR-T)  Total uncertainty (sigma)

(ERR-S)  Total uncorrelated uncertainty (sigma)

(ERR-1)  Correlated component due to dead time

correction (sample-in)

(ERR-2)  Correlated component due to background

Correction (sample-in)

(ERR-3)  Correlated component due to dead time

correction (sample-out)

(ERR-4)  Correlated component due to background

Correction (sample-out)

COVARIANCE (CHLSK)  Compiled in ERR-1 to ERR-4 in the AGS format

ENDBIB

NOCOMMON

DATA

EN         TOF-MIN    TOF-MAX    MISC1      DATA       ERR-T

ERR-S      MISC2      ERR-1      ERR-2      ERR-3      ERR-4

EV         NSEC       NSEC       NSEC       NO-DIM     NO-DIM

NO-DIM     NO-DIM     NO-DIM     NO-DIM     NO-DIM     NO-DIM

4.79930E+0   873301.2   873429.2      128.0 1.14780E+0 6.65562E-2

6.65376E-2 4.42725E-3 1.33447E-5-9.12646E-4-1.37145E-5 1.28552E-3

4.79790E+0   873429.2   873557.2      128.0 9.70250E-1 5.63176E-2

5.63021E-2 3.16993E-3 1.09942E-5-8.47529E-4-1.16680E-5 1.00913E-3

…

In this example, ERR-S gives Δ0σi and ERR-1 to ERR-4 give Δkσi  (k=1,2,3,4, i=1,2,…,m) in Eq.(6).

References

[1]	S. Kopecky, I. Ivanov, M. Moxon, P. Schillebeeckx, P. Siegler, I. Sirakov, “The total cross section and resonance parameters for the 0.178 eV resonance of 113Cd”, Nuclear Instruments and Methods B 267 (2009) 2345 - 2350

[2]	C. Bastian, “General procedures and computational methods for generating covariance matrices”, Proc. Int. Symposium on Nuclear Data Evaluation Methodology, Brookhaven National Laboratory, USA, October 12-16, 1992, p642.

[1]	B. Becker et al., “Data reduction and uncertainty propagation of time-of-flight spectra with AGS”, J. Instrum. 7 (2012) P11002.

[2]	N. Otuka, A. Borella, S. Kopecky, C. Lampoudis, P. Schillebeeckx, “Database for time-of-flight spectra including covarainces”, J. Kor. Phys. Soc. 59 (2011)1314.

[3]	D.L. Smith, N. Otuka, “Experimental nuclear reaction data uncertainties: Basic concepts and documentation”, Nucl. Data. Sheets 113 (2012) 3006.

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru, cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

iwamoto.osamu@jaea.go.jp

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kamskaya@expd.vniief.ru

kato@nucl.sci.hokudai.ac.jp

kiyoshi.matsumoto@oecd.org

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

sbabykina@yandex.ru

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn

cc:

peter.schillebeeckx@ec.europa.eu

stefan.kopecky@ec.europa.eu