Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/700

Date:		18 May 2011

To:		Distribution

From:		N. Otsuka, S.P. Simakov

Subject:		Compilation of light-ion induced neutron spectra for application

Neutrons generation from light-ion induced reactions on light element targets (e.g., 7Li(p,xn), 7Li(p,xn), 9Be(d,xn)) have been recognized as practical useful neutron fields for cross section measurements, detector calibrations, material irradiation and validation of the neutron transport through the shields. Theoretical modeling of the differential cross sections for these reactions faces with difficulties and incapability to verify models against experimental data. This resulted to unavailability of complete evaluated nuclear data files for many neutron production reactions. Therefore the collection of experimental numerical spectra in EXFOR will have high importance.

There are still many experimental works missed in the EXFOR database. Many measurements were done and published in period 1960-1980. Data there are usually presented as numerous data points (and not always point-wise) in the figures. Compilation of all relevant data by priority is proposed.

Distribution:

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.

cc:

babam@cyric.tohoku.ac.jp

bem@ujf.cas.cz

hagi@post.kek.jp

uwamino@riken.jp

Experimental neutron spectra and angular distributions from thick Li and other targets bombarded with light charged-particle

(“Table” in source means data from authors are available)

(2011-03-01)

| Targ. | Proj. | Unit | Emin (eV) | Emax (eV) | Lab. | Author | Publication | Vol | Page | Year | Source | Centre | Additional reference |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Li | d | PYT2 | 1.5+7 | 2.3+7 | 1CACCRC | M.A.Lone+ | J,NIM | 143 | 331 | 1977 | Point | NNDC | NBIR-77-1279,5,1977 |
| Li | p | PYT2 | 1.5+7 | 2.3+7 | 1CACCRC | M.A.Lone+ | J,NIM | 143 | 331 | 1977 | Point | NNDC | NBIR-77-1279,5,1977 |
| Be9 | d | PYT2 | 1.5+7 | 2.3+7 | 1CACCRC | M.A.Lone+ | J,NIM | 143 | 331 | 1977 | Point | NNDC | NBIR-77-1279,5,1977 |
| Be9 | p | PYT2 | 1.5+7 | 2.3+7 | 1CACCRC | M.A.Lone+ | J,NIM | 143 | 331 | 1977 | Point | NNDC | NBIR-77-1279,5,1977 |
| Li | d | PYTA | 1.5+7 | 2.3+7 | 1CACCRC | M.A.Lone+ | J,NIM | 143 | 331 | 1977 | Point | NNDC | NBIR-77-1279,5,1977 |
| Li | p | PYTA | 1.5+7 | 2.3+7 | 1CACCRC | M.A.Lone+ | J,NIM | 143 | 331 | 1977 | Point | NNDC | NBIR-77-1279,5,1977 |
| Be9 | d | PYTA | 1.5+7 | 2.3+7 | 1CACCRC | M.A.Lone+ | J,NIM | 143 | 331 | 1977 | Point | NNDC | NBIR-77-1279,5,1977 |
| Be9 | p | PYTA | 1.5+7 | 2.3+7 | 1CACCRC | M.A.Lone+ | J,NIM | 143 | 331 | 1977 | Point | NNDC | NBIR-77-1279,5,1977 |
| Li | p | arb. | 3.5+7 | 6.5+7 | 1USADAV | H.I.Amols+ | J,MED | 4 | 486 | 1977 | Curve | NNDC |  |
| Li | d | arb. | 3.5+7 |  | 1USADAV | H.I.Amols+ | J,MED | 4 | 486 | 1977 | Curve | NNDC |  |
| Li | p | PYTA | 3.5+7 | 6.5+7 | 1USADAV | H.I.Amols+ | J,MED | 4 | 486 | 1977 | Table | NNDC |  |
| Li | d | PYTA | 3.5+7 |  | 1USADAV | H.I.Amols+ | J,MED | 4 | 486 | 1977 | Table | NNDC |  |
| Li | d | PYT2 | 3.5+7 |  | 1USADAV | D.L.Johnson+ | J,JNM | 85-86 | 467 | 1979 | Curve | NNDC | BNL-NCS-51245,99,1980 |
| Li | d | PYTA | 3.5+7 |  | 1USADAV | D.L.Johnson+ | J,JNM | 85-86 | 467 | 1979 | Point | NNDC | BNL-NCS-51245,99,1980 |
| Be9 | d | DAE | 8.8+6 | 1.8+7 | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218.002 | UCRL-51310,1972 |
| Be9 | d | PYT2 | 8.8+6 | 1.8+7 | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218.003 | UCRL-51310,1972 |
| C | d | PYT2 | 1.8+7 |  | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218.005 | UCRL-51310,1972 |
| Li | d | PYT2 | 1.9+7 |  | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218.004 | UCRL-51310,1972 |
| 2H | d | DAE | 1.9+7 |  | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218.006 | UCRL-51310,1972 |
| Be9 | d | DA | 4.0+6 | 1.8+7 | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218 | UCRL-51310,1972 |
| Be9 | d | PYTA | 3.0+6 | 2.0+7 | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218 | UCRL-51310,1972 |
| Li | d | PYTA | 5.0+6 | 1.9+7 | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218 | UCRL-51310,1972 |
| C | d | PYTA | 1.2+7 | 1.8+7 | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | F0218 | UCRL-51310,1972 |
| 2H | d | DA | 1.7+7 | 1.9+7 | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Point | CNPD | UCRL-51310,1972 |
| 2H | d | PYTA | 8.0+6 | 1.9+7 | 1USALRL | K.A.Weaver+ | J,NSE | 52 | 35 | 1973 | Table | CNPD | UCRL-51310,1972 |
| Li | d | PYT2 | 1.3+7 | 3.4+7 | 1USANRL | A.N.Goland+ | J,IRE | 22 | 1776 | 1975 | Point | NNDC |  |
| Li | d | PYTA | 1.3+7 | 3.4+7 | 1USANRL | A.N.Goland+ | J,IRE | 22 | 1776 | 1975 | Table | NNDC |  |
| Li | d | PYT2 | 3.5+7 |  | 1USANRL | L.S.August+ | R,NBSIR | 77-1279 | 31 | 1977 | Point | NNDC |  |
| Be9 | h | PYT2 | 8.1+7 |  | 1USANRL | L.S.August+ | R,NBSIR | 77-1279 | 31 | 1977 | Point | NNDC |  |
| Be9 | d | PYT2 | 4.0+7 |  | 1USAORL | M.J.Saltmarsh+ | J,NIM | 145 | 81 | 1977 | Point | NNDC | NBIR-77-1279,24,1977 |
| Be9 | d | PYTA | 4.0+7 |  | 1USAORL | M.J.Saltmarsh+ | J,NIM | 145 | 81 | 1977 | Table | NNDC | NBIR-77-1279,24,1977 |
| Li | d | PYT2 | 8.0+6 | 1.5+7 | 1USATNL | C.E.Nelson+ | R,NBSIR | 77-1279 | 1 | 1977 | Point | NNDC |  |
| Li | p | PYT2 | 1.5+7 |  | 1USATNL | C.E.Nelson+ | R,NBSIR | 77-1279 | 1 | 1977 | Point | NNDC |  |
| Li | d | PYTA | 8.0+6 | 1.5+7 | 1USATNL | C.E.Nelson+ | R,NBSIR | 77-1279 | 1 | 1977 | Table | NNDC |  |
| Li | p | PYTA | 1.5+7 |  | 1USATNL | C.E.Nelson+ | R,NBSIR | 77-1279 | 1 | 1977 | Table | NNDC |  |
| Be9 | d | PYT2 | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Histgram | NEA DB |  |
| 12C | d | PYT2 | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Histgram | NEA DB |  |
| Cu | d | PYT2 | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Histgram | NEA DB |  |
| Mo | d | PYT2 | 1.6+7 | 3.3+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Histgram | NEA DB |  |
| Ta181 | d | PYT2 | 3.3+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Histgram | NEA DB |  |
| Au197 | d | PYT2 | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Histgram | NEA DB |  |
| Be9 | d | PYTA | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Table | NEA DB |  |
| C12 | d | PYTA | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Table | NEA DB |  |
| Cu | d | PYTA | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Table | NEA DB |  |
| Mo | d | PYTA | 1.6+7 | 3.3+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Table | NEA DB |  |
| Ta181 | d | PYTA | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Table | NEA DB |  |
| Au197 | d | PYTA | 1.6+7 | 5.0+7 | 2BLGLVN | J.P.Meulders+ | J,PMB | 20 | 235 | 1975 | Table | NEA DB |  |
| Be9 | d | PYT2 | 4.0+7 | 5.4+7 | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| C | d | PYT2 | 4.0+7 | 5.4+7 | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Al | d | PYT2 | 4.0+7 | 5.4+7 | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Fe | d | PYT2 | 5.4+7 |  | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Co | d | PYT2 | 5.4+7 |  | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Ni | d | PYT2 | 5.4+7 |  | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Cu | d | PYT2 | 4.0+7 | 5.4+7 | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Nb | d | PYT2 | 5.4+7 |  | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Mo | d | PYT2 | 5.4+7 |  | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Pd | d | PYT2 | 5.4+7 |  | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Ag | d | PYT2 | 4.0+7 | 5.4+7 | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Ta | d | PYT2 | 5.4+7 |  | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Pt | d | PYT2 | 5.4+7 |  | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Au197 | d | PYT2 | 4.0+7 | 5.4+7 | 2GERKFK | G.W.Schweimer | J,NP/A | 100 | 537 | 1967 | Table | NEA DB |  |
| Be9 | d | PYTA | 9.4+6 | 1.4+7 | 2GERKFK | H.J.Brede+ | J,NIM/A | 274 | 332 | 1989 | Table | D0523 |  |
| Be9 | p | PYTA | 1.7+7 | 2.2+7 | 2GERKFK | H.J.Brede+ | J,NIM/A | 274 | 332 | 1989 | Table | D0523.004 |  |
| Li | d | PYT2 | 3.2+7 |  | 2JPN? | M.Sugimoto+ | Priv. Comm. |  |  | 1995 | Table | JCPRG | Missing, |
| LI | d | PYT2 | 7.0+7 | 2.1+8 | 2JPNIPC | N.Nakao+ | J,NIM/A | 420 | 218 | 1999 | Table | E2298 | in compilation |
| Li | d | PYT2 | 4.0+7 | 9.0+7 | 2JPNJAE | M.Baba+ | J,NIM/A | 428 | 454 | 1999 | Table | E1808.003 | in compilation |
| Li | d | PYT2 | 2.5+8 | 3.9+8 | 2JPNOSA | Y.Iwamoto+ | J,NIM/B | 629 | 43 | 2011 | Table | E2297.002 | in compilation |
| Li | d | PYT2 | 2.0+7 | 4.0+7 | 2JPNTOH | Y.Uwamino+ | J,NIM/A | 389 | 463 | 1997 | Table | E1826.005 | in compilation |
| Li | d | DAE | 2.5+7 |  | 2JPNTOH | M.Hagiwara+ | J,JNM | in press |  |  | Table | E2322 |  |
| Li | d | DA | 2.5+7 |  | 2JPNTOH | M.Hagiwara+ | J,JNM | in press |  |  | Table | E2322 |  |
| Li | d | CS |  | 4.0+7 | 2JPNTOH | M.Hagiwara+ | J,JNM | in press |  |  | Table | E2323 |  |
| Li | d | TTT | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,JNM | in press |  |  | Table | E2323 |  |
| Al27 | d | TTT | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,JNM | in press |  |  | Table | E2323 |  |
| C | d | TTT | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,JNM | in press |  |  | Table | E2323 |  |
| C | p | PYT2 | 5.0+7 |  | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 | Table | E1856 |  |
| C | p | PYT2 | 7.0+7 |  | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 | Point | JCPRG |  |
| W | p | PYT2 | 5.0+7 |  | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 | Table | E1856 |  |
| W | p | PYT2 | 7.0+7 |  | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 | Point | JCPRG |  |
| Li | d | PYT2 | 4.0+7 |  | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 | Table | E1986.002 |  |
| Li | d | DAE | 4.0+7 |  | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 | Table | E1986.005 |  |
| Li | p | DAE | 7.0+7 |  | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 | Plot | JCPRG | E2110? |
| Li | d | CS | 7.0+6 | 4.0+7 | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 |  | JCPRG | E2323? |
| Li | d | TTT | 4.0+7 |  | 2JPNTOH | M.Baba+ | C,2004SANTA | 1 | 884 | 2004 |  | JCPRG | E2323? |
| Li | d | PYT2 | 2.5+7 |  | 2JPNTOH | M.Baba+ | J,JNM | 307-311 | 1715 | 2002 | Table | E1893 |  |
| Li | d | TTT | 2.5+7 |  | 2JPNTOH | M.Baba+ | J,JNM | 307-311 | 1715 | 2002 | Table | E1893.002 |  |
| C | d | PYT2 | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,JNM | 329-333 | 218 | 2004 | Table | E1985.002 |  |
| Al27 | d | PYT2 | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,JNM | 329-333 | 218 | 2004 | Table | E1985.003 |  |
| Al27 | d | CS | 2.1+7 | 3.9+7 | 2JPNTOH | M.Hagiwara+ | J,JNM | 329-333 | 218 | 2004 | Table | E1985 |  |
| C | d | CS | 2.3+7 | 4.0+7 | 2JPNTOH | M.Hagiwara+ | J,JNM | 329-333 | 218 | 2004 | Table | E1985.007 |  |
| Li | d | PYT2 | 2.5+7 |  | 2JPNTOH | T.Aoki+ | J,NST | 41 | 399 | 2004 | Table | E1893 |  |
| Be9 | d | PYT2 | 2.5+7 |  | 2JPNTOH | T.Aoki+ | J,NST | 41 | 399 | 2004 | Table | E1893 |  |
| Li | d | TTT | 2.5+7 |  | 2JPNTOH | T.Aoki+ | J,NST | 41 | 399 | 2004 | Table | E1893.022 |  |
| Be9 | d | TTT | 2.5+7 |  | 2JPNTOH | T.Aoki+ | J,NST | 41 | 399 | 2004 | Table | E1893.023 |  |
| Li | d | PYT2 | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,FST | 48 | 1320 | 2005 | Table | E1986.002 |  |
| Li | d | PYTA | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,FST | 48 | 1320 | 2005 | Table | E1986.003 |  |
| Li | d | PYT | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,FST | 48 | 1320 | 2005 | Table | E1986.004 |  |
| Li | d | DAE | 4.0+7 |  | 2JPNTOH | M.Hagiwara+ | J,FST | 48 | 1320 | 2005 | Table | E1986.005 |  |
| Be9 | d | PYT2 | 2.0+7 | 4.0+7 | 2JPNTOK | Y.Uwamino+ | J,NIM/A | 271 | 546 | 1988 | Point | E2296 | in compilation |
| C | d | 1/AE | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Cu | d | 1/AE | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Pb | d | 1/AE | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| C | h | 1/AE | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Cu | h | 1/AE | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Pb | h | 1/AE | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| C | a | 1/AE | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Cu | a | 1/AE | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Pb | a | 1/AE | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| C | d | 1/A | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Cu | d | 1/A | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Pb | d | 1/A | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| C | p | 1/A | 3.0+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Cu | p | 1/A | 3.0+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Fe | p | 1/A | 3.0+0 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Pb | p | 1/A | 3.0+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| C | d | 1/A | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Cu | d | 1/A | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Fe | d | 1/A | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Pb | d | 1/A | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| C | h | 1/A | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Cu | h | 1/A | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Fe | h | 1/A | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Pb | h | 1/A | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| C | a | 1/A | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Cu | a | 1/A | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Fe | a | 1/A | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| Pb | a | 1/A | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Point | JCPRG |  |
| C | p | YLD | 3.0+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Cu | p | YLD | 3.0+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Fe | p | YLD | 3.0+0 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Pb | p | YLD | 3.0+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| C | d | YLD | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Cu | d | YLD | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Fe | d | YLD | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Pb | d | YLD | 3.3+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| C | h | YLD | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Cu | h | YLD | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Fe | h | YLD | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Pb | h | YLD | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| C | a | YLD | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Cu | a | YLD | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Fe | a | YLD | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Pb | a | YLD | 6.5+7 |  | 2JPNTOK | K.Shin+ | J,PR/C | 29 | 1307 | 1984 | Table | JCPRG |  |
| Be9 | d | 1/AE | 6.5+7 |  | 2SF JVV | Z.Radivojevic+ | J,NIM/B | 183 | 212 | 2001 | Table | O1050.003 |  |
| C | d | 1/AE | 5.0+7 |  | 2SF JVV | Z.Radivojevic+ | J,NIM/B | 183 | 212 | 2001 | Table | O1050.002 |  |
| Be9 | d | 1/A | 6.5+7 |  | 2SF JVV | Z.Radivojevic+ | J,NIM/B | 183 | 212 | 2001 | Table | O1050.005 |  |
| C | d | 1/A | 5.0+7 |  | 2SF JVV | Z.Radivojevic+ | J,NIM/B | 183 | 212 | 2001 | Table | O1050.004 |  |
| C | d | 1/AE | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.002 |  |
| C | d | 1/A | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.005.1 |  |
| C | d | YLD | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.008.1 |  |
| D2O | d | 1/AE | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.002 |  |
| D2O | d | 1/A | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.007.1 |  |
| D2O | d | YLD | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.010.1 |  |
| WTR | d | 1/AE | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.004 |  |
| WTR | d | 1/A | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.006.1 |  |
| WTR | d | YLD | 4.0+7 |  | 2SF JVV | G.Lhersonneau+ | J,NIM/A | 603 | 228 | 2009 | Point | O1746.009.1 |  |
| Li | d |  | 1.6+7 | 1.7+7 | 3CZRUFJ | P.Bem+ | Internal report |  |  |  |  | NDS |  |
| Be9 | d | PYT2 | 2.1+7 |  | 4RUSFEI | V.K.Daruga+ | J,SJA | 30 | 493 | 1971 | Point | CAJaD | SJA,24,71,1968 |
| Li | d | PYT2 | 2.1+7 |  | 4RUSFEI | V.K.Daruga+ | S,SJA | 30 | 493 | 1971 | Point | CAJaD | SJA,24,71,1968 |