Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/772

Date:		14 December 2012

To:		Distribution

From:		N. Otsuka

Subject:		Data measured with slowing-down spectrometers (Modifier SDT)

Lead slowing-down (time) spectrometers (LSDS) are neutron spectrometers on time of slowing-down in lead, and have been utilized to measure neutron-induced cross sections, mainly for fission cross sections of minor actinides. Data measured with LSDS has been flagged by the method code SLODT in the relevant EXFOR entries.

LSDS measurements can be done nearby neutron sources, and allow us to perform measurements with a small amount of sample under intense neutron beams. However its energy resolution is worse than conventional time-of-flight method. An example of comparison of cross sections from LSDS data, TOF data and evaluated data is shown in Fig.1 for 237Np(n,f) cross sections (LSDS data from KURRI, TOF data from n_TOF). Point-wise cross sections (e.g., cross sections in ENDF libraries) must be broadened according to the LSDS resolution function before comparison with LSDS data. To utilize LSDS data in EXFOR in validation of point-wise cross sections, I propose to include resolution functions under the keyword INC-SPECT.

Another question is the modifier for data averaged over the LSDS resolution function. During finalization of 14259.002 (TRANS.1385), Otto Schwerer mentioned that the modifier SPA could not be compatible with the heading EN. Actually 14259.002 does not give computer readable resolution information (e.g., EN-RSL), and I agree with him. I would propose a new spectrum modifier (e.g., SDT, or any other good code?) for data broadened by the LSDS resolution function.

# Dictionary 34 (Modifiers)

SDT	Slowing-down time average

Except for the RPI (RINS) cases [2-4] and a few cases of KURRI (KULS) and INR (SZR-100) cases [13,19], it is difficult to find parameters determined by the experimentalists in their final publications. T. Nakagawa et al. compiled resolution functions [1] for RPI and KURRI data for comparison with JENDL-3.3, and we can see the resolution function for KURRI (KULS) [5] received by T. Nakagwa from K. Kobayashi in 1999. Motivated by this compilation, I also have compiled resolution functions for LSDS cross sections from INR (SZR-100) with V. Shorin in October 2011 for the IAEA CRP “MANREAD”. These are tabulated in this memo.

V. Shorin informed me LSDS data taken at Kurchatov Institute [21] which reports their resolution function approximated by “Pearson distribution”. Their energy dependent cross sections were digitized from [21] and compiled in EXFOR 41369.

Table: Resolution functions for the lead slowing-down (time) spectrometers (E in eV)

| EXFOR | Target | Ref. | Emin | Emax | ΔEFWHM/E | φ(E) | Plot |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 12788.002 | 244Cm | [2] | 1.4-1 | 8.0+4 | (0.0746+0.130E-1+2.52×10-5E)1/2 | ? | RPI1 |
| 12788.003 | 246Cm | [2] | 1.4-1 | 8.0+4 |  |  |  |
| 12788.004 | 248Cm | [2] | 1.4-1 | 8.0+4 |  |  |  |
| 12991.002 | 242Cm | [3] | 1.1-1 | 9.8+4 |  |  |  |
| 12991.004 | 238Pu | [3] | 1.0-1 | 9.8+4 |  |  |  |
| 13197.002 | 247Cm | [4] | 1.2-1 | 9.8+4 | (0.0835+0.128E -1+3.05×10-5E)1/2 | ? | RPI2 |
| 22422.005 | 243Am | [6] | 5.6-2 | 7.9+3 | 0.162899E-1/2+0.352787+7.599×10-5E Note that a factor E is missing in p101 of [1] (informed by T. Nakagawa in 10 Dec. 2012). | ? | KUR1 |
| 22479.002 | 241Am | [7] | 9.5-2 | 1.1+4 |  |  |  |
| 22644.003 | 242mAm | [8] | 2.8-2 | 1.3+4 |  |  |  |
| 22647.003 | 231Pa | [9] | 8.9-2 | 1.3+4 |  |  |  |
| 22647.004 | 229Th | [9] | 1.3-2 | 1.0+4 |  |  |  |
| 22731.002 | 237Np | [10] | 1.1+0 | 4.6+3 |  |  |  |
| 22858.003 | 237Np | [11] | 1.5-1 | 1.3+3 |  |  |  |
| 23186.002 | 237Np | [12] | 1.0-1 | 2.2+3 | (0.111+0.214E -1+0.003 E 1/2)1/2 Fitting performed by K. Hirose to Table 3 (exp. data) of [5]. | LN | KUR2 |
| 23186.003 | 242mAm | [12] | 1.0-1 | 2.2+3 |  |  |  |
| 23186.004 | 245Cm | [12] | 1.0-1 | 2.2+3 |  |  |  |
| 41503.003 | 236U | [13] | 1.1+0 | 1.9+4 | (0.302 + 3×10-5 E + 0.025/E)1/2 | TN | INR1 |
| 41523.002 | 242mAm | [14] | 2.9-2 | 2.1+4 | 2.345(0.1322 + 7.5×10-5 E + 0.044/E)1/2 These parameters were determined for 235U and 239Pu [15]. No detailed analysis was done for 242mAm and 245Cm. |  | INR2 |
| 41523.004 | 245Cm | [14] | 2.8-2 | 2.1+4 |  |  |  |
| 41524.002 | 244Cm | [16] | 7.4-2 | 2.3+4 | (0.3082 + 1.1×10-4 E + 0.24/E)1/2 |  | INR3 |
| 41578.002 | 243Am | [17] | 3.0-1 | 8.7+3 | (0.332 + 1.1×10-4 E + 0.178/E)1/2 |  | INR4 |
| 41532.002 | 243Cm | [18] | 3.1-2 | 1.4+4 | The parameters were not determined. |  |  |
| 41533.002 | 246Cm | [19] | 1.4-1 | 2.1+4 | (0.322 + 1.1×10-4 E + 0.178/E)1/2 These parameters are given in [20]. |  | INR5 |
| 41533.007 | 247Cm | [19] | 3.0-2 | 2.0+4 |  |  |  |
| 41533.008 | 248Cm | [19] | 1.2-1 | 2.1+4 |  |  |  |

Fig.1 Comparison of LSDS data (22731.002) with TOF data (23126.004) and JENDL-4.

Fig.2 Energy dependence of energy resolution.

In the table, φ(E) = LN and TN are for lognormal and truncated normal distribution.

References

[1] T. Nakagawa and O. Iwamoto, Report JAERI-Data/Code 2002-02 (2002).

[2] H.T. Maguire Jr. et al., Nucl. Sci. Eng. 89 (1985) 293.

[3] B. Alam et al., Nucl. Sci. Eng. 99 (1988) 267.

[4] Y. Danon et al., Nucl. Sci. Eng. 109 (1991) 341.

[5] K. Kobayashi et al., Nucl. Instrum. Meth. A385 (1997) 145.

[6] K. Kobayashi et al., J. Nucl. Sci. Technol. 36 (1999) 20.

[7] S. Yamamoto et al., Nucl. Sci. Eng. 126 (1997) 201.

[8] T. Kai et al., Ann. Nucl. Energy 28 (2001) 723.

[9] K. Kobayashi et al., Nucl. Sci. Eng. 139 (2001) 273.

[10] A. Yamanaka et al., J. Nucl. Sci. Technol. 30 (1993) 863.

[11] K. Kobayashi et al., J. Nucl. Sci. Technol. 39 (2002) 111.

[12] K. Hirose et al., J. Nucl. Sci. Technol. 49 (2012) 1057.

[13] A.A. Alekseev et al., Phys. Atom. Nucl. 71 (2008) 1351.

[14] A.A. Alekseev et al., Atom. Energy 106 (2009) 133.

[15] V.S.  Shorin, Yad. Konst. 2008 No.1-2, p 60 (2008).

[16] A.A. Alekseev et al., Phys. Atom. Nucl. 73 (2010) 1487.

[17] A.A. Alekseev et al., Atom. Energy 111 (2012) 428.

[18] A.A. Alekseev et al., Atom. Energy 107 (2009) 110.

[19] A.A. Alekseev et al., Atom. Energy 109 (2011) 408.

[20] A.A. Alekseev et al., Atom. Energy 110 (2011) 51.

[21] V.F Gerasimov et al., Report JINR-E3-97-213,348 (1997).

# Proposed revision to LEXFOR “Spectrum Average”

# Spectrum Average

Cross sections averaged over a broad incident-projectile energy spectrum may be entered into EXFOR using the proper modifier to REACTION SF8. The type of spectrum and its characteristic should be entered in free text under the keyword INC(SPECT.

The following spectrum types are defined:

## …

Slowing-Down Time Spectrum Average

REACTION coding:  SDT in SF8.

Slowing-down time spectrum averaged cross section is defined as

For a given slowing-down time t, the corresponding average neutron energy E is expressed by <E> = K / (t0 + t)2, where K is the slowing-down constant and t0 is a correction factor to account for the time it takes neutrons to slow down from source energies. The flux distribution φ(E) is typically approximated by the Gaussian distribution centred at <E> with its standard deviation σ(<E>). The average energy quoted will be, typically, EN. The width information (e.g., FWHM) is essential for comparison with better resolution data sets, and must be given under the keyword INC-SPECT. Compilation of some FWHM values determined by experimentalists is seen in [x].

REACTION coding:  SIG in SF6; SDT in SF8.

…

Reference

[x] T. Nakagawa, O. Iwamoto, Report JAERI-Data/Code 2002-025 p.101 (2002).

# Proposed revision to LEXFOR “General Quantity Modifiers”

# General Quantity Modifiers

The general quantity modifiers (reaction SF8) are flagged with ‘GENQ’ in Archive dictionary 34 of and are listed in the beginning of Archive and TRANS dictionary 236.  They can be added to any quantity without requiring an entry in Dictionary 236.  Some of them require clarification:

…

## Spectrum Average Modifiers

Used for data measured over a broad incident energy spectrum.  For such data one of the spectrum modifiers are used BRA, BRS, EPI, FIS, FST, MXW, SDT, and SPA; see Spectrum Average for details. The spectrum average modifier must be coded before other general quantity modifiers.

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

chiba@earth.sgu.ac.jp

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn

cc:

danony@rpi.edu

hirose.kentaro@jaea.go.jp

iwamoto.osamu@jaea.go.jp

k_koba84@tg8.so-net.ne.jp

nakagawa_tsuneo@ybb.ne.jp

shorin@ippe.ru

# Footnotes

Cross sections measured as a function of energy and then averaged over a discrete energy range are entered as average (modifier AV). See General Quantity Modifiers.