Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/783

Date:		18 April 2013

To:		Distribution

From:		N. Otsuka, O. Schwerer

Subject:		Branch codes IND, CUM, M+ and M-

The usages of branch codes to indicate contributions of precursors (IND, CUM, M+, M-) are explained in LEXFOR “Independent and Cumulative Data”.

When a nuclide AJ has an isomer, the cross section derived by observation of the ground state of nuclide AgJ (e.g., detection of β delayed gamma from AgJ) is

σobs (AgJ )= σdir(AgJ) + a σdir(AmJ) +Σi bi σpre,i ,

where “dir” is for the cross section for direct production of the nuclide wihtout decay, and “pre,i”is for contribution of the precursor i which may decay to AgJ. The figure shows a β++EC decay precusour AL contributes to the 3rd term. For simplicity we assume there is only one precursor, and

σobs (AgJ )= σdir(AgJ) + a σdir(AmJ) +b σpre.

The coefficient a and b may depend on decay data (T1/2, IT transition probability etc.) as well as measurement condition like cooling time. Combinations of SF4 and SF5 are summarized below for various conditions for a and b:

|  | a=0 | 0<a<1 | a=1 | a=? | No a |
| --- | --- | --- | --- | --- | --- |
| b=0 | Z-S-A-G,IND | Z-S-A-G,IND/M+ | Z-S-A,IND | Z-S-A-G,(M) | Z-S-A-G,IND |
| 0<b≤1 | Z-S-A-G,CUM/M- | Z-S-A-G,CUM | Z-S-A,CUM | Z-S-A-G,CUM | Z-S-A-G,CUM |
| b=? | Z-S-A-G,(CUM)/M- | Z-S-A-G,(CUM)/M+ | Z-S-A,(CUM) | Z-S-A-G,(CUM) | Z-S-A-G,(CUM) |
| No b | Z-S-A-G,IND | Z-S-A-G,M+ | Z-S-A | Z-S-A-G,(M) | Z-S-A-G |

=0: Contribution is excluded (e.g., subtraction of its contribution, short cooling time, decay-curve analysis,  on-line separation etc.)

=1: Full contribution is expected (e.g., 100% branching ratio to AgJ, long cooling time, T1/2(AgJ)>>T1/2(AmJ) or T1/2 (AL) etc.)

No: AJ is physical shielded from AmJ or AL (e.g., stable state, no decay branch to AgJ, T1/2(AgJ)<<T1/2(AmJ) or T1/2 (AL)).

Proposed corrections to LEXFOR “Independent and Cumulative Data”

- Addition of the above table.

- Corrections to the explanation of (CUM) and (M).

The current LEXFOR explanation is inconsistent with dictionary 31, and I would believe the parenthesized codes will be more useful if we define (CUM) and (M) as above. The corresponding expansions in dictionary 236 should be corrected so that they are consistent with the expansions in dictionary 31.

| Branch Code | Definition |
| --- | --- |
| ... | ... |
| (CUM) | Uncertain if the formation via radioactive decay and isomeric transition are included. |
| ... | ... |
| (M) | Uncertain if the formation by partial feeding via isomeric transition is included. |

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn

# Text boxes

AZJ

AZ+1L

g.s.

m.s.

EC

I T