Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/789

Date:		15 May 2013

To:		Distribution

From:		N. Otsuka, S.P. Simakov

Subject:		Energy resolution given in units of a reciprocal velocity

The LEXFOR entry “Resolution” explains that the energy resolution can be given in units of reciprocal velocity, and actually energy resolution is coded under the heading EN-RSL with NSEC/M. I learned conversion of it to the energy resolution in eV from Peter Schillebeeckx (EC-JRC IRMM), and it is summarized below (See also [1]):

The kinetic energy of the neutron is given by

E = mc2 (γ – 1),

where m is the mass of neutron (939.6 MeV/c2), c is the light velocity (0.2998 m/nsec), and

γ = [1-(v/c)2]-1/2

is the Lorentz factor. If we differentiate the kinetic energy by the velocity,

dE/dv = (E/v) (γ + 1) γ

and therefore the energy resolution ΔE is related with the velocity resolution Δv by

ΔE/E = (γ + 1) γ (Δv/v).

If we introduce a new variable τ = 1/v,

Δτ/τ = - Δv/v

and therefore the energy resolution is related with this new variable by

ΔE/E = (γ + 1) γ |Δτ| /τ.

The absolute value of Δτ is the resolution given in units of a reciprocal velocity. From this equation,

ΔE = E (γ + 1) γ |Δτ| v ~ 2E (2E/m)1/2 |Δτ| ~ 2.766 × 10-2 E3/2 |Δτ|

at the non-relativistic limit (γ→1) with ΔE in MeV and Δτ in nsec/m.

Some questionable coding of EN-RSL with NSEC/M:

- Time resolution given in nsec by the authors, but coded with nsec/m.

Example: EXFOR 41110.001, where the time resolution given by the authors (2.5 nsec) is coded as 2.5 nsec/m.

- Time resolution was not given by the authors in units of nsec/m, but was coded with nsec/m by the compiler.

Example 1: EXFOR 22820.001 and 22822.001, where the time resolution given by the compiler (0.5 nsec/m) is not known by the first author (V. Semkova).

Example 2: EXFOR 41138.001, where the meaning, units (and relevance for incident neutron energy) of the time resolution given by the compiler (12 nsec/m) are now not understandable and hence acceptable for an author (S. Simakov). Also should the name of another co-author Glavatch be compiled in the original transcription, i.e. Hlavac?

Reference

P. Schillebeeckx et al., Nucl. Data Sheets 113 (2012) 3054.

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn

cc:

peter.schillebeeckx@ec.europa.eu