Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/798

Date:		28 June 2013

To:		Distribution

From:		N. Otsuka

Subject:		Revision of LEXFOR “Neutron Yield”

A revision of the description on eta values in LEXFOR “Neutron Yield” is proposed below to give more clear definition for fast neutrons.

Eta (η)

Definition:  The average neutron yield per nonelastic event for neutron-induced reactions:

,

where the summation is taken over all nonelastic channels, and ni is the average neutron multiplicity of the i-th nonelastic channel. For example, ni =0 for (n,γ), (n,p), (n,α); =1 for (n,n’), (n,np), (n,nα); =2 for (n,2n); = for (n,f).

For the thermally fissile isotopes, where fission and capture are, up to a certain threshold, the only nonelastic processes, η is defined as average neutron yield per absorption:

REACTION Coding:  NON or ABS in SF3, and ETA in SF6.

Examples:

(N,NON),,ETA)	η, in general

(N,ABS),,ETA)	η below (n,n’) threshold

(N,ABS),,ETA,,RES)	η at resonance below (n,n’) threshold

For further related quantity codes see Dictionary 236.

References

[1] P.P. Lebedev et al., J. Nucl. Energy A 11(1959) 39.

[2] E.R. Graves et al., Phys. Rev. 97 (1955) 1205.

The REACTION SF3 code for eta values must be NON when the incident neutron energy is higher than the inelastic threshold energy. I checked non-thermal eta values compiled in EXFOR entries, and found 21 data sets giving eta values for neutrons higher than the inelastic threshold and coded with ABS in SF3. It must be changed to NON if eta values are given.

| Subentry | Target | En, max (eV) | Ex,1st (eV) |
| --- | --- | --- | --- |
| 20002.006 | Pu-239 | 3.0e+4 | 7.8e+3 |
| 20938.024 | U-235 | 2.0e+2 | 7.7e+1 |
| 20938.029 | U-235 | 2.0e+2 | 7.7e+1 |
| 21019.009 | Th-232 | 7.0e+6 | 4.9e+4 |
| 21019.014 | U-238 | 7.0e+6 | 4.5e+4 |
| 21019.026 | U-238 | 7.0e+6 | 4.5e+4 |
| 21210.002 | U-238 | 1.4e+7 | 4.5e+4 |
| 21750.006 | Th-232 | 1.4e+7 | 4.9e+4 |
| 40350.008 | U-233 | 9.0e+5 | 4.0e+4 |
| 40350.009 | U-235 | 9.0e+2 | 7.7e+1 |
| 40350.010 | Pu-239 | 9.0e+5 | 7.8e+3 |
| 40350.011 | U-233 | 2.5e+5 | 4.0e+4 |
| 40350.012 | U-235 | 3.0e+4 | 7.7e+1 |
| 40350.013 | Pu-239 | 2.5e+5 | 7.8e+3 |
| 40385.004 | U-235 | 8.8e+5 | 7.7e+1 |
| 40385.010 | Pu-239 | 8.8e+5 | 7.8e+3 |
| 40639.003 | Pu-239 | 1.4e+7 | 7.8e+3 |
| 40806.002 | U-235 | 1.4e+7 | 7.7e+1 |
| 40806.004 | U-238 | 1.4e+7 | 4.5e+4 |
| 40808.004 | Pu-239 | 2.4e+4 | 7.8e+3 |
| 40808.007 | U-235 | 2.4e+7 | 7.7e+1 |

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn