Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/813

Date:		5 November 2013

To:		Distribution

From:		N. Otsuka, O. Schwerer

Subject:		Excitation energy for inclusive reaction (SF3=X)

Reference:	Memo CP-D/811

Introduction – E2135.002

In some EXFOR double-differential cross section (DDX) data sets, the excitation energy is defined for an inclusive reaction, for example,

SUBENT        E2135002   20130309

…

REACTION   (28-NI-58(P,X)0-NN-1,,DA/DE)

EN-SEC     ANG-CM is polar angle (c.m.) between beam and neutron

(E-EXC,29-CU-58)

…

EN         EN-RSL     ANG-CM

MEV        MEV        ADEG

198.       0.3        0.

…

E-EXC      DATA-CM

MEV        MB/SR/MEV

-3.02210   0.00077

…

The incident proton energy (Ep=198 MeV) is enough higher than the (p,2n) reaction threshold (Ep=22 MeV), and therefore the data set must be treated as 58Ni(p,n+x) rather than 58Ni(p,n)58Cu in general. But the energy spectrum is given as a function of the excitation energy of 58Cu calculated by the two body kinematics, and the heading E-EXC is related with 58Cu (see EN-SEC) even though this nuclide is not always produced by the reaction process expressed by the REACITON code.

A similar data set has been sometimes coded in a different way. For example, Dr. K. Miki (EXFOR E2382 [1]) informed JCPRG that his (t,3He+x) DDX data sets (Et=300 MeV/A, θ~0) must be related with the two body (t,3He) reaction because he regards that the direct process is dominant. This opinion is taken into account in this EXFOR entry, for example,

(40-ZR-90(T,HE3)39-Y-90,,DA/DE)

instead of

(40-ZR-90(T,X)2-HE-3,,DA/DE).

It could be difficult for EXFOR compilers to make a right decision (especially when the authors are not available). For example, EXFOR F1183 [2] gives angular distributions (25 deg <θcm<165 deg) of DDX for 65Cu(α,p+x) at Eα=24.4 MeV and a constant excitation energy of 68Zn derived by the two body kinematics. The threshold energy of the (α,2p) reaction is about 13 MeV.

Proposal

A possible solution could be use of a new branch code (say, INC), for example

(28-NI-58(P,N)29-CU-58,INC,DA/DE,N/RSD).

For E2135.002. The new branch code expresses that the data are not corrected for other channels emitting the same outgoing particle considered. When necessary, one may also propose a similar code

(INC): uncertain if the data sets are corrected for the many body final states.

# Dictionary 31 (Branch codes)

# INC			Not corrected for other channels emitting the same particle

# Dictionary 236 (Quantities)

INC,DA/DE,*/RSD	Double diff. cross section d2/dA(*)/dE(residual nucleus) not corrected for other channels emitting the same particle

| Quantity | Reaction Type | Dimension | Subentry |
| --- | --- | --- | --- |
| INC,DA/DE,*/RSD | DAE | DAE | E2135.002-008 F1183.002-005,010-011 O0223.002-009 |

Addition to LEXFOR “Production and Emission Cross sections”

Production Cross Section defined with Excitation Energy

Sometimes the production cross section is given as a function of the excitation energy of the reaction product from a specific process (e.g., two body reaction). This may happen when the contribution of the direct process is expected to be dominant (e.g., data at forwarded angle). In this case the production cross section may be coded with the specific process considered by the author under REACTION with a branch code INC.

Example:

(28-NI-58(P,N)29-CU-58,INC,DA/DE,N/RSD)

Double differential cross section dσ/dΩndEx(58Cu) for 58Ni(p,n+x) reaction.

Problematic entries

In this occasion, I went through EXFOR entries where

- REACTION SF3=X and SF6=*DE* and the secondary energy is coded under E-EXC

- REACTION SF3=X and the secondary energy is coded under Q-VAL.

Problematic entries are summarized at the end of this memo with proposed corrections.

References

[1] K. Miki et al., Phys. Rev. Lett. 108 (2012) 262503 (EXFOR E2382).

[2] A.V. Smirnov et al., Izv. Akadem. Nauk. USSR, Ser. Fiz. 49 (1985) 138 (EXFOR F2135).

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

iwamoto.osamu@jaea.go.jp

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

kiyoshi.matsumoto@oecd.org

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn

cc:

miki@rcnp.osaka-u.ac.jp

hsakai@ribf.riken.jp

Error list 1: REACTION SF3=X and SF6=*DE* and the secondary energy is coded under E-EXC

|  |  | REACTION | Proposed correction |
| --- | --- | --- | --- |
| C0728 | 002 | (2-HE-3(P,X)0-NN-1,,DA/DE) | E-EXC → E-RL; add (E-RL,P+P+P) under EN-SEC. (Excitation energy measured from 3 proton mass energy) |
|  | 003 | (2-HE-3(P,X)0-NN-1,,POL/DA/DE,,ANA) |  |
| E2135 | 002, 004 | (28-NI-58(P,X)0-NN-1,,DA/DE) | Use (28-NI-58(P,N)29-CU-58,INC,DA/DE,N/RSD). |
|  | 003 | (50-SN-120(P,X)0-NN-1,,DA/DE) | Use (50-SN-120(P,N)51-SB-120,INC,DA/DE,N/RSD). |
|  | 005 | (30-ZN-70(P,X)0-NN-1,,DA/DE) | Use (30-ZN-70(P,N)31-GA-70,INC,DA/DE,N/RSD). |
|  | 006 | (48-CD-114(P,X)0-NN-1,,DA/DE) | Use (48-CD-114(P,N)49-IN-114,INC,DA/DE,N/RSD). |
|  | 007 | (50-SN-118(P,X)0-NN-1,,DA/DE) | Use (50-SN-118(P,N)51-SB-118,INC,DA/DE,N/RSD). |
|  | 008 | (50-SN-120(P,X)0-NN-1,,DA/DE) | Use (50-SN-120(P,N)51-SB-120,INC,DA/DE,N/RSD). |
| E2382 | 002-010 | (82-PB-208(T,HE3)81-TL-208,,DA/DE) | Use (82-PB-208(T,HE3)81-TL-208,INC,DA/DE). |
|  | 011- 019 | (40-ZR-90(T,HE3)39-Y-90,,DA/DE) | Use (40-ZR-90(T,HE3)39-Y-90,INC,DA/DE). |
| F1183 | 002- 005 | (29-CU-65(A,X)1-H-1,,DA/DE) | Use (29-CU-65(A,P)30-ZN-68,INC,DA/DE,P/RSD). |
|  | 010, 011 | (29-CU-65(A,X)2-HE-4,,DA/DE) | Use (29-CU-65(A,P)30-ZN-68,INC,DA/DE,P/RSD). |
| J1601 | 002 | (6-C-12(PIP,X)1-KP-0,,IPA/DE) | ? The current Z-S-A formalism does not support hyper nuclei (e.g., 12ΛC) |
| M0285 | 004. 005 | (13-AL-27(G,X)0-NN-1,,DA/DE,,BRS/REL) | Delete EN-MAX; E-EXC → EN; DA/DE → DA (Excitation function of the direct reaction part assuming two body kinematics: Eγ=(27/26)En+Eth). (c.f. Fig.4). |
| O0176 | 002- 004 | (40-ZR-90(P,X)0-NN-1,PAR,DA/DE) | Delete PAR.; Delete E-EXC. Delete EN-SEC. Neutrons are not corresponding to IAS excitation (c.f. Figs.3-4). |
|  | 005- 007 | (82-PB-208(P,X)0-NN-1,PAR,DA/DE) |  |
| O0223 | 002- 009 | (6-C-12(P,X)1-H-1,,DA/DE) | Use (6-C-12(P,INL)6-C-12,INC,DA/DE,P/RSD). |
| O0819 | 002 | (1-H-1(P,X)1-PP-0,PAR,DA/DE,,RAW) | E-EXC → E-RL; add(E-RL,N+P) under EN-SEC. ε in figures gives the excitation energy measured from proton + neutron mass energy. |

Error list 2: REACTION SF3=X and the secondary energy is coded under Q-VAL.

|  |  | REACTION | Proposed correction |
| --- | --- | --- | --- |
| 21984 | 055 | (6-C-12(N,X)0-NN-1,PAR,DA) | Separate to two data sets: (6-C-12(N,EL)6-C-12,,DA).for Q=0. (6-C-12(N,INL)6-C-12,PAR,DA) for Q≠0. |
|  | 063 | (6-C-12(N,X)0-NN-1,PAR,SIG) | Use (6-C-12(N,INL)6-C-12,PAR,SIG). |
|  | 090 | (8-O-16(N,X)0-NN-1,PAR,DA) | Separate to two data sets: (8-O-16(N,EL)8-O-16,,DA).for Q=0. (8-O-16(N,INL)8-O-16,PAR,DA) for Q≠0. |
|  | 094 | (8-O-16(N,X)0-NN-1,PAR,SIG) | Use (8-O-16(N,INL)8-O-16,PAR,SIG). |
| 22025 | 023 | (24-CR-0(N,X)0-NN-1,PAR,DA) | Separate to two data sets: (24-CR-0(N,EL)24-CR-0,,DA) for Q=0. (24-CR-0(N,INL)24-CR-0,PAR,DA) for Q=-1.43 MeV (2+ of 52Cr). |
|  | 041 | (26-FE-0(N,X)0-NN-1,PAR,DA) | Use (26-FE-0(N,SCT)26-FE-0,PAR,DA). Q=0 + Q=-0.84 MeV (2+ of 56Fe) |
|  | 059 | (28-NI-0(N,X)0-NN-1,PAR,DA) | Separate to two data sets: (28-NI-0(N,EL)28-NI-0,PAR,DA)for Q=0. (28-NI-0(N,EL)28-NI-0,PAR,DA)for Q=-1.33 + -1.45 MeV (2+ of 58,60Ni). |
| 22077 | 014 | (29-CU-0(N,X)0-NN-1,PAR,DA) | Use (29-CU-0(N,INL)29-CU-0,PAR,DA)?? |
|  | 029 | (22-TI-0(N,X)0-NN-1,PAR,DA) | Use (22-TI-0(N,INL)22-TI-0,PAR,DA)?? |
|  | 044 | (40-ZR-0(N,X)0-NN-1,PAR,DA) | Use (40-ZR-0(N,INL)40-ZR-0,PAR,DA)?? |
|  | 059 | (6-C-12(N,X)0-NN-1,PAR,DA) | Separate to two data sets: (6-C-12(N,EL)6-C-12,,DA).for Q=0. (6-C-12(N,INL)6-C-12,PAR,DA) for Q≠0. Also delete EN=14.1 MeV in the COMMON section!!! |
| 22157 | 034 | (8-O-16(N,X)0-NN-1,PAR,DA) | Use (8-O-16(N,INL)8-O-16,PAR,DA). |
| O0090 | 002 | (13-AL-27(P,X)0-NN-1,PAR,DA) | Use (13-AL-27(P,N)14-SI-27,PAR,DA). |
|  | 003 | (41-NB-93(P,X)0-NN-1,PAR,DA) | Use (41-NB-93(P,N)42-MO-93,PAR,DA). |
|  | 004 | (50-SN-120(P,X)0-NN-1,PAR,DA) | Use (50-SN-120(P,N)51-SB-120,PAR,DA). |
|  | 005 | (82-PB-208(P,X)0-NN-1,PAR,DA) | Use (82-PB-208(P,N)83-BI-208,PAR,DA). |
|  | 006 | (13-AL-27(P,X)0-NN-1,PAR,DA) | Use (13-AL-27(P,N)68-ER-165,PAR,DA). |
|  | 007 | (13-AL-27(P,X)0-NN-1,PAR,DA) | Use (13-AL-27(P,N)14-SI-27,PAR,DA). |
|  | 008 | (26-FE-54(P,X)0-NN-1,PAR,DA) | Use (26-FE-54(P,N)27-CO-54,PAR,DA). |
|  | 009 | (26-FE-56(P,X)0-NN-1,PAR,DA) | Use (26-FE-56(P,N)27-CO-56,PAR,DA). |
|  | 010 | (41-NB-93(P,X)0-NN-1,PAR,DA) | Use (41-NB-93(P,N)42-MO-93,PAR,DA). |
|  | 011 | (50-SN-120(P,X)0-NN-1,PAR,DA) | Use (50-SN-120(P,N)51-SB-120,PAR,DA). |
|  | 012 | (82-PB-208(P,X)0-NN-1,PAR,DA) | Use (82-PB-208(P,N)83-BI-208,PAR,DA). |
|  | 013 | (67-HO-165(P,X)0-NN-1,PAR,DA) | Use (67-HO-165(P,N)68-ER-165,PAR,DA). |