Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/924

Date:		24 February 2017

To:		Distribution

From:		N. Otsuka

Subject:		Recommended resonance integrals in EXFOR V1001 and V1002

Regarding Action 52 from the NRDC 2016 meeting,

“Check V1001.532, V1002.082, V1002.126, V1002.173 and V1002.572 against Mughabghab’s Atlas (c.f. slide #23 of Cabellos’s presentation “Provide a list of erroneous and suspicious outliers by using various statistical approaches”).

I checked each case with Mughabghab’s Atlas and the resonance integral values calculated from ENDF/B-VII.1, JEFF-3.2, JENDL-4.0u2 and TENDL-2014 by Oscar.

General remark

The highest energy of the resonances listed in the Atlas is often coded under EN-MAX (i.e., upper boundary of integration). But this is not correct even if the resonance integral is constructed from the listed parameters. The Atlas defines the resonance integral with the energy integration from 0.5 eV to infinity (cf. Eq.2.85 of the Atlas), and we always should see EN-MIN=0.5 eV without EN-MAX in these EXFOR entries. Consequently REACTION SF8=LIM should not be used. Corrections are probably necessary not only for these five subentries but more systematically in the two EXFOR entries.

In the following comments,

ENDF/B	ENDF/B-VII.1

JEFF		JEFF-3.2

JENDL	JENDL-4.0u2

TENDL	TENDL-2014

V1001.532.2

REACTION: (50-SN-124(N,G)50-SN-125-G,,RI,,LIM,RECOM)

| EN-MIN (eV) | EN-MAX (eV) | EXFOR (mb) | Evaluated data (b) calculated by Oscar |
| --- | --- | --- | --- |
|  |  |  | ENDF/B | JEFF | JENDL | TENDL |
| 0.5 | 314750 | 0.083(25) | N/A | 1.87E-1 | N/A | 3.57E-1 |

- EN-MAX and LIM in EXFOR must be deleted.

- The unit “mb” printed in the Atlas must be “b”. (Oscar’s comment is right and also confirmed by Dr. Mughabghab on 23 Feb. 2017.)

- EXFOR 22632.009 (0.083±0.025 b) is adopted.

V1002.082.2

REACITON: (55-CS-135(N,G)55-CS-136,,RI,,LIM,CALC)

| EN-MIN (eV) | EN-MAX (eV) | EXFOR (b) | Evaluated data (b) Upper: calculated by Oscar. Lower: taken from text of the ENDF file. |
| --- | --- | --- | --- |
|  |  |  | ENDF/B | JEFF | JENDL | TENDL |
| 0.5 | 219.5 | 3 | 4.11E+1 | 4.11E+1 | 4.58E+1 | 4.11E+1 |
| 0.5 | ∞ |  | 5.09E+1 | 5.09E+1 | 5.35E+1 | 5.04E+1 |

- EN-MAX and LIM in EXFOR must be deleted.

- I could not find the source of the Atlas value. The Atlas gives a complete resonance parameter set for only one resonance at 42.2 eV.

V1002.126

REACITON: (58-CE-138(N,G)58-CE-139,,RI,,LIM,RECOM)

| EN-MIN (eV) | EN-MAX (eV) | EXFOR (b) | Evaluated data (b) Upper: calculated by Oscar. Lower: taken from text of the ENDF file. |
| --- | --- | --- | --- |
|  |  |  | ENDF/B | JEFF | JENDL | TENDL |
| 0.5 | 10 | 6.7(34) | 2.97E-1 | 4.20E-1 | N/A | 4.20E-1 |
| 0.5 | ∞ |  | 9.12E+0 | 6.76E+0 | N/A | 6.90E+0 |

- EN-MAX and LIM in EXFOR must be deleted.

- This value is very close to EXFOR 12866.129 (6.7±3.1 b).

V1002.173

REACTION: (61-PM-148-M(N,G)61-PM-149,,RI,,LIM,RECOM)

| EN-MIN (eV) | EN-MAX (eV) | EXFOR (b) | Evaluated data (b) Upper: calculated by Oscar. Lower: taken from text of the ENDF file. |
| --- | --- | --- | --- |
|  |  |  | ENDF/B | JEFF | JENDL | TENDL |
| 0.0253 |  | 3600(2400) | 5.47E+4 | 5.47E+4 | 5.32E+4 | 5.13E+4 |
| 0.5 | ∞ |  | 4.79E+3 | 4.79E+3 | 4.20E+3 | 8.27E+2 |

- EN-MIN must be 0.5 eV according to the definition of the resonance integral in the Atlas.

- I could not find the source of the Atlas value. The Atlas gives a complete resonance parameter set for only one resonance at 0.169 eV.

V1002.572.4

REACTION: (91-PA-233(N,G)91-PA-234,,RI,,LIM,CALC)

| EN-MIN (eV) | EN-MAX (eV) | EXFOR (b) | Evaluated data (b) calculated by Oscar |
| --- | --- | --- | --- |
|  |  |  | ENDF/B | JEFF | JENDL | TENDL |
| 0.5 | 17 | 3.0 | 7.02E+2 | 7.02E+2 | 7.03E+2 | 7.63E+2 |

- EN-MAX and LIM in EXFOR must be deleted.

- (N,G) must be (N,F). Oscar’s comment is right.

- I could not find the source of the Atlas value. The Atlas does not give any fission width. Also there is no experimental resonance integral in EXFOR.

Distribution:

a.koning@iaea.org

aloks279@gmail.com

cgc@ciae.ac.cn

dbrown@bnl.gov

draj@barc.gov.in

dvoytenkov@ippe.ru

ebata@nucl.sci.hokudai.ac.jp

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

iwamoto.osamu@jaea.go.jp

jhchang@kaeri.re.kr

jmwang@ciae.ac.cn

kaltchenko@kinr.kiev.ua

jim.gulliford@oecd.org

manuel.bossant@oecd.org

marema08@gmail.com

masaaki@nucl.sci.hokudai.ac.jp

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

n.otsuka@iaea.org

nrdc@jcprg.org

nurzat.kenzhebaev@gmail.com

ogritzay@kinr.kiev.ua

oscar.cabellos@oecd.org

otto.schwerer@aon.at

pikulina@expd.vniief.ru

pritychenko@bnl.gov

samaev@obninsk.ru

sbabykina@yandex.ru

scyang@kaeri.re.kr

selyankina@expd.vniief.ru

sonzogni@bnl.gov

stakacs@atomki.hu

stanislav.hlavac@savba.sk

s.a.dunaeva@yandex.ru

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zholdybayev@inp.kz

zhuangyx@ciae.ac.cn

cc:

mugabgab@bnl.gov