FENDL-3.0

Evaluated nuclear data library
for fusion applications

Summary documentation prepared by

D. López Aldama
Centro de Gestión de Información y Desarrollo de la Energía

La Habana, Cuba

and

R. Capote Noy
Nuclear Data Section
International Atomic Energy Agency
Vienna, Austria

December 2011

__________________________________________________________________

IAEA  NUCLEAR  DATA  SECTION,  WAGRAMER  STRASSE  5,  A-1400  VIENNA

INDC documents may be downloaded in electronic form from http://www-nds.iaea.or.at/indc_sel.html or sent as an e-mail attachment. Requests for hardcopy or e-mail transmittal should be directed to services@iaeand.iaea.org or to:

Nuclear Data Section

International Atomic Energy Agency

PO Box 100

Wagramer Strasse 5

A-1400 Vienna

Austria

Produced by the IAEA in Austria

December 2011

INDC(NDS)-XXX

Distr.  FE

FENDL-3.0

Evaluated nuclear data library
for fusion applications

Summary documentation prepared by

D. López Aldama
Centro de Gestion de Informacion y Desarrollo de la Energia

La Habana, Cuba

and

R. Capote Noy
Nuclear Data Section
International Atomic Energy Agency
Vienna, Austria

Abstract

A description of the work undertaken towards the development of a new version of the Fusion Evaluated Nuclear Data Library (FENDL) for applications is summarized. The main issues related with the selection and processing of evaluated nuclear data files using the NJOY-99 and PREPRO-2010 processing systems are described. The new version of FENDL for applications, termed FENDL-3.0, includes the evaluated nuclear data files in ENDFB-6 format, the continuous-energy cross section files in ACE format for the MCNP family of Monte Carlo codes and the multi-group data library in MATXS format for deterministic transport calculations up to 55 MeV for 180 isotopes. Further, additional data are supplied in GENDF format for sensitivity studies. The library is freely available from the Nuclear Data Section at International Atomic Energy Agency.

December 2011

TABLE OF CONTENTS

Introduction …………………………………………………………………………….

1.  FENDL-3.0 Evaluated Nuclear Data Files (FENDL/E-3.0) ……………………………

2.  Processing FENDL/E-3.0 data for fusion applications ……………………..………….

3.  Continuous-energy data library FENDL/MC-3.0 for MCNP …………………………..

4.  Multi-group cross section data library FENDL/MG-3.0 ……………………………….

5.  Verification of processed FENDL/MC-3.0 and FENDL/MG-3.0 ..…………………….

6.  Point-wise data library FENDL/PD-3.0 in ENDFB-6 format………………………….

7.  Accessing FENDL-3.0 data …………………………………………………………….

8.  Final remarks and recommendations …………………………………………………...

References ……………………………………………………………………………...

Appendices

1.  NJOY local updates at IAEA-NDS …………………………………………………..

2. Energy boundaries for the 211-group structure for fusion applications ………………

3. Example of NJOY-99.364+ inputs for FENDL-3.0. …………………………………

Introduction

As a result of the Coordinated Research Program entitled “Nuclear Reaction Data for Advances Systems – Fusion Devices” the third version of the Fusion Evaluated Nuclear Data Library FENDL-3.0 has been released. It represents a substantial extension of the presently available FENDL-2.1 library [1] toward higher energies for fusion applications as IFMIF and also for design studies of DEMO, which represent the next generation devices beyond ITER.

In order to produce nuclear-application libraries for advanced fusion systems, the IAEA Nuclear Data Section supported the generation of the FENDL/MC-3.0 library - point-wise continuous-energy cross section data in ACE format for Monte Carlo calculations - and the FENDL/MC-3.0 library – multi-group cross section data up to 55 MeV for deterministic transport codes - by a Special Service Agreement to Daniel López Aldama. The FENDL/MC-3.0 and FENDL/MG-3.0 libraries are now freely available from the Nuclear Data Section webpage (http://www-nds.iaea.org). The package ACEDOP [2], which allows Doppler broadening of ACE-formatted cross sections files in the resolved resonance range, is also available as for FENDL-2.1.

The work carried out to produce FENDL-3.0 application libraries is described in this report. The evaluated nuclear data files were selected from FENDL-3.0. The continuous-energy cross section data files in ACE format and the multi-group cross section data in MATXS format were produced by NJOY-99.364+ [3] at IAEA-NDS. Point-wise cross section data files in ENDFB-6 format were generated using PREPRO-2010 code package [4]. A qualitative verification of processed files was also performed and the main findings and recommendations are also reported.

1. FENDL-3.0 Evaluated Nuclear Data Files (FENDL/E-3.0)

The evaluated nuclear data files for neutrons were taken from the third release of FENDL-3.0 evaluations, dated on October 24, 2011. The general information of each evaluated nuclear data file is presented in Table 1. Note the extension to higher energies of the upper energy limit (Emax) compared to 20 MeV in FENDL-2.1 evaluated nuclear data library.

The evaluated data files were analyzed using the preprocessing packages PREPRO [4] and ENDF utilities [5] to check general compliance with ENDFB-6 format rules [6]. The main findings that affect reaction data processing are listed below:

- Derived cross section data from MT=200-208 were found for all the isotopes of titanium (Ti), bromine (Br), zirconium (Zr), niobium (Nb), molybdenum (Mo) and hafnium (Hf). It is not recommended to include these derived data into primary evaluations, therefore derived reactions from MT=200 up to MT=450 were deleted.

- Partial fission reactions (MT=19,20,21 and 38) were not consistent with total fission (MT=18) reaction data for U-235 and U-238. To solve this problem the partial fission reactions were removed from the primary evaluation

- It was detected that the transition probability data in case of Nb-93 were omitted for MT = 51 in File 12 (MF=12). The data were included using the code chmf35 [7].

Table 1: FENDL-3.0 evaluated nuclear data files

| No. | Isotope | MAT | Library | Emax [MeV] | Filename [*.txt] |
| --- | --- | --- | --- | --- | --- |
| 1 | 1-H-1 | 125 | FENDL-3.0 | 150 | n_0125_1-H-1 |
| 2 | 1-H-2 | 128 | ENDF/B-VII | 150 | n_0128_1-H-2 |
| 3 | 1-H-3 | 131 | ENDF/B-VII | 60 | n_0131_1-H-3 |
| 4 | 2-He-3 | 225 | JENDL-4.0 | 60 | n_0225_2-He-3 |
| 5 | 2-He-4 | 228 | ENDF/B-VII | 60 | n_0228_2-He-4 |
| 6 | 3-Li-6 | 325 | FENDL-3.0 | 200 | n_0325_3-Li-6 |
| 7 | 3-Li-7 | 328 | FENDL-3.0 | 200 | n_0328_3-Li-7 |
| 8 | 4-Be-9 | 425 | FENDL-3.0 | 200 | n_0425_4-Be-9 |
| 9 | 5-B-10 | 525 | FENDL-3.0 | 200 | n_0525_5-B-10 |
| 10 | 5-B-11 | 528 | FENDL-3.0 | 200 | n_0528_5-B-11 |
| 11 | 6-C-12 | 625 | FENDL-3.0 | 150 | n_0625_6-C-12 |
| 12 | 6-C-13 | 628 | TENDL-2010 | 200 | n_0628_6-C-13 |
| 13 | 7-N-14 | 725 | FENDL-3.0 | 200 | n_0725_7-N-14 |
| 14 | 7-N-15 | 728 | FENDL-3.0 | 200 | n_0728_7-N-15 |
| 15 | 8-O-16 | 825 | ENDF/B-VII | 150 | n_0825_8-O-16 |
| 16 | 8-O-17 | 828 | TENDL-2010 | 200 | n_0828_8-O-17 |
| 17 | 8-O-18 | 831 | TENDL-2010 | 200 | n_0831_8-O-18 |
| 18 | 9-F-19 | 925 | FENDL-3.0 | 150 | n_0925_9-F-19 |
| 19 | 11-Na-23 | 1125 | FENDL-3.0 | 150 | n_1125_11-Na-23 |
| 20 | 12-Mg-24 | 1225 | FENDL-3.0 | 150 | n_1225_12-Mg-24 |
| 21 | 12-Mg-25 | 1228 | FENDL-3.0 | 150 | n_1228_12-Mg-25 |
| 22 | 12-Mg-26 | 1231 | FENDL-3.0 | 150 | n_1231_12-Mg-26 |
| 23 | 13-Al-27 | 1325 | JEFF-311 | 150 | n_1325_13-Al-27 |
| 24 | 14-Si-28 | 1425 | ENDF/B-VII | 150 | n_1425_14-Si-28 |
| 25 | 14-Si-29 | 1428 | ENDF/B-VII | 150 | n_1428_14-Si-29 |
| 26 | 14-Si-30 | 1431 | ENDF/B-VII | 150 | n_1431_14-Si-30 |
| 27 | 15-P-31 | 1525 | TENDL-2010 | 200 | n_1525_15-P-31 |
| 28 | 16-S-32 | 1625 | TENDL-2010 | 200 | n_1625_16-S-32 |
| 29 | 16-S-33 | 1628 | TENDL-2010 | 200 | n_1628_16-S-33 |
| 30 | 16-S-34 | 1631 | TENDL-2010 | 200 | n_1631_16-S-34 |
| 31 | 16-S-36 | 1637 | TENDL-2010 | 200 | n_1637_16-S-36 |
| 32 | 17-Cl-35 | 1725 | FENDL-3.0 | 200 | n_1725_17-Cl-35 |
| 33 | 17-Cl-37 | 1731 | FENDL-3.0 | 150 | n_1731_17-Cl-37 |
| 34 | 18-Ag-36 | 1825 | FENDL-3.0 | 150 | n_1825_18-Ar-36 |
| 35 | 18-Ag-38 | 1831 | FENDL-3.0 | 150 | n_1831_18-Ar-38 |
| 36 | 18-Ag-40 | 1837 | FENDL-3.0 | 150 | n_1837_18-Ar-40 |
| 37 | 19-K-39 | 1925 | TENDL-2010 | 150 | n_1925_19-K-39 |
| 38 | 19-K-40 | 1928 | TENDL-2010 | 150 | n_1928_19-K-40 |
| 39 | 19-K-41 | 1931 | TENDL-2010 | 150 | n_1931_19-K-41 |
| 40 | 20-Ca-40 | 2025 | FENDL-3.0 | 150 | n_2025_20-Ca-40 |
| 41 | 20-Ca-42 | 2031 | FENDL-3.0 | 150 | n_2031_20-Ca-42 |
| 42 | 20-Ca-43 | 2034 | FENDL-3.0 | 150 | n_2034_20-Ca-43 |
| 43 | 20-Ca-44 | 2037 | FENDL-3.0 | 150 | n_2037_20-Ca-44 |
| 44 | 20-Ca-46 | 2043 | FENDL-3.0 | 150 | n_2043_20-Ca-46 |
| 45 | 20-Ca-48 | 2049 | FENDL-3.0 | 150 | n_2049_20-Ca-48 |
| 46 | 21-Sc-45 | 2125 | JEFF-3.1.1 | 200 | n_2125_21-Sc-45 |
| 47 | 22-Ti-46 | 2225 | FENDL-3.0 | 150 | n_2225_22-Ti-46 |
| 48 | 22-Ti-47 | 2228 | FENDL-3.0 | 150 | n_2228_22-Ti-47 |
| 49 | 22-Ti-48 | 2231 | FENDL-3.0 | 150 | n_2231_22-Ti-48 |
| 50 | 22-Ti-49 | 2234 | FENDL-3.0 | 150 | n_2234_22-Ti-49 |
| 51 | 22-Ti-50 | 2237 | FENDL-3.0 | 150 | n_2237_22-Ti-50 |
| 52 | 23-V-50 | 2325 | FENDL-3.0 | 150 | n_2325_23-V-50 |
| 53 | 23-V-51 | 2328 | FENDL-3.0 | 150 | n_2328_23-V-51 |
| 54 | 24-Cr-50 | 2425 | KIT-2010 | 200 | n_2425_24-Cr-50 |
| 55 | 24-Cr-52 | 2431 | ENDF/A-1 | 150 | n_2431_24-Cr-52 |
| 56 | 24-Cr-53 | 2434 | KIT-2010 | 200 | n_2434_24-Cr-53 |
| 57 | 24-Cr-54 | 2437 | KIT-2010 | 200 | n_2437_24-Cr-54 |
| 58 | 25-Mn-55 | 2525 | INDL/V-3 | 60 | n_2525_25-Mn-55 |
| 59 | 26-Fe-54 | 2625 | ENDF/B-VII | 150 | n_2625_26-Fe-54 |
| 60 | 26-Fe-56 | 2631 | JEFF-3.1.1 | 200 | n_2631_26-Fe-56 |
| 61 | 26-Fe-57 | 2634 | ENDF/B-VII | 150 | n_2634_26-Fe-57 |
| 62 | 26-Fe-58 | 2637 | JEFF-3.1.1 | 200 | n_2637_26-Fe-58 |
| 63 | 27-Co-59 | 2725 | FENDL-3.0 | 150 | n_2725_27-Co-59 |
| 64 | 28-Ni-58 | 2825 | ENDF/B-VII | 150 | n_2825_28-Ni-58 |
| 65 | 28-Ni-60 | 2831 | ENDF/B-VII | 150 | n_2831_28-Ni-60 |
| 66 | 28-Ni-61 | 2834 | ENDF/B-VII | 150 | n_2834_28-Ni-61 |
| 67 | 28-Ni-62 | 2837 | ENDF/B-VII | 150 | n_2837_28-Ni-62 |
| 68 | 28-Ni-64 | 2843 | ENDF/B-VII | 150 | n_2843_28-Ni-64 |
| 69 | 29-Cu-63 | 2925 | ENDF/B-VII | 150 | n_2925_29-Cu-63 |
| 70 | 29-Cu-65 | 2931 | ENDF/B-VII | 150 | n_2931_29-Cu-65 |
| 71 | 30-Zn-64 | 3025 | FENDL-3.0 | 150 | n_3025_30-Zn-64 |
| 72 | 30-Zn-66 | 3031 | FENDL-3.0 | 150 | n_3031_30-Zn-66 |
| 73 | 30-Zn-67 | 3034 | FENDL-3.0 | 150 | n_3034_30-Zn-67 |
| 74 | 30-Zn-68 | 3037 | FENDL-3.0 | 150 | n_3037_30-Zn-68 |
| 75 | 30-Zn-70 | 3043 | FENDL-3.0 | 150 | n_3043_30-Zn-70 |
| 76 | 31-Ga-69 | 3125 | FENDL-3.0 | 150 | n_3125_31-Ga-69 |
| 77 | 31-Ga-71 | 3131 | FENDL-3.0 | 150 | n_3131_31-Ga-71 |
| 78 | 32-Ge-70 | 3225 | JEFF-3.1.1 | 200 | n_3225_32-Ge-70 |
| 79 | 32-Ge-72 | 3231 | JEFF-3.1.1 | 200 | n_3231_32-Ge-72 |
| 80 | 32-Ge-73 | 3234 | JEFF-3.1.1 | 200 | n_3234_32-Ge-73 |
| 81 | 32-Ge-74 | 3237 | JEFF-3.1.1 | 200 | n_3237_32-Ge-74 |
| 82 | 32-Ge-76 | 3243 | JEFF-3.1.1 | 200 | n_3243_32-Ge-76 |
| 83 | 35-Br-79 | 3525 | FENDL-3.0 | 200 | n_3525_35-Br-79 |
| 84 | 35-Br-81 | 3531 | FENDL-3.0 | 200 | n_3531_35-Br-81 |
| 85 | 39-Y-89 | 3925 | FENDL-3.0 | 200 | n_3925_39-Y-89 |
| 86 | 40-Zr-90 | 4025 | FENDL-3.0 | 150 | n_4025_40-Zr-90 |
| 87 | 40-Zr-91 | 4028 | FENDL-3.0 | 150 | n_4028_40-Zr-91 |
| 88 | 40-Zr-92 | 4031 | FENDL-3.0 | 150 | n_4031_40-Zr-92 |
| 89 | 40-Zr-94 | 4037 | FENDL-3.0 | 150 | n_4037_40-Zr-94 |
| 90 | 40-Zr-96 | 4043 | FENDL-3.0 | 150 | n_4043_40-Zr-96 |
| 91 | 41-Nb-93 | 4125 | FENDL-3.0 | 150 | n_4125_41-Nb-93 |
| 92 | 42-Mo-92 | 4225 | FENDL-3.0 | 150 | n_4225_42-Mo-92 |
| 93 | 42-Mo-94 | 4231 | FENDL-3.0 | 150 | n_4231_42-Mo-94 |
| 94 | 42-Mo-95 | 4234 | FENDL-3.0 | 150 | n_4234_42-Mo-95 |
| 95 | 42-Mo-96 | 4237 | FENDL-3.0 | 150 | n_4237_42-Mo-96 |
| 96 | 42-Mo-97 | 4240 | FENDL-3.0 | 150 | n_4240_42-Mo-97 |
| 97 | 42-Mo-98 | 4243 | FENDL-3.0 | 150 | n_4243_42-Mo-98 |
| 98 | 42-Mo-100 | 4249 | FENDL-3.0 | 150 | n_4249_42-Mo-100 |
| 99 | 45-Rh-103 | 4525 | FENDL-3.0 | 200 | n_4525_45-Rh-103 |
| 100 | 47-Ag-107 | 4725 | FENDL-3.0 | 200 | n_4725_47-Ag-107 |
| 101 | 47-Ag-109 | 4731 | FENDL-3.0 | 200 | n_4731_47-Ag-109 |
| 102 | 48-Cd-106 | 4825 | FENDL-3.0 | 200 | n_4825_48-Cd-106 |
| 103 | 48-Cd-108 | 4831 | FENDL-3.0 | 200 | n_4831_48-Cd-108 |
| 104 | 48-Cd-110 | 4837 | FENDL-3.0 | 200 | n_4837_48-Cd-110 |
| 105 | 48-Cd-111 | 4840 | FENDL-3.0 | 200 | n_4840_48-Cd-111 |
| 106 | 48-Cd-112 | 4843 | FENDL-3.0 | 200 | n_4843_48-Cd-112 |
| 107 | 48-Cd-113 | 4846 | FENDL-3.0 | 200 | n_4846_48-Cd-113 |
| 108 | 48-Cd-114 | 4849 | FENDL-3.0 | 200 | n_4849_48-Cd-114 |
| 109 | 48-Cd-116 | 4855 | FENDL-3.0 | 200 | n_4855_48-Cd-116 |
| 110 | 50-Sn-112 | 5025 | FENDL-3.0 | 200 | n_5025_50-Sn-112 |
| 111 | 50-Sn-114 | 5031 | FENDL-3.0 | 200 | n_5031_50-Sn-114 |
| 112 | 50-Sn-115 | 5034 | FENDL-3.0 | 200 | n_5034_50-Sn-115 |
| 113 | 50-Sn-116 | 5037 | FENDL-3.0 | 200 | n_5037_50-Sn-116 |
| 114 | 50-Sn-117 | 5040 | FENDL-3.0 | 200 | n_5040_50-Sn-117 |
| 115 | 50-Sn-118 | 5043 | FENDL-3.0 | 200 | n_5043_50-Sn-118 |
| 116 | 50-Sn-119 | 5046 | FENDL-3.0 | 200 | n_5046_50-Sn-119 |
| 117 | 50-Sn-120 | 5049 | FENDL-3.0 | 200 | n_5049_50-Sn-120 |
| 118 | 50-Sn-122 | 5055 | FENDL-3.0 | 200 | n_5055_50-Sn-122 |
| 119 | 50-Sn-124 | 5061 | FENDL-3.0 | 200 | n_5061_50-Sn-124 |
| 120 | 51-Sb-121 | 5125 | FENDL-3.0 | 200 | n_5125_51-Sb-121 |
| 121 | 51-Sb-123 | 5131 | FENDL-3.0 | 200 | n_5131_51-Sb-123 |
| 122 | 53-I-127 | 5325 | FENDL-3.0 | 200 | n_5325_53-I-127 |
| 123 | 55-Cs-133 | 5525 | FENDL-3.0 | 200 | n_5525_55-Cs-133 |
| 124 | 56-Ba-130 | 5625 | FENDL-3.0 | 200 | n_5625_56-Ba-130 |
| 125 | 56-Ba-132 | 5631 | FENDL-3.0 | 200 | n_5631_56-Ba-132 |
| 126 | 56-Ba-134 | 5637 | FENDL-3.0 | 200 | n_5637_56-Ba-134 |
| 127 | 56-Ba-135 | 5640 | FENDL-3.0 | 200 | n_5640_56-Ba-135 |
| 128 | 56-Ba-136 | 5643 | FENDL-3.0 | 200 | n_5643_56-Ba-136 |
| 129 | 56-Ba-137 | 5646 | FENDL-3.0 | 200 | n_5646_56-Ba-137 |
| 130 | 56-Ba-138 | 5649 | FENDL-3.0 | 200 | n_5649_56-Ba-138 |
| 131 | 57-La-138 | 5725 | TENDL-2010 | 200 | n_5725_57-La-138 |
| 132 | 57-La-139 | 5728 | TENDL-2010 | 200 | n_5728_57-La-139 |
| 133 | 58-Ce-136 | 5825 | FENDL-3.0 | 200 | n_5825_58-Ce-136 |
| 134 | 58-Ce-138 | 5831 | FENDL-3.0 | 200 | n_5831_58-Ce-138 |
| 135 | 58-Ce-140 | 5837 | FENDL-3.0 | 200 | n_5837_58-Ce-140 |
| 136 | 58-Ce-142 | 5843 | FENDL-3.0 | 200 | n_5843_58-Ce-142 |
| 137 | 64-Gd-152 | 6425 | FENDL-3.0 | 200 | n_6425_64-Gd-152 |
| 138 | 64-Gd-154 | 6431 | FENDL-3.0 | 200 | n_6431_64-Gd-154 |
| 139 | 64-Gd-155 | 6434 | FENDL-3.0 | 200 | n_6434_64-Gd-155 |
| 140 | 64-Gd-156 | 6437 | FENDL-3.0 | 200 | n_6437_64-Gd-156 |
| 141 | 64-Gd-157 | 6440 | FENDL-3.0 | 200 | n_6440_64-Gd-157 |
| 142 | 64-Gd-158 | 6443 | FENDL-3.0 | 200 | n_6443_64-Gd-158 |
| 143 | 64-Gd-160 | 6449 | FENDL-3.0 | 200 | n_6449_64-Gd-160 |
| 144 | 68-Er-162 | 6825 | FENDL-3.0 | 200 | n_6825_68-Er-162 |
| 145 | 68-Er-164 | 6831 | FENDL-3.0 | 200 | n_6831_68-Er-164 |
| 146 | 68-Er-166 | 6837 | FENDL-3.0 | 200 | n_6837_68-Er-166 |
| 147 | 68-Er-167 | 6840 | FENDL-3.0 | 200 | n_6840_68-Er-167 |
| 148 | 68-Er-168 | 6843 | FENDL-3.0 | 200 | n_6843_68-Er-168 |
| 149 | 68-Er-170 | 6849 | FENDL-3.0 | 200 | n_6849_68-Er-170 |
| 150 | 71-Lu-175 | 7125 | TENDL-2010 | 200 | n_7125_71-Lu-175 |
| 151 | 71-Lu-176 | 7128 | TENDL-2010 | 200 | n_7128_71-Lu-176 |
| 152 | 72-Hf-174 | 7225 | FENDL-3.0 | 200 | n_7225_72-Hf-174 |
| 153 | 72-Hf-176 | 7231 | FENDL-3.0 | 200 | n_7231_72-Hf-176 |
| 154 | 72-Hf-177 | 7234 | FENDL-3.0 | 200 | n_7234_72-Hf-177 |
| 155 | 72-Hf-178 | 7237 | FENDL-3.0 | 200 | n_7237_72-Hf-178 |
| 156 | 72-Hf-179 | 7240 | FENDL-3.0 | 200 | n_7240_72-Hf-179 |
| 157 | 72-Hf-180 | 7243 | FENDL-3.0 | 200 | n_7243_72-Hf-180 |
| 158 | 73-Ta-181 | 7328 | FENDL-3.0 | 150 | n_7328_73-Ta-181 |
| 159 | 74-W-180 | 7425 | INDL/V-3 | 150 | n_7425_74-W-180 |
| 160 | 74-W-182 | 7431 | INDL/V-3 | 150 | n_7431_74-W-182 |
| 161 | 74-W-183 | 7434 | INDL/V-3 | 150 | n_7434_74-W-183 |
| 162 | 74-W-184 | 7437 | INDL/V-3 | 150 | n_7437_74-W-184 |
| 163 | 74-W-186 | 7443 | INDL/V-3 | 150 | n_7443_74-W-186 |
| 164 | 75-Re-185 | 7525 | TENDL-2010 | 200 | n_7525_75-Re-185 |
| 165 | 75-Re-187 | 7531 | TENDL-2010 | 200 | n_7531_75-Re-187 |
| 166 | 78-Pt-190 | 7825 | TENDL-2010 | 200 | n_7825_78-Pt-190 |
| 167 | 78-Pt-192 | 7831 | TENDL-2010 | 200 | n_7831_78-Pt-192 |
| 168 | 78-Pt-194 | 7837 | TENDL-2010 | 200 | n_7837_78-Pt-194 |
| 169 | 78-Pt-195 | 7840 | TENDL-2010 | 200 | n_7840_78-Pt-195 |
| 170 | 78-Pt-196 | 7843 | TENDL-2010 | 200 | n_7843_78-Pt-196 |
| 171 | 78-Pt-198 | 7849 | TENDL-2010 | 200 | n_7849_78-Pt-198 |
| 172 | 79-Au-197 | 7925 | FENDL-3.0 | 150 | n_7925_79-Au-197 |
| 173 | 82-Pb-204 | 8225 | JEFF-3.1.1 | 200 | n_8225_82-Pb-204 |
| 174 | 82-Pb-206 | 8231 | JEFF-3.1.1 | 200 | n_8231_82-Pb-206 |
| 175 | 82-Pb-207 | 8234 | JEFF-3.1.1 | 200 | n_8234_82-Pb-207 |
| 176 | 82-Pb-208 | 8237 | JEFF-3.1.1 | 200 | n_8237_82-Pb-208 |
| 177 | 83-Bi-209 | 8325 | JEFF-3.1.1 | 200 | n_8325_83-Bi-209 |
| 178 | 90-Th-232 | 9040 | ENDF/B-VII.1 | 60 | n_9040_90-Th-232 |
| 179 | 92-U-235 | 9228 | FENDL-3.0 | 150 | n_9228_92-U-235 |
| 180 | 92-U-238 | 9237 | FENDL-3.0 | 150 | n_9237_92-U-238 |

The number of elements included in the FENDL-3.0 library has been increased from 36 to 59 and all the evaluations contain isotopic data, therefore the number of materials has been increased from 71 in FENDL-2.1 up to 180 in FENDL-3.0.

As in FENDL-2.1 the photo atomic evaluated data were taken from ENDF/B-VI.8 (EDPL-97) for all the elements. General information of photo-atomic data is presented in Table 2.

Table 2: Photo-atomic evaluated data for FENDL-3.0

| No. | Element | MAT | Isotopes | Library | Filename [*.txt] |
| --- | --- | --- | --- | --- | --- |
| 1 | H | 100 | 1-H-1 | ENDF/B-VI.8 | ph_0100_1-H |
|  |  |  | 1-H-2 |  |  |
|  |  |  | 1-H-3 |  |  |
| 2 | He | 200 | 2-He-3 | ENDF/B-VI.8 | ph_0200_2-He |
|  |  |  | 2-He-4 |  |  |
| 3 | Li | 300 | 3-Li-6 | ENDF/B-VI.8 | ph_0300_3-Li |
|  |  |  | 3-Li-7 |  |  |
| 4 | Be | 400 | 4-Be-9 | ENDF/B-VI.8 | ph_0400_4-Be |
| 5 | B | 500 | 5-B-10 | ENDF/B-VI.8 | ph_0500_5-B |
|  |  |  | 5-B-11 |  |  |
| 6 | C | 600 | 6-C-12 | ENDF/B-VI.8 | ph_0600_6-C |
|  |  |  | 6-C-13 |  |  |
| 7 | N | 700 | 7-N-15 | ENDF/B-VI.8 | ph_0700_7-N |
|  |  |  | 7-N-14 |  |  |
| 8 | O | 800 | 8-O-16 | ENDF/B-VI.8 | ph_0800_8-O |
|  |  |  | 8-O-17 |  |  |
|  |  |  | 8-O-18 |  |  |
| 9 | F | 900 | 9-F-19 | ENDF/B-VI.8 | ph_0900_9-F |
| 10 | Na | 1100 | 11-Na-23 | ENDF/B-VI.8 | ph_1100_11-Na |
| 11 | Mg | 1200 | 12-Mg-24 | ENDF/B-VI.8 | ph_1200_12-Mg |
|  |  |  | 12-Mg-25 |  |  |
|  |  |  | 12-Mg-26 |  |  |
| 12 | Al | 1300 | 13-Al-27 | ENDF/B-VI.8 | ph_1300_13-Al |
| 13 | Si | 1400 | 14-Si-28 | ENDF/B-VI.8 | ph_1400_14-Si |
|  |  |  | 14-Si-29 |  |  |
|  |  |  | 14-Si-30 |  |  |
| 14 | P | 1500 | 15-P-31 | ENDF/B-VI.8 | ph_1500_15-P |
| 15 | S | 1600 | 16-S-32 | ENDF/B-VI.8 | ph_1600_16-S |
|  |  |  | 16-S-33 |  |  |
|  |  |  | 16-S-34 |  |  |
|  |  |  | 16-S-36 |  |  |
| 16 | Cl | 1700 | 17-Cl-35 | ENDF/B-VI.8 | ph_1700_17-Cl |
|  |  |  | 17-Cl-37 |  |  |
| 17 | Ar | 1800 | 18-Ar-36 | ENDF/B-VI.8 | ph_1800_18-Ar |
|  |  |  | 18-Ar-38 |  |  |
|  |  |  | 18-Ar-40 |  |  |
| 18 | K | 1900 | 19-K-39 | ENDF/B-VI.8 | ph_1900_19-K |
|  |  |  | 19-K-40 |  |  |
|  |  |  | 19-K-41 |  |  |
| 19 | Ca | 2000 | 20-Ca-40 | ENDF/B-VI.8 | ph_2000_20-Ca |
|  |  |  | 20-Ca-42 |  |  |
|  |  |  | 20-Ca-43 |  |  |
|  |  |  | 20-Ca-44 |  |  |
|  |  |  | 20-Ca-46 |  |  |
|  |  |  | 20-Ca-48 |  |  |
| 20 | Sc | 2100 | 21-Sc-45 | ENDF/B-VI.8 | ph_2100_21-Sc |
| 21 | Ti | 2200 | 22-Ti-46 | ENDF/B-VI.8 | ph_2200_22-Ti |
|  |  |  | 22-Ti-47 |  |  |
|  |  |  | 22-Ti-48 |  |  |
|  |  |  | 22-Ti-49 |  |  |
|  |  |  | 22-TI-50 |  |  |
| 22 | V | 2300 | 23-V-50 | ENDF/B-VI.8 | ph_2300_23-V |
|  |  |  | 23-V-51 |  |  |
| 23 | Cr | 2400 | 24-Cr-50 | ENDF/B-VI.8 | ph_2400_24-Cr |
|  |  |  | 24-Cr-52 |  |  |
|  |  |  | 24-Cr-53 |  |  |
|  |  |  | 24-Cr-54 |  |  |
| 24 | Mn | 2500 | 25-Mn-55 | ENDF/B-VI.8 | ph_2500_25-Mn |
| 25 | Fe | 2600 | 26-Fe-54 | ENDF/B-VI.8 | ph_2600_26-Fe |
|  |  |  | 26-Fe-56 |  |  |
|  |  |  | 26-Fe-57 |  |  |
|  |  |  | 26-Fe-58 |  |  |
| 26 | Co | 2700 | 27-Co-59 | ENDF/B-VI.8 | ph_2700_27-Co |
| 27 | Ni | 2800 | 28-Ni-58 | ENDF/B-VI.8 | ph_2800_28-Ni |
|  |  |  | 28-Ni-60 |  |  |
|  |  |  | 28-Ni-61 |  |  |
|  |  |  | 28-Ni-62 |  |  |
|  |  |  | 28-Ni-64 |  |  |
| 28 | Cu | 2900 | 29-Cu-63 | ENDF/B-VI.8 | ph_2900_29-Cu |
|  |  |  | 29-Cu-65 |  |  |
| 29 | Zn | 3000 | 30-Zn-64 | ENDF/B-VI.8 | ph_3000_30-Zn |
|  |  |  | 30-Zn-66 |  |  |
|  |  |  | 30-Zn-67 |  |  |
|  |  |  | 30-Zn-68 |  |  |
|  |  |  | 30-Zn-70 |  |  |
| 30 | Ga | 3100 | 31-Ga-69 | ENDF/B-VI.8 | ph_3100_31-Ga |
|  |  |  | 31-Ga-71 |  |  |
| 31 | Ge | 3200 | 32-Ge-70 | ENDF/B-VI.8 | ph_3200_32-Ge |
|  |  |  | 32-Ge-72 |  |  |
|  |  |  | 32-Ge-73 |  |  |
|  |  |  | 32-Ge-74 |  |  |
|  |  |  | 32-Ge-76 |  |  |
| 32 | Br | 3500 | 35-Br-79 | ENDF/B-VI.8 | ph_3500_35-Br |
|  |  |  | 35-Br-81 |  |  |
| 33 | Y | 3900 | 39-Y-89 | ENDF/B-VI.8 | ph_3900_39-Y |
| 34 | Zr | 4000 | 40-Zr-90 | ENDF/B-VI.8 | ph_4000_40-Zr |
|  |  |  | 40-Zr-91 |  |  |
|  |  |  | 40-Zr-92 |  |  |
|  |  |  | 40-Zr-94 |  |  |
|  |  |  | 40-Zr-96 |  |  |
| 35 | Nb | 4100 | 41-Nb-93 | ENDF/B-VI.8 | ph_4100_41-Nb |
| 36 | Mo | 4200 | 42-Mo-92 | ENDF/B-VI.8 | ph_4200_42-Mo |
|  |  |  | 42-Mo-94 |  |  |
|  |  |  | 42-Mo-95 |  |  |
|  |  |  | 42-Mo-96 |  |  |
|  |  |  | 42-Mo-97 |  |  |
|  |  |  | 42-Mo-98 |  |  |
|  |  |  | 42-Mo-100 |  |  |
| 37 | Rh | 4500 | 45-Rh-103 | ENDF/B-VI.8 | ph_4500_45-Rh |
| 38 | Ag | 4700 | 47-Ag-107 | ENDF/B-VI.8 | ph_4700_47-Ag |
|  |  |  | 47-Ag-109 |  |  |
| 39 | Cd | 4800 | 48-Cd-106 | ENDF/B-VI.8 | ph_4800_48-Cd |
|  |  |  | 48-Cd-108 |  |  |
|  |  |  | 48-Cd-110 |  |  |
|  |  |  | 48-Cd-111 |  |  |
|  |  |  | 48-Cd-112 |  |  |
|  |  |  | 48-Cd-113 |  |  |
|  |  |  | 48-Cd-114 |  |  |
|  |  |  | 48-Cd-116 |  |  |
| 40 | Sn | 5000 | 50-Sn-112 | ENDF/B-VI.8 | ph_5000_50-Sn |
|  |  |  | 50-Sn-114 |  |  |
|  |  |  | 50-Sn-115 |  |  |
|  |  |  | 50-Sn-116 |  |  |
|  |  |  | 50-Sn-117 |  |  |
|  |  |  | 50-Sn-118 |  |  |
|  |  |  | 50-Sn-119 |  |  |
|  |  |  | 50-Sn-120 |  |  |
|  |  |  | 50-Sn-122 |  |  |
|  |  |  | 50-Sn-124 |  |  |
| 41 | Sb | 5100 | 51-Sb-121 | ENDF/B-VI.8 | ph_5100_51-Sb |
|  |  |  | 51-Sb-123 |  |  |
| 42 | I | 5300 | 53-I-127 | ENDF/B-VI.8 | ph_5300_53-I |
| 43 | Cs | 5500 | 55-Cs-133 | ENDF/B-VI.8 | ph_5500_55-Cs |
| 44 | Ba | 5600 | 56-Ba-130 | ENDF/B-VI.8 | ph_5600_56-Ba |
|  |  |  | 56-Ba-132 |  |  |
|  |  |  | 56-Ba-134 |  |  |
|  |  |  | 56-Ba-135 |  |  |
|  |  |  | 56-Ba-136 |  |  |
|  |  |  | 56-Ba-137 |  |  |
|  |  |  | 56-Ba-138 |  |  |
| 45 | La | 5700 | 57-La-138 | ENDF/B-VI.8 | ph_5700_57-La |
|  |  |  | 57-La-139 |  |  |
| 46 | Ce | 5800 | 58-Ce-136 | ENDF/B-VI.8 | ph_5800_58-Ce |
|  |  |  | 58-Ce-138 |  |  |
|  |  |  | 58-Ce-140 |  |  |
|  |  |  | 58-Ce-142 |  |  |
| 47 | Gd | 6400 | 64-Gd-152 | ENDF/B-VI.8 | ph_6400_64-Gd |
|  |  |  | 64-Gd-154 |  |  |
|  |  |  | 64-Gd-155 |  |  |
|  |  |  | 64-Gd-156 |  |  |
|  |  |  | 64-Gd-157 |  |  |
|  |  |  | 64-Gd-158 |  |  |
|  |  |  | 64-Gd-160 |  |  |
| 48 | Er | 6800 | 68-Er-162 | ENDF/B-VI.8 | ph_6800_68-Er |
|  |  |  | 68-Er-164 |  |  |
|  |  |  | 68-Er-166 |  |  |
|  |  |  | 68-Er-167 |  |  |
|  |  |  | 68-Er-168 |  |  |
|  |  |  | 68-Er-170 |  |  |
| 49 | Lu | 7100 | 71-Lu-175 | ENDF/B-VI.8 | ph_7100_71-Lu |
|  |  |  | 71-Lu-176 |  |  |
| 50 | Hf | 7200 | 72-Hf-174 | ENDF/B-VI.8 | ph_7200_72-Hf |
|  |  |  | 72-Hf-176 |  |  |
|  |  |  | 72-Hf-177 |  |  |
|  |  |  | 72-Hf-178 |  |  |
|  |  |  | 72-Hf-179 |  |  |
|  |  |  | 72-Hf-180 |  |  |
| 51 | Ta | 7300 | 73-Ta-181 | ENDF/B-VI.8 | ph_7300_73-Ta |
| 52 | W | 7400 | 74-W-180 | ENDF/B-VI.8 | ph_7400_74-W |
|  |  |  | 74-W-182 |  |  |
|  |  |  | 74-W-183 |  |  |
|  |  |  | 74-W-184 |  |  |
|  |  |  | 74-W-186 |  |  |
| 53 | Re | 7500 | 75-Re-185 | ENDF/B-VI.8 | ph_7500_75-Re |
|  |  |  | 75-Re-187 |  |  |
| 54 | Pt | 7800 | 78-Pt-190 | ENDF/B-VI.8 | ph_7800_78-Pt |
|  |  |  | 78-Pt-192 |  |  |
|  |  |  | 78-Pt-194 |  |  |
|  |  |  | 78-Pt-195 |  |  |
|  |  |  | 78-Pt-196 |  |  |
|  |  |  | 78-Pt-198 |  |  |
| 55 | Au | 7900 | 79-Au-197 | ENDF/B-VI.8 | ph_7900_79-Au |
| 56 | Pb | 8200 | 82-Pb-204 | ENDF/B-VI.8 | ph_8200_82-Pb |
|  |  |  | 82-Pb-206 |  |  |
|  |  |  | 82-Pb-207 |  |  |
|  |  |  | 82-Pb-208 |  |  |
| 57 | Bi | 8300 | 83-Bi-209 | ENDF/B-VI.8 | ph_8300_83-Bi |
| 58 | Th | 9000 | 90-Th-232 | ENDF/B-VI.8 | ph_9000_90-Th |
| 59 | U | 9200 | 92-U-235 92-U-238 | ENDF/B-VI.8 | ph_9200_92-U |

2. Processing FENDL/E-3.0 data for fusion applications

The FENDL/E-3.0 evaluated nuclear data files were processed using the NJOY-99.364 modular code system with local updates at IAEA-NDS. Particularly, two additional updates were required to successfully process FENDL-3.0 evaluations, the first one for ACER and the second one for HEATR (Appendix 1). The update of ACER is a correction to the official update up360 included in the official release of NJOY-99.364. On the other hand, the update of HEATR allows the processing of large sections for angular distributions in File 4 (MF4) as you can find in some FENDL-3.0 evaluations.

The processing sequence for generating the FENDL/MC-3.0 and FENDL/MG-3.0 libraries is shown in Figure 1. FENDL/MC-3.0 is an ACE-formatted library suitable for use by the MCNP family of Monte-Carlo codes [8]. FENDL/MG-3.0 is a multi-group-formatted library, intended for use in deterministic transport codes like DORT and TORT [9].

The main processing options the specifications given in Refs. [1, 10, 11]. A summary of the main processing options is presented below for completeness:

- Reconstruction tolerance in RECONR: 0.1%.

- Resonance-integral-check tolerance in RECONR: 0.2%.

- Maximum resonance integral error in RECONR: 5.0E-08 (default for 0.1%).

- Temperature: 300K = 2.5852E-08 MeV.

- Thinning tolerance in BROADR: 0.1%.

- Integral criterion tolerance in BROADR: 0.2%.

- Integral thinning tolerance in BROADR: 5.0E-0.8 (default for 0.1%).

- Maximum energy in BROADR: 20 MeV.

- Number of probability bins in PURR: 20.

- Number of resonance ladders: 100.

- Bondarenko σ0 values: 1010, 105, 104, 103, 300, 100, 30, 10, 3, 1, 0.3, 0.1, 0.001 barns, not more than 10 out of this list (Table 3).

- No thermal data.

- No thinning in ACER.

- ACE-type 1 file.

- Suffix for zaid in ACER: .30

- New cumulative angle distributions in ACER.

- Detailed photon calculation in ACER.

- Neutron groups: 211 energy groups, 175 group Vitamin-J structure + 36 up to 55 MeV (Appendix 2)

- Gamma groups: 42 in Vitamin-J structure.

- Neutron weight function: VITAMIN-E (IWT=11 in NJOY).

- Gamma weight function: 1/E with roll-offs (IWT=3 in NJOY).

- Legendre order: P-6 for transport correction to P-5.

- Reactions included: all reactions contained in the evaluated FENDL/E-3.0 file plus total kerma (MT = 301), partial kermas (MT=302, 304, 404), total kinematic kerma (MT = 443), total damage (MT = 444) and gas production (MT=200s). For multi-group calculations, MT = 251 (μ), MT = 252 (χ), MT = 253 (γ) and MT = 259 (1/v) are also included.

Comparing to FENDL-2.1 processing options there are some changes:

- Tighter integral resonance criterion in RECONR and BROADR (0.2% instead of 0.3%)

- Higher upper energy limit in BROADR for Doppler broadening (20 instead of 2 MeV)

- 211-group energy structure up to 55 MeV instead of the 175-group Vitamin J energy structure up to 19.6403 MeV in GROUPR, GAMINR and MATXSR.

- Calculation of more partial kinematic kermas in HEATR

It is worthy to note, that plotting options of HEATR and ACER were used for quality assurance issues. Some examples of NJOY input options are given in Appendix 3. A complete set of NJOY inputs is available on the IAEA-NDS webpage.

All the evaluated data files were processed and the continuous energy cross section library FENDL/MC-3.0 and the FENDL/MG-3.0 multi-group library were generated for fusion applications.

Table 3: Bondarenko σ0 values for the multi-group data files.

| Material | 1010 | 105 | 104 | 3103 | 103 | 300. | 100. | 30. | 10. | 3. | 1. | 0.3 | 0.1 | .001 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1-H-1 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 1-H-2 | X |  | X |  | X |  | X |  | X |  | X |  |  |  |
| 1-H-3 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2-He-3 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 2-He-4 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3-Li-6 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 3-Li-7 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 4-Be-9 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 5-B-10 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 5-B-11 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 6-C-12 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 6-C-13 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 7-N-14 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 7-N-15 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 8-O-16 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 8-O-17 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 8-O-18 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 9-F-19 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 11-Na-23 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 12-Mg-24 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 12-Mg-25 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 12-Mg-26 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 13-Al-27 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 14-Si-28 | X |  |  |  |  |  | X |  | X |  | X |  |  |  |
| 14-Si-29 | X |  |  |  |  |  | X |  | X |  | X |  |  |  |
| 14-Si-30 | X |  |  |  |  |  | X |  | X |  | X |  |  |  |
| 15-P-31 | X |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 16-S-32 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 16-S-33 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 16-S-34 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 16-S-36 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 17-Cl-35 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 17-Cl-37 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 18-Ar-36 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 18-Ar-38 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 18-Ar-40 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 19-K-39 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 19-K-40 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 19-K-41 | X |  |  |  | X | X | X | X | X |  |  |  |  |  |
| 20-Ca-40 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 20-Ca-42 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 20-Ca-43 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 20-Ca-44 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 20-Ca-46 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 20-Ca-48 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 21-Sc-45 | X |  | X |  | X | X | X | X | X | X | X |  |  |  |
| 22-Ti-46 | X |  | X |  | X | X | X | X | X | X | X |  |  |  |
| 22-Ti-47 | X |  | X |  | X | X | X | X | X | X | X |  |  |  |
| 22-Ti-48 | X |  | X |  | X | X | X | X | X | X | X |  |  |  |
| 22-Ti-49 | X |  | X |  | X | X | X | X | X | X | X |  |  |  |
| 22-Ti-50 | X |  | X |  | X | X | X | X | X | X | X |  |  |  |
| 23-V-50 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 23-V-50 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 24-Cr-50 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 24-Cr-52 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 24-Cr-53 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 24-Cr-54 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 25-Mn-55 | X | X |  |  | X |  | X |  | X |  | X |  |  |  |
| 26-Fe-54 | X | X | X |  | X |  | X |  | X |  |  |  |  |  |
| 26-Fe-56 | X | X | X |  | X |  | X |  | X | X | X | X | X |  |
| 26-Fe-57 | X | X | X |  | X |  | X |  | X |  |  |  |  |  |
| 26-Fe-58 | X | X | X |  | X |  | X |  | X |  |  |  |  |  |
| 27-Co-59 | X | X | X |  | X |  | X |  | X |  |  |  |  |  |
| 28-Ni-58 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 28-Ni-60 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 28-Ni-61 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 28-Ni-62 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 28-Ni-64 | X |  |  |  | X | X | X | X | X | X | X |  |  |  |
| 29-Cu-63 | X |  | X |  |  | X | X | X | X |  | X |  | X |  |
| 29-Cu-65 | X |  | X |  |  | X | X | X | X |  | X |  | X |  |
| 30-Zn-64 | X |  | X |  |  | X | X | X | X |  | X |  | X |  |
| 30-Zn-66 | X |  | X |  |  | X | X | X | X |  | X |  | X |  |
| 30-Zn-67 | X |  | X |  |  | X | X | X | X |  | X |  | X |  |
| 30-Zn-68 | X |  | X |  |  | X | X | X | X |  | X |  | X |  |
| 30-Zn-70 | X |  | X |  |  | X | X | X | X |  | X |  | X |  |
| 31-Ga-69 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 31-Ga-71 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 32-Ge-70 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 32-Ge-72 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 32-Ge-73 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 32-Ge-74 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 32-Ge-76 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 35-Br-79 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 35-Br-81 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 39-Y-89 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 40-Zr-90 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 40-Zr-91 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 40-Zr-92 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 40-Zr-94 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 40-Zr-96 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 41-Nb-93 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 42-Mo-92 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 42-Mo-94 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 42-Mo-95 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 42-Mo-96 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 42-Mo-97 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 42-Mo-98 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 42-Mo-100 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 45-Rh-103 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 47-Ag-107 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 47-Ag-109 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 48-Cd-106 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 48-Cd-108 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 48-Cd-110 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 48-Cd-111 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 48-Cd-112 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 48-Cd-113 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 48-Cd-114 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 48-Cd-116 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-112 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-114 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-115 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-116 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-117 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-118 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-119 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-120 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-122 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 50-Sn-124 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 51-Sb-121 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 51-Sb-123 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 53-I-127 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 55-Cs-133 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 56-Ba-130 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 56-Ba-132 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 56-Ba-134 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 56-Ba-135 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 56-Ba-136 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 56-Ba-137 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 56-Ba-138 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 57-La-138 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 57-La-139 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 58-Ce-136 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 58-Ce-138 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 58-Ce-140 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 58-Ce-142 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 64-Gd-152 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 64-Gd-154 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 64-Gd-155 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 64-Gd-156 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 64-Gd-157 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 64-Gd-158 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 64-Gd-160 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 68-Er-162 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 68-Er-164 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 68-Er-166 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 68-Er-167 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 68-Er-168 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 68-Er-170 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 71-Lu-175 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 71-Lu-176 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 72-Hf-174 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 72-Hf-176 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 72-Hf-177 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 72-Hf-178 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 72-Hf-180 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 73-Ta-181 | X |  | X |  | X |  | X |  | X |  |  |  |  |  |
| W-182 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| W-183 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| W-184 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| W-186 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 75-Re-185 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 75-Re-187 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 78-Pt-190 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 78-Pt-192 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 78-Pt-194 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 78-Pt-195 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 78-Pt-196 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 78-Pt-198 | X |  | X |  | X | X | X | X | X |  | X |  | X | X |
| 79-Au-197 | X |  | X |  | X | X | X | X | X |  | X |  |  |  |
| 82-Pb-204 | X |  |  |  | X |  | X |  | X |  | X |  |  |  |
| 82-Pb-206 | X |  |  |  | X |  | X |  | X |  | X |  |  |  |
| 82-Pb-207 | X |  |  |  | X |  | X |  | X |  | X |  |  |  |
| 82-Pb-208 | X |  |  |  | X |  | X |  | X |  | X |  |  |  |
| 83-Bi-209 | X |  | X |  | X |  | X |  | X |  |  |  |  |  |
| 90-Th-232 | X |  | X |  | X |  | X | X | X | X | X |  | X | X |
| 92-U-235 | X |  | X | X | X | X | X | X | X | X | X |  |  |  |
| 92-U-238 | X |  | X |  | X |  | X | X | X | X | X |  | X | X |

3. Continuous-energy data library FENDL/MC-3.0 for MCNP

FENDL/MC-3.0 contains point-wise cross section data files for use in the Monte Carlo code MCNP. Two files are given for each material: one with extension “.ace” for the cross section data file in ACE type 1 (ASCII) format and the second one with extension “.xdr” with the information required by the XSDIR file from MCNP code system. Both files are prepared by the ACER module of NJOY-99. The .xdr files were rewritten by the UpdXSDIR code to give the correct ACE filename and to update the route to 0. Table 4 summarizes the information on the FENDL/MC-2.1 library. All the files were created at 300K, and probability tables (PT) were generated for those materials containing unresolved resonance data.

# Table 4: FENDL/MC-3.0 library-summary.

| No. | MATERIAL | ZAID | Emax [MeV] | PT | Filenames [*.ace ],[*.xdr] |
| --- | --- | --- | --- | --- | --- |
| 1 | 1-H-1 | 1001.30c | 150 |  | 01H_001 |
| 2 | 1-H-2 | 1002.30c | 150 |  | 01H_002 |
| 3 | 1-H-3 | 1003.30c | 60 |  | 01H_003 |
| 4 | 2-He-3 | 2003.30c | 60 |  | 02He003 |
| 5 | 2-He-4 | 2004.30c | 60 |  | 02He004 |
| 6 | 3-Li-6 | 3006.30c | 200 |  | 03Li006 |
| 7 | 3-Li-7 | 3007.30c | 200 |  | 03Li007 |
| 8 | 4-Be-9 | 4009.30c | 200 |  | 04Be009 |
| 9 | 5-B-10 | 5010.30c | 200 |  | 05B_010 |
| 10 | 5-B-11 | 5011.30c | 200 |  | 05B_011 |
| 11 | 6-C-12 | 6012.30c | 150 |  | 06C_012 |
| 12 | 6-C-13 | 6013.30c | 200 |  | 06C_013 |
| 13 | 7-N-14 | 7014.30c | 200 |  | 07N_014 |
| 14 | 7-N-15 | 7015.30c | 200 |  | 07N_015 |
| 15 | 8-O-16 | 8016.30c | 150 |  | 08O_016 |
| 16 | 8-O-17 | 8017.30c | 200 |  | 08O_017 |
| 17 | 8-O-18 | 8018.30c | 200 |  | 08O_018 |
| 18 | 9-F-19 | 9019.30c | 150 |  | 09F_019 |
| 19 | 11-Na-23 | 11023.30c | 150 |  | 11Na023 |
| 20 | 12-Mg-24 | 12024.30c | 150 |  | 12Mg024 |
| 21 | 12-Mg-25 | 12025.30c | 150 |  | 12Mg025 |
| 22 | 12-Mg-26 | 12026.30c | 150 |  | 12Mg026 |
| 23 | 13-Al-27 | 13027.30c | 150 |  | 13Al027 |
| 24 | 14-Si-28 | 14028.30c | 150 |  | 14Si028 |
| 25 | 14-Si-29 | 14029.30c | 150 |  | 14Si029 |
| 26 | 14-Si-30 | 14030.30c | 150 |  | 14Si030 |
| 27 | 15-P-31 | 15031.30c | 200 |  | 15P_031 |
| 28 | 16-S-32 | 16032.30c | 200 |  | 16S_032 |
| 29 | 16-S-33 | 16033.30c | 200 |  | 16S_033 |
| 30 | 16-S-34 | 16034.30c | 200 |  | 16S_034 |
| 31 | 16-S-36 | 16036.30c | 200 |  | 16S_036 |
| 32 | 17-Cl-35 | 17035.30c | 200 |  | 17Cl035 |
| 33 | 17-Cl-37 | 17037.30c | 150 |  | 17Cl037 |
| 34 | 18-Ar-36 | 18036.30c | 150 |  | 18Ar036 |
| 35 | 18-Ar-38 | 18038.30c | 150 |  | 18Ar038 |
| 36 | 18-Ar-40 | 18040.30c | 150 |  | 18Ar040 |
| 37 | 19-K-39 | 19039.30c | 150 |  | 19K_039 |
| 38 | 19-K-40 | 19040.30c | 150 |  | 19K_040 |
| 39 | 19-K-41 | 19041.30c | 150 |  | 19K_041 |
| 40 | 20-Ca-40 | 20040.30c | 150 |  | 20Ca040 |
| 41 | 20-Ca-42 | 20042.30c | 150 |  | 20Ca042 |
| 42 | 20-Ca-43 | 20043.30c | 150 |  | 20Ca043 |
| 43 | 20-Ca-44 | 20044.30c | 150 |  | 20Ca044 |
| 44 | 20-Ca-46 | 20046.30c | 150 |  | 20Ca046 |
| 45 | 20-Ca-48 | 20048.30c | 150 |  | 20Ca048 |
| 46 | 21-Sc-45 | 21045.30c | 200 |  | 21Sc045 |
| 47 | 22-Ti-46 | 22046.30c | 150 |  | 22Ti046 |
| 48 | 22-Ti-47 | 22047.30c | 150 |  | 22Ti047 |
| 49 | 22-Ti-48 | 22048.30c | 150 |  | 22Ti048 |
| 50 | 22-Ti-49 | 22049.30c | 150 |  | 22Ti049 |
| 51 | 22-Ti-50 | 22050.30c | 150 |  | 22Ti050 |
| 52 | 23-V-50 | 23050.30c | 150 |  | 23V_050 |
| 53 | 23-V-51 | 23051.30c | 150 |  | 23V_051 |
| 54 | 24-Cr-50 | 24050.30c | 200 |  | 24Cr050 |
| 55 | 24-Cr-52 | 24052.30c | 150 |  | 24Cr052 |
| 56 | 24-Cr-53 | 24053.30c | 200 |  | 24Cr053 |
| 57 | 24-Cr-54 | 24054.30c | 200 |  | 24Cr054 |
| 58 | 25-Mn-55 | 25055.30c | 60 | X | 25Mn055 |
| 59 | 26-Fe-54 | 26054.30c | 150 |  | 26Fe054 |
| 60 | 26-Fe-56 | 26056.30c | 200 |  | 26Fe056 |
| 61 | 26-Fe-57 | 26057.30c | 150 |  | 26Fe057 |
| 62 | 26-Fe-58 | 26058.30c | 200 | X | 26Fe058 |
| 63 | 27-Co-59 | 27059.30c | 150 |  | 27Co059 |
| 64 | 28-Ni-58 | 28058.30c | 150 |  | 28Ni058 |
| 65 | 28-Ni-60 | 28060.30c | 150 |  | 28Ni060 |
| 66 | 28-Ni-61 | 28061.30c | 150 |  | 28Ni061 |
| 67 | 28-Ni-62 | 28062.30c | 150 |  | 28Ni062 |
| 68 | 28-Ni-64 | 28064.30c | 150 |  | 28Ni064 |
| 69 | 29-Cu-63 | 29063.30c | 150 |  | 29Cu063 |
| 70 | 29-Cu-65 | 29065.30c | 150 |  | 29Cu065 |
| 71 | 30-Zn-64 | 30064.30c | 150 | X | 30Zn064 |
| 72 | 30-Zn-66 | 30066.30c | 150 | X | 30Zn066 |
| 73 | 30-Zn-67 | 30067.30c | 150 | X | 30Zn067 |
| 74 | 30-Zn-68 | 30068.30c | 150 | X | 30Zn068 |
| 75 | 30-Zn-70 | 30070.30c | 150 | X | 30Zn070 |
| 76 | 31-Ga-69 | 31069.30c | 150 | X | 31Ga069 |
| 77 | 31-Ga-71 | 31071.30c | 150 | X | 31Ga071 |
| 78 | 32-Ge-70 | 32070.30c | 200 |  | 32Ge070 |
| 79 | 32-Ge-72 | 32072.30c | 200 |  | 32Ge072 |
| 80 | 32-Ge-73 | 32073.30c | 200 |  | 32Ge073 |
| 81 | 32-Ge-74 | 32074.30c | 200 |  | 32Ge074 |
| 82 | 32-Ge-76 | 32076.30c | 200 |  | 32Ge076 |
| 83 | 35-Br-79 | 35079.30c | 200 | X | 35Br079 |
| 84 | 35-Br-81 | 35081.30c | 200 | X | 35Br081 |
| 85 | 39-Y-89 | 39089.30c | 200 |  | 39Y_089 |
| 86 | 40-Zr-90 | 40090.30c | 150 | X | 40Zr090 |
| 87 | 40-Zr-91 | 40091.30c | 150 | X | 40Zr091 |
| 88 | 40-Zr-92 | 40092.30c | 150 | X | 40Zr092 |
| 89 | 40-Zr-94 | 40094.30c | 150 | X | 40Zr094 |
| 90 | 40-Zr-96 | 40096.30c | 150 | X | 40Zr096 |
| 91 | 41-Nb-93 | 41093.30c | 150 | X | 41Nb093 |
| 92 | 42-Mo-92 | 42092.30c | 150 | X | 42Mo092 |
| 93 | 42-Mo-94 | 42094.30c | 150 | X | 42Mo094 |
| 94 | 42-Mo-95 | 42095.30c | 150 | X | 42Mo095 |
| 95 | 42-Mo-96 | 42096.30c | 150 | X | 42Mo096 |
| 96 | 42-Mo-97 | 42097.30c | 150 | X | 42Mo097 |
| 97 | 42-Mo-98 | 42098.30c | 150 | X | 42Mo098 |
| 98 | 42-Mo-100 | 42100.30c | 150 | X | 42Mo100 |
| 99 | 45-Rh-103 | 45103.30c | 200 | X | 45Rh103 |
| 100 | 47-Ag-107 | 47107.30c | 200 | X | 47Ag107 |
| 101 | 47-Ag-109 | 47109.30c | 200 | X | 47Ag109 |
| 102 | 48-Cd-106 | 48106.30c | 200 | X | 48Cd106 |
| 103 | 48-Cd-108 | 48108.30c | 200 | X | 48Cd108 |
| 104 | 48-Cd-110 | 48110.30c | 200 | X | 48Cd110 |
| 105 | 48-Cd-111 | 48111.30c | 200 | X | 48Cd111 |
| 106 | 48-Cd-112 | 48112.30c | 200 | X | 48Cd112 |
| 107 | 48-Cd-113 | 48113.30c | 200 | X | 48Cd113 |
| 108 | 48-Cd-114 | 48114.30c | 200 | X | 48Cd114 |
| 109 | 48-Cd-116 | 48116.30c | 200 | X | 48Cd116 |
| 110 | 50-Sn-112 | 50112.30c | 200 | X | 50Sn112 |
| 111 | 50-Sn-114 | 50114.30c | 200 | X | 50Sn114 |
| 112 | 50-Sn-115 | 50115.30c | 200 | X | 50Sn115 |
| 113 | 50-Sn-116 | 50116.30c | 200 | X | 50Sn116 |
| 114 | 50-Sn-117 | 50117.30c | 200 | X | 50Sn117 |
| 115 | 50-Sn-118 | 50118.30c | 200 | X | 50Sn118 |
| 116 | 50-Sn-119 | 50119.30c | 200 | X | 50Sn119 |
| 117 | 50-Sn-120 | 50120.30c | 200 | X | 50Sn120 |
| 118 | 50-Sn-122 | 50122.30c | 200 | X | 50Sn122 |
| 119 | 50-Sn-124 | 50124.30c | 200 | X | 50Sn124 |
| 120 | 51-Sb-121 | 51121.30c | 200 | X | 51Sb121 |
| 121 | 51-Sb-123 | 51123.30c | 200 | X | 51Sb123 |
| 122 | 53-I-127 | 53127.30c | 200 | X | 53I_127 |
| 123 | 55-Cs-133 | 55133.30c | 200 | X | 55Cs133 |
| 124 | 56-Ba-130 | 56130.30c | 200 | X | 56Ba130 |
| 125 | 56-Ba-132 | 56132.30c | 200 | X | 56Ba132 |
| 126 | 56-Ba-134 | 56134.30c | 200 | X | 56Ba134 |
| 127 | 56-Ba-135 | 56135.30c | 200 | X | 56Ba135 |
| 128 | 56-Ba-136 | 56136.30c | 200 | X | 56Ba136 |
| 129 | 56-Ba-137 | 56137.30c | 200 | X | 56Ba137 |
| 130 | 56-Ba-138 | 56138.30c | 200 |  | 56Ba138 |
| 131 | 57-La-138 | 57138.30c | 200 | X | 57La138 |
| 132 | 57-La-139 | 57139.30c | 200 | X | 57La139 |
| 133 | 58-Ce-136 | 58136.30c | 200 | X | 58Ce136 |
| 134 | 58-Ce-138 | 58138.30c | 200 | X | 58Ce138 |
| 135 | 58-Ce-140 | 58140.30c | 200 |  | 58Ce140 |
| 136 | 58-Ce-142 | 58142.30c | 200 | X | 58Ce142 |
| 137 | 64-Gd-152 | 64152.30c | 200 | X | 64Gd152 |
| 138 | 64-Gd-154 | 64154.30c | 200 | X | 64Gd154 |
| 139 | 64-Gd-155 | 64155.30c | 200 | X | 64Gd155 |
| 140 | 64-Gd-156 | 64156.30c | 200 | X | 64Gd156 |
| 141 | 64-Gd-157 | 64157.30c | 200 | X | 64Gd157 |
| 142 | 64-Gd-158 | 64158.30c | 200 | X | 64Gd158 |
| 143 | 64-Gd-160 | 64160.30c | 200 | X | 64Gd160 |
| 144 | 68-Er-162 | 68162.30c | 200 |  | 68Er162 |
| 145 | 68-Er-164 | 68164.30c | 200 |  | 68Er164 |
| 146 | 68-Er-166 | 68166.30c | 200 |  | 68Er166 |
| 147 | 68-Er-167 | 68167.30c | 200 | X | 68Er167 |
| 148 | 68-Er-168 | 68168.30c | 200 |  | 68Er168 |
| 149 | 68-Er-170 | 68170.30c | 200 | X | 68Er170 |
| 150 | 71-Lu-175 | 71175.30c | 200 | X | 71Lu175 |
| 151 | 71-Lu-176 | 71176.30c | 200 | X | 71Lu176 |
| 152 | 72-Hf-174 | 72174.30c | 200 | X | 72Hf174 |
| 153 | 72-Hf-176 | 72176.30c | 200 | X | 72Hf176 |
| 154 | 72-Hf-177 | 72177.30c | 200 | X | 72Hf177 |
| 155 | 72-Hf-178 | 72178.30c | 200 | X | 72Hf178 |
| 156 | 72-Hf-179 | 72179.30c | 200 | X | 72Hf179 |
| 157 | 72-Hf-180 | 72180.30c | 200 | X | 72Hf180 |
| 158 | 73-Ta-181 | 73181.30c | 150 | X | 73Ta181 |
| 159 | 74-W-180 | 74180.30c | 150 |  | 74W_180 |
| 160 | 74-W-182 | 74182.30c | 150 | X | 74W_182 |
| 161 | 74-W-183 | 74183.30c | 150 | X | 74W_183 |
| 162 | 74-W-184 | 74184.30c | 150 | X | 74W_184 |
| 163 | 74-W-186 | 74186.30c | 150 | X | 74W_186 |
| 164 | 75-Re-185 | 75185.30c | 200 | X | 75Re185 |
| 165 | 75-Re-187 | 75187.30c | 200 | X | 75Re187 |
| 166 | 78-Pt-190 | 78190.30c | 200 |  | 78Pt190 |
| 167 | 78-Pt-192 | 78192.30c | 200 |  | 78Pt192 |
| 168 | 78-Pt-194 | 78194.30c | 200 |  | 78Pt194 |
| 169 | 78-Pt-195 | 78195.30c | 200 |  | 78Pt195 |
| 170 | 78-Pt-196 | 78196.30c | 200 |  | 78Pt196 |
| 171 | 78-Pt-198 | 78198.30c | 200 |  | 78Pt198 |
| 172 | 79-Au-197 | 79197.30c | 150 |  | 79Au197 |
| 173 | 82-Pb-204 | 82204.30c | 200 |  | 82Pb204 |
| 174 | 82-Pb-206 | 82206.30c | 200 |  | 82Pb206 |
| 175 | 82-Pb-207 | 82207.30c | 200 |  | 82Pb207 |
| 176 | 82-Pb-208 | 82208.30c | 200 |  | 82Pb208 |
| 177 | 83-Bi-209 | 83209.30c | 200 |  | 83Bi209 |
| 178 | 90-Th-232 | 90232.30c | 60 | X | 90Th232 |
| 179 | 92-U-235 | 92235.30c | 150 | X | 92U_235 |
| 180 | 92-U-238 | 92238.30c | 150 | X | 92U_238 |

4. Multi-group cross section data library FENDL/MG-3.0

FENDL/MG-3.0 contains neutron-photon coupled multi-group cross section data in MATXS (ASCII) format. These data can be easily processed by the code TRANXS [12] for further use in deterministic transport codes like DORT and TORT. For neutrons 211-energy groups were applied between 0.00001 eV and 55 MeV. Below 19.64 MeV the energy structure matches with the Vitamin-J 175-group energy structure, additionally  one group is included between 19.64 and 20 MeV and 35 more groups are added between 20 and 55 MeV, being their energy-width equal to 1 MeV (see Appendix 2) . For photons the Vitamin-J 50-group energy structure was used between 1 KeV and 50 MeV. Cross section data are given at 300 K for the Bondarenko σ0 values given in Table 3.

Three data files are supplied for each material: one with extension “.m” containing the MATXS-formatted cross section data, and two additional files with extensions “.g” and “.gam” containing respectively GROUPR and GAMINR output in GENDF format, which could be useful for sensitivity analysis or for re-formatting the multi-group cross section files using NJOY-99. Table 5 summarizes the FENDL/MG-3.0 multi-group data library.

Table 5: FENDL/MG-3.0 library-summary.

| No. | MATERIAL | MAT (n) | MAT (ᵞ) | MATXS ID | Filenames [*.m ] n-ᵞ- MATXS [*.g] n-GENDF [*.gam] ᵞ-GENDF |
| --- | --- | --- | --- | --- | --- |
| 1 | 1-H-1 | 125 | 100 | h1 | 01H_001 |
| 2 | 1-H-2 | 128 |  | d | 01H_002 |
| 3 | 1-H-3 | 131 |  | h3 | 01H_003 |
| 4 | 2-He-3 | 225 | 200 | he3 | 02He003 |
| 5 | 2-He-4 | 228 |  | he4 | 02He004 |
| 6 | 3-Li-6 | 325 | 300 | li6 | 03Li006 |
| 7 | 3-Li-7 | 328 |  | li7 | 03Li007 |
| 8 | 4-Be-9 | 425 | 400 | be9 | 04Be009 |
| 9 | 5-B-10 | 525 | 500 | b10 | 05B_010 |
| 10 | 5-B-11 | 528 |  | b11 | 05B_011 |
| 11 | 6-C-12 | 625 | 600 | c12 | 06C_012 |
| 12 | 6-C-13 | 628 |  | c13 | 06C_013 |
| 13 | 7-N-14 | 725 | 700 | n14 | 07N_014 |
| 14 | 7-N-15 | 728 |  | n15 | 07N_015 |
| 15 | 8-O-16 | 825 | 800 | o16 | 08O_016 |
| 16 | 8-O-17 | 828 |  | o17 | 08O_017 |
| 17 | 8-O-18 | 831 |  | o18 | 08O_018 |
| 18 | 9-F-19 | 925 | 900 | f19 | 09F_019 |
| 19 | 11-Na-23 | 1125 | 1100 | na23 | 11Na023 |
| 20 | 12-Mg-24 | 1225 | 1200 | mg24 | 12Mg024 |
| 21 | 12-Mg-25 | 1228 |  | mg25 | 12Mg025 |
| 22 | 12-Mg-26 | 1231 |  | mg26 | 12Mg026 |
| 23 | 13-Al-27 | 1325 | 1300 | al27 | 13Al027 |
| 24 | 14-Si-28 | 1425 | 1400 | si28 | 14Si028 |
| 25 | 14-Si-29 | 1428 |  | si29 | 14Si029 |
| 26 | 14-Si-30 | 1431 |  | si30 | 14Si030 |
| 27 | 15-P-31 | 1525 | 1500 | p31 | 15P_031 |
| 28 | 16-S-32 | 1625 | 1600 | s32 | 16S_032 |
| 29 | 16-S-33 | 1628 |  | s33 | 16S_033 |
| 30 | 16-S-34 | 1631 |  | s34 | 16S_034 |
| 31 | 16-S-36 | 1637 |  | s36 | 16S_036 |
| 32 | 17-Cl-35 | 1725 | 1700 | cl35 | 17Cl035 |
| 33 | 17-Cl-37 | 1731 |  | cl37 | 17Cl037 |
| 34 | 18-Ar-36 | 1825 | 1800 | ar36 | 18Ar036 |
| 35 | 18-Ar-38 | 1831 |  | ar38 | 18Ar038 |
| 36 | 18-Ar-40 | 1837 |  | ar40 | 18Ar040 |
| 37 | 19-K-39 | 1925 | 1900 | k39 | 19K_039 |
| 38 | 19-K-40 | 1928 |  | k40 | 19K_040 |
| 39 | 19-K-41 | 1931 |  | k41 | 19K_041 |
| 40 | 20-Ca-40 | 2025 | 2000 | ca40 | 20Ca040 |
| 41 | 20-Ca-42 | 2031 |  | ca42 | 20Ca042 |
| 42 | 20-Ca-43 | 2034 |  | ca43 | 20Ca043 |
| 43 | 20-Ca-44 | 2037 |  | ca44 | 20Ca044 |
| 44 | 20-Ca-46 | 2043 |  | ca46 | 20Ca046 |
| 45 | 20-Ca-48 | 2049 |  | ca48 | 20Ca048 |
| 46 | 21-Sc-45 | 2125 | 2100 | sc45 | 21Sc045 |
| 47 | 22-Ti-46 | 2225 | 2200 | ti46 | 22Ti046 |
| 48 | 22-Ti-47 | 2228 |  | ti47 | 22Ti047 |
| 49 | 22-Ti-48 | 2231 |  | ti48 | 22Ti048 |
| 50 | 22-Ti-49 | 2234 |  | ti49 | 22Ti049 |
| 51 | 22-Ti-50 | 2237 |  | ti50 | 22Ti050 |
| 52 | 23-V-50 | 2325 | 2300 | v50 | 23V_050 |
| 53 | 23-V-51 | 2328 |  | v51 | 23V_051 |
| 54 | 24-Cr-50 | 2425 | 2400 | cr50 | 24Cr050 |
| 55 | 24-Cr-52 | 2431 |  | cr52 | 24Cr052 |
| 56 | 24-Cr-53 | 2434 |  | cr53 | 24Cr053 |
| 57 | 24-Cr-54 | 2437 |  | cr54 | 24Cr054 |
| 58 | 25-Mn-55 | 2525 | 2500 | mn55 | 25Mn055 |
| 59 | 26-Fe-54 | 2625 | 2600 | fe54 | 26Fe054 |
| 60 | 26-Fe-56 | 2631 |  | fe56 | 26Fe056 |
| 61 | 26-Fe-57 | 2634 |  | fe57 | 26Fe057 |
| 62 | 26-Fe-58 | 2637 |  | fe58 | 26Fe058 |
| 63 | 27-Co-59 | 2725 | 2700 | co59 | 27Co059 |
| 64 | 28-Ni-58 | 2825 | 2800 | ni58 | 28Ni058 |
| 65 | 28-Ni-60 | 2831 |  | ni60 | 28Ni060 |
| 66 | 28-Ni-61 | 2834 |  | ni61 | 28Ni061 |
| 67 | 28-Ni-62 | 2837 |  | ni62 | 28Ni062 |
| 68 | 28-Ni-64 | 2843 |  | ni64 | 28Ni064 |
| 69 | 29-Cu-63 | 2925 | 2900 | cu63 | 29Cu063 |
| 70 | 29-Cu-65 | 2931 |  | cu65 | 29Cu065 |
| 71 | 30-Zn-64 | 3025 | 3000 | zn64 | 30Zn064 |
| 72 | 30-Zn-66 | 3031 |  | zn66 | 30Zn066 |
| 73 | 30-Zn-67 | 3034 |  | zn67 | 30Zn067 |
| 74 | 30-Zn-68 | 3037 |  | zn68 | 30Zn068 |
| 75 | 30-Zn-70 | 3043 |  | zn70 | 30Zn070 |
| 76 | 31-Ga-69 | 3125 | 3100 | ga69 | 31Ga069 |
| 77 | 31-Ga-71 | 3131 |  | ga71 | 31Ga071 |
| 78 | 32-Ge-70 | 3225 | 3200 | ge70 | 32Ge070 |
| 79 | 32-Ge-72 | 3231 |  | ge72 | 32Ge072 |
| 80 | 32-Ge-73 | 3234 |  | ge73 | 32Ge073 |
| 81 | 32-Ge-74 | 3237 |  | ge74 | 32Ge074 |
| 82 | 32-Ge-76 | 3243 |  | ge76 | 32Ge076 |
| 83 | 35-Br-79 | 3525 | 3500 | br79 | 35Br079 |
| 84 | 35-Br-81 | 3531 |  | br81 | 35Br081 |
| 85 | 39-Y-89 | 3925 | 3900 | y89 | 39Y_089 |
| 86 | 40-Zr-90 | 4025 | 4000 | zr90 | 40Zr090 |
| 87 | 40-Zr-91 | 4028 |  | zr91 | 40Zr091 |
| 88 | 40-Zr-92 | 4031 |  | zr92 | 40Zr092 |
| 89 | 40-Zr-94 | 4037 |  | zr94 | 40Zr094 |
| 90 | 40-Zr-96 | 4043 |  | zr96 | 40Zr096 |
| 91 | 41-Nb-93 | 4125 | 4100 | nb93 | 41Nb093 |
| 92 | 42-Mo-92 | 4225 | 4200 | mo92 | 42Mo092 |
| 93 | 42-Mo-94 | 4231 |  | mo94 | 42Mo094 |
| 94 | 42-Mo-95 | 4234 |  | mo95 | 42Mo095 |
| 95 | 42-Mo-96 | 4237 |  | mo96 | 42Mo096 |
| 96 | 42-Mo-97 | 4240 |  | mo97 | 42Mo097 |
| 97 | 42-Mo-98 | 4243 |  | mo98 | 42Mo098 |
| 98 | 42-Mo-100 | 4249 |  | mo100 | 42Mo100 |
| 99 | 45-Rh-103 | 4525 | 4500 | rh103 | 45Rh103 |
| 100 | 47-Ag-107 | 4725 | 4700 | ag107 | 47Ag107 |
| 101 | 47-Ag-109 | 4731 |  | ag109 | 47Ag109 |
| 102 | 48-Cd-106 | 4825 | 4800 | cd106 | 48Cd106 |
| 103 | 48-Cd-108 | 4831 |  | cd108 | 48Cd108 |
| 104 | 48-Cd-110 | 4837 |  | cd110 | 48Cd110 |
| 105 | 48-Cd-111 | 4840 |  | cd111 | 48Cd111 |
| 106 | 48-Cd-112 | 4843 |  | cd112 | 48Cd112 |
| 107 | 48-Cd-113 | 4846 |  | cd113 | 48Cd113 |
| 108 | 48-Cd-114 | 4849 |  | cd114 | 48Cd114 |
| 109 | 48-Cd-116 | 4855 |  | cd116 | 48Cd116 |
| 110 | 50-Sn-112 | 5025 | 5000 | sn112 | 50Sn112 |
| 111 | 50-Sn-114 | 5031 |  | sn114 | 50Sn114 |
| 112 | 50-Sn-115 | 5034 |  | sn115 | 50Sn115 |
| 113 | 50-Sn-116 | 5037 |  | sn116 | 50Sn116 |
| 114 | 50-Sn-117 | 5040 |  | sn117 | 50Sn117 |
| 115 | 50-Sn-118 | 5043 |  | sn118 | 50Sn118 |
| 116 | 50-Sn-119 | 5046 |  | sn119 | 50Sn119 |
| 117 | 50-Sn-120 | 5049 |  | sn120 | 50Sn120 |
| 118 | 50-Sn-122 | 5055 |  | sn122 | 50Sn122 |
| 119 | 50-Sn-124 | 5061 |  | sn124 | 50Sn124 |
| 120 | 51-Sb-121 | 5125 | 5100 | sb121 | 51Sb121 |
| 121 | 51-Sb-123 | 5131 |  | sb123 | 51Sb123 |
| 122 | 53-I-127 | 5325 | 5300 | i127 | 53I_127 |
| 123 | 55-Cs-133 | 5525 | 5500 | cs133 | 55Cs133 |
| 124 | 56-Ba-130 | 5625 | 5600 | ba130 | 56Ba130 |
| 125 | 56-Ba-132 | 5631 |  | ba132 | 56Ba132 |
| 126 | 56-Ba-134 | 5637 |  | ba134 | 56Ba134 |
| 127 | 56-Ba-135 | 5640 |  | ba135 | 56Ba135 |
| 128 | 56-Ba-136 | 5643 |  | ba136 | 56Ba136 |
| 129 | 56-Ba-137 | 5646 |  | ba137 | 56Ba137 |
| 130 | 56-Ba-138 | 5649 |  | ba138 | 56Ba138 |
| 131 | 57-La-138 | 5725 | 5700 | la138 | 57La138 |
| 132 | 57-La-139 | 5728 |  | la139 | 57La139 |
| 133 | 58-Ce-136 | 5825 | 5800 | ce136 | 58Ce136 |
| 134 | 58-Ce-138 | 5831 |  | ce138 | 58Ce138 |
| 135 | 58-Ce-140 | 5837 |  | ce140 | 58Ce140 |
| 136 | 58-Ce-142 | 5843 |  | ce142 | 58Ce142 |
| 137 | 64-Gd-152 | 6425 | 6400 | gd152 | 64Gd152 |
| 138 | 64-Gd-154 | 6431 |  | gd154 | 64Gd154 |
| 139 | 64-Gd-155 | 6434 |  | gd155 | 64Gd155 |
| 140 | 64-Gd-156 | 6437 |  | gd156 | 64Gd156 |
| 141 | 64-Gd-157 | 6440 |  | gd157 | 64Gd157 |
| 142 | 64-Gd-158 | 6443 |  | gd158 | 64Gd158 |
| 143 | 64-Gd-160 | 6449 |  | gd160 | 64Gd160 |
| 144 | 68-Er-162 | 6825 | 6800 | er162 | 68Er162 |
| 145 | 68-Er-164 | 6831 |  | er164 | 68Er164 |
| 146 | 68-Er-166 | 6837 |  | er166 | 68Er166 |
| 147 | 68-Er-167 | 6840 |  | er167 | 68Er167 |
| 148 | 68-Er-168 | 6843 |  | er168 | 68Er168 |
| 149 | 68-Er-170 | 6849 |  | er170 | 68Er170 |
| 150 | 71-Lu-175 | 7125 | 7100 | lu175 | 71Lu175 |
| 151 | 71-Lu-176 | 7128 |  | lu176 | 71Lu176 |
| 152 | 72-Hf-174 | 7225 | 7200 | hf174 | 72Hf174 |
| 153 | 72-Hf-176 | 7231 |  | hf176 | 72Hf176 |
| 154 | 72-Hf-177 | 7234 |  | hf177 | 72Hf177 |
| 155 | 72-Hf-178 | 7237 |  | hf178 | 72Hf178 |
| 156 | 72-Hf-179 | 7240 |  | hf179 | 72Hf179 |
| 157 | 72-Hf-180 | 7243 |  | hf180 | 72Hf180 |
| 158 | 73-Ta-181 | 7328 | 7300 | ta181 | 73Ta181 |
| 159 | 74-W-180 | 7425 | 7400 | w180 | 74W_180 |
| 160 | 74-W-182 | 7431 |  | w182 | 74W_182 |
| 161 | 74-W-183 | 7434 |  | w183 | 74W_183 |
| 162 | 74-W-184 | 7437 |  | w184 | 74W_184 |
| 163 | 74-W-186 | 7443 |  | w186 | 74W_186 |
| 164 | 75-Re-185 | 7525 | 7500 | re185 | 75Re185 |
| 165 | 75-Re-187 | 7531 |  | re187 | 75Re187 |
| 166 | 78-Pt-190 | 7825 | 7800 | pt190 | 78Pt190 |
| 167 | 78-Pt-192 | 7831 |  | pt192 | 78Pt192 |
| 168 | 78-Pt-194 | 7837 |  | pt194 | 78Pt194 |
| 169 | 78-Pt-195 | 7840 |  | pt195 | 78Pt195 |
| 170 | 78-Pt-196 | 7843 |  | pt196 | 78Pt196 |
| 171 | 78-Pt-198 | 7849 |  | pt198 | 78Pt198 |
| 172 | 79-Au-197 | 7925 | 7900 | au197 | 79Au197 |
| 173 | 82-Pb-204 | 8225 | 8200 | pb204 | 82Pb204 |
| 174 | 82-Pb-206 | 8231 |  | pb206 | 82Pb206 |
| 175 | 82-Pb-207 | 8234 |  | pb207 | 82Pb207 |
| 176 | 82-Pb-208 | 8237 |  | pb208 | 82Pb208 |
| 177 | 83-Bi-209 | 8325 | 8300 | bi209 | 83Bi209 |
| 178 | 90-Th-232 | 9040 | 9000 | th232 | 90Th232 |
| 179 | 92-U-235 | 9228 | 9200 | u235 | 92U_235 |
| 180 | 92-U-238 | 9237 |  | u238 | 92U_238 |

5. Verification of FENDL/MC-3.0 and FENDL/MG-3.0

The main verification technique used was to check the NJOY output file for each material. The “warning messages” generated were understood, and most of them were related to incomplete or inconsistent evaluations. Some comments about the major findings are given below:

- Evaluations for H-3 and He-4 do not have photon production data.

- For several evaluations File 6 (MF = 6) is used, although incomplete: the energy distribution is not given for the recoil nucleus. NJOY-99 applied one particle approximation in these cases.

- For Li-6, Li-7, Be-9, B-10, C-12, N-14, N-15, F-19, Na-23, Mg-24,-25,-26, Cl-35,-37,  Ti- 46, -47, -48, 49, -50, Co-59, Br-79,-81, Zr-92, -94, -96, Nb-93, Mo-92, -94, -95, -96, -97,-98, -100, Ag-107, Cd-106, Cd-111, Er-162,-164,-166, -167, -168, -170, Hf-174, -176, -177, -178, -179, -180, Ta-181, Au-197, U-235, -238 discontinuities were found in the gamma files. Corrective action was done by NJOY-99

- For 119 materials inconsistencies were found at several incident energies because E<E’. Corrective action was done by NJO-Y99.

- For Br-81, Mo-92, -94, -95, -96, -97, -98 and Hf-180 problems were found with the sum of the photon production. Re-normalization was applied as corrective action by NJOY-99.

All the corrective actions performed in the second run of ACER were considered appropriate.

Additionally, the plots generated by ACER were visually inspected and none trivial errors were detected.

A second verification technique was used for all the ACE-formatted files. Processed data were converted back to ENDF-6 format using the code ACELST [13]. The original evaluation was processed using the PREPRO-2010 code system (LINEAR+RECENT+SIGMA1), and the two ENDF-6 formatted files were compared using COMHARD.

No significant deviations in the cross section data were found for most of materials. The main sources of differences could be a different treatment of small cross sections and energy discontinuity problems by NJOY-99 and PREPRO-2010 code systems. However, some differences are worthy to note. For Rh-103, I-127 and U-238 it seems that could be a double counting of one partial reaction as you can see in figures 2, 3 and 4. To clear the origin of the difference the sequence LINEAR+RECENT+FIXUP was run over FENDL/E-3.0 evaluated nuclear data files, in such a way that redundant cross sections were obtained by summation of the corresponding partial cross section data according to the ENDFB-6 format rules. The resulting files from RECENT were compared to the ones from FIXUP. Figures 5, 6 and 7 show the comparison for Rh-103, I-127 and U-238 respectively. As you can see after running FIXUP the cross sections have the same shapes that the ones processed by NJOY-99, so the differences could come from some inconsistencies lying on the primary evaluated nuclear data files.

Figures 8, 9 and 10 present the Rh-103, I-127 and U-238 evaluated cross section data. From the plots you can see that it is likely that some partial cross section data that is contributing to the inelastic (non-elastic) cross section (MT=3) is also included into the (n,x) cross section (MT=5) in the energy range between 20 and 30 MeV.

After running these basic verification procedures, the processed data were judged to be acceptable for transport calculations in fusion applications. The cross section data of FENDL/MC-3.0 and FENDL/MG-3.0 libraries seem to have the same quality of the primary FENDL/E-3.0 evaluated nuclear data file in ENDFB-6 format.

6. Point-wise data library FENDL/PD-3.0 in ENDFB-6 format

As a result of the verification process for the transport cross section libraries a point-wise evaluated nuclear data library was produce at 0K for neutrons. The sequence of processing was LINEAR+RECENT+FIXUP+STANEF. The first three codes from the PREPRO-2010 system and the last one from an updated version of the 8.02 ENDFB-6 utilities. All primary evaluated nuclear data files from FENDL/E-3.0 for neutrons were successfully processed using the following main options:

- Reconstruction tolerance: 0.1%

- Temperature: 0K

- Minimal cross section: 10-10 barns.

- FIXUP corrective options:

  - Correct ZA and AWR in all cross sections

  - Correct cross section thresholds

  - Reconstruction of redundant cross section according to the ENDFB-6 format summing rules.

  - Insure non-negative cross sections

  - Delete energies that are not in ascending order, energy repetition is allowed.

  - Eliminate duplicate unnecessary points

  - Check MF/MT in each section according to ENDFB-6 format

The files were re-sequenced and the directory section was updated using STANEF.

The names of the files are the same that those for the FENDL/E-3.0 library, but the extension is *.PND, pointing to a point-wise evaluated nuclear data file. The rest of parameters as the same that ones for the FENDL/E-3.0 library (Table 1).

The point-wise library FENDL/PD-3.0 could be useful for evaluators and give a clear image of the cross section data.

Figure 2: FENDL/MC-3.0 vs FENDL/E-3.0 for Rh-103 total cross section

Figure 3: FENDL/MC-3.0 vs FENDL/E-3.0 for I-127 total cross section

Figure 4: FENDL/MC-3.0 vs FENDL/E-3.0 for U-238 total cross section

Figure 5: FENDL/PD-3.0 vs FENDL/E-3.0 for Rh-103

Figure 6: FENDL/PD-3.0 vs FENDL/E-3.0 for I-127

Figure 7: FENDL/PD-3.0 vs FENDL/E-3.0 for U-238

Figure 8: FENDL/E-3.0 cross sections for Rh-103

Figure 9: FENDL/E-3.0 cross sections for I-127

Figure 10: FENDL/E-3.0 cross sections for U-238

7. Accessing FENDL-3.0 data

The FENDL-3.0 data library is freely available from the IAEA-NDS upon request, and is also readily accessible at http://www-nds.iaea.org/ web site.

FENDL-3.0 package includes the following information:

- FENDL/E-3.0 evaluated nuclear data files for neutron and photo-atomic interaction data in ENDFB-6 format.

- FENDL/PW-3.0 point-wise evaluated nuclear data files in ENDFB-6 format at 0K (preprocessed by PREPRO10 code package)

- FENDL/MC-3.0: continuous energy data files for MCNP calculations (*.ace and *.xdr files).

- FENDL/MG-3.0: coupled neutron-photon multi-group data library for transport calculations (*.m,*.g,*.gam files).

- NJOY inputs for generation of FENDL-3.0.

- Auxiliary programs and MSDOS/WINDOWS batch procedures used in the generation and verification of the FENDL-3.0 transport libraries.

- Documentation: INDC(NDS) report (this document).

8. Final remarks and recommendations

A new version of FENDL (termed FENDL-3.0) has been assembled and made available for fusion applications. All evaluated nuclear data files (180 materials) from FENDL/E-3.0 were processed using the NJOY-99.364+ code system. FENDL/MC-3.0 and FENDL/MG-3.0 libraries were assembled. A point-wise evaluated nuclear data library in ENDFB-6 format was also produced at 0K.

FENDL-3.0 libraries, input files and report are freely available on the web site http://www-nds.iaea.org/ or can be requested on CD-ROM from the IAEA-NDS.

An extensive and intensive benchmarking of the transport libraries is strongly recommended, analysing an appropriate set of benchmarks as was done for the FENDL-2.1 library.

Afterwards, a revision of the FENDL/E-3.0 evaluated nuclear data library is recommended to finally set up all the files and to include the feedback coming from bechmarking.

References

- López Aldama, D., Trkov, A., “FENDL-2.1: Update of an evaluated nuclear data library for fusion applications”, INDC(NDS)-467, IAEA Nuclear Data Section, December 2004.

- Sharma A. R. et al., “Integral validation and use of improved nuclear data in fusion blanket studies”, 302-F4-IND-11566 (B5-IND-29641), 2002.

- MacFarlane, R. E., Muir, D. M., “NJOY-99.0: Code System for Producing Pointwise and Multigroup Neutron and Photon Cross Sections from ENDF/B data”, Los Alamos National Laboratory, PSR-480, 2000.

- Cullen, D. E., “PREPRO 2010: 2010 ENDF/B Pre-processing codes (ENDF/B-VII Tested)”, IAEA-NDS-39, Rev. 14, October 31, 2010.

- Dunford, C. L., “ENDF Utility Codes Release &.01/02”, May 31, 2005

- Herman M, Trkov, A.,(editors), “ENDF-6 Formats Manuals”, ENDF-102, BNL-90365-2009, June 2009.

- Trkov, A., Private communication on chmf32 code, November 2011.

- Briesmeister, J. F., “MCNP – A General Monte Carlo N-Particle Transport Code, Version 4C”, Los Alamos National Laboratory, LA-13709-M, 2000.

- Rhoades, W. A., et al., “DOORS 3.2, One-, Two-, Three-Dimensional Discrete Ordinates Neutron/Photon Transport Code System”, RSICC, Oak Ridge National Laboratory, CCC-650, 1998.

- Forrest, R., Trkov, A., “Maintain FENDL Library for Fusion Applications. FENDL-2 Library for Fusion Applications – Status and Future Developments”, Summary Report of an IAEA Consultants’ Meeting, 10-12 November 2003, Vienna, INDC(NDS)-451, 2003.

- Herman, M., “Validation and Improvement of the FENDL-2.0 Transport Sublibraries”, Report on an IAEA Consultants’ Meeting, Vienna, Austria, 12-14 October 1998, INDC(NDS)-395, 1999

- MacFarlane, R. E., “TRANSX 2: A Code for Interfacing MATXS Cross Section Libraries to Nuclear Transport Codes”, Los Alamos National Laboratory, LA-12312-MS, 1992.

- Trkov, A., Private communication on ACELST code, December 2002.

APPENDIX 1: NJOY local updates at IAEA-NDS.

  - OECD/NEA updates

*/

*/ OECD/NEA compilation of NJOY updates

*/ compatible with the official patch distribution up364

*/

*/ The patches include those carried-over from the set compatible

*/ with the official up296 but not adopted in up364.

*/

*ident upnea001

*/ njoy - C. Broeders, 6-Oct-2006

*/        Open scratch files in local disc area

*/        Ref.: Comments by D.E. Cullen in PrePro-2004 (Scratcha.f) on p.19 of:

*/        "http://www-nds.iaea.org/ndspub/endf/prepro/DOCUMENT/PDF/Overview.pdf"

*/        Status "scratch" does not work with Lahey compiler on Linux,

*/        therefore 'age" is set "unknown"

*d njoy.470

age='unknown'

*d njoy.471

write(fn,'(a,i2.2)') 'temp',nun

open(nun,file=fn,form=for,status=age)

*/

*ident upnea004

*/ groupr - C. Broeders, 6-Oct-2006

*/          extend IWT=5 spectrum definition up to 200MeV

*/ -------------------------------------------

*d groupr.2145

dimension w1(92),w2(92),w3(10)

*d groupr.2150

data w1/0d0,0d0,0d0,0d0,1.d0,93.d0,93.d0,5.d0,

*i groupr.2175

data w3/3.d7,1.0318d-10,5.d7,6.1908d-11,1.d8,3.0954d-11,

&1.5d8,2.0636d-11,2.d8,1.5477d-11/

*d groupr.2358

iw=194

*i groupr.2365

do i=1,10

a(i+183+iwght)=w3(i)

enddo

*/

*/ *ident upnea019 is included in up265

*/

*/ *ident upnea020 is included in up235

*/

*/ *ident upnea021 is included in up261

*/

*/ *ident upnea022 is included in up260

*/

*/ *ident upnea023 is included in up272

*/

*/ *ident upnea024 is included in up273

*/

*/ *ident upnea025 is included in up315

*/

*/ *ident upnea026 is included in up316

*/

*/ *ident upnea027 is included mostly in up317, except a few statements

*/                 which are placed in upnea068

*/

*/ *ident upnea028 is included in up318

*/

*/ *ident upnea029 is included in up316

*/

*/ *ident upnea030 is included in up272

*/

*/ *ident upnea031 is included in up289

*/

*ident upnea032

*/ acer     A. Trkov, 30 May 2008

*/          Plots of discrete inelastic make sense below 10 MeV

*d acer.19586

c                       limit discrete inelastic plots to 10 MeV

if (x.gt.xmax) xmax=min(x,10.)

*/

*/ *ident upnea033 included in up278

*/

*/ *ident upnea034 included in up277

*/

*/ *ident upnea035 included in up279

*/

*/ *ident upnea036 included in up279

*/

*/ *ident upnea037 included in up277

*/

*ident upnea038

*/ covr    A. Trkov, 20 October 2008

*          Fix diagnostic message

*d covr.1793,1805

zero=0

if (abs(crit).gt.zero) write(strng,

&      '(''i'',i3,'' j'',i3,'' xa(i,j)='',1p,e12.4,'' xa(j,i)='',

&     1p,e12.4)') i,im1,xa(im1ind,i),xa(iind,im1)

if (abs(crit).gt.test .and. abs(xa(im1ind,i)).gt.1e-20) then

call error('press','matrix not symmetric',strng)

endif

test=1

test=test/1000000

if (abs(crit).lt.test) go to 250

call mess('press','matrix not symmetric',strng)

*/

*/ *ident upnea039 included in up272

*/

*ident upnea040

*/

*/ GROUPR - R. Perry, 15 October 2008

*/          (Original update name: upwe6)

*/          Problem with thermal scattering matricies in GROUPR

*/          There were small discrepancies between the sums thermal scatter

*/          matrices and the group cross-sections. This update renormalises

*/          the interpolated spectra (produced during integration)

*/          to sum to unity.

*/          (guarding against array overflow added by A. Trkov)

*i groupr.6915

integer nsi

parameter (mxnsi=15000)

*i groupr.6922

dimension sint(2,mxnsi)

*i groupr.7030

nsi = 0

*i groupr.7146

c

c store interpolated function.

c

nsi = nsi+1

if(nsi.gt.mxnsi)

&   call error('getaed','mxnsi array limit exceeded',' ')

sint(1,nsi) = ei

sint(2,nsi) = fi(1)

*i groupr.7155

c

c sum interpolated spectrum and adjust aed.

c

sisum = 0.0

do il = 1, nsi - 1

sisum = sisum + (sint(2,il)+sint(2,il+1))*

&                                  (sint(1,il+1)-sint(1,il))/2

enddo

c

c don't re-normalise if scatter source above top energy group.

c

if(i .lt. ngn .or. (k1 .eq. nlo .and. k2 .eq. nhi) ) then

do il = 1, i

aed(1,il) = aed(1,il)/sisum

enddo

endif

*/

*/ *ident upnea041 included in up282

*/

*/ *ident upnea042 is not included; it is redefined in upnea069

*/

*/ *ident upnea043 included in up282

*/

*/ *ident upnea044 included in up273

*/

*/ *ident upnea045 included in up282

*/

*/ *ident upnea046 withdrawn

*/

*/ *ident upnea047 included in up287

*/

*/ *ident upnea048 included in up329 and extended

*/

*/ *ident upnea049 is included in up290

*/

*/ *ident upnea050 is included in up289

*/

*/ *ident upnea051 is included in up363

*/

*/ *ident upnea052 is included in up361

*/

*/ *ident upnea053 is included in up307

*/

*ident upnea054

*/ errorr D.L. Aldama, July 2009

*/        Fix weighting function option

*d errorj.660

if (iwt.eq.1.or.iwt.eq.4.or.iwt.eq.5.or.

&     (iwt.ge.7.and.iwt.lt.11))

*d errorj.1492

if (iwt.eq.1.or.iwt.eq.4.or.iwt.eq.5.or.

&     (iwt.ge.7.and.iwt.lt.11))

*/

*/ *ident upnea055 is included in up314

*/

*/ *ident upnea056 is included in up312

*/

*/ *ident upnea057 is included in up305

*/

*/ *ident upnea058 is included in up318

*/

*/ *ident upnea059 is included in up205

*/

*/ *ident upnea060 is not needed due to alternative coding in up329

*/

*/ *ident upnea061 is superseeded by upnea068

*/

*/ *ident upnea062 is included in up324

*/

*/ *ident upnea063 is dealt with differently in upnea315

*/

*ident upnea064

*/ acer    A. Trkov, February 2010

*/         Particle emission spectra in the acer plots are corrupted

*/         for MF6 Law 1 LANG 1 when more than one interpolation range

*/         is specified for the distributions on incident particle

*/         energies. In some cases the MCNP calculations are also wrong.

*/         A fix is done when writing the data to a temporary file.

*/         The multiple ranges are suppressed. The first interpolation

*/         law is prescribed over the entire incident energy range

*/         and a message is printed.

*/         WARNING:

*/         This is a temporary patch before a proper solution is found.

*/         The true error probably occurs somewhere near acer.6651

*/         or later, and/or possibly in MCNP.

*/         Implications:

*/         JENDL-HE files truncated to 150 MeV (as proposed for FENDL-3)

*/         led to strongly discrepant results in a benchmark model

*/         calculation representative of the ITER device. The discrepancy

*/         is greatly reduced with the use of this patch. The assumption

*/         in the patch has no influence on the evaluated data because

*/         the interpolation law changes above 20 MeV where the yield

*/         drops to zero due to the reaction representation in MT5.

*d acer.2373,2374

call tab2io(nin,0,0,b,nb,nw)

nr=n1h

ne=nint(b(6))

if(nr.gt.1) then

write(string,'(a,i3)')

&                   'multiple interp. ranges for mf6, mt',mt

call mess('topfil',string

&                    ,'first law applied everywhere')

nr=1

b(5)=nr

b(7)=ne

end if

call tab2io(0,nout,0,b,nb,nw)

*/

*/ *ident upnea065 included in up341

*/

*/ *ident upnea066 is included in up342

*/

*/ *ident upnea067 is included in up363

*/

*ident upnea068

*/ acer    A. Trkov, January 2010

*/         (Revision of upnea061, noticed by Skip Kahler)

*d acer.119,120

c     *               7   read fast ace files to print or edit         *

c     *               8   read thermal ace files to print or edit      *

c     *               9   read dosimetry ace files to print or edit    *

*d acer.407

else if (iopt.eq.6.or.iopt.gt.9) then

*d acer.435

else if (iopt.ge.7.and.iopt.le.9) then

*i acer.17639

c

c     ***read type 3 ace format file

else if (itype.eq.3) then

if (mcnpx.eq.0) then

read(nin) hz(1:10),aw0,tz,hd,hko,hm,(izo(i),awo(i),i=1,16),

&       (nxs(i),i=1,16),(jxs(i),i=1,32)

else

read(nin) hz(1:13),aw0,tz,hd,hko,hm,(izo(i),awo(i),i=1,16),

&       (nxs(i),i=1,16),(jxs(i),i=1,32)

endif

len2=nxs(1)

n=(len2+ner-1)/ner

l=0

do i=1,n

max=len2-l

if (max.gt.ner) max=ner

read (nin) (xss(l+j),j=1,max)

l=l+max

enddo

call closz(-nin)

c        flag incident particle "undefined"

izai=-1

awi =-1

*/

*/ *ident upnea069 is included in up362

*/

*/ *ident upnea070 is included in up363

*/

*/ *ident upnea071 is included in up363

*/

*ident upnea073

*/ acer    A. Trkov, January 2011

*/         Error message lenth exceeds string size

*d up360.91,93

write(strng,'(''mtd='',i3,'' mt='',i6,

&                       '' ie='',i4,i5,'' nd='',3i4,'' ed='',

&                       1p,e9.3e1)')

*/

*ident upnea074

*/ acer    A. Trkov, June 2011

*/         zaid is re-defined incorrectly when editing fast ace files if original

*/         suffix is greater than 0.50

*d acer.17652

iza=int(zaid+0.001)

*/

*ident upnea075

*/ errorr  A. Trkov, June 2011

*/         One more case to skip input if there are no data to process

*i up324.105

if(iwt.eq.4) read(nsysi,*) eb,tb,ec,tc

*/

*ident upnea076

*/

*/ HEATR  - K. Vignitchouk, 06/09/11

*/          Calculate mean neutron energy for law 12-energy

*/          dependent fission neutron spectrum (madland-nix)

*/          (originaly submitted as upwd20)

*/

*i heatr.2169

c

c     ***law 12--energy dependent fission neutron spectrum (madland-nix)

else if (lf.eq.12) then

s=((a(lnext)+a(lnext+1))/2)+(4*theta/3)

*/

*ident upnea077

*/ broadr  A. Trkov, October 2011

*/         Increase the maximum number of no-threshold cross sections

*/         (case: NNDC evaluation of Tm-168)

*d up175.13

parameter (nttmax=48)

*d up175.21

parameter (nttmax=48)

*d up175.25

parameter (nttmax=48)

*d up175.30

parameter (nttmax=48)

*d up175.34

parameter (nttmax=48)

*/

  - Updates for processing FENDL-3.0 at IAEA-NDS

*ident upnds01

*/

*/ ACER  - D. L. Aldama (IAEA/NDS Consultant)

*/         Nov./2011

*/         Correction to NJOY update up360 for processing

*/         MF6(16) with different number of discrete

*/         photon energies by sections

*d up360.17

nwordg=2000

*d up360.94

a(idise)=ep

*i up360.95

else if (abs(ep).lt.abs(a(idise+nd0-1))) then

a(idise+nd0)=ep

nd0=nd0+1

*d up360.123

&                     nwordg,nd0

*/

*ident upnds02

*/

*/ HEATR  - D. L. Aldama (IAEA/NDS Consultant)

*/          Nov./2011

*/          Correction for large MF4/MT=2 sections

*i heatr.3832

if (nb.ne.0) then

l=iraw

do while (nb.ne.0)

l=l+nwc

call moreio(nin,0,0,c(l),nb,nwc)

enddo

endif

*i heatr.3837

if (nb.ne.0) then

l=iraw

do while (nb.ne.0)

l=l+nwc

call moreio(nin,0,0,c(l),nb,nwc)

enddo

endif

*i heatr.3877

if (nb.ne.0) then

l=iraw

do while (nb.ne.0)

l=l+nwc

call moreio(nin,0,0,c(l),nb,nwc)

enddo

endif

*/

APPENDIX 2: Energy boundaries for the 211-group structure for fusion applications

(175 groups of VITAMIN-J + 36 groups up to 55 MeV)

N                    N+1                          N+2                           N+3                              N+4

0         1.0000100E-05   1.0000100E-01   4.1399401E-01   5.3157902E-01

4    6.8256003E-01   8.7642503E-01   1.1230000E+00   1.4400001E+00

8    1.8553900E+00   2.3823700E+00   3.0590200E+00   3.9278600E+00

12   5.0434799E+00   6.4759498E+00   8.3152905E+00   1.0677000E+01

16   1.3709600E+01   1.7603500E+01   2.2603300E+01   2.9023199E+01

20   3.7266499E+01   4.7851200E+01   6.1442101E+01   7.8893204E+01

24   1.0130100E+02   1.3007300E+02   1.6701700E+02   2.1445399E+02

28   2.7536401E+02   3.5357501E+02   4.5399899E+02   5.8294702E+02

32   7.4851801E+02   9.6111700E+02   1.2341000E+03   1.5846100E+03

36   2.0346801E+03   2.2486699E+03   2.4851699E+03   2.6125901E+03

40   2.7465400E+03   3.0353899E+03   3.3546299E+03   3.7074399E+03

44   4.3074199E+03   5.5308398E+03   7.1017402E+03   9.1188203E+03

48   1.0594600E+04   1.1708800E+04   1.5034400E+04   1.9304500E+04

52   2.1874900E+04   2.3578600E+04   2.4175500E+04   2.4787500E+04

56   2.6058400E+04   2.7000100E+04   2.8501100E+04   3.1827801E+04

60   3.4306699E+04   4.0867699E+04   4.6309199E+04   5.2475199E+04

64   5.6562199E+04   6.7379500E+04   7.2024500E+04   7.9498703E+04

68   8.2503398E+04   8.6517000E+04   9.8036500E+04   1.1109000E+05

72   1.1678600E+05   1.2277300E+05   1.2906800E+05   1.3568600E+05

76   1.4264200E+05   1.4995600E+05   1.5764400E+05   1.6572700E+05

80   1.7422400E+05   1.8315600E+05   1.9254700E+05   2.0241900E+05

84   2.1279700E+05   2.2370800E+05   2.3517700E+05   2.4723500E+05

88   2.7323700E+05   2.8724600E+05   2.9451800E+05   2.9721100E+05

92   2.9849100E+05   3.0197400E+05   3.3373300E+05   3.6883200E+05

96   3.8774200E+05   4.0762200E+05   4.5049200E+05   4.9787100E+05

100  5.2339700E+05   5.5023200E+05   5.7844300E+05   6.0810100E+05

104  6.3927900E+05   6.7205500E+05   7.0651200E+05   7.4273600E+05

108  7.8081700E+05   8.2085000E+05   8.6293600E+05   9.0718000E+05

112  9.6167200E+05   1.0025900E+06   1.1080300E+06   1.1648400E+06

116  1.2245600E+06   1.2873500E+06   1.3533500E+06   1.4227400E+06

120  1.4956900E+06   1.5723700E+06   1.6529900E+06   1.7377400E+06

124  1.8268400E+06   1.9205000E+06   2.0189700E+06   2.1224800E+06

128  2.2313000E+06   2.3069300E+06   2.3457000E+06   2.3653300E+06

132  2.3851300E+06   2.4659700E+06   2.5924000E+06   2.7253200E+06

136  2.8650500E+06   3.0119400E+06   3.1663700E+06   3.3287100E+06

140  3.6787900E+06   4.0657000E+06   4.4932900E+06   4.7236700E+06

144  4.9658500E+06   5.2204600E+06   5.4881200E+06   5.7695000E+06

148  6.0653100E+06   6.3762800E+06   6.5924100E+06   6.7032000E+06

152  7.0468800E+06   7.4081800E+06   7.7880100E+06   8.1873100E+06

156  8.6070800E+06   9.0483700E+06   9.5122900E+06   1.0000000E+07

160  1.0512700E+07   1.1051700E+07   1.1618300E+07   1.2214000E+07

164  1.2523200E+07   1.2840300E+07   1.3498600E+07   1.3840300E+07

178  1.4190700E+07   1.4549900E+07   1.4918200E+07   1.5683100E+07

172  1.6487200E+07   1.6904600E+07   1.7332500E+07   1.9640300E+07

176  2.0000000E+07   2.1000000E+07   2.2000000E+07   2.3000000E+07

180  2.4000000E+07   2.5000000E+07   2.6000000E+07   2.7000000E+07

184  2.8000000E+07   2.9000000E+07   3.0000000E+07   3.1000000E+07

198  3.2000000E+07   3.3000000E+07   3.4000000E+07   3.5000000E+07

192  3.6000000E+07   3.7000000E+07   3.8000000E+07   3.9000000E+07

196  4.0000000E+07   4.1000000E+07   4.2000000E+07   4.3000000E+07

200  4.4000000E+07   4.5000000E+07   4.6000000E+07   4.7000000E+07

204  4.8000000E+07   4.9000000E+07   5.0000000E+07   5.1000000E+07

208  5.2000000E+07   5.3000000E+07   5.4000000E+07   5.5000000E+07

APPENDIX 3: Examples of NJOY-99.364+ inputs for FENDL-3.0

3.1 NJOY input option for Fe-56

moder / Extract/convert neutron evaluated data

1 -21

'26-Fe-56 for FENDL-3.0'/

20 2631

0/

moder / Extract/convert photo-atomic data

1 -41

'26-Fe-56 from FENDLE photo-atomic'/

40 2600

0/

reconr / Reconstruct XS for neutrons

-21 -22

'PENDF for 26-Fe-56'/

2631 2/

0.001 0. 0.002/

'26-Fe-56 from JEFF-3.1.1'/

'Processed by NJOY99.364+  on 20111125'/

0/

broadr / Doppler broaden XS

-21 -22 -23

2631 1 0 0 0./

0.001 2.0e7 0.002/

300.

0/

heatr / Add heating kerma and damage energy

-21 -23 -24 34/

2631 5 0 0 0 2/

302 304 404 443 444/

viewr / Plot energy balance from HEATR

34 32

gaspr / Add gas production

-21 -24 -25

purr / Process Unresolved Resonance Range if any

-21 -25 -26

2631 1 10 20 100/

300.

1.E+10 1.E+05 1.E+04 1.E+03 1.E+02 1.E+01 3.E+00 1.E+00 3.E-01 1.E-01

0/

acer / Prepare ACE files

-21 -26 0 27 28

1 0 1 .30/

'26-Fe-56 for FENDL-3.0 from JEFF-3.1.1 with NJOY99.364+  on 20111125'/

2631 300.

1 1/

/

acer / Check ACE files

0 27 34 29 30

7 1 1 -1/

/

viewr / Plot ACE cross sections

34 35

groupr / Prepare multigroup data for neutrons

-21 -26 0 31

2631 1 10 11 6 1 10 1/

'26-Fe-56 for FENDL-3.0 from JEFF-3.1.1 with NJOY99.364+  on 20111125'/

300.

1.E+10 1.E+05 1.E+04 1.E+03 1.E+02 1.E+01 3.E+00 1.E+00 3.E-01 1.E-01

211

1.0000100E-05   1.0000100E-01   4.1399401E-01   5.3157902E-01

6.8256003E-01   8.7642503E-01   1.1230000E+00   1.4400001E+00

1.8553900E+00   2.3823700E+00   3.0590200E+00   3.9278600E+00

5.0434799E+00   6.4759498E+00   8.3152905E+00   1.0677000E+01

1.3709600E+01   1.7603500E+01   2.2603300E+01   2.9023199E+01

3.7266499E+01   4.7851200E+01   6.1442101E+01   7.8893204E+01

1.0130100E+02   1.3007300E+02   1.6701700E+02   2.1445399E+02

2.7536401E+02   3.5357501E+02   4.5399899E+02   5.8294702E+02

7.4851801E+02   9.6111700E+02   1.2341000E+03   1.5846100E+03

2.0346801E+03   2.2486699E+03   2.4851699E+03   2.6125901E+03

2.7465400E+03   3.0353899E+03   3.3546299E+03   3.7074399E+03

4.3074199E+03   5.5308398E+03   7.1017402E+03   9.1188203E+03

1.0594600E+04   1.1708800E+04   1.5034400E+04   1.9304500E+04

2.1874900E+04   2.3578600E+04   2.4175500E+04   2.4787500E+04

2.6058400E+04   2.7000100E+04   2.8501100E+04   3.1827801E+04

3.4306699E+04   4.0867699E+04   4.6309199E+04   5.2475199E+04

5.6562199E+04   6.7379500E+04   7.2024500E+04   7.9498703E+04

8.2503398E+04   8.6517000E+04   9.8036500E+04   1.1109000E+05

1.1678600E+05   1.2277300E+05   1.2906800E+05   1.3568600E+05

1.4264200E+05   1.4995600E+05   1.5764400E+05   1.6572700E+05

1.7422400E+05   1.8315600E+05   1.9254700E+05   2.0241900E+05

2.1279700E+05   2.2370800E+05   2.3517700E+05   2.4723500E+05

2.7323700E+05   2.8724600E+05   2.9451800E+05   2.9721100E+05

2.9849100E+05   3.0197400E+05   3.3373300E+05   3.6883200E+05

3.8774200E+05   4.0762200E+05   4.5049200E+05   4.9787100E+05

5.2339700E+05   5.5023200E+05   5.7844300E+05   6.0810100E+05

6.3927900E+05   6.7205500E+05   7.0651200E+05   7.4273600E+05

7.8081700E+05   8.2085000E+05   8.6293600E+05   9.0718000E+05

9.6167200E+05   1.0025900E+06   1.1080300E+06   1.1648400E+06

1.2245600E+06   1.2873500E+06   1.3533500E+06   1.4227400E+06

1.4956900E+06   1.5723700E+06   1.6529900E+06   1.7377400E+06

1.8268400E+06   1.9205000E+06   2.0189700E+06   2.1224800E+06

2.2313000E+06   2.3069300E+06   2.3457000E+06   2.3653300E+06

2.3851300E+06   2.4659700E+06   2.5924000E+06   2.7253200E+06

2.8650500E+06   3.0119400E+06   3.1663700E+06   3.3287100E+06

3.6787900E+06   4.0657000E+06   4.4932900E+06   4.7236700E+06

4.9658500E+06   5.2204600E+06   5.4881200E+06   5.7695000E+06

6.0653100E+06   6.3762800E+06   6.5924100E+06   6.7032000E+06

7.0468800E+06   7.4081800E+06   7.7880100E+06   8.1873100E+06

8.6070800E+06   9.0483700E+06   9.5122900E+06   1.0000000E+07

1.0512700E+07   1.1051700E+07   1.1618300E+07   1.2214000E+07

1.2523200E+07   1.2840300E+07   1.3498600E+07   1.3840300E+07

1.4190700E+07   1.4549900E+07   1.4918200E+07   1.5683100E+07

1.6487200E+07   1.6904600E+07   1.7332500E+07   1.9640300E+07

2.0000000E+07   2.1000000E+07   2.2000000E+07   2.3000000E+07

2.4000000E+07   2.5000000E+07   2.6000000E+07   2.7000000E+07

2.8000000E+07   2.9000000E+07   3.0000000E+07   3.1000000E+07

3.2000000E+07   3.3000000E+07   3.4000000E+07   3.5000000E+07

3.6000000E+07   3.7000000E+07   3.8000000E+07   3.9000000E+07

4.0000000E+07   4.1000000E+07   4.2000000E+07   4.3000000E+07

4.4000000E+07   4.5000000E+07   4.6000000E+07   4.7000000E+07

4.8000000E+07   4.9000000E+07   5.0000000E+07   5.1000000E+07

5.2000000E+07   5.3000000E+07   5.4000000E+07   5.5000000E+07

3/

3  251 'mubar'/

3  252 'xi'/

3  253 'gamma'/

3  259 '1/v'/

6/

16/

0/

0/

reconr / Reconstruct photo-atomic data

-41 -42

'PENDF photo-atomic data for 26-Fe-56'/

2600 2/

0.001 0. 0.003/

'26-Fe-56 from ENDF/B-VI'/

'Processed by NJOY99.364+  on 20111125'/

0/

gaminr / Prepare multigroup data for photons

-41 -42 0 43/

2600 10 3 6 1/

'26-Fe-56 for FENDL-3.0 from JEFF-3.1.1 with NJOY99.364+  on 20111125'/

-1/

0/

matxsr / Produce MATXS file

31 43 44/

1 'FENDL-3.0fe56'/

2 3 3 1

'26-Fe-56 FENDL-3.0 from JEFF-3.1.1'/

'Photo-atomic data from ENDF/B-VI'/

'Processed by NJOY99.364+  on 20111125'/

'n' 'g'/

211  42

'nscat' 'ng' 'gscat'/

1 1 2/

1 2 2/

'fe56' 2631 2600/

stop

3.2 NYOY input option for W-184

moder / Extract/convert neutron evaluated data

1 -21

'74-W-184 for FENDL-3.0'/

20 7437

0/

moder / Extract/convert photo-atomic data

1 -41

'74-W-184 from FENDLE photo-atomic'/

40 7400

0/

reconr / Reconstruct XS for neutrons

-21 -22

'PENDF for 74-W-184'/

7437 2/

0.001 0. 0.002/

'74-W-184 from INDL/V-3'/

'Processed by NJOY99.364+  on 20111125'/

0/

broadr / Doppler broaden XS

-21 -22 -23

7437 1 0 0 0./

0.001 2.0e7 0.002/

300.

0/

heatr / Add heating kerma and damage energy

-21 -23 -24 34/

7437 5 0 0 0 2/

302 304 404 443 444/

viewr / Plot energy balance from HEATR

34 32

gaspr / Add gas production

-21 -24 -25

purr / Process Unresolved Resonance Range if any

-21 -25 -26

7437 1 10 20 100/

300.

1.E+10 1.E+04 1.E+03 3.E+02 1.E+02 3.E+01 1.E+01 1.E+00 1.E-01 1.E-03

0/

acer / Prepare ACE files

-21 -26 0 27 28

1 0 1 .30/

'74-W-184 for FENDL-3.0 from INDL/V-3 with NJOY99.364+  on 20111125'/

7437 300.

1 1/

/

acer / Check ACE files

0 27 34 29 30

7 1 1 -1/

/

viewr / Plot ACE cross sections

34 35

groupr / Prepare multigroup data for neutrons

-21 -26 0 31

7437 1 10 11 6 1 10 1/

'74-W-184 for FENDL-3.0 from INDL/V-3 with NJOY99.364+  on 20111125'/

300.

1.E+10 1.E+04 1.E+03 3.E+02 1.E+02 3.E+01 1.E+01 1.E+00 1.E-01 1.E-03

211

1.0000100E-05   1.0000100E-01   4.1399401E-01   5.3157902E-01

6.8256003E-01   8.7642503E-01   1.1230000E+00   1.4400001E+00

1.8553900E+00   2.3823700E+00   3.0590200E+00   3.9278600E+00

5.0434799E+00   6.4759498E+00   8.3152905E+00   1.0677000E+01

1.3709600E+01   1.7603500E+01   2.2603300E+01   2.9023199E+01

3.7266499E+01   4.7851200E+01   6.1442101E+01   7.8893204E+01

1.0130100E+02   1.3007300E+02   1.6701700E+02   2.1445399E+02

2.7536401E+02   3.5357501E+02   4.5399899E+02   5.8294702E+02

7.4851801E+02   9.6111700E+02   1.2341000E+03   1.5846100E+03

2.0346801E+03   2.2486699E+03   2.4851699E+03   2.6125901E+03

2.7465400E+03   3.0353899E+03   3.3546299E+03   3.7074399E+03

4.3074199E+03   5.5308398E+03   7.1017402E+03   9.1188203E+03

1.0594600E+04   1.1708800E+04   1.5034400E+04   1.9304500E+04

2.1874900E+04   2.3578600E+04   2.4175500E+04   2.4787500E+04

2.6058400E+04   2.7000100E+04   2.8501100E+04   3.1827801E+04

3.4306699E+04   4.0867699E+04   4.6309199E+04   5.2475199E+04

5.6562199E+04   6.7379500E+04   7.2024500E+04   7.9498703E+04

8.2503398E+04   8.6517000E+04   9.8036500E+04   1.1109000E+05

1.1678600E+05   1.2277300E+05   1.2906800E+05   1.3568600E+05

1.4264200E+05   1.4995600E+05   1.5764400E+05   1.6572700E+05

1.7422400E+05   1.8315600E+05   1.9254700E+05   2.0241900E+05

2.1279700E+05   2.2370800E+05   2.3517700E+05   2.4723500E+05

2.7323700E+05   2.8724600E+05   2.9451800E+05   2.9721100E+05

2.9849100E+05   3.0197400E+05   3.3373300E+05   3.6883200E+05

3.8774200E+05   4.0762200E+05   4.5049200E+05   4.9787100E+05

5.2339700E+05   5.5023200E+05   5.7844300E+05   6.0810100E+05

6.3927900E+05   6.7205500E+05   7.0651200E+05   7.4273600E+05

7.8081700E+05   8.2085000E+05   8.6293600E+05   9.0718000E+05

9.6167200E+05   1.0025900E+06   1.1080300E+06   1.1648400E+06

1.2245600E+06   1.2873500E+06   1.3533500E+06   1.4227400E+06

1.4956900E+06   1.5723700E+06   1.6529900E+06   1.7377400E+06

1.8268400E+06   1.9205000E+06   2.0189700E+06   2.1224800E+06

2.2313000E+06   2.3069300E+06   2.3457000E+06   2.3653300E+06

2.3851300E+06   2.4659700E+06   2.5924000E+06   2.7253200E+06

2.8650500E+06   3.0119400E+06   3.1663700E+06   3.3287100E+06

3.6787900E+06   4.0657000E+06   4.4932900E+06   4.7236700E+06

4.9658500E+06   5.2204600E+06   5.4881200E+06   5.7695000E+06

6.0653100E+06   6.3762800E+06   6.5924100E+06   6.7032000E+06

7.0468800E+06   7.4081800E+06   7.7880100E+06   8.1873100E+06

8.6070800E+06   9.0483700E+06   9.5122900E+06   1.0000000E+07

1.0512700E+07   1.1051700E+07   1.1618300E+07   1.2214000E+07

1.2523200E+07   1.2840300E+07   1.3498600E+07   1.3840300E+07

1.4190700E+07   1.4549900E+07   1.4918200E+07   1.5683100E+07

1.6487200E+07   1.6904600E+07   1.7332500E+07   1.9640300E+07

2.0000000E+07   2.1000000E+07   2.2000000E+07   2.3000000E+07

2.4000000E+07   2.5000000E+07   2.6000000E+07   2.7000000E+07

2.8000000E+07   2.9000000E+07   3.0000000E+07   3.1000000E+07

3.2000000E+07   3.3000000E+07   3.4000000E+07   3.5000000E+07

3.6000000E+07   3.7000000E+07   3.8000000E+07   3.9000000E+07

4.0000000E+07   4.1000000E+07   4.2000000E+07   4.3000000E+07

4.4000000E+07   4.5000000E+07   4.6000000E+07   4.7000000E+07

4.8000000E+07   4.9000000E+07   5.0000000E+07   5.1000000E+07

5.2000000E+07   5.3000000E+07   5.4000000E+07   5.5000000E+07

3/

3  251 'mubar'/

3  252 'xi'/

3  253 'gamma'/

3  259 '1/v'/

6/

16/

0/

0/

reconr / Reconstruct photo-atomic data

-41 -42

'PENDF photo-atomic data for 74-W-184'/

7400 2/

0.001 0. 0.003/

'74-W-184 from ENDF/B-VI'/

'Processed by NJOY99.364+  on 20111125'/

0/

gaminr / Prepare multigroup data for photons

-41 -42 0 43/

7400 10 3 6 1/

'74-W-184 for FENDL-3.0 from INDL/V-3 with NJOY99.364+  on 20111125'/

-1/

0/

matxsr / Produce MATXS file

31 43 44/

1 'FENDL-3.0w184'/

2 3 3 1

'74-W-184 FENDL-3.0 from INDL/V-3'/

'Photo-atomic data from ENDF/B-VI'/

'Processed by NJOY99.364+  on 20111125'/

'n' 'g'/

211  42

'nscat' 'ng' 'gscat'/

1 1 2/

1 2 2/

'w184' 7437 7400/

stop

| Nuclear Data Section International Atomic Energy Agency P.O. Box 100 A-1400 Vienna Austria | e-mail: services@iaeand.iaea.org fax: (43-1) 26007 cable: INATOM VIENNA telex: 1-12645 telephone: (43-1) 2600-21710 |
| --- | --- |
|  | Online: TELNET or FTP: iaeand.iaea.org username: IAEANDS for interactive Nuclear Data Information System usernames: ANONYMOUS for FTP file transfer; FENDL2 for FTP file transfer of FENDL-2.0; RIPL for FTP file transfer of RIPL; NDSONL for FTP access to files saved in “NDIS” Telnet session. Web: http://www-nds.iaea.org |  |

# Text boxes

_________      __      ________________________________________________________________________________________________________

I N D C  INTERNATIONAL NUCLEAR DATA COMMITTEE

_____________________________________________________________________________________________________________________

INTERNATIONAL ATOMIC ENERGY AGENCY

INDC(NDS)-XXXX

Distr. FE

FENDL/E-3.0

Neutron data

MODER

RECONR

BROADR

HEATR

GASPR

PURR

ACER

(create ACE file)

ACER

(check ACE file)

GROUPR

(n-multigroup data)

RECONR

GAMINR

(γ-multigroup data)

MATXSR

(create MATXS file)

Figure 1: NJOY processing sequence for FENDL/MC-3.0 and FENDL/MG-3.0.

MODER

FENDL/E-3.0

Photo-atomic

FENDL/MC-3.0

FENDL/MG-3.0