Global Assessment of Nuclear Data
(GANDR Project )

Volume 3. GANDR Programs GAPREP,
GAPOST and GABROW

D. W. Muir

Revision 4: 28 November 2011

ABSTRACT

This is part of a series of documents related to the Global Assessment of Nuclear Data (GANDR project). This report contains a brief description of the programs GAPREP, GAPOST and GABROW. These programs, together with the generalized least squares solver ZOTTVL, described in Volume 2, make up the primary suite of computer programs employed in the GANDR system.
TABLE OF CONTENTS

3-I. Introduction	-------------------------------------------------------------------------------------	3-3

3-II. General Considerations: The Evaluation Model	-----------------------------------------	3-3

3-III. Evaluation Methodology	-------------------------------------------------------------------	3-4

3-IV. Impact of Non-Linearities	-----------------------------------------------------------------	3-5

3-V. Treatment of Offsets	-------------------------------------------------------------------------	3-7

3-VI. Initialization of Parameters and Covariances	-------------------------------------------	3-7

3-VII. Re-Initialization of Subsequent Outer Iterations	--------------------------------------	3-8

3-VIII. Test Facility for Gauss-Newton Iteration	----------------------------------------------	3-8

3-IX. Relation Between the Codes: GAPREP	-------------------------------------------------	3-8

3-X. Relation Between the Codes: The GANRUN Controller	------------------------------	3-10

3-XI. Codes Controlled by GANRUN: ZOTTVL, GAPOST and PLOTR	----------------	3-10

3-XII. Interactive Data Browser GABROW	----------------------------------------------------	3-13

References	-------------------------------------------------------------------------------------------	3-15

          1. LIST OF FIGURES

Fig. 3-1. Plot from GANDR W-184 Example	-------------------------------------------------	3-11

3-I. Introduction

The primary suite of computer programs employed in the GANDR system consists of the generalized least squares evaluation-update program ZOTTVL, as well as a number of special pre-processing and post-processing programs. Programs included in this second category include the GAPREP code, which prepares a complete input deck for ZOTTVL, the GAPOST code, which post-processes the output data from ZOTTVL to prepare plots, etc., and the GABROW code, which permits the browsing of individual lines of data in both the pre-update and post-update versions of the binary GANDR library.

The present chapter explains the purpose and logical structure of the GANDR computer programs. In explaining the techniques they employ to carry out this purpose, it is necessary to begin by reviewing some basic definitions and assumptions. We then explore the inter-relationship of the programs through the use of a simple, representative example.

3-II. General Considerations: The Evaluation Model

A number of fundamental principles and assumptions guide the GANDR evaluation process. The first is the assumption that it is possible to identify a data evaluation of relevant nuclear data that is suitable to serve as the "basis" evaluation for the entire evaluation procedure. For reasons discussed below, the basis evaluation should be widely available, as complete as possible, reasonably detailed, and rather accurate. In recent applications of the GANDR system, we have chosen ENDF/B-VII.0 as the basis, but other choices are clearly possible.

To understand the role of the basis evaluation, consider a particular physical quantity, such as the neutron capture cross section of Al-27. Let us denote by σbas(E) the energy-dependent cross section for this reaction in the basis evaluated data file. In the GANDR evaluation framework, we assume that the true value of the cross section can be obtained from the basis cross section by applying an energy-dependent correction factor Atrue(E),

σtrue(E) = Atrue(E) σbas(E)

In GANDR we limit consideration of such correction functions to continuous, piecewise-linear functions, defined on a fixed energy grid.

We next introduce a set of discrete parameters a(n). Also, we denote by H(n,E) the n-th unit "hat" function, defined in Appendix 1A in Volume 1. Then the energy-dependent correction functions A(E) mentioned above are related to the GANDR parameters via the following summation:

A(E) = Σ a(n) H(n,E)
n
The summation here extends over one of the three standard GANDR energy grids. The number of grid points depends on the material under consideration. As discussed in Volume 1, there are 74 grid points for most of the common materials widely used in nuclear applications, 56 grid points for resonance absorbers and 28 for fission products. (For some important materials, the basis evaluation contains so much information on partial reactions that, due to storage limitations, the normal 74-node grid has to be considerably coarsened, for example down to just 46 nodes for Pb-208.) The reason that we can accept such coarse grids is that our basis evaluation is already fairly accurate. Because of this accuracy, the role of the continuous function A(E) is limited to applying a limited number of small, “fine tuning” type changes to this starting data evaluation.

In the GANDR evaluation process, we assume that all uncertainty resides in the magnitude of the dimensionless parameters a(n) just defined. In the GANDR project, we employ minimum variance estimation, as implemented in the ZOTTVL program to refine our knowledge of the parameters a(n) and to determine their uncertainties and correlations, that is, their covariances, based on a comparison of the evaluation model explained above with experimental data.

3-III. Evaluation Methodology

As discussed in detail in Volume 2, ZOTTVL takes an existing set of parameters a and updates them by confronting them with a set of measurements b. In this Chapter, the boldface symbols a and b denote column vectors of dimension na (the number of parameters) and nb (the number of measurements), respectively. From a and b and their assessed uncertainties, together with an nb-row×na-column sensitivity matrix R relating the measurements to the parameters, ZOTTVL calculates a new set of parameters a' that makes optimal use of all input information. We introduce the symbol Z to indicate the operation performed by ZOTTVL to produce the adjusted data set a'.

a' = Z(a, b, R)	(1)

In the GANDR process, the experimental data b is grouped into nk data blocks bk, where general correlations may exist between the measurement results within a single block, but no correlations are allowed between blocks. Under these conditions the adjusted parameters from processing the first block can be treated as a direct measurement of a for input to the second stage of adjustment, and so, thereby forming an "inner iteration," of nk steps with fixed sensitivities R,

a'k = Z(ak, bk, R) , where	(2)

ak = a'k-1 for k = 2 to nk	(3)

Initiation of this process clearly requires choosing a "prior" evaluation a1 of the parameter set. The GANDR system allows two different approaches to be applied. For the purpose of making a global survey of data uncertainties, which was the original purpose of the GANDR system, it is acceptable to work with the GANDR default initialization procedure. This procedure assumes that our knowledge of the nuclear data, prior to introduction of the first real experimental information, consists of a single "pseudo-measurement" and that the results of that measurement are identical to the data contained in the basis evaluation, σpri(E) = σbas(E). We are free to make this arbitrary, but convenient, choice for the prior data evaluation, because we also assume that these prior data have very large, uncorrelated uncertainties. Because of the large uncertainties, the actual values chosen for σpri(E) will not significantly influence the final evaluated data values following the introduction of the nk blocks of real measurements bk.

As a consequence of the identification σpri(E) with σbas(E), the a priori value of the correction factor Apri(E) is unity for all GANDR materials, reaction types and incident neutron energies. Put another way, the prior values of the parameters apri(n) are all unity, since

Apri(E) = Σ apri(n) H(n,E) = Σ H(n,E) = 1
n	n

Model-Generated Prior Covariances
An alternative initialization approach, implemented fairly recently in the GANDR system and extensively improved in version GANDR-4.4, is to assume that the parameter values are initialized at the nominal values of unity, as above, but establishes the prior covariances of the parameters using a nuclear model code such as EMPIRE (Ref. 1). This is the recommended path to follow when GANDR is being used to produce a high-quality evaluation for a single nuclide or a small number of neighboring nuclides. The use of model-generated covariances places strong constraints on the least-squares solution for the parameters, especially in areas where the experimental data is sparse.

Generally speaking, such constraints are beneficial, because they avoid unphysical irregularities in the shape of the evaluated data. However, care needs to be exercised when using this approach, in order to avoid obtaining unrealistically low final covariances. This means, in particular, to include all significant sources of modeling uncertainty in the prior, even those which may be difficult to describe quantitatively.

3-IV. Impact of Non-linearities

We next need to address the additional complexity introduced by non-linearities. In those parts of the evaluation exercise where the input measurement data are strictly linear functions of the parameters (for example, measured total cross sections), the parameter sensitivities are independent of the parameter values.

However, it is planned that the input data will also include accurate measurements of complex integral quantities such as a critical masses. In these cases, the parameter sensitivities R exhibit a moderate dependence on the nuclear data being evaluated. In describing the recommended procedures, we shall follow the notation introduced in Appendix 1A of Volume 1 and denote by aref the point in the GANDR parameter space where the parameter sensitivities were most recently calculated.

To expand somewhat on the relation between parameters and sensitivities, the calculation of sensitivities using perturbation theory in the usual way requires the calculation of neutron fluxes using multigroup neutron transport codes. We can employ the reference parameters aref to obtain the reference evaluated nuclear data σref ,
σref (E) = Aref(E) σbas(E) = Σ aref(n) H(n,E) σbas(E)	(4)
n
and these data can, in turn, be processed to construct the multigroup cross section library for these neutronics and perturbation-theory calculations.

Because of the considerable labor involved in a re-calculation of the sensitivities, it is recommended that the sensitivity matrix be treated as a constant quantity throughout the first processing with ZOTTVL of all of the blocks of data, as shown in Eqs. (2) and (3). However, once this sequence is completed, the sensitivities R can be re-calculated using the final, improved parameters from the evaluation exercise. These updated sensitivities, can then be used to repeat the entire process, starting from the first data block. We shall refer to this procedure as introducing an "outer iteration" to the evaluation process. In the statistics literature, such a process is described as a “Gauss-Newton” iteration.

Let us assume that the first complete pass through all available measurement data using the ZOTTVL program leads us from the prior data set apri to the generation of "first round" adjusted data set aadj. It is common practice to employ this adjusted set aadj as an updated reference point aref for the re-calculation of sensitivities for a second pass through all the data. If non-linearities are present, this will yield a new solution point aadj. This process should be repeated until aadj does not change from one iteration to the next. The solution can then be said to be converged. This process is known as Gauss-Newton Iteration. The evolution of the reference parameter set during the outer iteration process can be represented as follows:

aref,1 = apri	(5)

aref,j = aadj,j-1 for j = 2 to nj	(6)

In practical applications, this iteration process generally does converge rapidly, so that the first-order Taylor series expansion,

badj,j – bref,j = R(aref,j) [ aadj,j – aref,j ]	(7)

becomes highly accurate after just a few iterations. Here badj denotes the vector of observables as calculated in a full (non-linear) calculation at aadj, and bref denotes the observables calculated similarly at aref.

As indicated in Eq. (5), for the first outer iteration, aref,1 will be set equal to apri. However, in subsequent outer iterations, the two quantities will differ, with aref,j approaching aadj,j while apri remains fixed.

3-V. Treatment of Offsets

The coding of ZOTTVL requires a strict linear relationship between the true values of the data and parameter vectors,

btrue = R atrue	(8)

Comparison of Eqs. (7) and (8) makes it clear that the measurements b that need to be supplied as input to the ZOTTVL code, for example in Eqs. (1) - (3), are actually the differences from the corresponding reference values.

b = bmeas - bref	(9)

The ZOTTVL program does not allow a separate input of the reference values discussed at length above. Thus, the application of the "offsets" to bmeas, according to Eq. (9), are performed external to ZOTTVL in the program GAPREP, which has been developed specifically for the GANDR project. In particular, the calculation of bref is performed in subroutine GETBSE.

3-VI. Initialization of Parameters and Covariances

In general, the parameters a also require a consideration of offsets. During the execution of one pass through the GANDR inner iteration sequence (that is, with a fixed reference set aref), the first set of parameters supplied as input to ZOTTVL (recalling the discussion of Section III above) will be

a1 = apri - aref	(10)

Since the reference set will be taken initially to be equal to the prior set (both being equal to unity), this means that the parameter vector will be initialized at zero at the beginning of the first outer iteration. These pre-sets are accomplished in subroutine INITA of the GAPREP program. The initialization of the parameter covariance matrix is performed by the similar subroutine INITCA and INITCB of GAPREP. See the following section for a description of the initialization of subsequent iterations.

Because of logical structure of the code, the adjusted parameter vector a' subsequently produced and output by ZOTTVL implicitly includes the offset,

a' = aadj - aref	(11)

Referring back to the GANDR "inner iteration" sequence described above in Eqs. (2) and (3), we see from Eq. (11) that the adjusted parameters a'1 generated by processing of the first block of measurements will already be in the correct (relative) form to be used as the input parameters a2 for processing the second block, and so on.
3-VII. Re-Initialization of Subsequent Outer Iterations

After all data sets are processed with ZOTTVL, with the final adjusted data result a'nk having been written to disk by the code, we are ready to initiate a new outer iteration. To do this, we need to re-set the reference set for the calculations to a new set âref equal to the final adjusted data result obtained with the previous reference set,

âref = aadj,nk = a'nk + aref	(12)

Because of the relocation of the reference point, one must introduce a new set of starting parameters â1 in order to reflect the new offsets.

â1 = apri - âref	(13)

Compare Eq. (13) with, for example, Eq. (10). The re-initialization operations shown in Eqs. (12) and (13) are performed in subroutine RENITA of GAPREP. When a new outer iteration is initiated using RENITA, the GAPREP code also resets the parameter covariances to the appropriate “prior” state using subroutine INITCA and INITCB.

As mentioned previously, in treating complex integral data (meaning data for which the analysis requires non-trivial neutron transport calculations), one will also need at this point to use the new reference set âref to recalculate the multigroup cross section library, the neutron fluxes, and the sensitivity matrices.

3-VIII. Test Facility for Gauss-Newton Iteration

As a convenient facility for testing the Gauss-Newton logic in GAPREP, the program contains the internal capability of introducing a non-linear model, namely,

A(E) = Σ [a(n)]iltest H(n,E) .	(14)
n
The power-law exponent iltest is a user-input parameter. Choosing iltest = 1 requests the normal GANDR parametrization. iltest = 2 is a convenient choice for demonstrating the Gauss-Newton capability of the program.

3-IX. Relation Between the Codes: GAPREP

The relation between the different GANDR programs is best demonstrated by discussing a simple example. The procedure for performing a GANDR evaluation update normally begins with the user changing the directory /usr/work (the normal working directory) and then creating a short script, such as the following:

echo yes > permit
gaprep.x << EOF
 12 0 1 2/ imode,inopt,ipick,idef,iprint,iredo,iloop,xneg
 74184 1/ matnam,mtplot
 / igrid,imoc,ipend,inmt5,iltest (select default grid)
 1/ mte,mfe,idx1,idx2 (retrieve the data for mte=1 from master EXFOR library)
 1/ listex(i) (select EXFOR data set no. 1, by K. Knopf, et al.)
 0 0 0/ inca,covmin,irelco,isys,iglobl (standard uncertainty treatment)
EOF
chmod u+x ganrun
ganrun

The first line here is recommended to be used as the first line of any GANDR UNIX script. It properly initializes the GANDR facility for “fail-safe” operation. This refers to the fact that. if one of the GANDR programs fails during the execution of a complex script, execution will be blocked for all remaining GANDR programs in the script. This prevents the generation of a flood of uninformative error messages and helps protect the integrity of existing data files.

The next line of the user's script launches the executable of the important GAPREP code. In addition to performing the parameter and covariance initialization operations just discussed, GAPREP also produces a complete set of input data for the ZOTTVL code described Volume 2. In this case, this requires calculating and applying the appropriate "offsets" to the four Knopf measurements and computing the sensitivities of these measurements to each of the 692 GANDR parameters for W-184.

The purpose of the each of the GAPREP input instructions appearing on the next several lines are explained in detail in Volume 4 in this series. That report also provides complete scripts for a more realistic set of sample problems. For the present purposes, it is necessary only to note that the "KNOPF" data set contains measurements of the W-184 total cross section at four neutron energies.

There is little need for code users to dwell on the details of the ZOTTVL input format, since this input is prepared completely automatically by GAPREP. However, for the sake of completeness, we list below the contents of zottvl.in, which is the ZOTTVL input file for this simple 4-measurement example.

     4 700 1 0 1 9999 1.0000E+08 -1.0000E+06/ nb,na,nmat, iprint,istart,istop,tl,xneg
# ZOTTVL input for GANDR system
 -5.00273940E+00 2.87415824E+00 2.69584421E+00 -4.95456010E-01
74184
        3*0.00000000E+00 3.03020350E+00 1.78832910E+00
      586*0.00000000E+00 7.34778143E+00 4.33642537E+00
      107*0.00000000E+00
*****
74184
       18*0.00000000E+00 2.83713074E+00 1.42327474E+00
      586*0.00000000E+00 1.50124726E-01 7.53115558E-02
       92*0.00000000E+00
*****
74184
       20*0.00000000E+00 7.38309030E-01 3.45417614E+00
      586*0.00000000E+00 1.61434673E-02 7.55271535E-02
       90*0.00000000E+00
*****
74184
       41*0.00000000E+00 2.23046675E+00 6.19201325E+00
      347*0.00000000E+00 4.82770969E-02 1.34022363E-01
      237*0.00000000E+00 2.40132395E-02 6.66633105E-02
       69*0.00000000E+00
*****
# Covariance matrix for GANDR evaluation update
 1 4 /
 6.40000000E-01 /
 9.00000000E-02 /
 4.00000000E-02 /
 2.50000000E-01 /

3-X. Relation Between the Codes: The GANRUN Controller

From the viewpoint of the code user, it is more important to discuss the the contents of the GANRUN “run-time” controller script. The script for our short example is listed below. As can be seen there, the script controls the core functions of the GANDR evaluation process. Further information on these core functions is provided in Section 3-XI below. Note that the EVINCE utility is an open-source PostScript viewer that is supplied with Fedora Linux.

 mkdir -p 0012.0000.74184
 sort names.ztv > names.zottvl
 zottvl.x2 < zottvl.in
 mv zottvl.out.* zottvl.out
 gapost.x
 xnjoy < plotr.in
 mv tape32 gapost.ps
 evince gapost.ps
 mv tape5* 0012.0000.74184
 mv tape6* 0012.0000.74184
 mv tape7* 0012.0000.74184
 mv plotr.in 0012.0000.74184
 mv output 0012.0000.74184
 cp gapost.ps 0012.0000.74184
 mv names.zottvl 0012.0000.74184
 cp names.gapost 0012.0000.74184
 cp ganrun 0012.0000.74184
 mv gaprep.out 0012.0000.74184
 mv zottvl.in 0012.0000.74184
 mv zottvl.out 0012.0000.74184
 mv gapost.out 0012.0000.74184
 cp /usr/gandr/zott/list/74184 0012.0000.74184/list
 tail -4 gandr.log

3-XI. The Codes ZOTTVL, GAPOST and PLOTR

When the GANRUN script is invoked, the first action that takes place is that the ZOTTVL program is executed using the GAPREP-prepared input file zottvl.in. After ZOTTVL, the GAPOST code is executed. This program performs two basic post-processing functions on the updated evaluated data produced by ZOTTVL. First, it produces an output listing of the adjustment on file gapost.out. It also produces an interpreted listing of the updated data on the file list. In Volume 4 of this series, one can find examples the listings produced by GAPOST, as well as a brief explanation of the format of the interpreted listings.

Second, since output plots have been requested here (iprint = 0), GAPOST reconstructs numerical tables of the total cross section, based on both prior and adjusted values of the GANDR parameters. To help enforce internal consistency, GAPOST uses the same logical steps as GAPREP and a shared Fortran subroutine library. GAPOST then prepares a full input file plotr.in for plotting these reconstructed curves using the NJOY-PLOTR module. From this input PLOTR, in turn, produces PostScript plots (gapost.ps) with side-by-side comparisons of the basis evaluation and the newly evaluated data for this isotope. If all goes well, execution of the GANRUN script should result in the display of plots similar to the screenshot below appearing on the user's computer screen. One can use the EVINCE “next” and “previous” buttons to scroll through linear, logarithmic, and semi-log plots of the data.

Fig. 3-1. Plot from GANDR W-184 Example

Following execution of the programs ZOTTVL, GAPOST and PLOTR, the GANRUN script completes the current GANDR update run by making a directory to store the output graphics and listings and then moving the relevant files to that directory.

In the execution of a “stack” of GANRUN scripts, one such output directory is created or accessed for each execution of GAPREP. The actual name of the output directory (here, (0012.0000.74184) is built automatically by the program, based on seven key GAPREP input parameters (inopt, ipick, idef, iprint, igrid, imoc and ipend) plus the material name 74184 of the material of interest. Note that ipick is allocated two spaces in the directory name, “01” here, because it occasionally has a value greater than 9.
In realistic applications, one will need to perform a whole series of GANDR updates. In such a series, each update will involve the execution of a script similar to our example. These scripts may be executed individually or "stacked" together to make a much longer script. In such a sequence of updates, the set of input parameters listed above (especially inopt) will change to some extent for each invocation of the GAPREP code. The directory-naming convention described in the previous paragraph prevents the output from one update from being overwritten by the output of a later update in the stack.

The final line of the GANRUN script, tail -4 gandr.log, displays the final records of the GANDR history log to indicate the time and date of the most recent runs and the name of the corresponding output directories. After two executions of our short sample problem, once with W-186 as the targeted nuclide and once with W-184, the final lines of gandr.log are as follows:

 GANDR-4.3 preprocessing complete at 10:34:21 on 11/28/11.
 Output directory: 0012.0000.74186
 GANDR-4.3 postprocessing complete at 10:34:33 on 11/28/11

 GANDR-4.3 preprocessing complete at 10:52:06 on 11/28/11.
 Output directory: 0012.0000.74184
 GANDR-4.3 postprocessing complete at 10:52:19 on 11/28/11

This short display makes it very convenient to examine the actual output of the most recent runs. For example, one can now change directory to the last-mentioned output directory. In that directory, one can open, for example, the file gapost.out with a text editor. Below is an extract of this particular output file showing the effect of the evaluation update on the elastic scattering cross sections (MT=2) for W-174 at low energies, resulting from the incorporation of the Knopf et al. measurement of the total. Note that, since we have executed GANDR in the original or “survey” mode, each data point effects only the two nearest nodal values of the cross sections, a point that is also clear from the data plot previously mentioned. The two lines shown in bold red refer to the “bumps” in the adjusted data appearing in the plot at 1 and 5.62 eV.

...
...
...

 GANDR reaction index (ire) 1
 ENDF index of final component of reaction ire 2
 Parameter index of threshold node for ire 1
 Parameter index of highest-energy node for ire 74

 Grid index/energy Param index/adjusted value/uncertainty
 ----------------- --------------------------------------
    1 1.00000E-05 1 1.00000E+00 1.00000E+00
    2 3.16228E-05 2 1.00000E+00 1.00000E+00
    3 1.00000E-04 3 1.00000E+00 1.00000E+00
    4 3.16228E-04 4 8.23348E-01 9.44987E-01
    5 1.00000E-03 5 8.95746E-01 9.81189E-01
    6 1.77828E-03 6 1.00000E+00 1.00000E+00
    7 3.16228E-03 7 1.00000E+00 1.00000E+00
    8 5.62341E-03 8 1.00000E+00 1.00000E+00
    9 1.00000E-02 9 1.00000E+00 1.00000E+00
   10 1.58489E-02 10 1.00000E+00 1.00000E+00
   11 2.53000E-02 11 1.00000E+00 1.00000E+00
   12 3.54813E-02 12 1.00000E+00 1.00000E+00
   13 5.01187E-02 13 1.00000E+00 1.00000E+00
   14 7.07946E-02 14 1.00000E+00 1.00000E+00
   15 1.00000E-01 15 1.00000E+00 1.00000E+00
   16 1.77828E-01 16 1.00000E+00 1.00000E+00
   17 3.16228E-01 17 1.00000E+00 1.00000E+00
   18 5.62341E-01 18 1.00000E+00 1.00000E+00
   19 1.00000E+00 19 1.79998E+00 4.58615E-01
   20 1.77828E+00 20 1.40132E+00 8.95136E-01
   21 3.16228E+00 21 1.15894E+00 9.77993E-01
   22 5.62341E+00 22 1.74362E+00 2.17257E-01
   23 1.00000E+01 23 1.00000E+00 1.00000E+00
   24 1.77828E+01 24 1.00000E+00 1.00000E+00
   25 3.16228E+01 25 1.00000E+00 1.00000E+00
...
...
...

While in the mentioned output directory one can also re-visit the data plot by typing “evince gapost.ps.”

3-XII. Interactive Data Browser GABROW

The effect of the evaluation process is summarized in a variety of ways in the list and plot files described above. However, occasionally one needs to be able to view the actual GANDR library files, that is, the parameter vector a and the large covariance matrix D(a), including off-diagonal elements of the covariance matrix. However, there is a difficulty here. These data files are read from disk, updated, and written back out, always in binary format. The prevents casual inspection of a and D(a) using a text editor. To meet the need to “browse” the GANDR library data, the auxiliary code GABROW is provided.

Below is an illustration of an interactive session in which GABROW is invoked, first to display the final adjusted parameter values. In the program prompt below, adjusted parameter values are referenced using the shorthand notation “ap”. Hence, the desired data type is “3”. From GABROW code output shown below (a large number of trailing data lines are deleted for convenience), it can be seen that parameters 19 and 20 (the cross section multipliers for MT=2 at 1 and 1.77828 eV, respectively) have been adjusted upward from their initial values of zero to 0.80 and 0.40, respectively. (See the bold red entries.) These adjustments reflect the impact of the second Knopf data point, which is significantly higher than the basis evaluation, ENDF/B-VII.0.

User Input
gabrow.x

Program Prompt:
 Enter iopt (1/2/3/4/5/6/7 = a/caa/ap/caap/aref/r/modcov)
 and material name [92235] or / to quit

User Input
3 74184

Program Output:
 1.1E-12 1.1E-12 1.1E-12-1.8E-01-1.0E-01 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12
 1.1E-12 1.1E-12 1.1E-12 8.0E-01 4.0E-01 1.6E-01 7.4E-01 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12 1.1E-12
...
...
...

Knowing that parameters 19 and 20 have been strongly adjusted away from their initial values of zero, the user may wish to request a display of the 19th and 20th lines of the final covariance matrix (caap), data type = 4. Since the matrix is symmetric, in accommodating this request the program displays one row of the upper right triangle of the matrix, starting with the diagonal element.

Program Prompt:
 Enter iopt (1/2/3/4/5/6/7 = a/caa/ap/caap/aref/r/modcov)
 and material name [92235] or / to quit

User Input:
4 74184

Program Prompt:
 Enter second material name or / for self-covariances

User Input:
/

Program Prompt:
 Enter row index of symmetric matrix to print, -1 to read in full matrix, or / to go back

User Input:
19

Program Output:
 Row 19 of covariance matrix
 2.1E-01-4.0E-01-1.9E-13 4.5E-14-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13
-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-1.4E-13 5.8E-14-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13
-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13-2.5E-13
...
...
...

Program Prompt:
 Enter row index of symmetric matrix to print, -1 to read in full matrix, or / to go back

User Input:
20

Program Output:
 Row 20 of covariance matrix
 8.0E-01 2.8E-13-6.8E-14 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13
 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 2.1E-13-8.8E-14 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13
 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13 3.7E-13
...
...
...

From the above results (again, see bold red entries), the sub-block of the adjusted covariance matrix involving parameters 19 and 20 is, then,

2.1E-01	-4.0E-01
-4.0E-01	8.0E-01

In this adjustment example we have gained a substantial improvement in the accuracy of the two mentioned parameters, relative to their large a priori variances of 1.0. However, as expected, this reduction in uncertainty is accompanied by the introduction of large negative correlations.

The final few input entries terminate the GABROW retrieval operation.

Program Prompt:
 Enter row index of symmetric matrix to print, -1 to read in full matrix, or / to go back

User Input:
/

Program Prompt:
 Enter iopt (1/2/3/4/5/6/7 = a/caa/ap/caap/aref/r/modcov)
 and material name [74184] or / to quit

User Input:
/

We leave it as an exercise for the reader to compare the adjusted data presented immediately above (i.e., parameters 19 and 20 plus their covariance sub-matrix) with corresponding information extracted in Section 3-XI from the file gapost.out. In carrying out this comparison, it is important to recall that the adjusted parameters a' stored in the GANDR library are actually differences between the adjusted parameters aadj and the reference parameters aref, as detailed earlier in Eq. (11). That result can be re-arranged as

aadj = a' + aref	(15)
The GABROW code displays the actual GANDR library data a', whereas the GAPOST code lists the “reconstructed” parameters aadj. The translation between the two representations is not difficult, because this exercise does not involve Gauss-Newton iteration, so that all of the elements of the aref vector are equal to unity. Also note that the numbers printed by GAPOST under the heading “uncertainty” are standard deviations and must be squared before comparing with variances read from the library.

Reference
1. M. Herman, R. Capote, B.V. Carlson, et al., “EMPIRE: Nuclear Reaction Model Code System for Data Evaluation,” Nuclear Data Sheets, 108, 2655 (2007).