Global Assessment of Nuclear Data
(GANDR Project)

Volume 6. Multigroup Sensitivities

D. W. Muir

Revision2: 28 November 2011

ABSTRACT

We consider here the calculation of the sensitivity of multigroup neutron cross sections to the GANDR “point” parameters. In the present analysis, we limit our consideration to the parameter sensitivity of infinitely dilute cross sections.

TABLE OF CONTENTS

6-I. Introduction to Multigroup Sensitivities	----------------------------------------------------	6-3

6-II. Union-Group Cross Sections	-----------------------------------------------------------------	6-3

6-III. User-Group Cross Sections	-----------------------------------------------------------------	6-6

References	--------------------------------------------------------------------------------------------	6-7

6-I. Parameter Sensitivities of Multigroup Data
In this document, we review the calculation of the sensitivity of multigroup constants to the GANDR parameters. An unusual feature of these sensitivities is that they provide an interface between the evaluated “point” parameters and covariances in the GANDR library and quantities calculated externally in a multigroup framework. Much of the material presented here also appears, using slightly different notation, in the Appendix of Ref. 1.

We limit our considerations to the parameter sensitivity of "infinitely dilute" cross sections. Because of this, the results presented below are useful primarily for the analysis of fast-neutron systems, where there is little resonance self-shielding. The analysis given here may also provide a useful model for later work to address the sensitivity of self-shielded cross sections to the GANDR parameters.

As seen below, because of the simplicity of the GANDR evaluation model, it is possible to calculate the sensitivity of infinitely dilute multigroup cross sections to the GANDR parameters without approximation, simply by manipulating information obtained from existing multigroup processing programs.

6-II. Union-Group Cross Sections
We begin our consideration of multigroup issues by introducing an energy grid that is the union of the external user's multigroup grid and the GANDR evaluation grid. The GANDR evaluation grid will be either the standard 74-node grid, as defined in Ref. 2, or a subset of that grid.

We focus our attention on one of 25 "official" GANDR reactions, having a true, or modeled, value of s(E) at incident neutron energy E. For simplicity, we omit the reaction index. Further let S(i) denote the multigroup cross section for the reaction in union group i. The upper and lower boundaries of the union group are labeled E(i) and E(i+1) respectively. The user specified flux weighting function is c(E). Then, as usual,

E(i+1)
S(i) = F-1(i)	∫ c(E) s(E) dE	(1)
E(i)

where F(i) is the integral of c(E) over the group,

E(i+1)
F(i) =	∫ c(E) dE	(2)
E(i)

In the GANDR evaluation model, s(E) is assumed to differ from the reference evaluation sref(E) by at most a piecewise-linear correction factor A(E). As discussed in Ref. 2, this correction function can, in turn, be expressed in terms of the values of the 25 GANDR parameters an and a set of "hat" functions Hn(E), so that,

s(E) = A(E) sref(E) = ∑ an Hn(E) sref(E)	(3)
n
We can similarly introduce the reference value of the multigroup cross section S(i),

E(i+1)
Sref(i) = F-1(i)	∫ c(E) sref(E) dE	(4)
E(i)

By definition, the union group i contains no interior GANDR nodes, so the function A(E) is strictly linear within group i. We denote by elo(i) and ehi(i) the two GANDR nodes that span the group, elo(i) ≤ E(i) < E(i+1) ≤ehi(i). The location of these nearest nodes elo(i) and ehi(i), together with the values of the GANDR parameters corresponding to these nodes, determine the slope and magnitude of A(E) within the group.

Let hlo(E,i) and hhi(E,i) denote hat functions centered at elo(i) and ehi(i), respectively. By definition, hlo(E,i) declines linearly from unity at elo(i) to zero at ehi(i), while hhi(E,i) rises from zero at elo(i) up to unity at ehi(i). As explicit functions of energy, then,

hlo(E,i) = [ehi(i) - E] / [ehi(i) - elo(i)]	(5)

hhi(E,i) = [E - elo(i)] / [ehi(i) - elo(i)]	(6)

Let alo(i) and ahi(i) denote the parameter values corresponding to the nearest GANDR nodes. Over the range of integration, then, s(E) has the following simple energy dependence,

s(E) = A(E) sref(E) = [alo(i) hlo(E,i) + ahi(i) hhi(E,i)] sref(E)	(7)

Substituting this result for s(E) into Eq. (1), we obtain

E(i+1)
S(i) = F-1(i)	∫ c(E) [alo(i) hlo(E,i) + ahi(i) hhi(E,i)] sref(E) dE	(8)
E(i)

The derivative of the group constant S(i) with respect to alo(i), then, is just

E(i+1)
∂S(i)/∂alo(i) = F-1(i) ∫ c(E) hlo(E,i) sref(E) dE	(9)
E(i)

An analogous relation holds for ahi(i),

E(i+1)
∂S(i)/∂ahi(i) = F-1(i) ∫ c(E) hhi(E,i) sref(E) dE .	(10)
E(i)

Combining Eqs. (5) and (9), we obtain

E(i+1)
∂S(i)/∂alo(i) = F-1(i)	∫ c(E) [ehi(i) - E] / [ehi(i) - elo(i)] sref(E) dE	(11)
E(i)

Recalling the definition of Sref(i) from Eq. (4), we have

∂S(i)/∂alo(i) = [ehi(i) Sref(i) - W(i)] / [ehi(i) - elo(i)] ,	(12)

where we have introduced a new integral quantity W(i). It resembles a group constant, except that it contains an extra E term in the integrand,

E(i+1)
W(i) = F-1(i)	∫ c(E) E sref(E) dE .	(13)
E(i)

Similarly, combining Eqs. (6) and (10), we obtain

E(i+1)
∂S(i)/∂ahi(i) = F-1(i)	∫ c(E) [E - elo(i)] / [ehi(i) - elo(i)] sref(E) dE ,	(14)
E(i)

so that

∂S(i)/∂ahi(i) = [W(i) - elo(i) Sref(i)] / [ehi(i) - elo(i)]	(15)

To use Eqs. (12) and (15) for practical calculations of sensitivities, we need a procedure for calculating the various integral quantities involved.

Clearly, S(i) and the corresponding group flux F(i) can be calculated, for any user-specified weighting flux c(E), by a multigroup processing program such as NJOY. Less obviously, a code like NJOY can also be used to calculate the special group integral W(i), with no code changes.

To see this, let us introduce a new group constant T(i) and group flux G(i), both calculated in the usual way with NJOY, but using as the user specified weight function the modified weighting function cmod(E) = E c(E).

E(i+1)
T(i) = G-1(i)	∫ [E c(E)] sref(E) dE .	(16)
E(i)

The group flux G(i) for this case is the integral of cmod(E) over the group,

E(i+1)
G(i) =	∫ [E c(E)] dE .	(17)
E(i)

Observing the equality of the integrands in Eqs. (13) and (16), we have at once

W(i) F(i) = T(i) G(i) ,	(18)

or

W(i) = T(i) G(i) / F(i) ,	(19)

Combining Eqs. (12), (15) and (19), we have our results for the union group multigroup sensitivities,

∂S(i)/∂alo(i) = [ehi(i) Sref(i) - T(i) G(i) / F(i)] / [ehi(i) - elo(i)] ,	(20)

and

∂S(i)/∂ahi(i) = [T(i) G(i) / F(i) - elo(i) Sref(i)] / [ehi(i) - elo(i)]	(21)

To summarize, a multigroup cross section, calculated in union group i, has sensitivities to the GANDR parameters that are non-zero only for the GANDR nodes lying at energies just above and below that group. As shown in Eqs. (20) and (21), these sensitivities can be obtained by combining integrated quantities computed by standard multigroup codes such as NJOY without any code changes.

6-III. User-Group Cross Sections
Having obtained the derivatives of S(i) with respect to ahi(i) and alo(i), we can now proceed to the computation of derivatives of linear functions of the union group cross sections with respect to the GANDR parameters. This includes the important case of cross sections in the user's group structure, obtained by collapsing group cross sections from the union group structure to the user’s structure.

To show the details, let fij denote the fraction of the weighting flux in user group j that falls within union group i. Then the user-group cross section in group j, Uj, is related to the union-group cross sections S(i) as follows:

Uj = ∑ fij S(i)	(22)
i, j
Let ak denote one of the GANDR parameters for the current material of interest, where k is the standard GANDR index of the parameter. To obtain the desired sensitivities, it is helpful to formally consider the previously introduced quantities alo(i) and ahi(i) to be linear functions of the ak,

alo(i) =	∑ Plo(i,n) an	(23)
n
where Plo(i,n) is a delta-function type pointer array having the value unity when n is equal to the GANDR index of the node lying just below the union group i and otherwise having the value of zero. Similarly,

ahi(i) =	∑ Phi(i,n) an	(24)
n
where Phi(i,n) is a pointer array having the value unity when n is equal to the GANDR index of the node lying just above the union group and otherwise zero.

From Eq. (22) the sensitivity of the user-group constant Uj to ak is then obtained by applying the chain rule,

∂Uj /∂ak = ∑ fij [∂S(i)/∂alo(i) ∂alo(i)/∂ak + ∂S(i)/∂ahi(i) ∂ahi(i)/∂ak]	(25)
i, j

From Eqs. (23) and (24),

∂alo(i)/∂ak = ∑ Plo(i,n) δnk = Plo(i,k)	(26)
n
and

∂ahi(i)/∂ak =	∑ Phi(i,n) δnk = Phi(i,k)	(27)
n
so that
∂Uj /∂ak = ∑ fij [∂S(i)/∂alo(i) Plo(i,k) + ∂S(i)/∂ahi(i) Phi(i,k)]	(28)
i, j
where the quantities ∂S(i)/∂alo(i) and ∂S(i)/∂ahi(i) are given in Eqs. (20) and (21) above.

                1. References

1. D.W. Muir, A. Mengoni and I. Kodeli, “Integration of the International Standards Evaluation into a Global Data Assessment,” Nuclear Data Sheets 109 (2008) 2874-2879.

2. D.W. Muir, The Global Assessment of Nuclear Data Requirements (GANDR Project). Volume 1. Project Overview. Available online at www-nds.iaea.org/gandr/docs.html.