Memo issued on behalf of

National Nuclear Data Center

Brookhaven National Laboratory

USA

Memo CP-C/406

Date:		9 May 2012

To:		Distribution

From:		O. Schwerer and N.Otsuka

Subject:		Probability for emitting N particles: Proposal for new coding

Currently, probabilities for the emission of a given number of particles are coded with REACTION SF5 = NUM and REACTION SF4 = NPART.

The independent variable PART-OUT is used for the number of outgoing particles.

The quantity is also called multiplicity distribution. It has to be distinguished from multiplicities as quantity (SF6 = MLT), as here the multiplicity is not the result but the independent variable.

As the current practice in compiling such data is not always consistent, and new and more complex cases are being compiled, we propose the following new scheme.

- All such data must have SF5 = NUM and independent variable PART-OUT.
(No change from before)

- SF4 = NPART is cancelled. It is not absolutely necessary to define the quantity but it prevents us from using SF4 for product particles.

- In SF6, existing codes NU, FY, PY, SIG continue to be used. No new parameter will be needed.

- With 2 exceptions, all quantities with SF5 = NUM are probabilities normalized to 1, and have therefore dimension NO-DIM.
The 2 exceptions are:
 - NUM,SIG,(*)	given in mb or equivalent units
 - Unnormalized probabilities, to be given with SF8 = REL and ARB-UNITS

This system will allow us to compile more complex cases in a consistent way, while the changes to existing entries will be manageable. When need arises, more quantities in the same style can be added (e.g. NUM,MLT).

Quantities in dictionary 236

| Quantity | Type and dimension | Definition | Dimension |
| --- | --- | --- | --- |
| NUM,NU | NUP NO | Probability for emission of N (fission) neutrons | Probabilities are normalized, i.e. sum of all probabilities = 1 and units = NO-DIM |  |
| PR/NUM,NU | NUP NO | Probability for emission of N prompt neutrons |  |  |
| NUM,FY and NUM,FY,* (New) | FY NO | Probability for emission of N fission particles (other than neutrons) |  |  |
| NUM,PY | PY NO | Probability for emission of N product particles (SF3 ≠ F) |  |  |
| NUM,SIG,(*) (new with blank SF7) | CS B | Cross section for emission of N product particles | Units = mb or equivalent |  |

In case of unnormalized probabilities, SF8 = REL and ARB-UNITS must be used.

Changes in existing entries

| Accession no. | REACTION | Change(s) required |
| --- | --- | --- |
| 14064.002 | ...(0,F)NPART,NUM,NU | Delete NPART |
| 30367.005-007 | ...(0,F)NPART,NUM,NU | Delete NPART |
| 30544.002 | ...(N,F)NPART,PR/NUM,NU | - Delete NPART - Change units to NO-DIM |
| 30609.005-007 | ...(0,F)NPART,NUM,NU | Delete NPART |
| 41056.003 | ...(0,F)NPART,PR/NUM,NU | Delete NPART |
| 41425.002-004 | ...(0,F),PR/NUM,NU | No change needed |
| 41539.003-004 | ...(0,F)NPART,PR/NUM,NU | Delete NPART |
| 41559.003-004 | ...(0,F)NPART,PR/NUM,NU | Delete NPART |
| A0361.002 | 79-AU-197(92-U-238,X)NPART, NUM,SIG,HF | - Delete NPART - Add keyword MISC-COL (no. of detected events) |
| O0837.002 O0837.003 O0837.004 | ..(P,X)NPART,NUM,SIG,PIP ..(P,X)NPART,NUM,SIG,PIN ..(P,X)NPART,NUM,SIG,P | Change REACTIONs to: (P,X)1-PP-0,NUM,SIG (P,X)1-PN-0,NUM,SIG (P,X)1-H-1,NUM,SIG |
| O0848.002-008 O0848.009-012 | ..(P,X)NPART,NUM,SIG,N ..(P,X)NPART,NUM,SIG,N,REL | Change REACTIONs to: (P,X)0-NN-1,NUM,SIG (P,X)0-NN-1,NUM,SIG,REL |
| Changes in existing entries (continued) |
| Accession no. | REACTION | Change(s) required |
| O0953.002-017 | ..(..,..) NPART,NUM,SIG,N | Change REACTIONs to: (..,..) 0-NN-1,NUM,SIG |
| O1086.002-004 | ..(P,X)1-H-1,NUM,PY | - Change units to NO-DIM - Add main reference J,EPJ/A,21,273,2004 |
| O1426.002-011 | ...(P,X)NPART,NUM,SIG,N | Change REACTIONs to: (..,..) 0-NN-1,NUM,SIG |
| V0045011-014 | (N,F)NPART,PR/NUM,NU,,,EVAL | Delete NPART |

New entries (Prelim 1379)

| 14286 | D.L.Bleuel+,J,NIM/A,624,691,2010 |  |
| --- | --- | --- |
| .002 | 98-CF-252(0,F)0-G-0,NUM,FY,,REL | Unnormalized over all multiplicity distribution (Fig.6, author's data) |
| .003 | (1) 98-CF-252(0,F)42-MO-106,NUM,FY,G (2) 98-CF-252(0,F)46-PD-108,NUM,FY,G | Normalized multiplicity distributions for 2 identified fission channels (Fig.7, author's data) |
| .004 | 98-CF-252(0,F)ELEM/MASS,NUM,FY,G | Normalized multiplicity distribution for channel with 2 identified products defined with ELEM1,2 and MASS1,2 (2n channel, Fig.12, author's data) |
| .005 | 98-CF-252(0,F)ELEM/MASS,NUM,FY,G | Normalized multiplicity distribution for channel with 2 other identified products defined with ELEM1,2 and MASS1,2 (4n channel, Fig.12, author's data) |
| 14315 | A.Chyzh+,J,PR/C,85,021601,2012 |  |
| .002 | 98-CF-252(0,F)0-G-0,PR,FY/DE,,RAW | (Existing quantity) (Fig. 1a, author's data) |
| .003 | 98-CF-252(0,F)0-G-0,NUM,FY | Normalized over all multiplicity distribution (Fig. 2a, author's data) |

Appendix: Coding examples from new entries 14286 and 14315

Appendix: Coding examples from new entries 14286 and 14315

1) Entry 14286

ENTRY            14286

SUBENT        14286001

BIB                  8         21

TITLE      Gamma-ray multiplicity measurement of the spontaneous

fission of 252Cf in a segmented HPGe/BGO detector

array

AUTHOR     (D.L.Bleuel,L.A.Bernstein,J.T.Burke,J.Gibelin,

M.D.Heffner,J.Mintz,E.B.Norman,L.Phair,N.D.Scielzo,

S.A.Sheets,N.J.Snyderman,M.A.Stoyer,M.Wiedeking)

INSTITUTE  (1USALRL,1USABRK)

REFERENCE  (J,NIM/A,624,691,2010)

SAMPLE     Cf-252 source, 1.5E6 fission/minutes, on a nickel foil

backing, 90 microg/cm2

METHOD     (COINC) Coincidence of gamma rays from fission

fragments

DETECTOR   (HPGE) The experiment was performed using six EURISYS

high-purity germanium (HPGe) Clover detectors of the

Livermore-Berkeley Array for Collaborative Experiments

Each Clover consists of four HPGe crystals in a shared

cryostat surrounded by 16 SCIONIX bismuth-germanate

detectors. The system had high degre of segmentation

with 19 HPGe and 94 BGO  detectors and good solid

angle coverage.

HISTORY    (20110201) Compiled by S.H.

ENDBIB              21          0

NOCOMMON             0          0

ENDSUBENT           24          0

SUBENT        14286002   20120330

BIB                  3          5

REACTION   (98-CF-252(0,F)0-G-0,NUM,FY,,REL)

Overall gamma ray multiplicity spectra

ERR-ANALYS (ERR-S) Statistical uncertainty

STATUS     (TABLE ) Data presented in Fig. 6 of the reference

sent by author (D.L.B.)

ENDBIB               5          0

NOCOMMON             0          0

DATA                 3         36

PART-OUT   DATA       ERR-S

NO-DIM     ARB-UNITS  ARB-UNITS

0.0      292.8E+5   124.8E+2

1.0      453.2E+6   580.1E+2

2.0      340.1E+6   340.2E+2

3.0      190.7E+6   196.4E+2

4.0      102.3E+6   119.5E+2

etc.

…...

33.0      437.6E+0   127.4E+0

34.0      167.0E+0   121.2E+0

35.0      157.0E+0   111.3E+0

ENDDATA             38          0

ENDSUBENT           48          0

SUBENT        14286003   20120330

BIB                  5         10

REACTION  1(98-CF-252(0,F)42-MO-106,NUM,FY,G)

2(98-CF-252(0,F)46-PD-108,NUM,FY,G)

ANALYSIS   Gamma ray multiplicities in both channels are

normalized to sum to unity.

ERR-ANALYS (ERR-S) Statistical uncertainty

STATUS     (TABLE) Data presented in fig. 7 of the reference

sent by author (D.L.B.)

ENDBIB              10          0

NOCOMMON             0          0

DATA                 4         60

PART-OUT   DATA      1ERR-S     1DATA      2ERR-S     2

NO-DIM     NO-DIM     NO-DIM     NO-DIM     NO-DIM

1.0      -4.96E-02   2.24E-03   5.64E-01   1.62E-03

2.0       8.18E-02   2.40E-03   2.65E-01   1.73E-03

3.0       7.18E-02   1.94E-03   1.17E-01   1.42E-03

4.0       8.31E-02   1.51E-03   3.05E-02   1.01E-03

5.0       9.65E-02   1.25E-03   7.59E-03   7.95E-04

6.0       1.07E-01   1.16E-03   2.24E-03   7.28E-04

etc.

….........

30.0      -9.78E-06   1.08E-05   1.93E-06   6.97E-06

ENDDATA             62          0

ENDSUBENT           77          0

SUBENT        14286004   20120330

BIB                  5         15

REACTION   (98-CF-252(0,F)ELEM/MASS,NUM,FY,G)

ANALYSIS   Number of emitted neutrons in various fission channels

was determined from correlated discrete gamma rays of

fission products

2n channel  106Mo x 144Ba

4n channel  106Mo x 142Ba

Multiplicities in both channels are normalized

to sum to unity.

This table contains the gamma ray multiplicity of events

with 2 neutrons emitted. For the 4n channel see

subentry 5.

ERR-ANALYS (ERR-S) Statistical uncertainty

STATUS     (TABLE) Data presented in fig. 12 of the reference

sent by author (D.L.B.)

ENDBIB              15          0

COMMON

ELEM1      MASS1      ELEM2      MASS2

NO-DIM     NO-DIM     NO-DIM     NO-DIM

42.          106.      56.        144.

ENDCOMMON

DATA

PART-OUT   DATA       ERR-S

NO-DIM     NO-DIM     NO-DIM

2.0       1.59E-02   6.31E-03

3.0       1.20E-02   9.35E-03

4.0       1.15E-02   1.10E-02

5.0       6.37E-02   1.20E-02

6.0       8.74E-02   1.34E-02

etc.

…...

28.0      -1.80E-03   7.06E-04

29.0      -2.58E-04   5.16E-04

30.0       5.16E-04   2.58E-04

ENDDATA             60          0

ENDSUBENT           80          0

SUBENT        14286005   20120330

BIB                  5         15

REACTION   (98-CF-252(0,F)ELEM/MASS,NUM,FY,G)

ANALYSIS   Number of emitted neutrons in various fission channels

was determined from correlated discrete gamma rays of

fission products

2n channel  106Mo x 144Ba

4n channel  106Mo x 142Ba

Multiplicities in both channels are normalized

to sum to unity.

This table contains the gamma ray multiplicity of events

with 4 neutrons emitted. For the 2n channel see

subentry 4.

ERR-ANALYS (ERR-S) Statistical uncertainty

STATUS     (TABLE) Data presented in fig. 12 of the reference

sent by author (D.L.B.)

ENDBIB              15          0

COMMON

ELEM1      MASS1      ELEM2      MASS2

NO-DIM     NO-DIM     NO-DIM     NO-DIM

42.          106.      56.        142.

ENDCOMMON

DATA

PART-OUT   DATA       ERR-S

NO-DIM     NO-DIM     NO-DIM

2.0       2.06E-02   4.42E-03

3.0       3.48E-02   6.60E-03

4.0       2.22E-02   7.63E-03

5.0       4.79E-02   8.06E-03

6.0       4.68E-02   9.16E-03

7.0       5.94E-02   1.04E-02

etc

…...

28.0       9.37E-04   4.68E-04

29.0       4.68E-04   3.70E-04

30.0       1.17E-04   2.62E-04

ENDDATA             60          0

ENDSUBENT           80          0

ENDENTRY

2) Entry 14315

ENTRY            14315   20120229

SUBENT        14315001   20120229

BIB                 10         36

TITLE      Evidence for the stochastic aspect of prompt gamma

emission in spontaneous fission

AUTHOR     (A.Chyzh,C.Y.Wu,E.Kwan,R.A.Henderson,J.M.Gostic,

T.A.Bredeweg,R.C.Haight,A.C.Hayes-Sterbenz,M.Jandel,

J.M.O'Donnell,J.L.Ullmann)

INSTITUTE  (1USALRL,1USALAS)

REFERENCE  (J,PR/C,85,021601,2012)

DETECTOR   (PPAC) 252Cf source covered with aluminized mylar

served as a cathode. The two anodes, made of the same

thickness aluminized mylar sheet, were placed on both

sides of the cathode at a distance of 3 mm and

electrically connected. The PPAC was operated with

isobutane gas at the 4.00 torr pressure stabilized by

a feedback loop of constant gas flow. It has

efficiency of 82% for the detection of fission

fragments

(BAF2) Gamma ray energy and multiplicity was measured

with a 4pi g-ray calorimeter DANCE made of 160 BaF2

crystals; each crystal has equal solid- angle

coverage.Beside capture studies,DANCE can be used for

the precision measurement of the E-gamma and M-gamma

distributions as well as the total gamma-ray energy

METHOD     (COINC) Coincidence between fission fragments

detected by avalanche counter and DANCE detectors was

required to identify prompt gamma rays fromfission

SAMPLE     A 252Cf source with a strength 0.15 mu-Ci was

prepared by stippling the material on a 3 mu-m thick

titanium foil, and then covered by a 1.4 mu-m thick

aluminized mylar to serve as a cathode.

ANALYSIS   Data were obtained by unfolding of raw data. Response

matrices for gamma energy as well as gamma

multiplicity were calculated using GEANT4. The

unfolding was done using both the iterative Bayesian

and singular value decomposition (SVD) methods.

ERR-ANALYS (DATA-ERR) No information given

HISTORY    (20120229C) Compiled by S.H.

ENDBIB              36          0

NOCOMMON             0          0

ENDSUBENT           39          0

…......

…......

SUBENT        14315003   20120229

BIB                  2          7

REACTION  1(98-CF-252(0,F)0-G-0,NUM,FY,,RAW) Original exper.data

2(98-CF-252(0,F)0-G-0,NUM,FY)  Multiplicity distribution

based on unfolded spectra using SVD method

3(98-CF-252(0,F)0-G-0,NUM,FY) Multiplicity distribution

based on unfolded spectra using Bayesian approach

STATUS     (TABLE) Data presented in fig. 2a of the reference

sent by author (A.Ch.)

ENDBIB               7          0

COMMON               1          3

E-ERR

MEV

0.1

ENDCOMMON            3          0

DATA                 7         20

PART-OUT   DATA      1DATA-ERR  1DATA      2DATA-ERR  2DATA      3

DATA-ERR  3

NO-DIM     NO-DIM     NO-DIM     NO-DIM     NO-DIM     NO-DIM

NO-DIM

1.0   4.55E-03   3.73E-05

2.0   3.83E-02   1.08E-04   2.09E-02   1.93E-04   1.94E-02

1.07E-04

3.0   7.85E-02   1.55E-04   4.44E-02   2.15E-04   4.39E-02

1.52E-04

4.0   1.22E-01   1.93E-04   7.05E-02   2.86E-04   7.11E-02

1.86E-04

5.0   1.52E-01   2.16E-04   9.39E-02   3.38E-04   9.56E-02

2.12E-04

6.0   1.62E-01   2.22E-04   1.10E-01   3.69E-04   1.13E-01

2.30E-04

7.0   1.47E-01   2.12E-04   1.18E-01   3.93E-04   1.19E-01

2.43E-04

8.0   1.17E-01   1.89E-04   1.15E-01   4.13E-04   1.16E-01

2.53E-04

9.0   8.15E-02   1.58E-04   1.05E-01   4.28E-04   1.05E-01

2.62E-04

10.0   4.97E-02   1.23E-04   9.00E-02   4.35E-04   8.87E-02

2.74E-04

11.0   2.68E-02   9.04E-05   7.23E-02   4.40E-04   7.09E-02

2.87E-04

12.0   1.26E-02   6.19E-05   5.47E-02   4.46E-04   5.35E-02

3.04E-04

13.0   5.25E-03   4.00E-05   3.89E-02   4.50E-04   3.80E-02

3.24E-04

14.0   1.91E-03   2.41E-05   2.59E-02   4.58E-04   2.56E-02

3.49E-04

15.0   6.15E-04   1.37E-05   1.63E-02   4.86E-04   1.64E-02

3.84E-04

16.0   1.70E-04   7.20E-06   9.71E-03   5.36E-04   1.01E-02

4.44E-04

17.0   4.36E-05   3.65E-06   5.70E-03   5.84E-04   6.22E-03

5.31E-04

18.0   1.22E-05   1.93E-06   3.57E-03   6.30E-04   3.96E-03

6.34E-04

19.0   2.44E-06   8.63E-07   2.65E-03   9.99E-04   2.68E-03

9.54E-04

20.0   3.05E-07   3.05E-07   2.37E-03   2.48E-03   1.87E-03

1.87E-03

ENDDATA             44          0

ENDSUBENT           60          0

ENDENTRY             3          0

Distribution:

blokhin@ippe.ru

cgc@ciae.ac.cn

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

fukahori.tokio@jaea.go.jp

ganesan@barc.gov.in

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

j.roberts@iaea.org

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re

zhuangyx@ciae.ac.cn