Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/627

Date:		20 March 2010

To:		Distribution

From:		N. Otsuka. E. Dupont

Subject:		Automatic test of EXFOR with TALYS

As a part of activity of WPEC sg30, Arjan Koning (NRG Petten) created a complete nuclear reaction database SALTY by blind TALYS calculation, and compared the database with EXFOR for the following reaction/quantity:

Projectiles:	γ, n, p, d, t, 3He, α

Targets:		all stable isotopes with 9≤Z≤83

Inc. energy:	from thermal energies up to 200 MeV

Reaction:		total, elastic, non-elastic, exclusive partial cross sections (defined by the ENDF MT scheme), and residual production cross sections.

The deviation of the SALTY data from EXFOR data were evaluated by the following 4 averaged deviation factors:

Rolf Michel’s f-factor

C/E value

Chi-square

Absolute deviation

and compiled in one ASCII file (x4.sort), which was sent to NDS with the associated documentation (appended to this memo).

Then suspicious EXFOR subentries potentially involved in coding mistake (e.g. B ↔ MB) were selected by the NEA Data Bank using the following criteria (assuming that calculated value could be wrong by up to a factor of 2)

5×10-4 < R < 2×10-3  or  5×10+2 <R<2×10+3   or  500 < F < 2000

This selection of EXFOR subentries was further filtered at the NEA Data Bank by comparison with other experimental and evaluated data in order to eliminate false alarm, X4toC4 issue, and known errors. The result is summarized in Table 1. During this visual inspection, some additional outliers were found (outside the F or R selection range).

Finally 37 suspicious data sets were checked with original articles by NDS and real coding mistakes were found in 25 data sets. For several cases, NDS asked questions to authors, and Prof. R. Michel (Uni. Hannover) and T. Otsuki (Tohoku Univ.) answered us quickly.

Please find proposed corrections in “Report to WPEC SG30” appended to this memo. A short summary is also shown in the NRDC webpage:

http://www-nds.iaea.org/nrdc/error/exfor_err3.html.

Plots prepared by the NEA Data Bank were also added to the web page.

Table 1: Deviation factors of suspicious data sets after filtering of the list provided by A. Koning

| # EXFOR | E-min (eV) | E-max (eV) | F | R | χ2 | Δ |
| --- | --- | --- | --- | --- | --- | --- |
| 10492.008 | 8.70E-01 | 3.97E+00 | 332. | 517. | 1.483E+07 | 2.418E+03 |
| 12244.002 | 2.35E-08 | 2.35E-08 | 695. | 1.439E-03 | 5.05 | 8.987E+04 |
| 12758.006 | 3.00E-02 | 3.00E-02 | 887. | 1.127E-03 | 395. | 8.940E+04 |
| 13547.004 | 1.50E+00 | 3.50E+00 | 1.226E+03 | 8.626E-04 | 31.9 | 146. |
| 13783.004 | 2.53E-08 | 2.53E-08 | 521. | 1.921E-03 | 99.6 | 1.397E+07 |
| 14075.004 | 3.00E+00 | 4.00E+00 | 689. | 4.032E-03 | 108. | 91.0 |
| 21486.002 | 2.53E-08 | 2.53E-08 | 749. | 1.335E-03 | 12.6 | 3.196E+04 |
| 22347.006 | 1.35E+01 | 1.47E+01 | 1.438E+03 | 1.442E+03 | 1.146E+08 | 1.627E+03 |
| 22445.002.2 | 3.75E-02 | 3.75E-02 | 1.138E+03 | 8.785E-04 | 178. | 187. |
| 22873.003 | 3.65E-03 | 5.25E-02 | 1.190E+03 | 1.193E+03 | 6.020E+08 | 7.740E+03 |
| 31543.006 | 1.40E+01 | 1.40E+01 | 1.381E+03 | 7.240E-04 | 18.8 | 6.50 |
| 31602.002 | 2.53E-08 | 2.53E-08 | 1.312E+03 | 1.312E+03 | 9.536E+08 | 556. |
| 32205.019 | 1.45E+01 | 1.45E+01 | 653. | 1.531E-03 | 16.0 | 0.759 |
| 40244.048 | 4.00E+00 | 4.00E+00 | 1.042E+03 | 1.042E+03 | 9.533E+08 | 1.85 |
| 40244.049 | 4.00E+00 | 4.00E+00 | 521. | 521. | 2.676E+07 | 0.931 |
| 40336.102 | 2.50E+00 | 4.00E+00 | 821. | 1.240E-03 | 0.00 | 749. |
| A0401.002 | 3.97E+01 | 1.10E+01 | 1.113E+05 | 8.529E-04 | 24.6 | 2.77 |
| A0485.010 | 4.20E+01 | 1.03E+02 | 3.362E+04 | 1.499E-03 | 40.3 | 1.56 |
| O0282.005 | 5.32E+01 | 9.80E+01 | 8.860E+04 | 1.224E-03 | 81.1 | 1.75 |
| C0265.008 | 4.08E+01 | 3.56E+01 | 569. | 570. | 8.128E+06 | 0.131 |
| C0703.004.2 | 7.00E+00 | 1.10E+01 | 991. | 1.007E+03 | 2.644E+07 | 91.6 |
| C1159.003.1 | 1.92E+01 | 3.96E+01 | 89.6 | 697. | 3.742E+09 | 128. |
| C1523.004 | 3.66E+01 | 3.66E+01 | 635. | 635. | 2.129E+08 | 146. |
| D0433.002 | 4.64E+00 | 2.74E+01 | 5.858E+05 | 9.820E-04 | 44.4 | 108. |
| E1411.006 | 1.20E+01 | 1.80E+01 | 5.064E+04 | 5.683E-04 | 32.2 | 366. |

Table 2: Summary of checking with articles

| Not in error | 9 |
| --- | --- |
| Error (corrected) | 2 |
| Error (to be corrected) | 23 |
| Not resolved yet | 3 |
| Total | 37 |

Common remark to centres for all lists from WPEC sg30 activity:

Addition of CRITIQUE may help users even if deviation is not attributed to coding mistake!!

Distribution:

blokhin@ippe.ru

chiba@earth.sgu.ac.jp

claes.nordborg@oecd.org

emmeric.dupont@oecd.org

ganesan@barc.gov.in

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

j.roberts@iaea.org

kaltchenko@kinr.kiev.ua

katakura.junichi@jaea.go.jp

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

manuel.bossant@oecd.org

manokhin@ippe.ru

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.dunaeva@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

taova@expd.vniief.ru

tarkanyi@atomki.hu

varlamov@depni.sinp.msu.ru

vlasov@kinr.kiev.ua

vmclane@optonline.net

v.zerkin@iaea.org

yolee@kaeri.re.

cc:

koning@nrg.eu

Report to WPEC SG30

Analysis of a selected suspicious data from Arjan Koning’s list (x4.sort) (Draft Ver. 2010-03-20 by Naohiko)

Source:

Table: Table of data is given in the reference.

Curve: Plot of data is given in the reference.

SCSRS: Data translated from the SCISRS library.

Author: Data received from authors.

Trans: EXFOR transmission number if corrected

| Subentry | Reference | Reaction | Comments (AK+ED) | Source | Error? | Trans | Comments (NO) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 10492.008 | J,NSE,67,34,1978 | 24-CR-0(N,INL)24-CR-54,PAR,SIG | 30 times too low | Author | Yes |  | SF4: 24-CR-54→24-CR-0 or SF1: 24-CR-0 → 24-CR-54 SF8: Add A a (54Cr)=2.4%. Similar comments are applied to 002, 004, 006 (and 014?). |
| 12244.002 | W,HALDAR,1953 | 78-PT-192(N,G)78-PT-193-M,,SIG | 10 times too large | SCSRS | ? |  | Checking by NNDC (Supported by 31249.009) |
| 12758.006 | J,PR/C,29,2126,1984 | 82-PB-204(N,G)82-PB-205,,SIG,,MXW | 1000 times too large | Table | Yes |  | DATA(-ERR): B → MB In addition, EN-MEAN → KT DATA-ERR→ERR-T Add ERR-S=0.2%. Note that +/- 5.5 mb is given in p2134 of the article. But +/- 4.5 mb in the abstract is more consistent with the description in IV Discussion. |
| 13547.004 | J,JP/G,19,655,1993 | 21-SC-45(N,INL)21-SC-45,PAR,SIG | wrong level energy (1000 times too low) | Author | Yes |  | E-EXC(-ERR): KEV → MEV |
| 13783.004 | C,99SANTA,,111,1999 | 64-GD-148(N,G)64-GD-149,,SIG,,MXW | 100 times too large | Table | ? |  | Superseded by 14113.002 ? (Declared as a preliminary result in M.G. Rios et al., J,PR/C,74,044302,2006) |
| 14075.004 | J,NP/A,500,43,1989 | 40-ZR-96(N,INL)40-ZR-96,PAR,SIG | 5 times too large? (1st level only) | Table | Yes |  | Excitation energies for En=3.0 MeV and 3.5 MeV (except for last 3 levels) must be corrected. Also 12 mb → 2 mb for the 3483 keV level at En=4.0 MeV. |
| 14113.002 | J,PR/C,74,044302,2006 | 64-GD-148(N,G)64-GD-149,,SIG | 100 times too large (see 13783004.png) | Table | No |  |  |
| 21486.002 | J,CR,252,3973,1961 | 10-NE-0(N,G),,SIG | 1000 times too large | Table | Yes |  | DATA(-ERR): B → MB |
| 22347.006 | S,JAERI-97-004,177,1996 | 53-I-129(N,2N)53-I-128,,SIG | 1000 times too low | Table | Yes |  | MB→B (006) c.f. Fig.2. In addition, - 004-006. STATUS: “Data from main reference” is not applicable. 004-005 and 006 are from S,JAERI-97-C-005,216,1997 (Table 2) and S,JAERI-98-C-003,210,1998 (Table 2). - 002-005: Partial uncertainties are wrong. Information for 002-003 and 004-005 should be taken from S,JAERI-C-97-004, 177, 1996 (Table 2) and S, JAERI-C-97-005, 216, 1997 (Table 3), respectively. - INC-SPECT should be given according to MCNP calculation results explained in p218 of S,JAERI-C-97-005. Contribution of thermal, epithermal. MeV and DT neutron were 30%, negligible, 50% and 20% in 003, and contribution of the thermal neutrons were removed in 005. |
| 22445.002.2 | J,PR/C,52,3442,1995 | 16-S-36(N,G)16-S-37,,SIG,,MXW | 1000 times too large? (see also 224450021, 22445003) | Table | Yes |  | MB → MICRO-B (002.2 and 003) |
| 22873.003 | C,2004SANTA,,1462,2004 | 53-I-129(N,TOT),,SIG | 1000 times too low | Author | (Yes) | 2212 | MB → B |
| 22965.002 | J,PR/C,75,034617,2007 | 17-CL-36(N,P)16-S-36,,SIG) + (17-CL-36(N,A)15-P-33,,SIG) | 2 data sets in the same list?? | Author | ? |  | Waiting authors’ answer |
| 31249.009 | J,NP,41,372,1963 | 78-PT-192(N,G)78-PT-193,,SIG,,SPA | 10 times too large (see 12244002.png) | Table | Yes |  | SF4: 78-PT-193 → 78-PT-193-M Identified by KX-rays giving activity of T1/2=4.4 d. (T1/2= 50 y for g.s.) |
| 31316.010 | J,NP,69,153,1965 | 20-CA-40(N,T)19-K-38,,SIG | 1000 times too large | Table | No |  | Monitor cross section σ(56Fe(n,p)56Mn)=110 mb @ 14.8 MeV is not bad. No discussion in Z.T.Body et al., C,ANTWER,,368,1982 (EXFOR 30818.003). |
| 31543.006 | J,NP/A,722,568,2003 | 24-CR-54(N,N+P)23-V-53,,SIG | 1000 times too large? (threshold) | Table | No |  |  |
| 31602.002 | J,NIM/B,266,21,2008 | 72-HF-179(N,G)72-HF-180-M,,SIG | 1000 times too low | Table | Yes |  | DATA, ERR-T: MB→B In addition, ERR-T: 0.45 → 0.41 (003). |
| 32205.019 | J,NSTS,2,425,2002 | 57-LA-139(N,N+A)55-CS-135-M,,SIG | 1000 times too large? (threshold) | Author | Yes |  | MB → MICRO-B (Confirmed by UkrNDC, 2010-03-16) |
| 40244.048 | C,58GENEVA,15,50(2219),1958 | 23-V-51(N,G)23-V-52,,SIG | 1000 times too low | Table | Yes |  | DATA(-ERR): MB → B |
| 40244.049 | C,58GENEVA,15,50(2219),1958 | 25-MN-55(N,G)25-MN-56,,SIG | 1000 times too low | Table | Yes |  | DATA(-ERR): MB → B (049, 050) In addition, DATA → DATA-MAX (002, 009, 011, 017-018, 043, 045, 052, 058-059). Remove duplication pairs (e.g. 002=043+085) |
| 40336.102 | C,58GENEVA,15,18(2030),1958 | 22-TI-50(N,G)22-TI-51,,SIG | 1000 times too large | Table | Yes |  | B → MB (102) In addition, 5.9 +/- 0.0003 mb → 8.6 +/- 0.4 mb (096) |
| A0401.002 | J,JRN/L,128,403,1988 | 79-AU-197(A,G)81-TL-201,,SIG,,,EXP | 1000 times too large | Table | No |  | Add DECAY-DATA. Activation cross sections. Their decay data (0.16% and 10.6% for 165.9 keV and 167.4 keV gamma lines are good.). Experimental cross sections of 197Au(n,α)201Tl in EXFOR are scattered each other. The situation is depicted in Fig.3 in J,PAN,70,613,2007 (EXFOR F0858.005). |
| A0485.010 | J,YK,8,17,1990 | 12-MG-0(P,X)4-BE-7,,SIG,,,EXP | 10 times too low? (see also o0282005, C0095008) | Table | No |  | REFERENCE: J,YK,8,17,2001→J,VAT/I (1990) no. 8 p.17-24 In addition, STATUS: TABLE must be added (Taken from Table 2). ERR-ANALYSIS: “Data-point reader uncertainty” is probably incorrect. natMg(p,x)7Be cross section in Table 2 is consistent with Fig.9. |
| C0095.008 | J,ARI,41,349,1990 | (12-MG-0(P,X)4-BE-7,,SIG)+(8-O-0(P,X)4-BE-7,,SIG) | 10 times too high? (see A0485010.png) | Table | Yes? |  | SF8: Add FCT ? Data are for Mg(OH)2. Probably data are normalized to density of the molecule. Data close to twice of σ(natO(p,x)7Be) data in EXFOR C0401.002 and O0282.004. |
| C0265.008 | J,PR,131,1697,1963 | 23-V-51(A,N+2A)21-SC-46,,SIG | 1000 times too low | Table | Yes |  | MICRO-B→ MB (007-009) EN → EN-CM (010-013) 012: First three points should be coded under DATA-MAX. |
| C0703.004.2 | J,PR,133,B907,1964 | 28-NI-58(A,P)29-CU-61,,SIG,,,DERIV | 1000 times too low | Table | Yes |  | MICRO-B→ MB |
| C1159.003.1 | P,UCRL-115738-5,1,1993 | 39-Y-89(P,INL)39-Y-89,,SIG | wrong reaction? (threshold is wrong) | Table | Yes |  | SF3: INL, EL `→ X SF4: 39-Y-89 → 39-Y-87-M (003.1, 006.1) 39-Y-89 → 39-Y-87-G (003.2, 006.2) In addition, DECAY-DATA: T1/2 must be given.(c.f. Fig.1) METHOD: Add ACTIV. |
| C1523.004 | J,PR/C,29,764,1984 | 7-N-14(P,INL)7-N-14,PAR,SIG | 1000 times too low? (Partial xs) | Table | No |  | Partial for the 1st level. |
| D0433.002 | J,RCA,94,795,2006 | 23-V-0(P,X)23-V-48,,SIG | wrong reaction? (threshold is wrong by 30MeV) | Table | Yes |  | SF1: 23-V-0 → 22-TI-0 (002-006) |
| E1411.006 | J,PR/C,44,1405,1991 | 94-PU-242(P,F),,SIG | wrong shape? (but only 2 points at threshold) | Author | Yes |  | Swap two Ep values (12.0 MeV and 18.0 MeV). Misprint in the data table from authors. (Confirmed by Prof. T. Otsuki, 2010-03-16) |
| M0041.009 | J,NP/A,338,97,1980 | 73-TA-181(G,ABS),,SIG,,,EXP | wrong reaction? ("ATOMIC CROSS SECTION") | Table | Yes |  | Delete or add MSC in SF8 (002-014) Mainly from atomic interaction. |
| M0041.013 | J,NP/A,338,97,1980 | 79-AU-197(G,ABS),,SIG,,,EXP | wrong reaction? ("ATOMIC CROSS SECTION") | Table | Yes |  | (See above) |
| M0041.014 | J,NP/A,338,97,1980 | 83-BI-209(G,ABS),,SIG,,,EXP | wrong reaction? ("ATOMIC CROSS SECTION") | Table | Yes |  | (See above) |
| M0188.007 | J,NP/A,446,229(C),1985 | 13-AL-27(G,ABS),,SIG,,FCT,EVAL | 27 times too low ("XS WAS MULTIPLIED BY 1/A") | Author | No |  | FCT (times a factor) is indicated in SF8. In addition, this is not an experimental data set. |
| M0380.003 | J,JP/G,19,805,1993 | 73-TA-181(G,ABS),,SIG,,,EXP | 1000 times too low | Table | (Yes) | M051 | MICRO-B → MB (003, 005, 007) But they are not authors’ experimental data and have already deleted. |
| M0638.008 | J,PR/C,65,044622,2002 | 82-PB-0(G,F),,SIG,,FCT | 208 times too low ("XS WAS MULTIPLIED BY 1/A") | Table | No |  | DATA-ERR → ERR-S (008-013) FCT (times a factor) is indicated in SF8. |
| O0276.105 | J,NIM/B,129,153,1997 | 28-NI-0(P,X)24-CR-51,,SIG,,,EXP | xs value is wrong at EN = 126 MeV | Author | Yes |  | 0.037 mb → 37.0 mb @ 126 MeV (Confirmed by Prof.R.Michel, 2010-03-17) |
| O0282.005 | J,NIM/B,82,9,1993 | 12-MG-0(P,X)4-BE-7,,SIG | 10 times too low? (see A0485010.png) | Table | No |  |  |