Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/781 (Rev.)

Date:		15 April 2013

To:		Distribution

From:		N. Otsuka, S. Simakov

Subject:		Partial reaction and isomer production

The partial reaction and isomer production must be properly distinguished.

Example: 115In(n,n’)115mIn (Ex = 336 keV, T1/2 = 4.5 hrs) cross section for

- direct population of 115mIn by inelastically scattered neutrons resulting to this excitation level;

- “A” plus feeding from higher excitation levels to 115mIn.

Experimentally “A” can be determined by detection of the outgoing neutrons, while “B” can be determined by detection of gamma-ray transition from 115mIn to 115gIn .

The next figure shows experimental and evaluated cross sections for both cases. We observe significant difference above the threshold energy of the 2nd level excitation (~ 600 keV).

I believe that the cross sections for A and B should be coded as:

- (49-IN-115(N,INL)49-IN-115,PAR,SIG), E-LVL=336 keV

- (49-IN-115(N,INL)49-IN-115-M,,SIG), T1/2=4.5 hrs under DECAY-DATA.

However the underlined phrase of the following statement in LEXFOR “Partial Reactions” does not allow us to treat the direct population of an isomeric state (e.g., the quantity “A”) as a partial reaction:

In order to differentiate two cases appropriately, the following change (italicized part) in LEXFOR is proposed:

Differences between these two cases are summarized below:

|  | A. 115In(n,n1)115mIn | B. 115In(n,n’)115mIn |
| --- | --- | --- |
| Experiment |  |  |
| Detected particle | outgoing neutrons | IT transition gammas |
| EXFOR |  |  |
| REACTION (SF4-SF6) | IN-115,PAR,SIG | IN-115-M,SIG |
| E-LVL | 336 KEV | (not given) |
| DECAY-DATA | (not given) | 4.5 HOUR |
| ENDF-6 |  |  |
| MF | 3 (cross section) | 10 (production cross sections for radionuclides) |
| MT | 51 (Production of a neutron, with residual in the 1st excited state) | 4 (Production of one neutron in the exit channel) |

The following changes (italicized part) in LEXFOR “Reaction Product” and “Isomeric State” are also proposed:

1. LEXFOR “Reaction Product”

2. LEXFOR “Isomeric State”

In this opportunity, data sets coded with G+M or M+G in REACTION SF4 were extracted (Appendix B). These are illegal and must be deleted.

Appendix A. Definition of isomeric state and metastable state (LEXFOR)

An isomeric state is defined as a long-lived energy state, where long-lived is, generally, accepted as having a measurable half-life greater than ~0.1 sec.

A metastable state is an excited state having a half-life of the order of 0.1 seconds or longer. The term ‘isomeric states’ refers to the ground and all known metastable states.

Appendix B. Data sets with illegal combination of isomeric flags in SF4

| Subentry | REACTION |
| --- | --- |
| 20658.009 | 27-CO-59(N,G)27-CO-60-G+M,,RI/SUM,,RNV |
| 20658.023 | 55-CS-133(N,G)55-CS-134-G+M,,RI/SUM,,RNV |
| 21008.003 | (92-U-235(N,F)41-NB-97-G+M,IND,FY/SUM,,MXW)/ (92-U-235(N,F)MASS,CHN,FY,,MXW) |
| 22132.004 | 27-CO-59(N,2N)27-CO-58-M+G,,SIG |
| 31481.008 | 40-ZR-90(N,A)38-SR-87-M+G,,SIG |
| 41240.013 | 27-CO-59(N,2N)27-CO-58-M+G,,SIG |
| A0304.004.S | 46-PD-104(P,N)47-AG-104-G+M,,SIG |
| A0304.011.S | 46-PD-106(P,N)47-AG-106-G+M,,SIG |
| A0335.009 | 47-AG-109(HE3,N)49-IN-111-M+G,,SIG,,A,EXP |
| O0243.002.4 | 26-FE-58(P,N)27-CO-58-G+M,,SIG |
| O0243.003.4 | 26-FE-58(P,N)27-CO-58-G+M,,SIG |
| O0560.002.T | 94-PU-239(P,F)55-CS-134-M+G,,SIG |
| O0562.002 | 92-U-0(P,F)50-SN-113-M+G,IND,SIG |
| O0573.003 | 92-U-0(P,F)51-SB-120-M+G,IND,SIG |
| O0573.006 | 92-U-0(P,F)51-SB-124-M+G,,SIG |
| O0573.010 | 92-U-0(P,F)51-SB-126-M+G,IND,SIG |
| O0578.018 | (92-U-0(P,F)61-PM-148-M+G,IND,SIG)/ (92-U-0(P,F)MASS,,SIG,,,EVAL) |
| O0594.003 | 92-U-235(P,F)39-Y-90-M+G,IND,SIG |
| O0594.005 | 92-U-235(P,F)39-Y-91-M+G,IND,SIG |
| O0594.011 | 92-U-238(P,F)39-Y-90-M+G,IND,SIG |
| O0594.013 | 92-U-238(P,F)39-Y-91-M+G,IND,SIG |
| O0708.007 | 93-NP-237(P,F)55-CS-134-G+M,IND,SIG |
| O0721.003 | 92-U-235(P,F)55-CS-134-M+G,IND,SIG |
| O0721.006 | 92-U-233(P,F)55-CS-134-M+G,IND,SIG |
| O0768.204 | 82-PB-0(P,X)82-PB-195-M+G,IND,SIG |

Additional comments to the list

- O0573.003, 010, O0578.018, O0708.007, O0721.003, 006

SF5: Delete IND. No precursor exists.

- O0573.003, 006, 010

They are measured production cross sections for longer lived isomers multiplied by isomeric ratios reported by E.Hagebo (1967). Delete these data, or at least add DERIV in SF9 with an appropriate explanation under the keyword ANALYSIS.

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn

# Text boxes

Definition

A partial reaction, as defined for EXFOR, is a reaction leading to or proceeding through a specific level or emitting a specific gamma or particle group, and excludes isomeric states.

Definition

A partial reaction, as defined for EXFOR, is a reaction leading to or proceeding through a specific level or emitting a specific gamma or particle group, and excludes production of an isomeric state fed from higher levels to the isomeric state.

Definition

…

If no isomer code is given without PAR in SF5, then the reaction is to a nucleus in the ground state and includes decays from all isomeric states (i.e., all excitation levels). If an isomer code is given, a partial reaction for the formation of that isomeric state is given, and, in general, decays from higher the other isomeric states are not included. (See Isomeric States).

Examples:

(63-EU-151(N,G)63-EU-152,,SIG)

Sum of production cross sections for 152gEu (13.5 years), 152m1Eu (9.3 hours), and 152m2Eu (96 min)

(63-EU-151(N,G)63-EU-152-M1,,SIG)

Production cross sections for 152m1Eu (9.3 hours).

…

Coding

Where a nucleus has a known metastable state, (1) the target nucleus in an isomeric state, and (2) an isomeric state populated by direct production as well as by transition of higher levels to the isomeric state  are indicated by an isomer code following the isotope code, e.g., 95-AM-242-M1. (See EXFOR Exchange Formats Manual Chapter 6: Coding of nuclides and compounds)

Partial reactions leading to Isomeric states are coded by entering the isomer code in REACTION SF4. Sums and ratios are given algebraically.

Examples:	(…(…,…)Z-S-A-M1,,SIG)

(…(…,…)Z-S-A-M/G,,SIG/RAT)

(…(…,…)Z-S-A-M1+M2,,SIG)

Isomer codes are used in SF4 only for partial reactions. They must not be used when the total cross section (including isomeric decay) is measured, i.e., the extension G+M is never used.

…