Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/784

Date:		19 April 2013

To:		Distribution

From:		N. Otsuka

Subject:		Irradiation time for production thick target yield

Reference:	CP-D/631, CP-D/696

The physical thick target yield αphys is time independent, while the production thick target yield (i.e., unsaturated thick target yield) aprod depends on irradiation time t:

aprod (t) = αphys (1-e-λt) / λ ,

where λ is the decay constant of the reaction product. Addition of irradiation time in free text was proposed in Memo CP-D/631. Following discussion with Otto Schwerer on coding of thick target yields from BNL [1] (EXFOR C1954 transmitted in TRANS.C123), however, we concluded that irradiation time must be treated as coded information when we compile aprod. It is an essential variable for this quantity, and I would like to propose the following new heading code to implement this idea:

# Dictionary 24 (Data Headings)

TIME-IRRD	 Irradiation time

Reference

[1] D.G. Medvedev et al, Radiochim. Acta 99 (2011) 755 (EXFOR C1954).

Appendix: Determination of quantity code for EXFOR C1954

Articles reporting thick target yield (activity) often do not provide enough information for determination of EXFOR quantity code as discussed in Memo CP-D/696. It would be worthwhile to share my experience in determination of the quantity code for the 86Y (T1/2=15 hrs) yield compiled in EXFOR C1954 from Tables 2 and 3 of [1].

Among three thick target yields (activity) defined in EXFOR – (1) physical, (2) production (= unsaturated) and (3) saturated thick target yield, only physical one can be given in MBq/μAh (others must be in MBq/μA etc.). But the physical yield is time independent, and I was confused by “at EOB” (at the end of bombardment) in the caption of Table 3 of the article. Fortunately the corresponding author kindly explained me that the activity at EOB was divided by the accumulated charge to obtain the yield. The total activity after irradiation time t with current I can be expressed as I×aprod(t) while the total accumulated charge is expressed by I×t. Therefore the yield derived by the authors can be expressed as:

[I×aprod (t) ] / ( I×t ) = aprod (t) / t = αphys (1-e-λt) / λt ~ αphys.

The last approximation (~) is the “short irradiation approximation” (i.e., λt << 1).  The longer irradiation time in Table 2 (1 hr) and the half-life of 86Y (15 hrs) give

λt = ln 2 / T1/2 /t ~ 0.04.

Therefore the irradiation condition given in Table 2 probably satisfies the short irradiation approximation condition. But this logic is not described in the article, and I proposed Otto Schwerer to apply

,TTY,,(PHY) Thick target yield, uncertain if it is physical yield

to be on the safe side.

For this specific article case, fortunately I could receive key information from the corresponding author. But I would believe that the experimentalists should provide more clear derivation and definition of their thick target yields in general. A short article describing our problem is under preparation for submission to Radiochimica Acta.

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn