Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/785

Date:		19 April 2012

To:		Distribution

From:		N. Otsuka,

Subject:		Thick target production yield in charged-particle induced reaction

There are two conventions in normalization of the thick target production (e.g., neutron) yields:

- Y1: number of products per incident particle (e.g., 1 neutron/1 inc. proton)

- Y2: number of products per incident charge (e.g., 1 neutron/1 μCoulomb)

The second convention is more convenient for people who want to calculate yields from the beam current available at the facility.

These two normalizations are related by a simple (projectile type dependent) constant:

Y2=Y1 / (Ze),

where Z is the ionization charge state of the projectile and could be different from the atomic number of the projectile. Currently they are distinguished in both REACTION code and web quantity code levels.

Example: Thick target neutron production yield in 209Bi+p reaction

|  | REACTION code | Web quantity | Unit code |
| --- | --- | --- | --- |
| Y1 | (83-BI-209(P,X)0-NN-1,,PY,,TT) | PY | PRD/INC |
| Y2 | (83-BI-209(P,X)0-NN-1,,TTY/PY) | TT | PRD/MUCOUL |

There are several disadvantages due to this differentiation:

- Users should specify two web quantities PY and TT to receive a complete set of data sets;

- REACTION SF6=TTY and Web quantity= TT applied to Y2 are also used for thick target radioisotope activity A (e.g., Bq/ μCoulomb), for example,

(42-MO-0(P,X)43-TC-99-M,,TTY) - Saturated activity of 99mTc.

I would like to propose the following two changes:

1. Web quantity:

Apply PY to both Y1 and Y2 while apply TT to thick target induced activity.

2. REACTION code (SF5-SF8):

Apply ,PY,,TT for both Y1 and Y2.

If we still need to differentiate Y1 and Y2, I want to see very similar code, e.g., ,PY,,TT for Y1, and ,PY,,XX/TT for for Y2, where a new modifier XX stands for “per electric charge”.

Examples with proposed new rules (modified parts are underlined):

|  | REACTION code | Web quantity | Unit code |
| --- | --- | --- | --- |
| Y1 | (83-BI-209(P,X)0-NN-1,,PY,,TT) | PY | PRD/INC |
| Y2 | (83-BI-209(P,X)0-NN-1,,PY,,TT) or (83-BI-209(P,X)0-NN-1,,PY,,XX/TT) | PY | PRD/MUCOUL |
| A | (42-MO-0(P,X)43-TC-99-M,,TTY) | TT | MBQ/COUL |

I can volunteer to make retroactive corrections for entries maintained by other centres.

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn