Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/807

Date:		27 September 2013

To:		Distribution

From:		N. Otsuka, O. Schwerer

Subject:		Revision of LEXFOR “Fission Yields” and related dictionary 			additions

Reference:	CP-D/705 (=WP2011-31), CP-D/720

The following changes are proposed for LEXFOR “Fission Yields”:

- Revision of ”Yields of Correlated Fragment Pairs”

- Addition of “Energy Differential Fission Yield”

- Addition of “Quantities at Specific Total Kinetic Energy”

- Addition of “Quantities for Neutrons Emitted from a Specific Fragment”

Yields of Correlated Fragment Pairs

The Z and A of the correlated pair are entered under the field headings ELEM1, MASS1, and ELEM2, MASS2.

REACTION coding: CRN in SF5.

Example:

BIB

REACTION   (...(N,F)ELEM/MASS,IND/CRN,FY)

...

ENDBIB

COMMON

ELEM1      ELEM2

NO-DIM     NO-DIM

56.        42.

ENDCOMMON

DATA

MASS1      MASS2      DATA

NO-DIM     NO-DIM     PC/FIS

138.       104.       ...

138.       105.       ...

...        ...        ...

ENDDATA

…

Energy Differential Fission Yield (new section)

REACTION coding:  FY/DE in SF6.

Units:   a code from Dictionary 25 with the dimension FYDE (e.g., PC/FIS/MEV)

Example:

(98-CF-252(0,F),PRE,FY/DE,FF/LF+HF)

Differential yield of fission fragments with respect to total kinetic energy

(98-CF-252(0,F)MASS,PRE,FY/DE,LF+HF)

Differential yield of fission fragments specified with respect to total kinetic energy

Quantities at Specific Total Kinetic Energy (new section)

Total kinetic energy dependence of prompt fission neutron quantities (e.g., multiplicities, average emission energy) which is not partial for the total kinetic energy (i.e., not additive for total kinetic energy).

REACTION Coding: TKE in SF6.

Example:

(…(0,F),PR,NU/TKE)	Prompt fission neutron multiplicities at the total kinetic energy specified.

Quantities for Neutrons Emitted from a Specific Fragment (new section)

If a prompt fission neutron quantity (e.g., multiplicities, average emission energy) is given for a specific fragment (e.g., MASS in REACTION SF4) and the quantity is for neutrons emitted from the fragment specified, the branch code FRG is coded in SF5. Fragment mass dependence of such quantities Q(A) for fissioning of compound (mass Ac) is characterized by asymmetry with respect to the half of the compound mass Q(Ac-A) ≠ Q(A) (e.g., fragment mass dependence of fission neutron multiplicities known as “saw-tooth curve”).

Example:

(…(0,F)MASS,PR,NU)	Multiplicities of the prompt fission neutrons emitted with the fragment whose mass is specified.

(…(0,F)MASS,PR/FRG,NU)	Multiplicities of the prompt fission neutrons emitted from the fragment whose mass is specified.

(End of proposals of LEXFOR revision)

The addition of the last new section is related to revision of 14065.002, 004 and 006 [1] in PRELIM.1391 as well as 14369.002-004 [2] in PRELIM.1393, and we propose the following new codes:

Addition to dictionary 31 (Branch codes)

FRG	Referring to fragment specified

Additions to dictionary 236 (Quantities)

PR/FRG,NU	Multiplicity of prompt fission neutrons emitted from the fragment specified

PR/FRG,NU/TKE	Multiplicity of prompt fission neutrons emitted from the fragment specified at a given total kinetic energy

References:

[1] H.R. Bowman et al., Phys. Rev, 129 (1963) 2133 (EXFOR 14065).

[2] J.S. Fraser et al., Ann. Rev. Nucl. Phys. 16 (1966)379 (EXFOR 14369).

| Quantity | Reaction Type | Dim. | Subentries |
| --- | --- | --- | --- |
| PR/FRG,NU | NU | FY | 14065.002, 14369.002-004 |
| PR/FRG,NU/TKE | NUE | FY | 14065.004, 006 |

Distribution:

aikawa@jcprg.org

aloks279@gmail.com

blokhin@ippe.ru

cgc@ciae.ac.cn

emmeric.dupont@oecd.org

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

hongwei@ciae.ac.cn

jhchang@kaeri.re.kr

kaltchenko@kinr.kiev.ua

kamskaya@expd.vniief.ru

kato@nucl.sci.hokudai.ac.jp

kiralyb@atomki.hu

l.vrapcenjak@iaea.org

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

nklimova@kinr.kiev.ua

n.otsuka@iaea.org

nrdc@jcprg.org

oblozinsky@bnl.gov

ogritzay@kinr.kiev.ua

otto.schwerer@aon.at

pritychenko@bnl.gov

pronyaev@ippe.ru

r.forrest@iaea.org

samaev@obninsk.ru

s.babykina@polyn.kiae.su

scyang@kaeri.re.kr

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

vlasov@kinr.kiev.ua

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn