Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/893

Date:		23 February 2016

To:		Distribution

From:		N. Otsuka, S. Takács

Subject:		Incident Energy differential physical thick target yield (SF8=TM)

Reference:	CP-N/129, CP-A/155, CP-D/396, CP-A/152

LEXFOR “Thick- and Thin-Target Yields” explains that the production thick target yield per 1 MeV of target thickness is coded with TTY,,TM in REACTION SF6-SF8 and a unit code with dimension TTTE (e.g., CI/AHR/MEV), but it does not explain the idea of this quantity. As mentioned in Memo CP-A/155, this quantity has been typically seen in articles reporting charged-particle induced reaction activation experiments by the Milan group (M. Bonardi et al.).

The actual meaning of this quantity is the differential of the physical thick target yield with respect to the incident energy. From the equation of the LEXFOR entry, the physical thick target yield for the initial proton energy of E0 is

αphy(E0)=∫0E0dE[-(1/ρ)(dE/dx)]-1 σ(E) (1/Ze),

and its energy differential is

dαphy(E)/dE=(d/dE) ∫0E0dE’[-(1/ρ)(dE’/dx)]-1 σ(E’) (1/Ze)

= [-(1/ρ)(dE/dx)]-1 (1/Ze) σ(E),

where E is not a secondary energy but the incident energy. This equation implies that we can derive the cross section σ(E) by measuring the physical thick target yield at various incident energies.

In order to express the meaning of the quantity more appropriately, we propose to make obsolete two relevant quantity codes ,TTY,,TM and CUM,TTY,,TM, and replace them with ,TTY/DEN,,PHY and CUM,TTY/DEN,,PHY, where a new parameter code DEN is introduced to express “differential with respect to the incident energy”.

Dictionary 32 (Parameters)

DEN	Differential with incident energy

Dictionary 34 (Modifiers)

TM	(Obsolete)

Dictionary 236 (Quantities)

,TTY,,TM		(Obsolete)

CUM,TTY,,TM		(Obsolete)

,TTY/DEN,,PHY	Physical thick target yield differential with respect to incident energy

CUM,TTY/DEN,,PHY	Cumulative physical thick target yield differential with respect to incident energy

M+,TTY/DEN,,PHY	Physical thick target yield differential with respect to incident energy including formation by partial feeding via isomeric transition

There are 13 affected existing entries of which 1 is from area A, 2 are from area O, and 10 are from area D. If this proposal is accepted, M+,TTY/DEN,,PHY replaces M+,TTY,,TM proposed in Memo CP-N/129.

Revision of LEXFOR

Production Thick Target Yield per 1 MeV of Target Thickness

REACTION Coding: TTY,,TM in SF 6.

Units: a code from Dictionary 25 with dimension TTTE, e.g., CI/AHR/MEV

Physical Thick Target Yields Differential with respect to Incident Energy

REACTION Coding: ,TTY/DEN,,PHY.

Units: a code from Dictionary 25 with dimension TTTE, e.g., MBQ/C/MEV

Distribution:

aikawa@jcprg.org

a.koning@iaea.org

aloks279@gmail.com

cgc@ciae.ac.cn

dvoytenkov@ippe.ru

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

iwamoto.osamu@jaea.go.jp

jhchang@kaeri.re.kr

jmwang@ciae.ac.cn

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

n.otsuka@iaea.org

nrdc@jcprg.org

nurzat.kenzhebaev@gmail.com

ogritzay@kinr.kiev.ua

oscar.cabellos@oecd.org

otto.schwerer@aon.at

pikulina@expd.vniief.ru

pritychenko@bnl.gov

samaev@obninsk.ru

sbabykina@yandex.ru

scyang@kaeri.re.kr

selyankina@expd.vniief.ru

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn