Nuclear Data Section

International Atomic Energy Agency

P.O.Box 100, A-1400 Vienna, Austria

Memo CP-D/896

Date:		16 March 2016

To:		Distribution

From:		N. Otsuka, M. Mikhailiukova

Subject:		Two additions to LEXFOR “Isomeric flag”

Reference:	Memo CP-D/888

- Assignment of isomeric states

LEXFOR “Isomeric flag” mentions that the assignment of isomeric states for a given nucleus may vary in the literature according to the growing knowledge of a particular nucleus though it does not give any advice on selection of the isomeric flag to us.

A major example is 110In for which it is now known that the 69 min state is ~60 keV higher than the 4.9 hr ground state. However the 69 min state is often treated as the ground state in the old literature. F. Tárkányi [1] gives the following remark in his report on natCd(p,x)110mIn and 110gIn excitation functions: Here we have to notice that there is confusion in the literature regarding the ground and metastable state of this nucleus and we put Nortier’s, Kormali’s, Otozai’s and Skakun’s results on the proper category if it was necessary.

Many EXFOR users do not check half-lives coded under DECAY-DATA when they select data sets from search results and plot them. If we always adopt the assignment by the authors for REACTION SF4 coding, it could be a source of confusions for EXFOR users. In order to avoid it, addition of the following addition to “Assignment of Isomeric States” of this LEXFOR entry is proposed:

The compiler should assign the isomer code based on the current knowledge of the structure and decay data while the decay data given by the authors must be kept.

Example

Now the 4.9 hr state of 110In is known as the ground state to which isomeric transition from the 69 min metastable state is absent. When an article gives “110mIn (4.9 hr) production cross section”, 49-IN-110-G must be used in REACTION SF4 but the half-life reported in the article (4.9 hr) must be kept under DECAY-DATA.

- Order of isomeric flags in algebraic sums in REACTION SF4

In order to standardize the order of isomeric flags appearing in their sums in REACTION SF4, the following addition is proposed.

Isomeric flags appearing in their sums should be sorted in order of G, M1, M2, e.g., –G+M1 instead of -M1+G.

Reference

[1] F. Tárkányi et al., Nucl. Instrum. Meth. B245 (2006) 379.

Existing codes affected by this new rule (REACTION, MONITOR, ASSUMED)

| REACTION |  |  | Remark |
| --- | --- | --- | --- |
| 22069.003 | 61-PM-148-M/M+G | -M/M+G -> -M/T |  |
| 22637.069 | 63-EU-152-M2+G | -M2+G => -G+M2 |  |
| 22658.010 | 63-EU-152-M2+G | -M2+G => -G+M2 |  |
| 22919.006 | 63-EU-152-M2/M2+G | -M2/M2+G > -M2/G+M2 |  |
| 31411.005 | 77-IR-192-M1+G | -M1+G -> -G+M1 |  |
| 31638.003 | 77-IR-192-M1+G | -M1+G -> -G+M1 |  |
| A0222.008 | 79-AU-196-M1+G | -M1+G -> -G+M1 |  |
| D4192.002 | 77-IR-192-M1+G | -M1+G -> -G+M1 |  |
| G4041.002 | 52-TE-123-M/M+G | -M/M+G -> -M/T |  |
| O1267.005 | 67-HO-158-M1+G | -M1+G -> -G+M1 | in PRELIM.O056 |
| MONITOR |  |  | Remark |
| 21571.001 | 79-AU-198-M+G | Delete –M+G. |  |
| 31511.001 | 27-CO-58-M+G | Delete –M+G. |  |
| 31515.001 | 27-CO-58-M+G | Delete –M+G. |  |

Distribution:

aikawa@jcprg.org

a.koning@iaea.org

aloks279@gmail.com

cgc@ciae.ac.cn

dvoytenkov@ippe.ru

dbrown@bnl.gov

fukahori.tokio@jaea.go.jp

ganesan555@gmail.com

gezg@ciae.ac.cn

iwamoto.osamu@jaea.go.jp

jhchang@kaeri.re.kr

jmwang@ciae.ac.cn

kaltchenko@kinr.kiev.ua

kato@nucl.sci.hokudai.ac.jp

kiyoshi.matsumoto@oecd.org

manuel.bossant@oecd.org

manokhin@ippe.ru

marema08@gmail.com

mmarina@ippe.ru

mwherman@bnl.gov

nicolas.soppera@oecd.org

n.otsuka@iaea.org

nrdc@jcprg.org

nurzat.kenzhebaev@gmail.com

ogritzay@kinr.kiev.ua

oscar.cabellos@oecd.org

otto.schwerer@aon.at

pikulina@expd.vniief.ru

pritychenko@bnl.gov

samaev@obninsk.ru

sbabykina@yandex.ru

scyang@kaeri.re.kr

selyankina@expd.vniief.ru

s.simakov@iaea.org

stakacs@atomki.hu

stanislav.hlavac@savba.sk

sv.dunaeva@gmail.com

taova@expd.vniief.ru

tarkanyi@atomki.hu

vvvarlamov@gmail.com

v.semkova@iaea.org

v.zerkin@iaea.org

yolee@kaeri.re.kr

zhuangyx@ciae.ac.cn