### UCRL-ID-127776, Rev. 2

# POINT 2003

# A Temperature Dependent

ENDF/B-VI, Release 8

Cross Section Library

by

Dermott E. Cullen

University of California

Lawrence Livermore National Laboratory

P.O. Box 808

L-159

Livermore, CA 94550

tele: 510-423-7359

# E. Mail: cullen1@llnl.gov

website: http://www.llnl.gov/cullen1

May 22, 2003

Approved for public release; further dissemination unlimited.

# DISCLAIMER

This document was prepared as an account of work sponsored by an agency of the United States Government.  Neither the United States Government nor the University of California nor any of their employees, makes any warranty, express or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise, does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States Government or the University of California.  The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States Government or the University of California, and shall not be used for advertising or product endorsement purposes.

Work performed under the auspices of the U. S. Department of Energy by the University of California Lawrence Livermore National Laboratory under Contract W-7405-Eng-48.

This report has been reproduced

directly from the best available copy.

Available to DOE and DOE contractors from the

Office of Scientific and Technical Information

P.O. Box 62, Oak Ridge, TN  37831

Prices available from (423) 576-8401

http://apollo.osti.gov/bridge/

Available to the public from the

National Technical Information Service

U.S. Department of Commerce

5285 Port Royal Rd.,

Springfield, VA  22161

http://www.ntis.gov/

OR

Lawrence Livermore National Laboratory

Technical Information Department’s Digital Library

http://www.llnl.gov/tid/Library.html

### UCRL-ID-127776, Rev. 2

POINT 2003

A Temperature Dependent

ENDF/B-VI, Release 8

Cross Section Library

by

Dermott E. Cullen

University of California

Lawrence Livermore National Laboratory

P.O. Box 808

L-159

Livermore, CA 94550

tele: 510-423-7359

# E. Mail: cullen1@llnl.gov

website: http://www.llnl.gov/cullen1

May 22, 2003

###### Introduction

The ENDF/B data library has recently been updated and is now freely available through the National Nuclear Data Center (NNDC), Brookhaven National Laboratory. This most recent library is identified as ENDF/B-VI, Release 8. Release 8 completely supersedes all preceding releases. Release 8 will be the last release of ENDF/B-VI; the next release of ENDF/B data will be for the new ENDF/B-VII library.

As distributed the ENDF/B-VI, Release 8 data includes cross sections represented in the form of a combination of resonance parameters and/or tabulated energy dependent cross sections, nominally at 0 Kelvin temperature.

For use in applications this library has been processed into the form of temperature dependent cross sections at eight temperatures between 0 and 2100 Kelvin, in steps of 300 Kelvin. At each temperature the cross sections are tabulated and linearly interpolable in energy.

All results are in the computer independent ENDF/B-VI character format [1], which allows the data to be easily transported between computers. In its processed form this library is approximately 1.6 gigabyte in size and is distributed on three CDs.

Earlier Versions of ENDF/B-VI

Between the original distribution (Release 0) and Release 2 libraries, 74 evaluations were updated and distributed in July 1994 (see, UCRL-ID-117797). Between Release 2 and 3 libraries, 18 evaluations were updated and distributed in January 1996 (see, UCRL-ID-124171). Between Release 0 and 3 no completely new evaluations were added to the library. Between Release 3 and 4(see, UCRL-ID-127776), 87 evaluations were updated and five completely new evaluations were added, namely for Gd152, Gd154, Ir191, Ir193 and Pu236. In additional the evaluation for natural Cd was deleted and replaced by evaluations for the individual isotopes. Between  Release 4 and 7, 68 materials were modified; mostly to extend the cross sections from 20 to 150 MeV, and three new evaluations were added (14-Si-28, 14-Si-29, 14-Si-30). The result was a library of 324 evaluations.

For details, see the above mentioned three reports: UCRL-ID-117797, UCRL-ID-124171, and UCRL-ID-127776.

ENDF/B-VI, Release 8 Data

Between the last version of this library (POINT2000), which was based on release 7 data, and the current version (POINT2003), which is based on release 8 data, a direct cross section by cross section comparison will show minor (fraction of a %) differences in many cross sections, mainly due to improvements in the precision of the PREPRO2002 codes; these differences are not listed here. There are also many changes to the data that are not processed by PREPRO, this includes delayed neutron data, and neutron induced photon production data, that were not included in earlier versions of these evaluations; these changes are widespread throughout the library are also not listed here.

The following lists only significant changes to the evaluations cross sections (listed below in ascending ZA order),

Material 	Changes

4-Be-9	(n,t) 12 to 20 MeV

8-O-16	New cross sections

16-S –Nat	I removed bogus “fission widths” from resonance parameters

(note that this is the same correction I made for Release 7???)

17-Cl-35	New evaluation

17-Cl-37	New evaluation

42-Mo-95	New elastic and capture

43-Tc-99	New elastic and capture

44-Ru-101	New elastic and capture

45-Rh-103	New elastic and capture

46-Pd-105	New elastic and capture

47-Ag-109	New elastic and capture

50-Sn-120	New above 10 keV

50-Sn-122	New above 10 keV

50-Sn-124	New above 10 keV

51-Sb-121	New elastic, capture and inelastic

51-Sb-123	New elastic, capture and inelastic

54-Xe-131	New elastic and capture

60-Nd-143	New elastic and capture

60-Nd-145	New elastic and capture

62-Sm-147	New elastic and capture

62-Sm-150	New elastic and capture

62-Sm-151	New elastic and capture

62-Sm-152	Minor changes at upper end of resolved resonance region

64-Gd-155	New elastic and capture

64-Gd-157	New elastic and capture

91-Pa-232	New evaluation

92-U- 232	New elastic, inelastic, fission and capture

93-Np-236	New evaluation

The result is a library of 328 evaluations.

## PREPRO2002 Codes

In addition to the changes in the ENDF/B-VI evaluations, it should be noted that between the last version of this report, where the PREPRO2000 codes were used, and the current version, where the PREPRO2002 codes were used, there have been major improvements in the ENDF/B Pre-processing codes. The major improvements were both in terms of improving the basic methods used by the codes and in terms of incorporating the latest ENDF/B-VI Formats and Procedures used by the current evaluations. The result is more accurate cross section data throughout the POINT2003 library.

WARNING – due to recent changes in ENDF/B-VI Formats and Procedures only the latest version of the ENDF/B Pre-processing codes, namely PREPRO2002, can be used to accurately process all current ENDF/B-VI evaluations. If you fail to heed this warning and you use any earlier versions of these codes the results will be inaccurate.

The PREPRO2002 codes run on virtually any computer, and are now available FREE on-line from the Nuclear Data Section, IAEA, Vienna, Austria, website at,

http://www-nds.iaea.or.at/ndspub/endf/prepro/

## Requesting this Data

Please do not contact the author of this report to request this data; I do not have the resources necessary to directly respond to requests for this data. This data has been distributed to and is Internationally available from nuclear data/code centers throughout the World,

- Within the United States: contact the National Nuclear Data Center, Brookhaven National Laboratory, Vicki McLane at services@bnlnd2.dne.bnl.gov

- Within Western Europe: contact the OECD Nuclear Energy Agency/ Data Bank (NEA/DB), Paris, France, Enrico Sartori at sartori@nea.fr

- Otherwise: contact the Nuclear Data Section, international Atomic Energy Agency, Vienna, Austria, Vladimir Pronyaev at v.pronyaev@iaea.org

Data Processing

As distributed the original evaluated data includes cross sections represented in the form of a combination of resonance parameters and/or tabulated energy dependent cross sections, nominally at 0 Kelvin temperature. For use in applications, this data has been processed using the 2002 version of the ENDF/B Pre-processing codes (PREPRO2001) to produce temperature dependent, linearly interpolable in energy, tabulated cross sections, in the ENDF/B-VI format.

Data is included for eight temperatures between 0 and 2100 Kelvin, in steps of 300 Kelvin.

The steps required and codes used to produce room temperature, linearly interpolable tabulated cross sections, in the ENDF/B-VI format, are described below (the name of each code in given in parenthesis; for details of each code see reference [2]).

Here are the steps, and PREPRO2002 codes, used to process the data, in the order in which the codes were used.

1) Linearly interpolable, tabulated cross sections (LINEAR)

2) Including the resonance contribution (RECENT)

3) Doppler broaden all cross sections to temperature (SIGMA1)

- Check data, define redundant cross sections by summation (FIXUP)

- Update evaluation dictionary in MF/MT=1/451 (DICTIN)

For the "cold" (0 Kelvin) data steps 1), 2) and 4), 5) were used. For the data at other temperatures, after steps 1) and 2), the data was Doppler broadened to each temperature using step 3), and the results were then made consistent with the ENDF/B formats and conventions using steps 4) and 5), to produce the final distributed data.

The result is linearly interpolable in energy, tabulated, temperature dependent cross sections, in the ENDF/B-VI format, ready to be used in applications.

Note - this processing only involved the energy dependent neutron cross sections. All other data in the evaluations, e.g., angular and energy distributions, was not affected by this processing, and is identical in all versions of the final results, i.e., it is the same in all of the directories, ORIGINAL, as well as K0 through K2100, on the CDs.

Accuracy of Results

Each of the codes described above that was used to process data to obtain tabulated, linearly interpolable in energy cross sections, processed the data to within a user defined accuracy, or allowable uncertainty. The ENDF/B Pre-processing codes (PREPRO2002) are self-documenting, in the sense that the ENDF/B formatted output data that each code produces includes comments at the beginning of each evaluation defining the accuracy to which the cross sections were calculated. The combination of comments added by all of the codes defines the sequence and accuracy used by all of them. The accuracy is the same for all evaluations. Therefore, for exact details of the accuracy of the data, see the comments at the beginning of any evaluation.

The current results were generated using an energy dependent accuracy, to allow the low energy cross sections, where there are no narrow resonances, to be generated to much higher accuracy, without a significant increase in the overall size of the data base. This was done in order to improve the cross sections for use in thermal and slow neutron applications. Again, for details see the comments in any evaluation.

Contents of the Library

This library contains all of the evaluations in the ENDF/B-VI general purpose library. The following table summarizes the contents of the ENDF/B-VI general purpose library. This library contains evaluations for 328 materials (isotopes or naturally occurring elemental mixtures of isotopes).

This library does not contain data from special purpose ENDF/B-VI libraries, such as fission products, thermal scattering, photon interaction data. To obtain any of these special purpose libraries contact the National Nuclear Data Center, Brookhaven National Laboratory,

ENDF@bnlnd2.dne.bnl.gov

In this library each evaluation is stored as a separate file. The following table defines each material and the corresponding filename. The entire library is in the computer independent ENDF/B-VI character format, which allows the data to be easily transported between computers. The entire library requires approximately 1.6 gigabyte of storage and is distributed on three CDs; see below for details of the CD contents.

This library contains data for some metastable materials, which are indicated by an "M" at the end of their descriptions.

The majority of these evaluations are complete, in the sense that they include all cross sections over the energy range 10-5 eV to at least 20 MeV. However, the following are only partial evaluations that either only contain single reactions and no total cross section (Mg24, K41, Ti46, Ti47, Ti48, Ti50 and Ni59), or do not include energy dependent cross sections above the resonance region (Ar40, Mo92, Mo98, Mo100, In115, Sn120, Sn122 and Sn124).

CD Format and Layout

The CDs were written using ISO 9660 format that can be read on almost any computer. One restriction of the ISO 9660 format is that it is similar to DOS diskettes, in that it does not distinguish between upper and lower case characters. Therefore when the data is read from the CDs, on some computers the filenames will end up in upper case, and on other computers they will be lower case.

The three CDs are divided into ten directories,

CD # 1

DOCUMENT	- A copy of this report in various formats.

ORIGINAL	- The original ENDF/B data before it was processed.

K0		- 0 Kelvin cross sections

K300		- 300 Kelvin cross sections

CD # 2

K600		- 600 Kelvin cross sections

K900		- 900 Kelvin cross sections

K1200		- 1200 Kelvin cross sections

CD # 3

K1500		- 1500 Kelvin cross sections

K1800		- 1800 Kelvin cross sections

K2100		- 2100 Kelvin cross sections

With the exception of DOCUMENT, each of these directories contains 328 files, one file for each evaluation. Each file is a complete ENDF/B "tape" [1], including a starting "tape" identification line, and ending with a "tape" end line [1]. In this form, each file can be used by a wide variety of available computer codes that treat data in the ENDF/B format, e.g., all of the PREPRO codes.

The Effects of Temperature and Doppler Broadening

For those readers who are not familiar with the effects of temperature and Doppler broadening on neutron cross sections and transport, I suggest that you read references [3] and [4], listed below.

Users of neutron cross sections should be aware that there are several important effects of temperature and Doppler broadening,

1) There is the well known effect in the neutron resonance region, where as the temperature increases resonances become broader, hence the name Doppler broadening. Figure 1 illustrates the effect of temperature on the U238 capture cross section. From this figure we can see that as temperature increases the peaks of the resonances become lower, and the minima between resonances become higher. At extremely high temperature the entire resonance structure disappears and the cross sections approaches a simple 1/v (where v is the neutron speed) shape. This temperature effect will have a very important effect on resonance self-shielding in any neutron transport calculation.

2) Another, less well known, effect of Doppler broadening is at lower energies where as temperature increases the low energy constant scattering cross section increases, and at very low energies approaches a simple 1/v (where v is the neutron speed) shape; this effect is explained in detail in ref [3]. Figure 2 illustrates the effect of temperature on the hydrogen total cross section. From this figure we can see that starting from a “cold” (0 Kelvin) cross section that is constant at about 20 barns, as temperature increases the cross section increases. Compared to the “cold” 20 barn cross section, at thermal energy the Doppler broadened cross section is about 30 barns, i.e., 50 % higher. Note also from this figure that this effect extends well above thermal energy. For example, at 300 Kelvin the thermal energy is 0.0253 eV, but we can see this effect up to about 1 eV. From the lower half of figure 2 we can see that at very low energy the cross section approaches 1/v (where v is the neutron speed) and the cross sections at various temperatures become proportional to one another. This effect on the cross sections at low energy is very important for thermal and low energy neutron systems.

3) Yet another important effect of temperature is that at lower energies neutrons do not slow down in energy as quickly and neutron scatter can even result in the upscatter of neutrons, i.e., when neutrons scatter they can gain, rather than lose, energy. This is a well known effect at low energies, where thermal scattering law data or a free gas model is used to model the interaction of neutrons with target atoms that are moving about with thermal motion. This effect can also be important at higher energies, particularly near narrow resonances, where thermal motion of the target atoms can cause neutrons to slightly upscatter, but even slight upscatter can cause a neutron to scatter from below to above the energy of a very narrow resonance. See reference [4], below for a routine designed to be used in conjunction with the SIGMA1 method of Doppler broadening [3], to handle neutron thermal scattering. This routine [4] is completely compatible for use with the cross sections included here, since these cross sections were Doppler broadened using the SIGMA1 method [3].

The combination of SIGMA1 [3] Doppler broadened cross sections and THERMAL [4] to handle thermal scattering, is currently used in the TART Monte Carlo transport code [5].

Acknowledgments

I thank Vicki McLane and Marion Blennau, of the National Nuclear Data Center (NNDC), Brookhaven National Laboratory, for supplying the original ENDF/B, Release 8 data, used in this project. I thank Vladimir Pronyaev and Kevin McLaughlin, of the Nuclear Data Section, International Atomic Energy Agency, for supplying the ENDF/B Pre-processing codes, PREPRO2002, used in this project. I thank Bob MacFarlane, Maurice Greene, and Mike Dunn, for benchmarking their cross section processing codes (NJOY and AMPX) against the PREPRO2002 codes. These comparisons have led to significant improvements in the accuracy and reliability of the results produced by all three codes (NJOY, AMPX, PREPRO).

References

[1] Data Formats and Procedures for the Evaluated Nuclear Data File ENDF-6, BNL-NCS-44945, Rev. 11/95, edited by V. McLane, C.L. Dunford, P.F. Rose, National Nuclear Data Center, Brookhaven National Laboratory

[2] "PREPRO2002: The 2002 ENDF/B Pre-Processing Codes," by D.E. Cullen, Nuclear Data Section, International Atomic Energy Agency, Vienna, Austria, IAEA-NDS-39, Rev. 11, April 1, 2002.

[3] "Exact Doppler Broadening of Tabulated Cross Sections," by D.E. Cullen and C.R. Weisbin, Nuclear Science and Engineering 60, p. 199 (1975)

[4] "THERMAL: A Routine Designed to Calculate Neutron Thermal Scattering," by D.E. Cullen, Lawrence Livermore National Laboratory, UCRL-ID-120560-Rev-1, Sept. 1995.

[5] “TART2002: A Coupled Neutron-Photon 3-D, Time Dependent, Combinatorial Geometry Monte Carlo Transport Code," by D.E. Cullen, Lawrence Livermore National Laboratory, UCRL-ID-126455, Rev. 4, November, 2002.

ENDF/B-VI Release 8 Library (Z = 1 to 51) New Release 8 Evaluations in RED

Filename     Material

ZA001001      1-H -1

ZA001002      1-H -2

ZA001003      1-H -3

ZA002003      2-He-3

ZA002004      2-He-4

ZA003006      3-Li-6

ZA003007      3-Li-7

ZA004009      4-Be-9

ZA005010      5-B -10

ZA005011      5-B -11

ZA006000      6-C -Nat

ZA007014      7-N -14

ZA007015      7-N -15

ZA008016      8-O -16

ZA008017      8-O -17

ZA009019      9-F -19

ZA011023     11-Na-23

ZA012000     12-Mg-Nat

ZA012024     12-Mg-24

ZA013027     13-Al-27

ZA014000     14-Si-Nat

ZA014028     14-Si-28

ZA014029     14-Si-29

ZA014030     14-Si-30

ZA015031     15-P -31

ZA016000     16-S -Nat

ZA016032     16-S -32

ZA017000     17-Cl-Nat

ZA017035     17-Cl-35

ZA017037     17-Cl-37

ZA018040     18-Ar-40

ZA019000     19-K -Nat

ZA019041     19-K -41

ZA020000     20-Ca-Nat

ZA021045     21-Sc-45

ZA022000     22-Ti-Nat

ZA022046     22-Ti-46

ZA022047     22-Ti-47

ZA022048     22-Ti-48

ZA022050     22-Ti-50

ZA023000     23-V -Nat

ZA024050     24-Cr-50

ZA024052     24-Cr-52

ZA024053     24-Cr-53

ZA024054     24-Cr-54

ZA025055     25-Mn-55

ZA026054     26-Fe-54

ZA026056     26-Fe-56

ZA026057     26-Fe-57

ZA026058     26-Fe-58

ZA027059     27-Co-59

ZA028058     28-Ni-58

ZA028059     28-Ni-59

ZA028060     28-Ni-60

ZA028061     28-Ni-61

Filename     Material

ZA028062     28-Ni-62

ZA028064     28-Ni-64

ZA029063     29-Cu-63

ZA029065     29-Cu-65

ZA031000     31-Ga-Nat

ZA032072     32-Ge-72

ZA032073     32-Ge-73

ZA032074     32-Ge-74

ZA032076     32-Ge-76

ZA033075     33-As-75

ZA034074     34-Se-74

ZA034076     34-Se-76

ZA034077     34-Se-77

ZA034078     34-Se-78

ZA034080     34-Se-80

ZA034082     34-Se-82

ZA035079     35-Br-79

ZA035081     35-Br-81

ZA036078     36-Kr-78

ZA036080     36-Kr-80

ZA036082     36-Kr-82

ZA036083     36-Kr-83

ZA036084     36-Kr-84

ZA036085     36-Kr-85

ZA036086     36-Kr-86

ZA037085     37-Rb-85

ZA037086     37-Rb-86

ZA037087     37-Rb-87

ZA038084     38-Sr-84

ZA038086     38-Sr-86

ZA038087     38-Sr-87

ZA038088     38-Sr-88

ZA038089     38-Sr-89

ZA038090     38-Sr-90

ZA039089     39-Y -89

ZA039090     39-Y -90

ZA039091     39-Y -91

ZA040000     40-Zr-Nat

ZA040090     40-Zr-90

ZA040091     40-Zr-91

ZA040092     40-Zr-92

ZA040093     40-Zr-93

ZA040094     40-Zr-94

ZA040095     40-Zr-95

ZA040096     40-Zr-96

ZA041093     41-Nb-93

ZA041094     41-Nb-94

ZA041095     41-Nb-95

ZA042000     42-Mo-Nat

ZA042092     42-Mo-92

ZA042094     42-Mo-94

ZA042095     42-Mo-95

ZA042096     42-Mo-96

ZA042097     42-Mo-97

ZA042098     42-Mo-98

Filename     Material

ZA042099     42-Mo-99

ZA042100     42-Mo-100

ZA043099     43-Tc-99

ZA044096     44-Ru-96

ZA044098     44-Ru-98

ZA044099     44-Ru-99

ZA044100     44-Ru-100

ZA044101     44-Ru-101

ZA044102     44-Ru-102

ZA044103     44-Ru-103

ZA044104     44-Ru-104

ZA044105     44-Ru-105

ZA044106     44-Ru-106

ZA045103     45-Rh-103

ZA045105     45-Rh-105

ZA046102     46-Pd-102

ZA046104     46-Pd-104

ZA046105     46-Pd-105

ZA046106     46-Pd-106

ZA046107     46-Pd-107

ZA046108     46-Pd-108

ZA046110     46-Pd-110

ZA047107     47-Ag-107

ZA047109     47-Ag-109

ZA047111     47-Ag-111

ZA048106     48-Cd-106

ZA048108     48-Cd-108

ZA048110     48-Cd-110

ZA048111     48-Cd-111

ZA048112     48-Cd-112

ZA048113     48-Cd-113

ZA048114     48-Cd-114

ZA048115.M   48-Cd-115m

ZA048116     48-Cd-116

ZA049000     49-In-Nat

ZA049113     49-In-113

ZA049115     49-In-115

ZA050112     50-Sn-112

ZA050114     50-Sn-114

ZA050115     50-Sn-115

ZA050116     50-Sn-116

ZA050117     50-Sn-117

ZA050118     50-Sn-118

ZA050119     50-Sn-119

ZA050120     50-Sn-120

ZA050122     50-Sn-122

ZA050123     50-Sn-123

ZA050124     50-Sn-124

ZA050125     50-Sn-125

ZA050126     50-Sn-126

ZA051121     51-Sb-121

ZA051123     51-Sb-123

ZA051124     51-Sb-124

ZA051125     51-Sb-125

ENDF/B-VI Release 8 Library (Z = 51 to 99) New Release 8 Evaluations in RED

Filename     Material

ZA051126     51-Sb-126

ZA052120     52-Te-120

ZA052122     52-Te-122

ZA052123     52-Te-123

ZA052124     52-Te-124

ZA052125     52-Te-125

ZA052126     52-Te-126

ZA052127.M   52-Te-127m

ZA052128     52-Te-128

ZA052129.M   52-Te-129m

ZA052130     52-Te-130

ZA052132     52-Te-132

ZA053127     53-I -127

ZA053129     53-I -129

ZA053130     53-I -130

ZA053131     53-I -131

ZA053135     53-I -135

ZA054124     54-Xe-124

ZA054126     54-Xe-126

ZA054128     54-Xe-128

ZA054129     54-Xe-129

ZA054130     54-Xe-130

ZA054131     54-Xe-131

ZA054132     54-Xe-132

ZA054133     54-Xe-133

ZA054134     54-Xe-134

ZA054135     54-Xe-135

ZA054136     54-Xe-136

ZA055133     55-Cs-133

ZA055134     55-Cs-134

ZA055135     55-Cs-135

ZA055136     55-Cs-136

ZA055137     55-Cs-137

ZA056134     56-Ba-134

ZA056135     56-Ba-135

ZA056136     56-Ba-136

ZA056137     56-Ba-137

ZA056138     56-Ba-138

ZA056140     56-Ba-140

ZA057139     57-La-139

ZA057140     57-La-140

ZA058140     58-Ce-140

ZA058141     58-Ce-141

ZA058142     58-Ce-142

ZA058143     58-Ce-143

ZA058144     58-Ce-144

ZA059141     59-Pr-141

ZA059142     59-Pr-142

ZA059143     59-Pr-143

ZA060142     60-Nd-142

ZA060143     60-Nd-143

ZA060144     60-Nd-144

ZA060145     60-Nd-145

ZA060146     60-Nd-146

ZA060147     60-Nd-147

Filename     Material

ZA060148     60-Nd-148

ZA060150     60-Nd-150

ZA061147     61-Pm-147

ZA061148     61-Pm-148

ZA061148.M   61-Pm-148m

ZA061149     61-Pm-149

ZA061151     61-Pm-151

ZA062144     62-Sm-144

ZA062147     62-Sm-147

ZA062148     62-Sm-148

ZA062149     62-Sm-149

ZA062150     62-Sm-150

ZA062151     62-Sm-151

ZA062152     62-Sm-152

ZA062153     62-Sm-153

ZA062154     62-Sm-154

ZA063151     63-Eu-151

ZA063152     63-Eu-152

ZA063153     63-Eu-153

ZA063154     63-Eu-154

ZA063155     63-Eu-155

ZA063156     63-Eu-156

ZA063157     63-Eu-157

ZA064152     64-Gd-152

ZA064154     64-Gd-154

ZA064155     64-Gd-155

ZA064156     64-Gd-156

ZA064157     64-Gd-157

ZA064158     64-Gd-158

ZA064160     64-Gd-160

ZA065159     65-Tb-159

ZA065160     65-Tb-160

ZA066160     66-Dy-160

ZA066161     66-Dy-161

ZA066162     66-Dy-162

ZA066163     66-Dy-163

ZA066164     66-Dy-164

ZA067165     67-Ho-165

ZA068166     68-Er-166

ZA068167     68-Er-167

ZA071175     71-Lu-175

ZA071176     71-Lu-176

ZA072000     72-Hf-Nat

ZA072174     72-Hf-174

ZA072176     72-Hf-176

ZA072177     72-Hf-177

ZA072178     72-Hf-178

ZA072179     72-Hf-179

ZA072180     72-Hf-180

ZA073181     73-Ta-181

ZA073182     73-Ta-182

ZA074000     74-W -Nat

ZA074182     74-W -182

ZA074183     74-W -183

ZA074184     74-W –184

Filename     Material

ZA074186     74-W -186

ZA075185     75-Re-185

ZA075187     75-Re-187

ZA077191     77-Ir-191

ZA077193     77-Ir-193

ZA079197     79-Au-197

ZA082206     82-Pb-206

ZA082207     82-Pb-207

ZA082208     82-Pb-208

ZA083209     83-Bi-209

ZA090230     90-Th-230

ZA090232     90-Th-232

ZA091231     91-Pa-231

ZA091232     91-Pa-232

ZA091233     91-Pa-233

ZA092232     92-U -232

ZA092233     92-U -233

ZA092234     92-U -234

ZA092235     92-U -235

ZA092236     92-U -236

ZA092237     92-U -237

ZA092238     92-U -238

ZA093236     93-Np-236

ZA093237     93-Np-237

ZA093238     93-Np-238

ZA093239     93-Np-239

ZA094236     94-Pu-236

ZA094237     94-Pu-237

ZA094238     94-Pu-238

ZA094239     94-Pu-239

ZA094240     94-Pu-240

ZA094241     94-Pu-241

ZA094242     94-Pu-242

ZA094243     94-Pu-243

ZA094244     94-Pu-244

ZA095241     95-Am-241

ZA095242     95-Am-242

ZA095242.M   95-Am-242m

ZA095243     95-Am-243

ZA096241     96-Cm-241

ZA096242     96-Cm-242

ZA096243     96-Cm-243

ZA096244     96-Cm-244

ZA096245     96-Cm-245

ZA096246     96-Cm-246

ZA096247     96-Cm-247

ZA096248     96-Cm-248

ZA097249     97-Bk-249

ZA098249     98-Cf-249

ZA098250     98-Cf-250

ZA098251     98-Cf-251

ZA098252     98-Cf-252

ZA098253     98-Cf-253

ZA099253     99-Es-253

Fig.1: Effect of Doppler Broadening on Resonance Cross Sections

Fig.2: Effect of Doppler Broadening on Low Energy Cross Sections