# POINT 2009:

# A Temperature Dependent

ENDF/B-VII.0 Data

Cross Section Library

by

Dermott E. Cullen

Lawrence Livermore National Laboratory, retired

1466 Hudson Way

Livermore, CA 94550

Tel.: 925-443-1911

E. Mail: redcullen1@comcast.net

Website: home.comcast.net/~redcullen1

June 6, 2009

POINT 2009:

A Temperature Dependent

ENDF/B-VII.0

Cross Section Library

by

Dermott E. Cullen

Lawrence Livermore National Laboratory, retired

1466 Hudson Way

Livermore, CA 94550

Tel.: 925-443-1911

E. Mail: redcullen1@comcast.net

Website: home.comcast.net/~redcullen1

June 6, 2009

###### Overview

This report is one in the series of “POINT” reports that over the years have presented temperature dependent cross sections for the then current version of ENDF/B. In each case I have used publicly available nuclear data (the current ENDF/B data, available on-line at the National Nuclear Data Center, Brookhaven National Laboratory http://www.nndc.bnl.gov/) and publicly available computer codes (the current PREPRO codes, available on-line at the Nuclear Data Section, IAEA, Vienna, Austria http://www-nds.iaea.or.at/ndspub/endf/prepro/). I have used these in combination to produce the temperature dependent cross sections used in applications and presented in this report.

POINT 2009

ENDF/B-VII.0 was released by CSEWG in November 2006 and is to be frozen for three years until November 2009. As such the Original data included in POINT 2009 is identical to that included in the earlier release POINT 2007 [R1]. However, the processed, temperature dependent results may differ because of improvements in the PREPRO ENDF/B Preprocessing Codes, particularly with regard to accuracy, and correct interpretation of the ENDF/B rules as defined by the ENDF/B formats and procedures manual, ENDF-102.

POINT 2007

The version of ENDF/B, preceding ENDF/B-VII.0, namely ENDFV/B-VI, Release 8, contained 328 evaluations [R2]; of the evaluations 13 elemental evaluations are not included in ENDF/B-VII.0 (these have been replaced by isotopic evaluations).

ENDF/B-VII.0 includes 315 evaluations from ENDF/B-VI and 78 evaluations for new isotopes, for a total of 393 evaluations in ENDF/B-VII.0. The contents of ENDF/B-VII.0 are defined in the Appendix A. The appendix includes a variety of what I hope are useful summaries of the VII.0, including,

1) Contents of ENDF/B-VII.0 (78 new + 315 old = 393 total evaluations)

2) Elemental Evaluations Replaced by Isotopic evaluations (16 new, 19 old)

3) New Evaluations for ENDF/B-VII.0 (78 new)

4) Summary of  for all 65 fissile/fertile isotopes in ENDF/B-VII.0

5) Completeness of ENDF/B-VII.0 Evaluations

6) Same Evaluations in ENDF/B-VI and VII (315)

Deficiencies and Proposed Updates

ENDF/B-VII.0 was released by CSEWG in November 2006 and is to be frozen for three years until November 2009. All recognized ENDF/B-VII.0 deficiencies and proposed updates can be viewed at,

http://www.nndc.bnl.gov/exfor/4web/VII.0-deficiencies.html

These data will be reviewed by CSEWG and these data will serve as the basis for the next version of ENDF/B, namely ENDF/B-VII.1.

###### Introduction

The latest ENDF/B data library was released in November 2006 and is now freely available through the National Nuclear Data Center (NNDC), Brookhaven National Laboratory. This most recent library is identified as ENDF/B-VII.0; this is the first release of ENDF/B-VII. This release completely supersedes all preceding releases of ENDF/B.

As distributed the ENDF/B-VII.0 data includes cross sections represented in the form of a combination of resonance parameters and/or tabulated energy dependent cross sections, nominally at 0 Kelvin temperature.

For use in our applications the ENDF/B-VII.0 library has been processed into cross sections at eight neutron reactor like temperatures, between 0 and 2100 Kelvin, in steps of 300 Kelvin (the exception being 293.6 Kelvin, for exact room temperature at 20 Celsius). It has also been processed to five astrophysics like temperatures, 1, 10, 100 eV, 1 and 10 keV. For reference purposes, 300 Kelvin is approximately 1/40 eV, so that 1 eV is approximately 12,000 Kelvin. At each temperature the cross sections are tabulated and linearly interpolable in energy.

All results are in the computer independent ENDF-6 character format [R2], which allows the data to be easily transported between computers. In its processed form the POINT 2009 library is approximately 11 gigabyte in size and is distributed on three DVDs (see, below for the details of the contents of each DVD).

## PREPRO 2009 Codes

In addition to the changes in the ENDF/B-VII.0 evaluations, it should be noted that between the last version of this report, where the PREPRO 2007 codes were used, and the current version, where the PREPRO 2009 codes were used, there have been major improvements in the ENDF/B Pre-processing codes (PREPRO). The major improvements were both in terms of improving the basic methods used by the codes and in terms of incorporating the latest ENDF-6 Formats and Procedures used by the current evaluations. The result is more accurate cross section data throughout the POINT 2009 library.

WARNING – due to recent changes in ENDF-6 Formats and Procedures only the latest version of the ENDF/B Pre-processing codes, namely PREPRO 2009, can be used to accurately process all current ENDF/B-VII evaluations. If you fail to heed this warning and you use any earlier versions of these codes the results will be inaccurate.

The PREPRO 2009 codes run on virtually any computer, and will soon be available FREE on-line from the Nuclear Data Section, IAEA, Vienna, Austria, website at,

http://www-nds.iaea.or.at/ndspub/endf/prepro/

## Requesting POINT 2009 Data

Please do not contact the author of this report to request this data; I do not have the resources necessary to directly respond to requests for this data. This data has been distributed and is Internationally available from nuclear data/code centers throughout the World,

- Within the United States: contact the National Nuclear Data Center, Brookhaven National Laboratory, Mike Herman at,

services@bnlnd2.dne.bnl.gov

- Within Western Europe: contact the OECD Nuclear Energy Agency/ Data Bank (NEA/DB), Paris, France, Enrico Sartori at Sartori@nea.fr

- Otherwise: contact the Nuclear Data Section, International Atomic Energy Agency, Vienna, Austria, Alberto Mengoni at,

A.Mengoni@iaea.org

Data Processing

As distributed the original evaluated data includes cross sections represented in the form of a combination of resonance parameters and/or tabulated energy dependent cross sections, nominally at 0 Kelvin temperature. For use in applications, this data has been processed using the 2009 version of the ENDF/B Pre-processing codes (PREPRO 2009) to produce temperature dependent, linearly interpolable in energy, tabulated cross sections, in the ENDF-6 format.

For use in applications this library has been processed into the form of temperature dependent cross sections at eight neutron reactor like temperatures, between 0 and 2100 Kelvin, in steps of 300 Kelvin (the exception being 293.6 Kelvin, for exact room temperature at 20 Celsius). It has also been processed to five astrophysics like temperatures, 1, 10, 100 eV, 1 and 10 keV. For reference purposes, 300 Kelvin is approximately 1/40 eV, so that 1 eV is approximately 12,000 Kelvin. At each temperature the cross sections are tabulated and linearly interpolable in energy.

The steps required and codes used to produce room temperature, linearly interpolable tabulated cross sections, in the ENDF-6 format, are described below (the name of each code in given in parenthesis; for details of each code see reference [R3]).

Here are the steps, and PREPRO 2009 codes, used to process the data, in the order in which the codes were used.

1) Linearly interpolable, tabulated cross sections (LINEAR)

2) Including the resonance contribution (RECENT)

3) Doppler broaden all cross sections to temperature (SIGMA1)

4) Check data, define redundant cross sections by summation (FIXUP)

5) Update evaluation dictionary in MF/MT=1/451 (DICTIN)

For the "cold" (0 Kelvin) data steps 1), 2) and 4), 5) were used (no Doppler broadening). For the data at other temperatures, after steps 1) and 2), the data was Doppler broadened to each temperature using step 3), and the results were then made consistent with the ENDF/B formats and conventions using steps 4) and 5), to produce the final distributed data.

The result is linearly interpolable in energy, tabulated, temperature dependent cross sections, in the ENDF-6 format, ready to be used in applications.

Note - this processing only involved the energy dependent neutron cross sections. All other data in the evaluations, e.g., angular and energy distributions, was not affected by this processing, and is identical in all versions of the final results, i.e., it is the same in all of the directories, ORIGINAL, as well as K0 through K2100, and 1ev through 10kev, on the DVDs.

Accuracy of Results

Each of the codes described above that was used to process data to obtain tabulated, linearly interpolable in energy cross sections, processed the data to within a user defined accuracy, or allowable uncertainty. The ENDF/B Pre-processing codes (PREPRO 2009) are self-documenting, in the sense that the ENDF/B formatted output data that each code produces includes comments at the beginning of each evaluation defining the accuracy to which the cross sections were calculated. The combination of comments added by all of the codes defines the sequence and accuracy used by all of them. The accuracy is the same for all evaluations. Therefore, for exact details of the accuracy of the data, see the comments at the beginning of any evaluation. For use in Point 2009 all cross sections were reconstructed to within an accuracy of 0.01% in the thermal range, and 0.1 % at all other energies and temperatures; this is beyond the accuracy to which this data in known, so that I assume that the data processing does not add any significant additional error to the inherent error of the data.

Contents of the Library

This library contains all of the evaluations in the ENDF/B-VI.0 general purpose library. A table in the appendix summarizes the contents of the ENDF/B-VII.0 general purpose library. This library contains evaluations for 393 materials (isotopes or naturally occurring elemental mixtures of isotopes).

This library does not contain data from special purpose ENDF/B-VII libraries, such as fission products, thermal scattering, photon interaction data. To obtain any of these special purpose libraries contact the National Nuclear Data Center, Brookhaven National Laboratory,

ENDF@bnlnd2.dne.bnl.gov

In the POINT 2009 library each evaluation is stored as a separate file. The following table defines each material and the corresponding filename. The entire library is in the computer independent ENDF-6 character format, which allows the data to be easily transported between computers. The entire library requires approximately 11 gigabyte of storage and is distributed on three DVDs; see below for details of the DVDs.

This library contains data for some metastable materials, which are indicated by an "M" at the end of their descriptions.

The majority of these evaluations are complete, in the sense that they include all cross sections over the energy range 10-5 eV to at least 20 MeV. See the appendix for a list of all evaluations, plus a separate list of incomplete evaluations; there are now only a few.

The DVDs is divided into fifteen (15) directories, across three DVDS,

Part 1 (first DVD)

DOCUMENT	- A copy of this report in  MSWord and PDF formats.

ORIGINAL	- The original ENDF/B data before it was processed.

K0		- 0 Kelvin cross sections

K293.6		- 293.6 Kelvin cross sections

K600		- 600 Kelvin cross sections

K900		- 900 Kelvin cross sections

Part 2 (second DVD)

K1200		- 1200 Kelvin cross sections

K1500		- 1500 Kelvin cross sections

K1800		- 1800 Kelvin cross sections

K2100		- 2100 Kelvin cross sections

Part 3 (third DVD)

1eV		- 1 eV cross sections

10eV		- 10 eV cross sections

100eV		- 100 eV cross sections

1keV		- 1 keV cross sections

10keV		- 10 keV cross sections

With the exception of DOCUMENT, each of these directories contains 394 files, one file for each of the 393 evaluation, plus one HTML file to allow interactive data retrieval. Each file is a complete ENDF/B "tape" [R2], including a starting "tape" identification line, and ending with a "tape" end line [R2]. In this form, each file can be used by a wide variety of available computer codes that treat data in the ENDF/B format, e.g., all of the PREPRO codes.

Installation and Use of POINT 2009

I recommend that you create a directory named POINT 2009 and copy the entire contents of ALL three DVDs into this directory; this will allow you simple access to the data at all temperatures. These POINT 2009 directories include HTML routines to allow interactive retrieval of the data. The result will be a directory of about 11 gigabytes. To put that in perspective, today it costs less than $1 U.S. to purchase, install, and maintain on-line one gigabyte of disk storage. Therefore the cost of maintaining this 11 gigabyte library on-line is trivial.

Acknowledgments

I thank Said Mughabghab for his detailed explanation of the use of his newly published resonance parameters [R4] in ENDF/B-VII.0 evaluations. I thank Ramon E. Arcilla, Jr., of the National Nuclear Data Center (NNDC), Brookhaven National Laboratory, for supplying the original ENDF/B-VII.0, used in this project. I thank Kevin McLaughlin and Andre Trkov, of the Nuclear Data Section, International Atomic Energy Agency, for supplying the ENDF/B Pre-processing codes, PREPRO 2009, used in this project. I thank Nancy Larsen, Bob MacFarlane, Maurice Greene, and Mike Dunn, for their intercomparison of their cross section processing codes (SAMMY, NJOY and AMPX) against the PREPRO codes. These comparisons have led to significant improvements in the accuracy and reliability of the results produced by all four codes (SAMMY, NJOY, AMPX, PREPRO). I thank Dave Heinrichs for proofreading the draft of this report and making many helpful corrections and improvements, which I incorporated in the final report.

References

[R1] ”POINT 2007: A Temperature Dependent ENDF/B-VII.0 data Cross Section Library”, Lawrence Livermore National Laboratory, UCRL-TR-228089, February 2007.

[R2] Data Formats and Procedures for the Evaluated Nuclear Data File ENDF-6, BNL-NCS-44945, Rev. 11/95, edited by V. McLane, et al. National Nuclear Data Center, Brookhaven National Lab. http://www.nndc.bnl.gov/nndcscr/documents/endf/endf102/

[R3] now available, "PREPRO 2007: The 2007 ENDF/B Pre-Processing Codes," by D.E. Cullen, Nuclear Data Section, International Atomic Energy Agency, Vienna, Austria, IAEA-NDS-39, Rev. 12, Nov. 22, 2004; PREPRO 2009 will soon to publicly available. http://www-nds.iaea.or.at/ndspub/endf/prepro/

[R4] “Atlas of Nuclear Resonances”, by S.F. Mughabghab, National Nuclear Data Center, Brookhaven National Laboratory, published by Elsevier, March 2006.

[R5] "Exact Doppler Broadening of Tabulated Cross Sections," by D.E. Cullen and C.R. Weisbin, Nuclear Science and Engineering 60, p. 199 (1975)

[R6] "THERMAL: A Routine Designed to Calculate Neutron Thermal Scattering," by D.E. Cullen, Lawrence Livermore National Laboratory, UCRL-ID-120560-Rev-1, Sept. 1995.

http://home.comcast.net/~redcullen1

[R7] “Verification of High Temperature Free Atom Thermal Scattering in MERCURY Compared to TART”, by D.E. Cullen, Scott McKinley and Christian Hagmann, Lawrence Livermore National Laboratory, UCRL-TR-226340, August 1, 2006.

[R8] “TART2005: A Coupled Neutron-Photon 3-D, Time Dependent, Combinatorial Geometry Monte Carlo Transport Code," by D.E. Cullen, Lawrence Livermore National Laboratory, UCRL-SM-218009, Nov. 22, 2005.

Appendix A: Contents of ENDF/B-VII.0 (78 new + 315 old = 393 total evaluations)

| 1-H - 1 1-H - 2 1-H - 3 2-He- 3 2-He- 4 3-Li- 6 3-Li- 7 4-Be- 7 4-Be- 9 5-B - 10 5-B - 11 6-C -Nat 7-N - 14 7-N - 15 8-O - 16 8-O - 17 9-F - 19 11-Na- 22 11-Na- 23 12-Mg- 24 12-Mg- 25 12-Mg- 26 13-Al- 27 14-Si- 28 14-Si- 29 14-Si- 30 15-P - 31 16-S - 32 16-S - 33 16-S - 34 16-S - 36 17-Cl- 35 17-Cl- 37 18-Ar- 36 18-Ar- 38 18-Ar- 40 19-K - 39 19-K - 40 19-K - 41 20-Ca- 40 20-Ca- 42 20-Ca- 43 20-Ca- 44 20-Ca- 46 20-Ca- 48 21-Sc- 45 22-Ti- 46 22-Ti- 47 22-Ti- 48 22-Ti- 49 22-Ti- 50 23-V -Nat 24-Cr- 50 24-Cr- 52 24-Cr- 53 24-Cr- 54 25-Mn- 55 26-Fe- 54 26-Fe- 56 26-Fe- 57 26-Fe- 58 27-Co- 58 27-Co- 58M 27-Co- 59 28-Ni- 58 28-Ni- 58M | 28-Ni- 60 28-Ni- 61 28-Ni- 62 28-Ni- 64 29-Cu- 63 29-Cu- 65 30-Zn-Nat 31-Ga- 69 31-Ga- 71 32-Ge- 70 32-Ge- 72 32-Ge- 73 32-Ge- 74 32-Ge- 76 33-As- 74 33-As- 75 34-Se- 74 34-Se- 76 34-Se- 77 34-Se- 78 34-Se- 79 34-Se- 80 34-Se- 82 35-Br- 79 35-Br- 81 36-Kr- 78 36-Kr- 80 36-Kr- 82 36-Kr- 83 36-Kr- 84 36-Kr- 85 36-Kr- 86 37-Rb- 85 37-Rb- 86 37-Rb- 87 38-Sr- 84 38-Sr- 86 38-Sr- 87 38-Sr- 88 38-Sr- 89 38-Sr- 90 39-Y - 89 39-Y - 90 39-Y - 91 40-Zr- 90 40-Zr- 91 40-Zr- 92 40-Zr- 93 40-Zr- 94 40-Zr- 95 40-Zr- 96 41-Nb- 93 41-Nb- 94 41-Nb- 95 42-Mo- 92 42-Mo- 94 42-Mo- 95 42-Mo- 96 42-Mo- 97 42-Mo- 98 42-Mo- 99 42-Mo-100 43-Tc- 99 44-Ru- 96 44-Ru- 98 44-Ru- 99 | 44-Ru-100 44-Ru-101 44-Ru-102 44-Ru-103 44-Ru-104 44-Ru-105 44-Ru-106 45-Rh-103 45-Rh-105 46-Pd-102 46-Pd-104 46-Pd-105 46-Pd-106 46-Pd-107 46-Pd-108 46-Pd-110 47-Ag-107 47-Ag-109 47-Ag-110M 47-Ag-111 48-Cd-106 48-Cd-108 48-Cd-110 48-Cd-111 48-Cd-112 48-Cd-113 48-Cd-114 48-Cd-115M 48-Cd-116 49-In-113 49-In-115 50-Sn-112 50-Sn-113 50-Sn-114 50-Sn-115 50-Sn-116 50-Sn-117 50-Sn-118 50-Sn-119 50-Sn-120 50-Sn-122 50-Sn-123 50-Sn-124 50-Sn-125 50-Sn-126 51-Sb-121 51-Sb-123 51-Sb-124 51-Sb-125 51-Sb-126 52-Te-120 52-Te-122 52-Te-123 52-Te-124 52-Te-125 52-Te-126 52-Te-127M 52-Te-128 52-Te-129M 52-Te-130 52-Te-132 53-I -127 53-I -129 53-I -130 53-I -131 53-I -135 | 54-Xe-123 54-Xe-124 54-Xe-126 54-Xe-128 54-Xe-129 54-Xe-130 54-Xe-131 54-Xe-132 54-Xe-133 54-Xe-134 54-Xe-135 54-Xe-136 55-Cs-133 55-Cs-134 55-Cs-135 55-Cs-136 55-Cs-137 56-Ba-130 56-Ba-132 56-Ba-133 56-Ba-134 56-Ba-135 56-Ba-136 56-Ba-137 56-Ba-138 56-Ba-140 57-La-138 57-La-139 57-La-140 58-Ce-136 58-Ce-138 58-Ce-139 58-Ce-140 58-Ce-141 58-Ce-142 58-Ce-143 58-Ce-144 59-Pr-141 59-Pr-142 59-Pr-143 60-Nd-142 60-Nd-143 60-Nd-144 60-Nd-145 60-Nd-146 60-Nd-147 60-Nd-148M 60-Nd-150 61-Pm-147 61-Pm-148 61-Pm-148 61-Pm-149 61-Pm-151 62-Sm-144 62-Sm-147 62-Sm-148 62-Sm-149 62-Sm-150 62-Sm-151 62-Sm-152 62-Sm-153 62-Sm-154 63-Eu-151 63-Eu-152 63-Eu-153 63-Eu-154 | 63-Eu-155 63-Eu-156 63-Eu-157 64-Gd-152 64-Gd-153 64-Gd-154 64-Gd-155 64-Gd-156 64-Gd-157 64-Gd-158 64-Gd-160 65-Tb-159 65-Tb-160 66-Dy-156 66-Dy-158 66-Dy-160 66-Dy-161 66-Dy-162 66-Dy-163 66-Dy-164 67-Ho-165 67-Ho-166M 68-Er-162 68-Er-164 68-Er-166 68-Er-167 68-Er-168 68-Er-170 71-Lu-175 71-Lu-176 72-Hf-174 72-Hf-176 72-Hf-177 72-Hf-178 72-Hf-179 72-Hf-180 73-Ta-181 73-Ta-182 74-W -182 74-W -183 74-W -184 74-W -186 75-Re-185 75-Re-187 77-Ir-191 77-Ir-193 79-Au-197 80-Hg-196 80-Hg-198 80-Hg-199 80-Hg-200 80-Hg-201 80-Hg-202 80-Hg-204 82-Pb-204 82-Pb-206 82-Pb-207 82-Pb-208 83-Bi-209 88-Ra-223 88-Ra-224 88-Ra-225 88-Ra-226 89-Ac-225 89-Ac-226 89-Ac-227 | 90-Th-227 90-Th-228 90-Th-229 90-Th-230 90-Th-232 90-Th-233 90-Th-234 91-Pa-231 91-Pa-232 91-Pa-233 92-U -232 92-U -233 92-U -234 92-U -235 92-U -236 92-U -237 92-U -238 92-U -239 92-U -240 92-U -241 93-Np-235 93-Np-236 93-Np-237 93-Np-238 93-Np-239 94-Pu-236 94-Pu-237 94-Pu-238 94-Pu-239 94-Pu-240 94-Pu-241 94-Pu-242 94-Pu-243 94-Pu-244 94-Pu-246 95-Am-241 95-Am-242 95-Am-242M 95-Am-243 95-Am-244 95-Am-244M 96-Cm-241 96-Cm-242 96-Cm-243 96-Cm-244 96-Cm-245 96-Cm-246 96-Cm-247 96-Cm-248 96-Cm-249 96-Cm-250 97-Bk-249 97-Bk-250 98-Cf-249 98-Cf-250 98-Cf-251 98-Cf-252 98-Cf-253 98-Cf-254 99-Es-253 99-Es-254 99-Es-255 100-Fm-255 |
| --- | --- | --- | --- | --- | --- |

Elemental vs. Isotopic Evaluations

Successive versions of ENDF/B have replaced elemental evaluations by isotopic evaluations. Between ENDF/B-VI and VII 13 elemental evaluations were deleted (included in ENDF/B-VI, but not included in ENDF/B-VII); the below table summarizes the elemental evaluations deleted and the isotopic evaluations designed to replace them. The only remaining elemental evaluations in ENDF/B-VII are:

6-C–Nat	 6-C-12 98.93%/ 6-C-13 1.07% missing

23-V –Nat	 23-V-50 99.75%/ 23-V-51 0.25% missing

30-Zn-Nat 	 5 isotopes, all missing

All of these isotopes in VII.0 are complete, in the sense that they include major cross sections (elastic, capture, inelastic) over the energy range 10-5 eV up to at least 20 MeV. However, be aware that evaluating isotopes is difficult and the quality of minor isotopes may be poor. To my knowledge as yet the summing these isotopes to define equivalent elemental evaluations has not been verified against experimental measurements.

Elemental Evaluations Replaced by Isotopic evaluations (16 new, 19 old)

| Element Isotope | Element Isotope | Element Isotope |
| --- | --- | --- |
| 12-Mg-Nat 12-Mg- 24 12-Mg- 25 12-Mg- 26 14-Si-Nat 14-Si- 28 14-Si- 29 14-Si- 30 16-S -Nat 16-S - 32 16-S - 33 16-S - 34 16-S - 36 17-Cl-Nat 17-Cl- 35 17-Cl- 37 19-K -Nat 19-K - 39 19-K - 40 19-K - 41 20-Ca-Nat 20-Ca- 40 20-Ca- 42 20-Ca- 43 20-Ca- 44 20-Ca- 46 20-Ca- 48 | 22-Ti-Nat 22-Ti- 46 22-Ti- 47 22-Ti- 48 22-Ti- 49 22-Ti- 50 31-Ga-Nat 31-Ga- 69 31-Ga- 71 40-Zr-Nat 40-Zr- 90 40-Zr- 91 40-Zr- 92 40-Zr- 93 40-Zr- 94 40-Zr- 95 40-Zr- 96 | 42-Mo-Nat 42-Mo- 92 42-Mo- 94 42-Mo- 95 42-Mo- 96 42-Mo- 97 42-Mo- 98 42-Mo- 99 42-Mo-100 49-In-Nat 49-In-113 49-In-115 72-Hf-Nat 72-Hf-174 72-Hf-176 72-Hf-177 72-Hf-178 72-Hf-179 72-Hf-180 74-W -Nat 74-W -182 74-W -183 74-W -184 74-W -186 |

New Evaluations for ENDF/B-VII.0 (78 new)

After six versions of ENDF/B over almost 40 years, most of the important isotopes have already been evaluated and included in earlier versions of ENDF/B. The new ENDF/B-VII evaluations were difficult to do, since usually there is little experimental data for rarer isotopes. Most of the new evaluations are complete in the sense that they include major cross sections from 10-5 eV to 20 MeV. The except is 4-Be-7 which only extends up to 8.1 MeV, and only includes elastic and charged particle reactions; this is a theoretical evaluation that should not have been included in ENDF/B-VII.0. Many of the other evaluations are pretty bad; better than nothing, but crude, so CAVEAT EMPTOR!

The below table includes a list of all 78 new evaluations. If there are no comments, I judge the  evaluation to be o.k.

###### 78 New Evaluations

| Material Comments 4-Be- 7 Useless partial 11-Na- 22 Crude 12-Mg- 25 12-Mg- 26 16-S - 33 16-S - 34 16-S - 36 Crude 18-Ar- 36 Crude 18-Ar- 38 Crude 19-K - 39 19-K - 40 Very crude 20-Ca- 40 o.k. to 20 MeV 20-Ca- 42 “ 20-Ca- 43 “ 20-Ca- 44 “ 20-Ca- 46 Very crude 20-Ca- 48 o.k. to 20 MeV 22-Ti- 49 27-Co- 58 Very crude 27-Co- 58M Very crude 30-Zn-Nat Check (n,alpha) 31-Ga- 69 31-Ga- 71 32-Ge- 70 33-As- 74 34-Se- 79 Crude 47-Ag-110M (n,n') down to 3 eV? 50-Sn-113 Resonance gap 54-Xe-123 Very crude 56-Ba-130 56-Ba-132 Crude 56-Ba-133 57-La-138 58-Ce-136 58-Ce-138 58-Ce-139 64-Gd-153 66-Dy-156 66-Dy-158 | Material Comments 67-Ho-166M Crude 68-Er-162 68-Er-164 68-Er-168 68-Er-170 80-Hg-196 Crude 80-Hg-198 Crude, check capture 80-Hg-199 80-Hg-200 80-Hg-201 80-Hg-202 Crude, check capture 80-Hg-204 Very crude 82-Pb-204 88-Ra-223 Very crude 88-Ra-224 Very crude 88-Ra-225 Very crude 88-Ra-226 89-Ac-225 Very crude 89-Ac-226 Very crude 89-Ac-227 Very crude 90-Th-227 Very crude 90-Th-228 Rubbish 90-Th-229 (n,n’) down to 100 eV 90-Th-233 Very crude 90-Th-234 Rubbish 92-U -239 Weird resonances 92-U -240 92-U -241 Weird resonances 93-Np-235 Very crude 94-Pu-246 Very crude 95-Am-244 Very crude 95-Am-244M Very crude 96-Cm-249 96-Cm-250 Crude 97-Bk-250 Weird resonances 98-Cf-254 Very crude 99-Es-254 Very crude 99-Es-255 Very crude 100-Fm-255 Very crude |
| --- | --- |

Summary of  for all 65 fissile/fertile isotopes in ENDF/B-VII.0

For applications I require both prompt and delayed neutrons per fission. In the ENDF/B format the evaluator can optionally include: Total (T), Delayed (D) and/or Prompt (P). Below is a summary of all fissile/fertile materials in ENDF/B-VII.0, indicating the neutrons per fission data included for each isotope. In all cases the Total (T) is included, however in some cases no other data is included, so that we cannot define either Prompt (P) or Delayed (D). I will have to add the missing data before I can use these isotopes in my applications.

Summary of all 65 fissile/fertile isotopes in ENDF/B-VII.0

| Isotope <nu> Comments ZA088223 T No Delayed ZA088226 T No Delayed ZA089227 T No Delayed ZA090227 T D P ZA090228 T D P ZA090229 T D P ZA090230 T No Delayed ZA090232 T D P ZA090233 T D P ZA090234 T D P ZA091231 T D P ZA091232 T D P ZA091233 T D P ZA092232 T D P ZA092233 T D P ZA092234 T D P ZA092235 T D P ZA092236 T D P ZA092237 T D P ZA092238 T D P ZA092239 T D P ZA092240 T D P ZA092241 T D P ZA093235 T D P ZA093236 T D P ZA093237 T D P ZA093238 T D P ZA093239 T No Delayed ZA094236 T D P ZA094237 T No Delayed ZA094238 T D P ZA094239 T D P ZA094240 T D P | Isotope <nu> Comments ZA094241 T D P ZA094242 T D P ZA094243 T No Delayed ZA094244 T No Delayed ZA094246 T D P ZA095241 T D P ZA095242 T D P ZA095242.M T D P ZA095243 T D P ZA095244 T D P ZA095244.M T D P ZA096241 T No Delayed ZA096242 T D P ZA096243 T D P ZA096244 T D P ZA096245 T D P ZA096246 T D P ZA096247 T D P ZA096248 T No Delayed ZA096249 T D P ZA096250 T D P ZA097249 T D P ZA097250 T D P ZA098249 T D P ZA098250 T No Delayed ZA098251 T D P ZA098252 T No Delayed ZA098253 T No Delayed ZA098254 T D P ZA099254 T D P ZA099255 T D P ZA100255 T D P |
| --- | --- |

Completeness of ENDF/B-VII.0 Evaluations

For ENDF/B-VI.8, I judged that only about half of the 328 evaluations were complete and physically acceptable enough to be used in neutron transport calculations. In contrast in ENDF/B-VII.0, only a few evaluations are incomplete (10-5 eV to 20 MeV) or physically unacceptable (negative cross sections). Below is a summary (no comment = o.k.)

Material Comments ZA001001 mt= 50 no inelastic ZA001002 mt= 50 no inelastic ZA001003 mt= 102 no capture ZA001003 mt= 50 no inelastic ZA002003 mt= 50 no inelastic ZA002004 mt= 102 no capture ZA002004 mt= 50 no inelastic ZA004007 mt= 2 cross section ends 8.1000D+06 eV Incomplete only elastic ZA004007 mt= 1 no total up to 8.1 MeV ZA004007 mt= 102 no capture ZA004007 mt= 50 no inelastic ZA004009 mt= 50 no inelastic ZA005010 mt= 102 cross section ends 5.0000D+05 eV ZA017035 mt= 2 cross section start 1.4519D-05 eV Negative elastic ZA018040 mt= 2 cross section <=0 9.7825D+05 eV Negative elastic ZA020040 mt= 2 cross section <=0 5.0000D+05 eV Negative elastic ZA021045 mt= 102 cross section ends 5.0000D+06 eV ZA026056 mt= 2 cross section <=0 1.1971D+06 eV Negative elastic ZA027058 mt= 102 cross section <=0 8.4925D+00 eV Negative capture ZA027058.M mt= 51 level energy > 0 2.4900D+04 eV ZA028059 mt= 50 no inelastic Incomplete ZA028061 mt= 2 cross section <=0 7.4355D+05 eV Negative elastic ZA041093 mt= 2 cross section <=0 2.3344D+03 eV Negative elastic ZA047110.M mt= 51 level energy > 0 1.1760D+05 eV ZA047110.M mt= 52 level energy > 0 1.0660D+05 eV ZA048108 mt= 102 cross section ends 1.0000D+07 eV ZA048110 mt= 102 cross section ends 1.0000D+07 eV ZA048112 mt= 102 cross section ends 1.0000D+07 eV ZA048115.M mt= 51 level energy > 0 1.8100D+05 eV ZA048116 mt= 102 cross section ends 1.0000D+07 eV ZA052127.M mt= 51 level energy > 0 8.8260D+04 eV ZA052127.M mt= 52 level energy > 0 2.7140D+04 eV ZA052129.M mt= 51 level energy > 0 1.0550D+05 eV ZA054130 mt= 102 cross section ends 1.0000D+07 eV ZA061148.M mt= 51 level energy > 0 1.3790D+05 eV ZA061148.M mt= 52 level energy > 0 6.2200D+04 eV ZA064152 mt= 2 cross section <=0 3.3186D+01 eV Negative elastic ZA066160 mt= 2 cross section <=0 3.3293D+02 eV Negative elastic ZA067166.M mt= 51 level energy > 0 5.9850D+03 eV ZA082207 mt= 2 cross section <=0 4.7500D+05 eV Negative elastic ZA090228 mt= 18 cross section <=0 3.0000D+03 eV ZA090230 mt= 2 cross section <=0 1.2856D+00 eV Negative elastic ZA092240 mt= 2 cross section <=0 2.2262D+00 eV Negative elastic ZA094238 mt= 2 cross section <=0 5.9743D+01 eV Negative elastic ZA094242 mt= 2 cross section <=0 2.2348D+00 eV Negative elastic ZA094244 mt= 2 cross section <=0 2.0770D+01 eV Negative elastic ZA095242.M mt= 51 level energy > 0 4.8600D+04 eV ZA095242.M mt= 52 level energy > 0 4.5000D+03 eV ZA095244.M mt= 51 level energy > 0 8.8000D+04 eV ZA096241 mt= 102 cross section ends 4.0000D+06 eV ZA096242 mt= 2 cross section <=0 1.3448D+01 eV Negative elastic ZA096242 mt= 18 cross section <=0 2.7600D+02 eV ZA096248 mt= 2 cross section <=0 6.8142D+00 eV Negative elastic ZA098250 mt= 2 cross section <=0 1.4329D+01 eV Negative elastic ZA098252 mt= 2 cross section <=0 1.6674D+01 eV Negative elastic ZA098253 mt= 18 cross section ends 1.1000D+04 eV Incomplete only to 11 keV ZA098253 mt= 102 cross section ends 1.1000D+04 eV ZA098253 mt= 50 no inelastic ZA099253 mt= 102 cross section ends 1.1000D+04 eV Incomplete only to 11 keV ZA099253 mt= 50 no inelastic

Same Evaluations in ENDF/B-VI and VII (315)

Above I stated that ENDF/B-VII.0 includes 315 evaluations from ENDF/B-VI. By this I mean that there are evaluations for the same 315 elements or isotopes in both VI and VII. The contents of these evaluations may be identical to ENDF/B-VI, or completely different. Below I provide a brief, one line summary comparing the contents of ENDF/B-VII.0 to VI.8. These summaries are based only on my comparing major cross sections (total, elastic, capture and fission) for the 315 same evaluations. For more details of any given evaluation the reader can use the COMPLOT code [R3] to “see” comparisons.

The intent here is to hopefully save users time and effort by telling them which evaluations have or have not changed. For example, many metals and fissile isotopes have not changed. There are also materials where the cross sections are what I call “similar”, but which I mean similar resonance structure, but actual cross section values may be quite different.

- Many single level Breit-Wigner (SLBW) resonances have been changed to multi-level (MLBW). In many case this eliminates negative elastic cross sections, and results in what I identify in the following table as “similar”. WARNING – because of the use of non-physical average J values, switching from SLBW to MLBW does not always eliminate negative cross sections. WARNING – “similar” here means similar resonance structure; the actual energy dependent cross sections may be very different.

- Many incomplete ENDF/B-VI evaluations have now been extended up to 20 MeV and are now complete in VII.0. Also the high energy range of many other evaluations were re-done using nuclear model code calculations; this has changed some high energy cross sections by 10 to 20%.

- Many evaluations now include resonance parameters from the latest 2006 version of the atlas of nuclear resonances, BNL-325 [R4]; this has allowed many resonance regions to be extended to higher energies. However, in many cases no additional evaluation was performed to eliminate resonance gaps in the experimentally measured resonance parameters, and many isotopes do not included an unresolved resonance energy range.

- I try to identify evaluations where the major cross sections differ substantially; roughly speaking my criteria was differences of at least ~ 1% .

- I also compared <nu>, where smaller differences can be important. For the major fuel, U-233, U-235, and Pu-235, there have been minor ~ 0.5% changes in <nu> which may be reflected in calculated integral parameters, such as K-eff. Some minor fissile/fertile have changes in <nu> of 5 to 10%

315 Same Materials (1-H -  1 to 44-Ru- 99)

| 1-H - 1 Elastic 0.3% lower < 10 keV 1-H - 2 Same 1-H - 3 Elastic 30% higher < 1 MeV 2-He- 3 Same 2-He- 4 Same 3-Li- 6 Elastic 7% higher < 0.1 eV 3-Li- 7 Same 4-Be- 9 Elastic 10% different > 10 eV 5-B – 10 Elastic 8% higher ~ 100 keV 5-B – 11 Same 6-C –Nat Same 7-N – 14 Same 7-N – 15 Same 8-O – 16 Elastic 7% higher 4 to 9 MeV 8-O – 17 Same 9-F – 19 Different resonances < 1 MeV 11-Na- 23 Same 12-Mg- 24 Same 13-Al- 27 Different resonances < 1 MeV 14-Si- 28 Same 14-Si- 29 Same 14-Si- 30 Same 15-P – 31 Same 16-S – 32 Different resonances 17-Cl- 35 Different – resonances > 200 keV 17-Cl- 37 Different – resonances > 200 keV 18-Ar- 40 Completely different 19-K – 41 Same 21-Sc- 45 Same 22-Ti- 46 Same 22-Ti- 47 Same 22-Ti- 48 Same 22-Ti- 50 Same 23-V –Nat Same 24-Cr- 50 Same 24-Cr- 52 Same 24-Cr- 53 Same 24-Cr- 54 Same 25-Mn- 55 Same 26-Fe- 54 Same 26-Fe- 56 Same 26-Fe- 57 Same 26-Fe- 58 Same 27-Co- 59 Same 28-Ni- 58 Same 28-Ni- 59 Very narrow resonance differences 28-Ni- 60 Same 28-Ni- 61 Same 28-Ni- 62 Same 28-Ni- 64 Same 29-Cu- 63 Same 29-Cu- 65 Same 32-Ge- 72 New - completely different | 32-Ge- 73 New - completely different 32-Ge- 74 New - completely different 32-Ge- 76 New - completely different 33-As- 75 New - resonances > 2 keV 34-Se- 74 Different 34-Se- 76 Different 34-Se- 77 Different 34-Se- 78 Different 34-Se- 80 Different 34-Se- 82 Different 35-Br- 79 Different 35-Br- 81 Different 36-Kr- 78 Different 36-Kr- 80 Different 36-Kr- 82 Different 36-Kr- 83 Different 36-Kr- 84 Different 36-Kr- 85 Different 36-Kr- 86 Different 37-Rb- 85 Different - fewer resonances 37-Rb- 86 Different 37-Rb- 87 Different - fewer resonances 38-Sr- 84 Different 38-Sr- 86 Different 38-Sr- 87 Different 38-Sr- 88 Different 38-Sr- 89 Different - both rubbish 38-Sr- 90 Different - both rubbish 39-Y – 89 Different 39-Y – 90 Different – old rubbish 39-Y – 91 Different - both rubbish 40-Zr- 90 Different – fewer resonances 40-Zr- 91 Different - similar resonances 40-Zr- 92 Different – fewer resonances 40-Zr- 93 Different – old rubbish 40-Zr- 94 Similar 40-Zr- 95 Different - both rubbish 40-Zr- 96 Similar 41-Nb- 93 Same 41-Nb- 94 Different - both rubbish 41-Nb- 95 Different - both rubbish 42-Mo- 92 Very different > 20 keV 42-Mo- 94 Very different > 6 keV 42-Mo- 95 Same < 2 keV – 40% higher energy 42-Mo- 96 Very different > 4 keV 42-Mo- 97 Different 42-Mo- 98 Different – old rubbish 42-Mo- 99 Different - both rubbish 42-Mo-100 Very different > 4 keV 43-Tc- 99 Very different > 1 keV 44-Ru- 96 Different - both rubbish 44-Ru- 98 Different - both rubbish 44-Ru- 99 Different > 100 eV |
| --- | --- |

315 Same Materials (44-Ru- 100 to 61-Pm-148)

| 44-Ru-100 Old Rubbish – new poor 44-Ru-101 50% higher < 10 eV 44-Ru-102 Similar 44-Ru-103 Old Rubbish – new poor 44-Ru-104 Different > 1 keV 44-Ru-105 Similar - both rubbish 44-Ru-106 Similar - both rubbish 45-Rh-103 Same < 4 keV – 40% higher energy 45-Rh-105 Different - both rubbish 46-Pd-102 Old rubbish – new poor 46-Pd-104 Different – old rubbish 46-Pd-105 Same < 2 keV – 20% higher energy 46-Pd-106 Different – old rubbish 46-Pd-107 Very similar 46-Pd-108 Different – old poor 46-Pd-110 Different - old rubbish 47-Ag-107 Different > 3 keV 47-Ag-109 Similar < 5 keV - 7% > 100 keV 47-Ag-111 New - old rubbish 48-Cd-106 No resonances 600 eV - 3 keV 48-Cd-108 No resonances 350 eV – 2.6 keV 48-Cd-110 Similar 48-Cd-111 Different < 1 eV 60% lower 48-Cd-112 Similar < 2 keV 48-Cd-113 Similar < 2 keV 48-Cd-114 Same 48-Cd-115M New - old rubbish 48-Cd-116 Similar 49-In-113 New resonances > 50 eV 49-In-115 Very different > 1 keV 50-Sn-112 Similar 50-Sn-114 Different - more resonances 50-Sn-115 Different – both poor 50-Sn-116 New resonances > 2 keV 50-Sn-117 Different 50-Sn-118 Similar 50-Sn-119 Different 50-Sn-120 New resonances > 15 keV 50-Sn-122 New resonances > 900 eV 50-Sn-123 Different - both rubbish 50-Sn-124 New resonances > 700 eV 50-Sn-125 New - old rubbish 50-Sn-126 Different - both rubbish 51-Sb-121 More resonances > 2.5 keV 51-Sb-123 More resonances > 2.5 keV 51-Sb-124 Different - both rubbish 51-Sb-125 Different - both rubbish 51-Sb-126 Different - old rubbish 52-Te-120 Different - both rubbish 52-Te-122 More resonances > 4 keV 52-Te-123 More resonances > 500 eV 52-Te-124 More resonances > 6 keV 52-Te-125 More resonances > 1 keV | 52-Te-126 More resonances > 6 keV 52-Te-127M Different - both rubbish 52-Te-128 More resonances > 3.5 keV 52-Te-129M Different - both rubbish 52-Te-130 Different 52-Te-132 Different - old rubbish 53-I -127 More resonances > 1 keV 53-I -129 More resonances > 150 eV 53-I -130 Different - old rubbish 53-I -131 Different - both rubbish 53-I -135 Different - both rubbish 54-Xe-124 Similar 54-Xe-126 Different resonances 54-Xe-128 Similar 54-Xe-129 Similar 54-Xe-130 Similar 54-Xe-131 Same 54-Xe-132 Different 54-Xe-133 Different - both rubbish 54-Xe-134 Different 54-Xe-135 Same - both rubbish > 10 eV 54-Xe-136 New - old rubbish 55-Cs-133 Same - 14% > 100 keV 55-Cs-134 Similar 55-Cs-135 Similar 55-Cs-136 Different - new rubbish 55-Cs-137 Similar - both rubbish 56-Ba-134 Similar < 10 keV 56-Ba-135 Similar < 1 keV 56-Ba-136 Different 56-Ba-137 Different 56-Ba-138 Similar 56-Ba-140 Different – old rubbish 57-La-139 Different 57-La-140 Different - old rubbish 58-Ce-140 Different - old rubbish 58-Ce-141 Different - old rubbish 58-Ce-142 Different - old rubbish 58-Ce-143 Different - old rubbish 58-Ce-144 Different - both rubbish 59-Pr-141 Similar 59-Pr-142 Different - old rubbish 59-Pr-143 Different - old rubbish 60-Nd-142 Different 60-Nd-143 Similar - 4% > 100 keV 60-Nd-144 Different 60-Nd-145 Similar - 5% > 100 keV 60-Nd-146 Different 60-Nd-147 Different > 30 eV 60-Nd-148 Different 60-Nd-150 Different 61-Pm-147 No resonances > 100 eV 61-Pm-148 Different - both rubbish |
| --- | --- |

315 Same Materials (61-Pm-148M to 99-Es-293)

| 61-Pm-148M Similar - not great 61-Pm-149 Different - both rubbish 61-Pm-151 Different - old rubbish 62-Sm-144 Similar 62-Sm-147 Similar > 10 eV 62-Sm-148 Different - old rubbish 62-Sm-149 Very similar 62-Sm-150 Very similar 62-Sm-151 Same - 15% > 10 keV 62-Sm-152 Similar 62-Sm-153 Different - old rubbish 62-Sm-154 Different 63-Eu-151 Very similar 63-Eu-152 Same - 30% > 100 eV 63-Eu-153 Same - 16% > 100 eV 63-Eu-154 Different 63-Eu-155 Very similar 63-Eu-156 Different - both rubbish 63-Eu-157 Different - old rubbish 64-Gd-152 Different < 10 eV 64-Gd-154 Similar 64-Gd-155 Same - 20% > 200 eV 64-Gd-156 Different 64-Gd-157 Similar, same < 400 eV 64-Gd-158 Different 64-Gd-160 Different 65-Tb-159 Different > 100 eV 65-Tb-160 Different - old rubbish 66-Dy-160 Very similar 66-Dy-161 Similar 66-Dy-162 Similar < 5 keV 66-Dy-163 Similar 66-Dy-164 Similar < 7 keV 67-Ho-165 Different 68-Er-166 Similar < 2 keV 68-Er-167 Similar < 500 eV 71-Lu-175 Same 71-Lu-176 Same 72-Hf-174 Same 72-Hf-176 Same 72-Hf-177 Same 72-Hf-178 Same 72-Hf-179 Same 72-Hf-180 Same 73-Ta-181 Same 73-Ta-182 Same 74-W -182 Same 74-W -183 Same 74-W -184 Same 74-W -186 Same 75-Re-185 Same 75-Re-187 Same | 77-Ir-191 Very similar 77-Ir-193 Similar 79-Au-197 Similar 82-Pb-206 Very similar 82-Pb-207 Very similar, 3% ~ 10 MeV 82-Pb-208 Very similar 83-Bi-209 Same 90-Th-230 Same 90-Th-232 Different resonances 91-Pa-231 Similar < 15 eV 91-Pa-232 Similar 91-Pa-233 Similar < 40 eV 92-U -232 Same < 200 eV 92-U -233 Similar to 60 eV 92-U -234 Similar 92-U -235 Same - 1% ~ 20 MeV 92-U -236 Same - 6% ~ 500 keV 92-U -237 Similar – weird resonances 92-U -238 Similar < 10 keV 93-Np-236 Same 93-Np-237 Similar < 150 eV 93-Np-238 Different - both rubbish 93-Np-239 Same - both rubbish 94-Pu-236 Same 94-Pu-237 Same 94-Pu-238 Same 94-Pu-239 Same 94-Pu-240 Same 94-Pu-241 Same 94-Pu-242 Same 94-Pu-243 Same 94-Pu-244 Same 95-Am-241 Same 95-Am-242 Different - old bad 95-Am-242M Similar - 30% > 3.5 eV 95-Am-243 Same 96-Cm-241 Same 96-Cm-242 Same 96-Cm-243 Same 96-Cm-244 Similar < 500 eV 96-Cm-245 Same 96-Cm-246 Same 96-Cm-247 Different 96-Cm-248 Same – negative elastic 97-Bk-249 Same 98-Cf-249 Same 98-Cf-250 Same 98-Cf-251 Same 98-Cf-252 Same 98-Cf-253 Same – partial to 11 keV 99-Es-253 Same – partial to 11 keV |
| --- | --- |

Appendix B: The Effects of Temperature and Doppler Broadening

For those readers who are not familiar with the effects of temperature and Doppler broadening on neutron cross sections and transport, for details I suggest that you read references [R5] and [R6], listed below. Here I will give a brief description of these effects. Users of neutron cross sections should be aware that there are several important effects of temperature and Doppler broadening,

1) There is the well known effect in the neutron resonance region, where as the temperature increases resonances become broader, hence the name Doppler broadening. Figure 1 below illustrates the effect of temperature on the U238 capture cross section for neutron reactor like temperatures, and figure 2 illustrates this effect for astrophysical like temperatures. These figures each contain four sub-figures, with each sub-figure comparing cross sections at two progressively higher temperatures. In both figure 1 and 2 each sub-figure shows exactly the same energy and cross section range. From these figures we can see that as temperature increases the peaks of the resonances become lower, and the minima between resonances become higher. At extremely high temperature the entire resonance structure disappears and the cross section approaches a simple 1/v shape (where v is the neutron speed). This temperature effect will have a very important effect on resonance self-shielding in any neutron transport calculation. You should note from these figures that due to the large resonance spacing in U238 the resonance structure can still be seen up to very high temperatures.

To understand the importance of considering temperature we should consider reaction rates, such as captures/second, in various systems. In optically thin systems (few mean free paths dimensions) the flux will be unshielded, and our reaction rates will be defined by a simple cross section average,

Unshielded Capture =   = capture cross section times neutron flux

In optically thick systems (many mean free paths dimensions) the flux will be shielded (the flux is suppressed by the total cross section) and our reaction rates must include the effect of self-shielding on the cross section average,

Shielded Capture =  = including one over total cross section

Consider for example the U238 capture cross section between 1 and 10 keV as shown in fig. 1 and 2. If we calculate the unshielded and shielded average capture cross section for the energy interval over the range of temperatures shown in figs. 1 and 2, we obtain the results shown below in table 1.

What we see from these results is that the unshielded average capture cross section is virtually independent of temperature, being about 1 barn over the entire temperature range. In contrast the shielded average cross section varying by over a factor of three between the 0 K average (0.293 barns) and the 10 keV average (0.939 barns). The point to learn from this is that without including the effect of self-shielding in multi-group calculations, temperature has very little effect on the average cross sections, which is quite simply wrong for optically thick systems.

Table 1: Effect of Temperature on Average Cross Sections

Temp.		Unshielded	Shielded

(barns)	(barns)

0 K		0.996		0.293

293.6 K		0.966 	0.526

600 K		0.996		0.576

1,200 K		0.996		0.630

12,000 K (1 eV)	0.996		0.799

10 eV		0.998		0.905

100 eV		1.000		0.933

1 keV		1.004		0.935

10 keV		1.007		0.939

2) Another, less well known, effect of Doppler broadening is at lower energies where as temperature increases the low energy constant scattering cross section increases and at very low energies approaches a simple 1/v shape (where v is the neutron speed); this effect is explained in detail in ref [R5]. Figure 3 illustrates the effect of temperature on the hydrogen total cross section. From this figure we can see that starting from a “cold” (0 Kelvin) cross section that is constant at about 20 barns, as temperature increases the cross section increases. Compared to the “cold” 20 barn cross section, at thermal energy the Doppler broadened cross section is about 30 barns, i.e., 50 % higher. Note also from this figure that this effect extends well above thermal energy. For example, at 293.6 Kelvin the thermal energy is 0.0253 eV, but we can see this effect up to about 1 eV; a factor of 400 higher in energy. From the lower half of figure 2 we can see that at very low energy the cross section approaches a simple 1/v shape (where v is the neutron speed) and the cross sections at various temperatures become proportional to one another. This effect on the cross sections at low energy is very important for thermal and low energy neutron systems.

3) Yet another important effect of temperature is that at lower energies neutrons do not slow down in energy as quickly and neutron scatter can even result in the upscatter of neutrons, i.e., when neutrons scatter they can gain, rather than lose, energy. This is a well known effect at low energies, where thermal scattering law data or a free gas model is used to model the interaction of neutrons with target atoms that are moving about with thermal motion. Figure 4 illustrates the effect of temperature on the neutron spectrum over a wide range of temperatures [R7]. This effect can also be important at higher energies, particularly near narrow resonances, where thermal motion of the target atoms can cause neutrons to slightly upscatter, but even slight upscatter can cause a neutron to scatter from below to above the energy of a very narrow resonance. See reference [R6], below for a routine designed to be used in conjunction with the SIGMA1 method of Doppler broadening [R5], to handle neutron thermal scattering. This routine [R6] is completely compatible for use with the cross sections included here, since these cross sections were Doppler broadened using the SIGMA1 method [R5]. The combination of SIGMA1 [R5] Doppler broadened cross sections and THERMAL [R6] to handle thermal scattering, is currently used in the TART Monte Carlo transport code [R8].

Fig.1: Effect of Doppler Broadening on Resonance Cross Sections

Fig.2: Effect of Doppler Broadening on Resonance Cross Sections

Fig.3: Effect of Doppler Broadening on Low Energy Cross Sections

Fig.4: Effect of Doppler Broadening on Neutron Spectrum