LLNL-TR-534938

POINT 2012: ENDF/B-VII.1 Final

# Temperature Dependent

Cross Section Library

A Brief Library Summary

by

Dermott E. Cullen

Lawrence Livermore National Laboratory

P.O.Box 808/L-198

Livermore, CA 94550

January 7, 2012

Approved for public release; further dissemination unlimited

DISCLAIMER

This document was prepared as an account of work sponsored by an agency of the United States government. Neither the United States government nor Lawrence Livermore National Security, LLC, nor any of their employees makes any warranty, expressed or implied, or assumes any legal liability or responsibility for the accuracy, completeness, or usefulness of any information, apparatus, product, or process disclosed, or represents that its use would not infringe privately owned rights. Reference herein to any specific commercial product, process, or service by trade name, trademark, manufacturer, or otherwise does not necessarily constitute or imply its endorsement, recommendation, or favoring by the United States government or Lawrence Livermore National Security, LLC. The views and opinions of authors expressed herein do not necessarily state or reflect those of the United States government or Lawrence Livermore National Security, LLC, and shall not be used for advertising or product endorsement purposes.

This work performed under the auspices of the U.S. Department of Energy by Lawrence Livermore National Laboratory under Contract DE-AC52-07NA27344.

LLNL-TR-534938

POINT 2012: ENDF/B-VII.1 Final

# Temperature Dependent

Cross Section Library

A Brief Library Summary

by

Dermott E. Cullen

Lawrence Livermore National Laboratory

P.O.Box 808/L-198

Livermore, CA 94550

January 7, 2012

Table of Contents

- A Brief Library Summary

- Overview

- Introduction: POINT 2012: ENDF/B-VII.1 Final

- PREPRO 2012 Codes

- Data Processing

- Accuracy of Results

- Contents of the Library

- Requesting POINT 2012 Data

- Installation and Use of POINT 2012

- Acknowledgments

- References

- Appendix A: Contents of ENDF/B-VII.1

- Appendix B: Elemental vs. Isotopic Evaluations

- Appendix C: Completeness of VII.1 and VII.0

- Appendix D: Summary of  for all isotopes in ENDF/B-VII.1 and VII.0

- Appendix E: The Effects of Temperature and Doppler Broadening

A Brief Library Summary

This is merely an informal memo to briefly summarize the contents of the new ENDF/B-VII.1 Final library, released in December 2011; focus here is only on the quantity of data. A later document to planned to more completely document the quality of this new library.

###### Overview

This report is one in the series of “POINT” reports that over the years have presented temperature dependent cross sections for the then current version of ENDF/B [R1]. In each case I have used my personal computer at home and publicly available data and codes

:

- publicly available nuclear data (the current ENDF/B data, available on-line at the National Nuclear Data Center, Brookhaven National Laboratory,

http://www.nndc.bnl.gov/) and,

- publicly available computer codes (the current PREPRO codes, available on-line at the Nuclear Data Section, IAEA, Vienna, Austria,

http://www-nds.iaea.or.at/ndspub/endf/prepro/) and,

- My own personal computer located in my home.

I have used these in combination to produce the temperature dependent cross sections used in applications and described in this report. I should mention that today anyone with a personal computer can produce these results: by its very nature I consider this data to be born in the public domain.

Introduction: POINT 2012: ENDF/B-VII.1 Final

The latest ENDF/B-VII.1 Final data library was recently released and is now freely available through the National Nuclear Data Center (NNDC), Brookhaven National Laboratory. This release completely supersedes all preceding releases of ENDF/B.

Individual files and/or the complete tarball can also be downloaded from:

http://www.nndc.bnl.gov/

Compared to VII.0 which included 393 evaluations, VII.1 included 423 evaluations; this includes 32 new evaluations; 2 natural evaluations were dropped (23-V – Nat, and 30-Zn-Nat). The 32 new evaluations are; note the isotopes of 23-V and 30-Zn; these have replaced the natural evaluations in VII.0.

32 New Evaluation in VII.1 (not in VII.0)

| 23-V-50 23-V-51 30-Zn-64 30-Zn-65 | 30-Zn-66 30-Zn-67 30-Zn-68 30-Zn-70 | 69-Tm-168 69-Tm-169 69-Tm-170 73-Ta-180 | 74-W-180 81-Tl-203 81-Tl-205 90-Th-231 | 91-Pa-229 91-Pa-230 92-U-230 92-U-231 | 93-Np-234 95-Am-240 96-Cm-240 97-Bk-245 | 97-Bk-246 97-Bk-247 97-Bk-248 98-Cf-246 | 98-Cf-248 99-Es-251 99-Es-252 99-Es-254m |
| --- | --- | --- | --- | --- | --- | --- | --- |

423 Evaluations in VII.1 (32 new evaluations in RED)

| 1-H -1 1-H -2 1-H -3 2-He-3 2-He-4 3-Li-6 3-Li-7 4-Be-7 4-Be-9 5-B -10 5-B -11 6-C -Nat 7-N -14 7-N -15 8-O -16 8-O -17 9-F -19 11-Na-22 11-Na-23 12-Mg-24 12-Mg-25 12-Mg-26 13-Al-27 14-Si-28 14-Si-29 14-Si-30 15-P -31 16-S -32 16-S -33 16-S -34 16-S -36 17-Cl-35 17-Cl-37 18-Ar-36 18-Ar-38 18-Ar-40 19-K -39 19-K -40 19-K -41 20-Ca-40 20-Ca-42 20-Ca-43 | 20-Ca-44 20-Ca-46 20-Ca-48 21-Sc-45 22-Ti-46 22-Ti-47 22-Ti-48 22-Ti-49 22-Ti-50 23-V -50 23-V -51 24-Cr-50 24-Cr-52 24-Cr-53 24-Cr-54 25-Mn-55 26-Fe-54 26-Fe-56 26-Fe-57 26-Fe-58 27-Co-58 27-Co-58m 27-Co-59 28-Ni-58 28-Ni-59 28-Ni-60 28-Ni-61 28-Ni-62 28-Ni-64 29-Cu-63 29-Cu-65 30-Zn-64 30-Zn-65 30-Zn-66 30-Zn-67 30-Zn-68 30-Zn-70 31-Ga-69 31-Ga-71 32-Ge-70 32-Ge-72 32-Ge-73 | 32-Ge-74 32-Ge-76 33-As-74 33-As-75 34-Se-74 34-Se-76 34-Se-77 34-Se-78 34-Se-79 34-Se-80 34-Se-82 35-Br-79 35-Br-81 36-Kr-78 36-Kr-80 36-Kr-82 36-Kr-83 36-Kr-84 36-Kr-85 36-Kr-86 37-Rb-85 37-Rb-86 37-Rb-87 38-Sr-84 38-Sr-86 38-Sr-87 38-Sr-88 38-Sr-89 38-Sr-90 39-Y -89 39-Y -90 39-Y -91 40-Zr-90 40-Zr-91 40-Zr-92 40-Zr-93 40-Zr-94 40-Zr-95 40-Zr-96 41-Nb-93 41-Nb-94 41-Nb-95 | 42-Mo-92 42-Mo-94 42-Mo-95 42-Mo-96 42-Mo-97 42-Mo-98 42-Mo-99 42-Mo-100 43-Tc-99 44-Ru-96 44-Ru-98 44-Ru-99 44-Ru-100 44-Ru-101 44-Ru-102 44-Ru-103 44-Ru-104 44-Ru-105 44-Ru-106 45-Rh-103 45-Rh-105 46-Pd-102 46-Pd-104 46-Pd-105 46-Pd-106 46-Pd-107 46-Pd-108 46-Pd-110 47-Ag-107 47-Ag-109 47-Ag-110m 47-Ag-111 48-Cd-106 48-Cd-108 48-Cd-110 48-Cd-111 48-Cd-112 48-Cd-113 48-Cd-114 48-Cd-115m 48-Cd-116 49-In-113 | 49-In-115 50-Sn-112 50-Sn-113 50-Sn-114 50-Sn-115 50-Sn-116 50-Sn-117 50-Sn-118 50-Sn-119 50-Sn-120 50-Sn-122 50-Sn-123 50-Sn-124 50-Sn-125 50-Sn-126 51-Sb-121 51-Sb-123 51-Sb-124 51-Sb-125 51-Sb-126 52-Te-120 52-Te-122 52-Te-123 52-Te-124 52-Te-125 52-Te-126 52-Te-127m 52-Te-128 52-Te-129m 52-Te-130 52-Te-132 53-I -127 53-I -129 53-I -130 53-I -131 53-I -135 54-Xe-123 54-Xe-124 54-Xe-126 54-Xe-128 54-Xe-129 54-Xe-130 | 54-Xe-131 54-Xe-132 54-Xe-133 54-Xe-134 54-Xe-135 54-Xe-136 55-Cs-133 55-Cs-134 55-Cs-135 55-Cs-136 55-Cs-137 56-Ba-130 56-Ba-132 56-Ba-133 56-Ba-134 56-Ba-135 56-Ba-136 56-Ba-137 56-Ba-138 56-Ba-140 57-La-138 57-La-139 57-La-140 58-Ce-136 58-Ce-138 58-Ce-139 58-Ce-140 58-Ce-141 58-Ce-142 58-Ce-143 58-Ce-144 59-Pr-141 59-Pr-142 59-Pr-143 60-Nd-142 60-Nd-143 60-Nd-144 60-Nd-145 60-Nd-146 60-Nd-147 60-Nd-148 60-Nd-150 | 61-Pm-147 61-Pm-148 61-Pm-148m 61-Pm-149 61-Pm-151 62-Sm-144 62-Sm-147 62-Sm-148 62-Sm-149 62-Sm-150 62-Sm-151 62-Sm-152 62-Sm-153 62-Sm-154 63-Eu-151 63-Eu-152 63-Eu-153 63-Eu-154 63-Eu-155 63-Eu-156 63-Eu-157 64-Gd-152 64-Gd-153 64-Gd-154 64-Gd-155 64-Gd-156 64-Gd-157 64-Gd-158 64-Gd-160 65-Tb-159 65-Tb-160 66-Dy-156 66-Dy-158 66-Dy-160 66-Dy-161 66-Dy-162 66-Dy-163 66-Dy-164 67-Ho-165 67-Ho-166m 68-Er-162 68-Er-164 | 68-Er-166 68-Er-167 68-Er-168 68-Er-170 69-Tm-168 69-Tm-169 69-Tm-170 71-Lu-175 71-Lu-176 72-Hf-174 72-Hf-176 72-Hf-177 72-Hf-178 72-Hf-179 72-Hf-180 73-Ta-180 73-Ta-181 73-Ta-182 74-W -180 74-W -182 74-W -183 74-W -184 74-W -186 75-Re-185 75-Re-187 77-Ir-191 77-Ir-193 79-Au-197 80-Hg-196 80-Hg-198 80-Hg-199 80-Hg-200 80-Hg-201 80-Hg-202 80-Hg-204 81-Tl-203 81-Tl-205 82-Pb-204 82-Pb-206 82-Pb-207 82-Pb-208 83-Bi-209 88-Ra-223 | 88-Ra-224 88-Ra-225 88-Ra-226 89-Ac-225 89-Ac-226 89-Ac-227 90-Th-227 90-Th-228 90-Th-229 90-Th-230 90-Th-231 90-Th-232 90-Th-233 90-Th-234 91-Pa-229 91-Pa-230 91-Pa-231 91-Pa-232 91-Pa-233 92-U -230 92-U -231 92-U -232 92-U -233 92-U -234 92-U -235 92-U -236 92-U -237 92-U -238 92-U -239 92-U -240 92-U -241 93-Np-234 93-Np-235 93-Np-236 93-Np-237 93-Np-238 93-Np-239 94-Pu-236 94-Pu-237 94-Pu-238 94-Pu-239 94-Pu-240 94-Pu-241 | 94-Pu-242 94-Pu-243 94-Pu-244 94-Pu-246 95-Am-240 95-Am-241 95-Am-242 95-Am-242m 95-Am-243 95-Am-244 95-Am-244m 96-Cm-240 96-Cm-241 96-Cm-242 96-Cm-243 96-Cm-244 96-Cm-245 96-Cm-246 96-Cm-247 96-Cm-248 96-Cm-249 96-Cm-250 97-Bk-245 97-Bk-246 97-Bk-247 97-Bk-248 97-Bk-249 97-Bk-250 98-Cf-246 98-Cf-248 98-Cf-249 98-Cf-250 98-Cf-251 98-Cf-252 98-Cf-253 98-Cf-254 99-Es-251 99-Es-252 99-Es-253 99-Es-254 99-Es-254m 99-Es-255 100-Fm-255 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

## PREPRO 2012 Codes

In addition to the changes in the ENDF/B-VII.1 evaluations, it should be noted that between the last version of this report, where the PREPRO 2010 codes were used, and the current version, where the PREPRO 2012 codes were used, there have been improvements in the ENDF/B Pre-processing codes (PREPRO). The  improvements were both in terms of improving the basic methods used by the codes and in terms of incorporating the latest ENDF-6 Formats and Procedures used by the current evaluations. The result is more accurate cross section data throughout the POINT 2012 library.

WARNING – due to recent changes in ENDF-6 Formats and Procedures only the latest version of the ENDF/B Pre-processing codes, namely PREPRO 2012, can be used to accurately process all current ENDF/B-VII evaluations. If you fail to heed this warning and you use any earlier versions of these codes the results will be inaccurate.

The PREPRO 2012 codes run on virtually any computer, and will soon be available FREE on-line from the Nuclear Data Section, IAEA, Vienna, Austria, website at,

http://www-nds.iaea.or.at/ndspub/endf/prepro/

Data Processing

As distributed the original evaluated data includes cross sections represented in the form of a combination of resonance parameters and/or tabulated energy dependent cross sections, nominally at 0 Kelvin temperature. For use in applications, this data has been processed using the 2012 version of the ENDF/B Pre-processing codes (PREPRO 2012) to produce temperature dependent, linearly interpolable in energy, tabulated cross sections, in the ENDF-6 format.

For use in applications this library has been processed into the form of temperature dependent cross sections at eight neutron reactor like temperatures, between 0 and 2100 Kelvin, in steps of 300 Kelvin (the exception being 293.6 Kelvin, for exact room temperature at 20 Celsius). It has also been processed to five astrophysics like temperatures, 1, 10, 100 eV, 1 and 10 keV. For reference purposes, 300 Kelvin is approximately 1/40 eV, so that 1 eV is approximately 12,000 Kelvin. At each temperature the cross sections are tabulated and linearly interpolable in energy.

The steps required and codes used to produce room temperature, linearly interpolable tabulated cross sections, in the ENDF-6 format, are described below; the name of each code in given in parenthesis; for details of each code see reference [R3].

Here are the steps, and PREPRO 2012 codes, used to process the data, in the order in which the codes were used.

1) Linearly interpolable, tabulated cross sections (LINEAR)

2) Including the resonance contribution (RECENT)

3) Doppler broaden all cross sections to temperature (SIGMA1)

4) Check data, define redundant cross sections by summation (FIXUP)

5) Update evaluation dictionary in MF/MT=1/451 (DICTIN)

For the "cold" (0 Kelvin) data steps 1), 2) and 4), 5) were used (no Doppler broadening). For the data at other temperatures, after steps 1) and 2), the data was Doppler broadened to each temperature using step 3), and the results were then made consistent with the ENDF/B formats and conventions using steps 4) and 5), to produce the final distributed data.

The result is linearly interpolable in energy, tabulated, temperature dependent cross sections, in the ENDF-6 format, ready to be used in applications.

Note - this processing only involved the energy dependent neutron cross sections. All other data in the evaluations, e.g., angular and energy distributions, was not affected by this processing, and is identical in all versions of the final results, i.e., it is the same in all of the directories, ORIGINAL, as well as K0 through K2100, and 1ev through 10kev, on the DVDs.

Accuracy of Results

Each of the codes described above that was used to process data to obtain tabulated, linearly interpolable in energy cross sections, processed the data to within a user defined accuracy, or allowable uncertainty. The ENDF/B Pre-processing codes (PREPRO 2012) are self-documenting, in the sense that the ENDF/B formatted output data that each code produces includes comments at the beginning of each evaluation defining the accuracy to which the cross sections were calculated. The combination of comments added by all of the codes defines the sequence and accuracy used by all of them. The accuracy is the same for all evaluations. Therefore, for exact details of the accuracy of the data, see the comments at the beginning of any evaluation. For use in POINT 2012 all cross sections were reconstructed to within an accuracy of 0.01% in the thermal range, and 0.1 % at all other energies and temperatures; this is beyond the accuracy to which this data in known, so that I assume that the data processing does not add any significant additional error to the inherent error of the data.

Contents of the Library

This library contains all of the evaluations in the ENDF/B-VI.1 general purpose library. The below table summarizes the contents of the ENDF/B-VII.1 general purpose library. This library contains evaluations for 423 materials (isotopes or naturally occurring elemental mixtures of isotopes).

This library does not contain data from special purpose ENDF/B-VII libraries, such as fission products, thermal scattering, photon interaction data. To obtain any of these special purpose libraries contact the National Nuclear Data Center, Brookhaven National Laboratory,

ENDF@bnlnd2.dne.bnl.gov

In the POINT 2012 library each evaluation is stored as a separate file. The following table defines each material and the corresponding filename. The entire library is in the computer independent ENDF-6 character format, which allows the data to be easily transported between computers. The entire library requires approximately 15 gigabyte of storage and is distributed on one DVD compressed; see below for details of the DVD.

This library contains data for some metastable materials, which are indicated by an "M" at the end of their descriptions.

The majority of these evaluations are complete, in the sense that they include all cross sections over the energy range 10-5 eV to at least 20 MeV. See the appendix for a list of all evaluations, plus a separate list of incomplete evaluations; there are now only a few.

The DVD is compressed; when uncompressed you will find a single directory named POINT2012 containing fifteen (15) sub-directories,

DOCUMENT	- A copy of this report in  MSWord and PDF formats.

ORIGINAL	- The original ENDF/B data before it was processed.

K0		- 0 Kelvin cross sections

K293.6		- 293.6 Kelvin cross sections

K600		- 600 Kelvin cross sections

K900		- 900 Kelvin cross sections

K1200		- 1200 Kelvin cross sections

K1500		- 1500 Kelvin cross sections

K1800		- 1800 Kelvin cross sections

K2100		- 2100 Kelvin cross sections

1eV		- 1 eV cross sections

10eV		- 10 eV cross sections

100eV		- 100 eV cross sections

1keV		- 1 keV cross sections

10keV		- 10 keV cross sections

With the exception of DOCUMENT, each of these directories contains 424 files, one file for each of the 423 evaluation, plus one HTML file to allow interactive data retrieval. Each evaluation is a complete ENDF/B "tape" [R2], including a starting "tape" identification line, and ending with a "tape" end line [R2]. In this form, each file can be used by a wide variety of available computer codes that treat data in the ENDF/B format, e.g., all of the PREPRO codes.

## Requesting POINT 2012 Data

Please do not contact the author of this report to request this data; I do not have the resources necessary to directly respond to requests for this data. This data has been distributed and is Internationally available from nuclear data/code centers throughout the World,

- Within the United States: contact the National Nuclear Data Center, Brookhaven National Laboratory, Mike Herman at,

services@bnlnd2.dne.bnl.gov

- Within Western Europe: contact the OECD Nuclear Energy Agency/ Data Bank (NEA/DB), Paris, France, programs@nea.fr

- Otherwise: contact the Nuclear Data Section, International Atomic Energy Agency, Vienna, Austria, Alberto Mengoni at,

A.Mengoni@iaea.org

Installation and Use of POINT 2012

I recommend that you,

- Copy the single file from the POINT 2012 DVD to your computer,

- Uncompress and un-tar the file; then delete the compressed and tar files.

- You should then have one directory named POINT2012 containing all of the data

- To random access the data execute (double click) POINT2012.htm.

The main POINT2012 directory will contain the fifteen (15) sub-directories, described above. These POINT 2012 directories include HTML routines to allow interactive retrieval of the data. The result will be a directory of about 15 gigabytes. To put that in perspective, today it costs less than $0.10 U.S. to purchase, install, and maintain on-line one gigabyte of disk storage. Therefore the cost of maintaining this 16 gigabyte library on-line is trivial.

Acknowledgments

I thank Said Mughabghab for his detailed explanation of the use of his newly published resonance parameters [R4] in ENDF/B-VII.0 evaluations. I thank Ramon E. Arcilla, Jr., of the National Nuclear Data Center (NNDC), Brookhaven National Laboratory, for supplying the original ENDF/B-VII.0, used in this project. I thank Liam Costello, of the Nuclear Data Section, International Atomic Energy Agency, for supplying the ENDF/B Pre-processing codes, PREPRO 2012, used in this project. I thank Janice Arwood (RSICC, Oak Rdige) for carefully checking and recommending improvements. I thank Nancy Larsen, Bob MacFarlane, Maurice Greene, and Mike Dunn, for their comparison of their cross section processing codes (SAMMY, NJOY and AMPX) against the PREPRO codes. These comparisons have led to significant improvements in the accuracy and reliability of the results produced by all four codes (SAMMY, NJOY, AMPX, PREPRO). I thank Andre Trkov, Skip Kahler, Robert MacFarlane, Mike Herman and Dave Heinrichs for proofreading the draft of this report and making many helpful corrections and improvements, which I incorporated in the final report.

References

[R1a] ”POINT 2011: A Temperature Dependent ENDF/B-VII.0 data Cross Section Library”, Lawrence Livermore National Laboratory, UCRL-TR-479947, rev. 1, May 2011,

[R1b] ”POINT 2009: A Temperature Dependent ENDF/B-VII.0 data Cross Section Library, June 6, 2009.

[R1c] ”POINT 2007: A Temperature Dependent ENDF/B-VII.0 data Cross Section Library”, Lawrence Livermore National Laboratory, UCRL-TR-228089, February 2007.

[R2] Data Formats and Procedures for the Evaluated Nuclear Data File ENDF-6, BNL-NCS-44945, Rev. 11/95, edited by V. McLane, et al. National Nuclear Data Center, Brookhaven National Lab. http://www.nndc.bnl.gov/nndcscr/documents/endf/endf102/

[R3] "PREPRO 2010: The 2010 ENDF/B Pre-Processing Codes," by D.E. Cullen, Nuclear Data Section, International Atomic Energy Agency, Vienna, Austria, IAEA-NDS-39, Rev. 14, Oct. 31, 2010; PREPRO 2010 is now publicly available. http://www-nds.iaea.or.at/ndspub/endf/prepro/

PREPRO 2012 will be released for public use early in 2012; until then I recommend you use currently available PREPRO 2010 codes.

[R4] “Atlas of Nuclear Resonances”, by S.F. Mughabghab, National Nuclear Data Center, Brookhaven National Laboratory, published by Elsevier, March 2006.

[R5] "Exact Doppler Broadening of Tabulated Cross Sections," by D.E. Cullen and C.R. Weisbin, Nuclear Science and Engineering 60, p. 199 (1975)

[R6] "THERMAL: A Routine Designed to Calculate Neutron Thermal Scattering," by D.E. Cullen, Lawrence Livermore National Laboratory, UCRL-ID-120560-Rev-1, Sept. 1995.

http://home.comcast.net/~redcullen1

[R7] “Verification of High Temperature Free Atom Thermal Scattering in MERCURY Compared to TART”, by D.E. Cullen, Scott McKinley and Christian Hagmann, Lawrence Livermore National Laboratory, UCRL-TR-226340, August 1, 2006.

[R8] “TART2005: A Coupled Neutron-Photon 3-D, Time Dependent, Combinatorial Geometry Monte Carlo Transport Code," by D.E. Cullen, Lawrence Livermore National Laboratory, UCRL-SM-218009, Nov. 22, 2005.

Appendix A: Contents of ENDF/B-VII.1 (32 new + 391 old = 423 total evaluations)

| 1-H -1 1-H -2 1-H -3 2-He-3 2-He-4 3-Li-6 3-Li-7 4-Be-7 4-Be-9 5-B -10 5-B -11 6-C -Nat 7-N -14 7-N -15 8-O -16 8-O -17 9-F -19 11-Na-22 11-Na-23 12-Mg-24 12-Mg-25 12-Mg-26 13-Al-27 14-Si-28 14-Si-29 14-Si-30 15-P -31 16-S -32 16-S -33 16-S -34 16-S -36 17-Cl-35 17-Cl-37 18-Ar-36 18-Ar-38 18-Ar-40 19-K -39 19-K -40 19-K -41 20-Ca-40 20-Ca-42 20-Ca-43 | 20-Ca-44 20-Ca-46 20-Ca-48 21-Sc-45 22-Ti-46 22-Ti-47 22-Ti-48 22-Ti-49 22-Ti-50 23-V -50 23-V -51 24-Cr-50 24-Cr-52 24-Cr-53 24-Cr-54 25-Mn-55 26-Fe-54 26-Fe-56 26-Fe-57 26-Fe-58 27-Co-58 27-Co-58m 27-Co-59 28-Ni-58 28-Ni-59 28-Ni-60 28-Ni-61 28-Ni-62 28-Ni-64 29-Cu-63 29-Cu-65 30-Zn-64 30-Zn-65 30-Zn-66 30-Zn-67 30-Zn-68 30-Zn-70 31-Ga-69 31-Ga-71 32-Ge-70 32-Ge-72 32-Ge-73 | 32-Ge-74 32-Ge-76 33-As-74 33-As-75 34-Se-74 34-Se-76 34-Se-77 34-Se-78 34-Se-79 34-Se-80 34-Se-82 35-Br-79 35-Br-81 36-Kr-78 36-Kr-80 36-Kr-82 36-Kr-83 36-Kr-84 36-Kr-85 36-Kr-86 37-Rb-85 37-Rb-86 37-Rb-87 38-Sr-84 38-Sr-86 38-Sr-87 38-Sr-88 38-Sr-89 38-Sr-90 39-Y -89 39-Y -90 39-Y -91 40-Zr-90 40-Zr-91 40-Zr-92 40-Zr-93 40-Zr-94 40-Zr-95 40-Zr-96 41-Nb-93 41-Nb-94 41-Nb-95 | 42-Mo-92 42-Mo-94 42-Mo-95 42-Mo-96 42-Mo-97 42-Mo-98 42-Mo-99 42-Mo-100 43-Tc-99 44-Ru-96 44-Ru-98 44-Ru-99 44-Ru-100 44-Ru-101 44-Ru-102 44-Ru-103 44-Ru-104 44-Ru-105 44-Ru-106 45-Rh-103 45-Rh-105 46-Pd-102 46-Pd-104 46-Pd-105 46-Pd-106 46-Pd-107 46-Pd-108 46-Pd-110 47-Ag-107 47-Ag-109 47-Ag-110m 47-Ag-111 48-Cd-106 48-Cd-108 48-Cd-110 48-Cd-111 48-Cd-112 48-Cd-113 48-Cd-114 48-Cd-115m 48-Cd-116 49-In-113 | 49-In-115 50-Sn-112 50-Sn-113 50-Sn-114 50-Sn-115 50-Sn-116 50-Sn-117 50-Sn-118 50-Sn-119 50-Sn-120 50-Sn-122 50-Sn-123 50-Sn-124 50-Sn-125 50-Sn-126 51-Sb-121 51-Sb-123 51-Sb-124 51-Sb-125 51-Sb-126 52-Te-120 52-Te-122 52-Te-123 52-Te-124 52-Te-125 52-Te-126 52-Te-127m 52-Te-128 52-Te-129m 52-Te-130 52-Te-132 53-I -127 53-I -129 53-I -130 53-I -131 53-I -135 54-Xe-123 54-Xe-124 54-Xe-126 54-Xe-128 54-Xe-129 54-Xe-130 | 54-Xe-131 54-Xe-132 54-Xe-133 54-Xe-134 54-Xe-135 54-Xe-136 55-Cs-133 55-Cs-134 55-Cs-135 55-Cs-136 55-Cs-137 56-Ba-130 56-Ba-132 56-Ba-133 56-Ba-134 56-Ba-135 56-Ba-136 56-Ba-137 56-Ba-138 56-Ba-140 57-La-138 57-La-139 57-La-140 58-Ce-136 58-Ce-138 58-Ce-139 58-Ce-140 58-Ce-141 58-Ce-142 58-Ce-143 58-Ce-144 59-Pr-141 59-Pr-142 59-Pr-143 60-Nd-142 60-Nd-143 60-Nd-144 60-Nd-145 60-Nd-146 60-Nd-147 60-Nd-148 60-Nd-150 | 61-Pm-147 61-Pm-148 61-Pm-148m 61-Pm-149 61-Pm-151 62-Sm-144 62-Sm-147 62-Sm-148 62-Sm-149 62-Sm-150 62-Sm-151 62-Sm-152 62-Sm-153 62-Sm-154 63-Eu-151 63-Eu-152 63-Eu-153 63-Eu-154 63-Eu-155 63-Eu-156 63-Eu-157 64-Gd-152 64-Gd-153 64-Gd-154 64-Gd-155 64-Gd-156 64-Gd-157 64-Gd-158 64-Gd-160 65-Tb-159 65-Tb-160 66-Dy-156 66-Dy-158 66-Dy-160 66-Dy-161 66-Dy-162 66-Dy-163 66-Dy-164 67-Ho-165 67-Ho-166m 68-Er-162 68-Er-164 | 68-Er-166 68-Er-167 68-Er-168 68-Er-170 69-Tm-168 69-Tm-169 69-Tm-170 71-Lu-175 71-Lu-176 72-Hf-174 72-Hf-176 72-Hf-177 72-Hf-178 72-Hf-179 72-Hf-180 73-Ta-180 73-Ta-181 73-Ta-182 74-W -180 74-W -182 74-W -183 74-W -184 74-W -186 75-Re-185 75-Re-187 77-Ir-191 77-Ir-193 79-Au-197 80-Hg-196 80-Hg-198 80-Hg-199 80-Hg-200 80-Hg-201 80-Hg-202 80-Hg-204 81-Tl-203 81-Tl-205 82-Pb-204 82-Pb-206 82-Pb-207 82-Pb-208 83-Bi-209 88-Ra-223 | 88-Ra-224 88-Ra-225 88-Ra-226 89-Ac-225 89-Ac-226 89-Ac-227 90-Th-227 90-Th-228 90-Th-229 90-Th-230 90-Th-231 90-Th-232 90-Th-233 90-Th-234 91-Pa-229 91-Pa-230 91-Pa-231 91-Pa-232 91-Pa-233 92-U -230 92-U -231 92-U -232 92-U -233 92-U -234 92-U -235 92-U -236 92-U -237 92-U -238 92-U -239 92-U -240 92-U -241 93-Np-234 93-Np-235 93-Np-236 93-Np-237 93-Np-238 93-Np-239 94-Pu-236 94-Pu-237 94-Pu-238 94-Pu-239 94-Pu-240 94-Pu-241 | 94-Pu-242 94-Pu-243 94-Pu-244 94-Pu-246 95-Am-240 95-Am-241 95-Am-242 95-Am-242m 95-Am-243 95-Am-244 95-Am-244m 96-Cm-240 96-Cm-241 96-Cm-242 96-Cm-243 96-Cm-244 96-Cm-245 96-Cm-246 96-Cm-247 96-Cm-248 96-Cm-249 96-Cm-250 97-Bk-245 97-Bk-246 97-Bk-247 97-Bk-248 97-Bk-249 97-Bk-250 98-Cf-246 98-Cf-248 98-Cf-249 98-Cf-250 98-Cf-251 98-Cf-252 98-Cf-253 98-Cf-254 99-Es-251 99-Es-252 99-Es-253 99-Es-254 99-Es-254m 99-Es-255 100-Fm-255 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Appendix B: Elemental vs. Isotopic Evaluations

Successive versions of ENDF/B have replaced elemental evaluations by isotopic evaluations. Between ENDF/B-VI and VII 13 elemental evaluations were deleted, i.e., included in ENDF/B-VI, but not included in ENDF/B-VII, with VII.0 only including elemental evaluations for three elements: 6-C, 23-V, and 30-Zn. Between VII.0 and VII.1 2 elemental evaluations were deleted (23-V, and 30-Zn), and replaced by isotopic evaluations, leaving only 6-C: 6-C-12 98.93%/ 6-C-13 1.07% missing – so that 6C-Nat is almost entirely the single isotope 6-C-12.

In addition evaluations for the isotopes of 68-Tm and 81-Tl have been added.

All of these isotopes in VII.1 are complete, in the sense that they include major cross sections (elastic, capture, inelastic) over the energy range 10-5 eV up to at least 20 MeV.

WARNING: Be aware that evaluating isotopes is difficult and the quality of minor isotopes may be poor. To my knowledge as yet the summing these isotopes to define equivalent elemental evaluations has not been verified against experimental measurements.

New Isotopic evaluations in VII.1 (28 new, 19 old)

| Element Isotope | Element Isotope | Element Isotope |
| --- | --- | --- |
| 12-Mg-Nat 12-Mg- 24 12-Mg- 25 12-Mg- 26 14-Si-Nat 14-Si- 28 14-Si- 29 14-Si- 30 16-S -Nat 16-S - 32 16-S - 33 16-S - 34 16-S - 36 17-Cl-Nat 17-Cl- 35 17-Cl- 37 19-K -Nat 19-K - 39 19-K - 40 19-K - 41 20-Ca-Nat 20-Ca- 40 20-Ca- 42 20-Ca- 43 20-Ca- 44 20-Ca- 46 20-Ca- 48 | 22-Ti-Nat 22-Ti- 46 22-Ti- 47 22-Ti- 48 22-Ti- 49 22-Ti- 50 23-V –Nat 23-V - 50 23-V – 51 30-Zn-Nat 30-Zn- 64 30-Zn- 65 30-Zn- 66 30-Zn- 67 30-Zn- 68 30-Zn- 70 31-Ga-Nat 31-Ga- 69 31-Ga- 71 40-Zr-Nat 40-Zr- 90 40-Zr- 91 40-Zr- 92 40-Zr- 93 40-Zr- 94 40-Zr- 95 40-Zr- 96 | 42-Mo-Nat 42-Mo- 92 42-Mo- 94 42-Mo- 95 42-Mo- 96 42-Mo- 97 42-Mo- 98 42-Mo- 99 42-Mo-100 49-In-Nat 49-In-113 49-In-115 69-Tm-168 69-Tm-169 69-Tm-170 72-Hf-Nat 72-Hf-174 72-Hf-176 72-Hf-177 72-Hf-178 72-Hf-179 72-Hf-180 74-W -Nat 74-W -182 74-W -183 74-W -184 74-W -186 81-Tl-203 81-Tl-205 |

Appendix C: Completeness of VII.1 and VII.0

Here I present the results of simple tests to check the completeness of VV,1 and VII.0. Compared to the results for VII.0, the VII.1 show great improvement.

The results presented here should not be interpreted as indicating ERRORS, but rather as WARNINGS, that we should check the indicated data; in many cases I judge the data to be o.k. 4-Be-7 is a partial evaluations that failed almost all tests, and should never have been included in a ENDF/B general purpose library. Here I checked,

- MT=2, 102, 18, 4, 16 (elastic, capture, fission, inelastic, n,2n).

- MF=3, 4, 5 ,6 (cross sections, angular, energy, double differential)

For these test I assume,

- Every evaluation includes MT=2, 102, 4 and 16; this is obviously not true for some light isotopes, but for completeness they are included here, i.e., this is merely to inform users. Of the heavier isotopes only 28-Ni-59 appears to be a problem with no inelastic data.

- All cross sections are positive (>0) above their threshold up to at least 20 MeV. This is not true for some reactions which do not extend up to at least 20 MeV, particularly high energy capture, which is o.k. There are also a number of cases where the elastic is negative due to the resonance contribution.

- No isotopes with Z<90 include MT=18 (fission). For VII.0 this test found the obvious ERROR  in 43-Tc-99, which has positive fission widths = NONSENSE!!! This was corrected for VII.1. It also flagged isotopes of 88Ra and 89-Ac, which are questionable.

- I included many more completeness tests, but these were the only ones that failed.

VII.1 Completeness Results

Evaluation  MT=2    | MT=102  | MT=18   | MT=4    | MT=16   |

====================|=========|=========|=========|=========|

3 4 5 6 | 3 4 5 6 | 3 4 5 6 | 3 4 5 6 | 3 4 5 6 |

====================|=========|=========|=========|=========|

1-H -1     X X     | X     X |         |         |         |

1-H -2     X X     | X       |         |         | X     X |

1-H -3     X X     |         |         |         | X X X   |

2-He-3     X X     | X       |         |         |         |

2-He-4     X X     |         |         |         |         |

3-Li-6     X X     | X       |         | X X     |         |

4-Be-7     + X     |         |         |         |         |

4-Be-9     X X     | X       |         |         | X     X |

5-B -10    X X     | +       |         | X X     |         |

6-C -Nat   X X     | X       |         | X X X   |         |

28-Ni-59    X X     | X       |         |         | X X X   |

54-Xe-130   X X     | +       |         | + X X   | X X X   |

88-Ra-223   X X     | X       | ? ? ?   | X X X   | X X X   |

88-Ra-226   X X     | X       | ? ? ?   | X X X   | X X X   |

89-Ac-225   X X     | X     X | ? ? ?   | X     X | X     X |

89-Ac-226   X X     | X     X | ? ? ?   | X     X | X     X |

89-Ac-227   X X     | X     X | ? ? ?   | X     X | X     X |

The above rather short list for VII.1 can be compared to the below much longer list for VII.0 to see the improvements in completeness.

VII.0 Completeness Results

Evaluation  MT=2    | MT=102  | MT=18   | MT=4    | MT=16   |

====================|=========|=========|=========|=========|

3 4 5 6 | 3 4 5 6 | 3 4 5 6 | 3 4 5 6 | 3 4 5 6 |

====================|=========|=========|=========|=========|

1-H -1     X X     | X     X |         |         |         |

1-H -2     X X     | X       |         |         | X     X |

1-H -3     X X     |         |         |         | X X X   |

2-He-3     X X     | X       |         |         |         |

2-He-4     X X     |         |         |         |         |

3-Li-6     X X     | X       |         | X X     |         |

4-Be-7     + X     |         |         |         |         |

4-Be-9     X X     | X       |         |         | X     X |

5-B -10    X X     | +       |         | X X     |         |

6-C -Nat   X X     | X       |         | X X X   |         |

8-O -17    X X     | X       |         | X X X   | + X X   |

9-F -19    X X     | X       |         | X X   X | +     X |

12-Mg-26    X X     | X       |         | X X X   | + X X   |

16-S -33    X X     | X       |         | X X X   | + X X   |

16-S -36    X X     | X       |         | X X X   | + X X   |

17-Cl-35    + X     | X       |         | X     X | X     X |

19-K -39    X X     | X       |         | X X X   | + X X   |

19-K -40    X X     | X       |         | X X X   | + X X   |

28-Ni-59    X X     | X       |         |         | + X X   |

28-Ni-61    X X     | X       |         | +     X | X     X |

30-Zn-Nat   X X     | X       |         | X X X   | + X X   |

33-As-74    X X     | X     X |         |   ?   ? | X     X |

34-Se-76    X X     | X       |         | X X X   | + X X   |

36-Kr-86    X X     | X       |         | X X X   | + X X   |

37-Rb-87    X X     | X       |         | X X X   | + X X   |

38-Sr-90    X X     | X       |         | X X X   | + X X   |

39-Y -90    X X     | X     X |         |   ?   ? | X     X |

42-Mo-99    X X     | X       |         | X X X   | + X X   |

44-Ru-100   X X     | X       |         | X X X   | + X X   |

47-Ag-110m  X X     | X       |         | + X X   | X X X   |

48-Cd-106   X X     | X       |         | X X X   | + X X   |

48-Cd-115m  X X     | X     X |         | + X   X | X     X |

50-Sn-112   X X     | X       |         | X X X   | + X X   |

50-Sn-122   X X     | X       |         | X X X   | + X X   |

50-Sn-123   X X     | X       |         | X X X   | + X X   |

52-Te-122   X X     | X       |         | X X X   | + X X   |

52-Te-123   X X     | X       |         | X X X   | + X X   |

52-Te-125   X X     | X       |         | X X X   | + X X   |

52-Te-127m  X X     | X       |         | + X X   | X X X   |

52-Te-129m  X X     | X       |         | + X X   | X X X   |

53-I -129   X X     | X       |         | X X X   | + X X   |

54-Xe-129   X X     | X       |         | X X X   | + X X   |

54-Xe-130   X X     | +       |         | + X X   | X X X   |

55-Cs-134   X X     | X       |         | X X X   | + X X   |

55-Cs-135   X X     | X       |         | X X X   | + X X   |

56-Ba-132   X X     | X       |         | X X X   | + X X   |

56-Ba-135   X X     | X       |         | X X X   | + X X   |

56-Ba-137   X X     | X       |         | X X X   | + X X   |

58-Ce-144   X X     | X       |         | X X X   | + X X   |

61-Pm-148   X X     | X       |         | X X X   | + X X   |

63-Eu-151   X X     | X       |         | X X X   | + X X   |

67-Ho-166m  X X     | X     X |         | + X   X | X     X |

72-Hf-177   X X     | X       |         | + X X   | X X X   |

72-Hf-179   X X     | X       |         | + X X   | X X X   |

77-Ir-193   X X     | X     X |         | X X   X | +     X |

88-Ra-223   X X     | X       | ? ? ?   | X X X   | X X X   |

88-Ra-226   X X     | X       | ? ? ?   | X X X   | X X X   |

89-Ac-227   X X     | X       | ? ? ?   | X X X   | X X X   |

90-Th-228   X X     | X       | + X X   | X X X   | X X X   |

90-Th-230   + X     | X       | + X X   | X X X   | X X X   |

90-Th-232   X X     | X     X | +     X | X X   X | X     X |

90-Th-234   X X     | X       | + X X   | X X X   | X X X   |

91-Pa-231   X X     | X     X | X     X |   ?   ? | X     X |

91-Pa-233   X X     | X     X | +     X |   ?   ? | X     X |

92-U -235   X X     | X       | X X X   | + X   X | X     X |

93-Np-239   X X     | X       | + X X   | X X X   | X X X   |

94-Pu-238   X X     | X       | X X X   | + X X   | X X X   |

94-Pu-244   X X     | X       | + X X   | X X X   | X X X   |

94-Pu-246   X X     | X       | + X X   | X X X   | X X X   |

95-Am-242m  X X     | X       | X X X   | + X   X | X     X |

95-Am-244m  X X     | X       | X X X   | + X X   | X X X   |

96-Cm-241   X X     | +       | X X X   | + X X   | X X X   |

96-Cm-242   X X     | X       | + X X   | + X X   | X X X   |

96-Cm-248   + X     | X       | X X X   | + X X   | X X X   |

98-Cf-250   X X     | X       | + X X   | X X X   | + X X   |

98-Cf-251   X X     | X       | X X X   | X X X   | + X X   |

98-Cf-252   X X     | X       | X X X   | X X X   | + X X   |

98-Cf-253   X X     | +       | + X X   |         |         |

99-Es-253   X X     | +       |         |         |         |

Appendix D: Summary of  for all isotopes in ENDF/B-VII.1 and VII.0

For applications involving fission (F) I require both prompt and delayed neutrons per fission. In the ENDF/B format the evaluator can optionally include: Total (T), Delayed (D) and/or Prompt (P); given any two of these three we can uniquely define the third. Below is a summary of all fissile/fertile materials in ENDF/B-VII.1, indicating the neutrons per fission data included for each isotope. This table indicates each evaluation that includes,

F   = Fission cross section (MF/MT=3/18)

T   = Total          (MF/MT=1/452)

D  = Delayed     (MF/MT=1/455)

P  = Prompt        (MF/MT=1/456)

This table indicates VII.1 is in much better shape than VII.0, where more evaluations only included total (T) . In addition there are three evaluations that only include total (T) : 88-Ra-233, 88-Ra-226, and 94-Pu-243. It is also questionable whether or not 88-Ra and 89-Ac should be identified as fissile/fertile.

Summary of all fissile/fertile isotopes in ENDF/B-VII.1 (85 evaluations)

| 88-Ra-223 F T 88-Ra-226 F T 89-Ac-225 F T D P 89-Ac-226 F T D P 89-Ac-227 F T D P 90-Th-227 F T D P 90-Th-228 F T D P 90-Th-229 F T D P 90-Th-230 F T D P 90-Th-231 F T D P 90-Th-232 F T D P 90-Th-233 F T D P 90-Th-234 F T D P 91-Pa-229 F T D P 91-Pa-230 F T D P 91-Pa-231 F T D P 91-Pa-232 F T D P 91-Pa-233 F T D P 92-U -230 F T D P 92-U -231 F T D P 92-U -232 F T D P 92-U -233 F T D P 92-U -234 F T D P 92-U -235 F T D P 92-U -236 F T D P 92-U -237 F T D P 92-U -238 F T D P 92-U -239 F T D P | 92-U -240 F T D P 92-U -241 F T D P 93-Np-234 F T D P 93-Np-235 F T D P 93-Np-236 F T D P 93-Np-237 F T D P 93-Np-238 F T D P 93-Np-239 F T D P 94-Pu-236 F T D P 94-Pu-237 F T D P 94-Pu-238 F T D P 94-Pu-239 F T D P 94-Pu-240 F T D P 94-Pu-241 F T D P 94-Pu-242 F T D P 94-Pu-243 F T 94-Pu-244 F T D P 94-Pu-246 F T D P 95-Am-240 F T D P 95-Am-241 F T D P 95-Am-242 F T D P 95-Am-242m F T D P 95-Am-243 F T D P 95-Am-244 F T D P 95-Am-244m F T D P 96-Cm-240 F T D P 96-Cm-241 F T D P 96-Cm-242 F T D P 96-Cm-243 F T D P | 96-Cm-244 F T D P 96-Cm-245 F T D P 96-Cm-246 F T D P 96-Cm-247 F T D P 96-Cm-248 F T D P 96-Cm-249 F T D P 96-Cm-250 F T D P 97-Bk-245 F T D P 97-Bk-246 F T D P 97-Bk-247 F T D P 97-Bk-248 F T D P 97-Bk-249 F T D P 97-Bk-250 F T D P 98-Cf-246 F T D P 98-Cf-248 F T D P 98-Cf-249 F T D P 98-Cf-250 F T D P 98-Cf-251 F T D P 98-Cf-252 F T D P 98-Cf-253 F T D P 98-Cf-254 F T D P 99-Es-251 F T D P 99-Es-252 F T D P 99-Es-253 F T D P 99-Es-254 F T D P 99-Es-254m F T D P 99-Es-255 F T D P 100-Fm-255 F T D P |
| --- | --- | --- |

Summary of all fissile/fertile isotopes in ENDF/B-VII.0 (65 evaluations)

Comparing the above table for VII.1 and the below table for VII.0 we can see that the  data is much improved, but VII.1 still has the same three deficiencies that we found in VII.0, namely evaluations that only include total (T) : 88-Ra-233, 88-Ra-226, and 94-Pu-243.

| 88-Ra-223 F T 88-Ra-226 F T 89-Ac-227 F T 90-Th-227 F T D P 90-Th-228 F T D P 90-Th-229 F T D P 90-Th-230 F T 90-Th-232 F T D P 90-Th-233 F T D P 90-Th-234 F T D P 91-Pa-231 F T D P 91-Pa-232 F T D P 91-Pa-233 F T D P 92-U -232 F T D P 92-U -233 F T D P 92-U -234 F T D P 92-U -235 F T D P 92-U -236 F T D P 92-U -237 F T D P 92-U -238 F T D P 92-U -239 F T D P 92-U -240 F T D P | 92-U -241 F T D P 93-Np-235 F T D P 93-Np-236 F T D P 93-Np-237 F T D P 93-Np-238 F T D P 93-Np-239 F T 94-Pu-236 F T D P 94-Pu-237 F T 94-Pu-238 F T D P 94-Pu-239 F T D P 94-Pu-240 F T D P 94-Pu-241 F T D P 94-Pu-242 F T D P 94-Pu-243 F T 94-Pu-244 F T 94-Pu-246 F T D P 95-Am-241 F T D P 95-Am-242 F T D P 95-Am-242m F T D P 95-Am-243 F T D P 95-Am-244 F T D P 95-Am-244m F T D P | 96-Cm-241 F T 96-Cm-242 F T D P 96-Cm-243 F T D P 96-Cm-244 F T D P 96-Cm-245 F T D P 96-Cm-246 F T D P 96-Cm-247 F T D P 96-Cm-248 F T 96-Cm-249 F T D P 96-Cm-250 F T D P 97-Bk-249 F T D P 97-Bk-250 F T D P 98-Cf-249 F T D P 98-Cf-250 F T 98-Cf-251 F T D P 98-Cf-252 F T 98-Cf-253 F T 98-Cf-254 F T D P 99-Es-254 F T D P 99-Es-255 F T D P 100-Fm-255 F T D P |
| --- | --- | --- |

Appendix E: The Effects of Temperature and Doppler Broadening

For those readers who are not familiar with the effects of temperature and Doppler broadening on neutron cross sections and transport, for details I suggest that you read references [R5] and [R6], listed below. Here I will give a brief description of these effects. Users of neutron cross sections should be aware that there are several important effects of temperature and Doppler broadening,

1) There is the well known effect in the neutron resonance region, where as the temperature increases resonances become broader, hence the name Doppler broadening. Figure 1 below illustrates the effect of temperature on the U238 capture cross section for neutron reactor like temperatures, and figure 2 illustrates this effect for astrophysical like temperatures. These figures each contain four sub-figures, with each sub-figure comparing cross sections at two progressively higher temperatures. In both figure 1 and 2 each sub-figure shows exactly the same energy and cross section range. From these figures we can see that as temperature increases the peaks of the resonances become lower, and the minima between resonances become higher. At extremely high temperature the entire resonance structure disappears and the cross section approaches a simple 1/v shape (where v is the neutron speed). This temperature effect will have a very important effect on resonance self-shielding in any neutron transport calculation. You should note from these figures that due to the large resonance spacing in U238 the resonance structure can still be seen up to very high temperatures.

To understand the importance of considering temperature we should consider reaction rates, such as captures/second, in various systems. In optically thin systems (few mean free paths dimensions) the flux will be unshielded, and our reaction rates will be defined by a simple cross section average,

Unshielded Capture =   = capture cross section times neutron flux

In optically thick systems (many mean free paths dimensions) the flux will be shielded (the flux is suppressed by the total cross section) and our reaction rates must include the effect of self-shielding on the cross section average,

Shielded Capture =  = including one over total cross section

Consider for example the U238 capture cross section between 1 and 10 keV as shown in fig. 1 and 2. If we calculate the unshielded and shielded average capture cross section for the energy interval over the range of temperatures shown in figs. 1 and 2, we obtain the results shown below in table 1.

What we see from these results is that the unshielded average capture cross section is virtually independent of temperature, being about 1 barn over the entire temperature range. In contrast the shielded average cross section varying by over a factor of three between the 0 K average (0.293 barns) and the 10 keV average (0.939 barns). The point to learn from this is that without including the effect of self-shielding in multi-group calculations, temperature has very little effect on the average cross sections, which is quite simply wrong for optically thick systems.

Table 1: Effect of Temperature on Average Cross Sections

Temp.		Unshielded	Shielded

(barns)	(barns)

0 K		0.996		0.293

293.6 K		0.966 	0.526

600 K		0.996		0.576

1,200 K		0.996		0.630

12,000 K (1 eV)	0.996		0.799

10 eV		0.998		0.905

100 eV		1.000		0.933

1 keV		1.004		0.935

10 keV		1.007		0.939

2) Another, less well known, effect of Doppler broadening is at lower energies where as temperature increases the low energy constant scattering cross section increases and at very low energies approaches a simple 1/v shape (where v is the neutron speed); this effect is explained in detail in ref [R5]. Figure 3 illustrates the effect of temperature on the hydrogen total cross section. From this figure we can see that starting from a “cold” (0 Kelvin) cross section that is constant at about 20 barns, as temperature increases the cross section increases. Compared to the “cold” 20 barn cross section, at thermal energy the Doppler broadened cross section is about 30 barns, i.e., 50 % higher. Note also from this figure that this effect extends well above thermal energy. For example, at 293.6 Kelvin the thermal energy is 0.0253 eV, but we can see this effect up to about 1 eV; a factor of 400 higher in energy. From the lower half of figure 2 we can see that at very low energy the cross section approaches a simple 1/v shape (where v is the neutron speed) and the cross sections at various temperatures become proportional to one another. This effect on the cross sections at low energy is very important for thermal and low energy neutron systems.

3) Yet another important effect of temperature is that at lower energies neutrons do not slow down in energy as quickly and neutron scatter can even result in the upscatter of neutrons, i.e., when neutrons scatter they can gain, rather than lose, energy. This is a well known effect at low energies, where thermal scattering law data or a free gas model is used to model the interaction of neutrons with target atoms that are moving about with thermal motion. Figure 4 illustrates the effect of temperature on the neutron spectrum over a wide range of temperatures [R7]. This effect can also be important at higher energies, particularly near narrow resonances, where thermal motion of the target atoms can cause neutrons to slightly upscatter, but even slight upscatter can cause a neutron to scatter from below to above the energy of a very narrow resonance. See reference [R6], below for a routine designed to be used in conjunction with the SIGMA1 method of Doppler broadening [R5], to handle neutron thermal scattering. This routine [R6] is completely compatible for use with the cross sections included here, since these cross sections were Doppler broadened using the SIGMA1 method [R5]. The combination of SIGMA1 [R5] Doppler broadened cross sections and THERMAL [R6] to handle thermal scattering, is currently used in the TART Monte Carlo transport code [R8].

Fig.1: Effect of Doppler Broadening on Resonance Cross Sections

Fig.2: Effect of Doppler Broadening on Resonance Cross Sections

Fig.3: Effect of Doppler Broadening on Low Energy Cross Sections

Fig.4: Effect of Doppler Broadening on Neutron Spectrum